## Slide 1: Architectural Optimizations
David Ojika
March 27, 2014

## Slide 2: Focus
From OpenCL to High-Performance Hardware on FPGAs
    Tomasz S. Czajkowski, Altera OpenCL Optimization Group
    IEEE 2012
OpenCL for FPGAs: Prototyping a Compiler
    Tomasz S. Czajkowski, Altera OpenCL Optimization Group
    ESRA 2012

## Slide 3: Outline
Introduction
FPGA as an Acceleration Platform
HLS Vs. OpenCL in Accelerators
OpenCL-To-FPGA Compiler
System Integration
Implementation Details
Optimization Strategies
Memory Issues
Experimental Setup
Results
Conclusion

## Slide 4: Introduction
Traditionally, FPGAs been used as de-factor standard for many high-performance applications
  Some of the largest and most complex circuits
  Applications in medical imaging, molecular dynamics, etc.
Nowadays, FPGA’s being used as accelerator to speedup computationally-intensive applications
  Orders of magnitude reduction in runtime compared to traditional stand-alone computers
  Hardware parallelism enable many computations to be performed at same time
Traditional
Emerging

## Slide 5: FPGA as Acceleration Platform
FPGAs enable high application acceleration in many domains
  However, parallel computation at hardware level requires great expertise
    Poses limitations in adoption of FPGAs as hardware accelerators
GPUs being used as accelerators in computing for many years
  Interests by software programmers to use GPU in general-purpose computing lead to development of new programming models
    CUDA for GPU
    OpenCL for GPU, CPU, FPGA, DSP
FPGA Accelerator
Kernel
CUDA Model
OpenCL Model
FPGAs starting to compete with GPGPUs for app acceleration
GPGPU: General-Purpose Graphics Processing Unit

## Slide 6: HLS Vs. OpenCL in Accelerators
Tool implement FPGA circuit from software-like languages
  Many circuits can simultaneously process data
    Does not exploit parallelism in hardware
  Pipelining not explicit in C programming language
    Performance may be suffer comparable in to VHDL/Verilog implementation
Computation performed using combination of host & kernels
  Host responsible for I/O and setup of task
  Kernel perform computation on independent inputs
    Kernel can be implemented as high-performance circuit
    Kernel can be replicated to improve performance of application
Challenge  Efficiently synthesize kernel into HW circuits?
Solution  Compiler that performs architectural optimizations!
Traditional HLS
OpenCL

## Slide 7: OpenCL-To-FPGA Compiler
Framework based on LLVM compiler infrastructure
  Input 1: OpenCL app with set of kernels (.cl)
  Input 2: Host program (.c)
Kernel Compilation
  C language parser produces LLVM IR of each kernel
  Representation optimized to target FPGA platform
  Optimized LLVM converted to CDFG
  CDFG optimized to improve area and performance
  RTL generation produces Verilog HDL for kernel
  HDL compiled to generated bitstream for programming
Host Compilation
  ACL Host Library:
    Implements OpenCL function calls; allows exchange of information between host and FPGA
  Auto-Discovery module:
    Allows host program to discover types of kernels on FPGA
Output: Verilog HDL
Notes: LLVM IR: in form of instructions and dependencies between them
    Auto-Discovery Module: Embedded in system by kernel compiler; stores information pertaining to kernels

## Slide 8: System Integration
Host accesses kernel
  Specifies workspace parameter (global & local work size)
  Sets kernel arguments
  Enqueues kernel
Device replicates kernel
  Runs kernel
  Provides result to DDR mem.
FPGA Accelerator
Kernel

## Slide 9: Implementation Details
1. ACL Host Library
  Host Library: Implements OpenCL data and control specs.
2. Kernel Compiler
  Kernel: Compute-intensive workload offloaded from CPU

## Slide 10: ACL Host Library
Implements Platform & Runtime APIs of OpenCL 1.0 spec
Platform API
  Discover FPGA accelerator device
  Manage execution contexts
Runtime API
  Manage command queues
  Memory objects
  Program objects
  Discover and invoke precompiled kernels
Consists of two layers
Platform Independent Layer: Performs device independent processing
  Provides user visible OpenCL API functions
  Performs generic book-keeping and scheduling
Hardware Abstraction Layer: adapts to platform specifics
  Provides low-level services to platform independent layer
    Device and kernel discovery, raw memory allocation, memory transfers, kernel launch and completion

## Slide 11: Kernel Compiler
Compiles kernel into hardware circuit using LLVM open-source compiler
  Extends compiler to target FPGA platforms
LLVM Flow:
  Represents program as sequence of instructions: load, add, store
  Each instruction has associated input; produces results that can be used in downstream computation
  Basic Block: group of instructions in contiguous sequence
  Basic block have a terminal instruction that ends program or redirects execution to another basic block
  Compiler uses representation to create hardware implementation of each basic block; put together to form complete kernel circuit
Notes: Each basic block constitutes an input and output interface with which it talks to other basic blocks
- First and last basic blocks have interfaces exposed at top level, forming input and output of kernel module

## Slide 12: Optimization Strategies
1. C-Language Front-End
    Produce intermediate representation
2. Live Variable Analysis
    Identifies variables produced and consumed by each basic block
3. CDFG Generation
  Challenge: Each operational node can be independently stalled when successor node unable to accept data
  Solution: Two signals and gates. Valid signal into node is AND gate of its data sources
Loop Handling (Handled in Basic Block building step)
  Challenge: It is entirely possible that a loop can stall
  Solution: Insert addition stage of registers into merged node; allows pipeline to have additional spot into which that can be placed
1
2
3
4
5

## Slide 13: Optimization Strategies
4. Scheduling
  Challenge: No sharing of resources occurs; need to sequence operations into pipeline
  Solution: Apply SDC scheduling algorithm; uses system of linear equations to schedule operations while minimizing cost function
  Objective: Area reduction & amount of pipeline balancing regs required
  Solution: Minimize cost function that reduces number of bits required by pipeline
5. Hardware Generation
  Challenge: Potentially large number of independent threads need to execute using a kernel hardware
  Solution: Implement each basic block module as pipelined circuit rather than finite state machine with datapath (FSMD)
1
2
3
4
5
Notes:   Scheduling: No sharing of resources occurs; need to sequence operations into pipeline where independent operations occurs in parallel

## Slide 14: Memory Issues
Global memory
Local memory
Private memory

## Slide 15: Global Memory
Designated for access by all threads
Large capacity for data storage; I/O by all threads
Long access latency
Optimization
  Access are coalesced when possible to increase throughput
  Compiler can detect when accesses are random or sequential and takes advantage of it
    When access sequential, special read or write module that includes large buffer created for burst transactions
    When access random, coalescing unit collects request to see if seemingly random accesses address the same 256-bit word in memory. If so, request coalesced in single data transfer, improving memory throughput

## Slide 16: Local Memory
Access by threads in same work group
Short latency and multiple ports; efficient kernel access by kernels
Enable synchronized exchange of data
Barriers/memory fences used to force threads to wait on one another before proceeding
  Enables complex algorithm that require collaboration of threads, E.g. Bitonic sort
Optimization
  Shared memory space for each LD/ST to any local memory
    Map logical ports required by kernel unto set of dual-ported on-chip memory modules
    Access split into multiple memory banks to enable faster data access

## Slide 17: Private Memory
Implemented with registers; store data on per-thread basis
Pipelined through kernel to ensure each thread keeps data required as it proceeds with execution through the kernel
Optimization
  None

## Slide 18: Experimental Setup
Accelerator
  Stratix-IV on Terasic DE4 board
Host
  Windows XP 64-bit machine
Offline Kernel Compiler
  ACDS 12.0
Benchmarks
  Monte Carlo Black-Scholes
  Matrix Multiplication
  Finite Differences
  Particle Simulation

## Slide 19: Results
Monte Carlo Black Scholes
  OpenCL against Verilog code
    Throughput: 2.2 Gsims/sec in comparison to 1.8 GSims/sec with 2 Stratix-III FPGAs
Finite Difference and Particle Simulation
  Not much comparative performance with previous work recorded
Table 1: Circuit Summary and Application Throughput
Matrix Multiplication
  1024 x 1024 matrix size
  Vectorized kernel
    Improves thread access to memory; increased throughput by x4
  Unrolled inner loop
    Performs 64 floating-point multiplications and addition simultaneously
    Results in 88.4 GFLOPS throughput

## Slide 20: Conclusion
Developed compilation framework that includes host library for communicating with kernels
Developed OpenCL-to-FPGA compiler with optimizations
  Results show that tool flow is not only feasible, but also effective in designing high-performance circuits
Results indicate that OpenCL well suited for automatic generation of efficient circuits for FPGA
  Coverage of OpenCL language: synchronization (barriers), support for local memory and floating-point operations
THANKS!