## Slide 1
Energy-efficient Phase-based Cache Tuning of Multimedia Applications in Embedded Systems
+ Also Affiliated with NSF Center for High-Performance Reconfigurable Computing
This work was supported by National Science Foundation (NSF) grant CNS-0953447
Tosiron Adegbija and Ann Gordon-Ross+
Department of Electrical and Computer Engineering
University of Florida, Gainesville, Florida, USA

## Slide 2: Introduction and Motivation
Embedded systems are prevalent and have several design challenges
  Design goals for optimization: reduce cost, energy consumption, time to market, increase performance, etc
  Design constraints: energy, area, real time, cost, etc
Multimedia applications very common in embedded systems
  Consumers demand advanced functionality and performance
    More energy and computational capabilities
  Multimedia applications have data-intensive bandwidth requirements
  Caches used to bridge processor-memory performance gap
Multimedia applications increase pressure on design challenges in embedded systems

## Slide 3: Introduction and Motivation
Caches account for up to 50% of embedded system processor’s power
Thus, caches are good candidates for optimization
Different applications have vastly different cache parameter value requirements
  Configurable parameters: size, line size, associativity
  Parameter values that do not match an application’s needs can waste over 60% of energy (Gordon-Ross ‘05)
Cache tuning determines the best configuration
(combination of configurable parameters) that
meets optimization goals (e.g., lowest energy)
However, cache tuning is challenging
due to potentially large design spaces
Design space
100’s – 10,000’s
Lowest energy

## Slide 4: Configurable Caches
Configurable caches enable cache tuning
  Specialized hardware enables the cache to be configured at startup or dynamically during runtime
2KB
2KB
2KB
2KB
8 KB, 4-way base cache
2KB
2KB
2KB
2KB
8 KB, 2-way
2KB
2KB
2KB
2KB
8 KB, direct-mapped
Way concatenation
2KB
2KB
2KB
2KB
4 KB, 2-way
2KB
2KB
2KB
2KB
2 KB, direct-mapped
Way shutdown
Configurable Line size
16 byte physical line size
A Highly Configurable Cache (Zhang ‘03)
Tunable Associativity
Tunable Size
Tunable Line Size

## Slide 5: Dynamic Cache Tuning
Energy
Executing in base
configuration
Tunable cache
Tuning hardware
TC
Cache Tuning
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
Download application
Microprocessor
Cache energy savings of 62% on average!
(Gordon-Ross ‘05)
Dynamic cache tuning changes system parameter values at runtime
  Dynamically determines best cache configuration with respect to optimization goals (e.g., lowest energy/best performance)
  Requires tunable cache and cache tuner
    Cache tuner evaluates different configurations to determine the best configuration
Lowest energy
Execution time

## Slide 6: Dynamic Cache Tuning
Advantages
  Adapts to the runtime operating environment and input stimuli
  Specializes cache configurations to executing applications
Disadvantages
  Large design space
    Challenging to determine the best cache configuration
  Runtime cache tuning overhead (e.g., energy, power, performance)
    Energy consumed and additional execution time incurred during cache tuning
Tunable cache
Tuning hardware
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
Download application
Microprocessor

## Slide 7: Phase-based Cache Tuning
Time varying behavior for IPC, level one data cache hits, branch predictor hits, and power consumption for SPEC2000 gcc (using the integrate input set)
Base energy
Application-tuned
Time
Energy Consumption
Phase-tuned
Change configuration
Greater savings when tuning is phase-based, rather than application-based
Applications have dynamic requirements during execution
  Different phases of execution
Tune when the phase changes, rather than when the application changes
  Phase = a length of execution where application characteristics are relatively stable
    Characteristics: cache misses, branch mispredictions, etc

## Slide 8: Phase-based Cache Tuning
Phase classification
Application x
Conf1
Conf2
Conf3
Conf4
Conf5
Profiler
Fixed length intervals
Variable length intervals
Notes: Divide application into fixed or variable length intervals
Group intervals with similar characteristics
5 different configurations work best for the phases in this scenerio

## Slide 9: Multimedia Applications
Periodically process units of data - frames
  Multimedia applications exhibit stable frame-to-frame application characteristics (Hughes ’01)
  Different frame types constitute phase-based behavior
Thus, multimedia applications are ideal candidates for phase-based cache tuning
  Fine-grained tuning
  Improve energy consumption
Frames typically have deadlines
  Cache configurations must not significantly increase execution time
How to determine the best cache configurations
for the different phases?

## Slide 10: Previous Cache Tuning Methods
Possible Cache Configurations
Energy
Heuristic method
Execution time
Energy
Execution time
Energy
Possible Cache Configurations
Energy
Analytical method
Execution time
Energy
Possible Cache Configurations
Energy
Exhaustive method
A lot of tuning
overhead
Less tuning
overhead
No tuning overhead
but computationally
complex/not dynamic
Previous work proposed Phase Distance Mapping (PDM):
a low-overhead and dynamic analytical method (ICCD ‘12).

## Slide 11
Base phase
Phase Pi
Cache characteristics | Cache configuration
Pb | ConfigPb
Cache characteristics | Cache configuration
Pi | 
New phase
d (Pb, Pi)
Phase distance
Configuration distance
ConfigPi_pdm
??
Phase Distance Mapping (PDM)
Previously characterized phase
Distance windows
Phase distance
ranges
Configuration
change from
ConfigPb
Configuration estimation
algorithm
Phase history table

## Slide 12: Contributions
We present an approach to cache tuning for multimedia applications
  Leverages fundamental PDM concepts
    Reduces tuning overhead
Achieves fine-grained energy optimization
  Use energy delay product (EDP) to take into account energy and execution time
  Minimal designer effort
  29% system EDP savings and 1% execution time overhead
Algorithm considers multimedia applications’ characteristics
  Variable execution characteristics
  High spatial locality
  Block-partitioning algorithms
  Data memory references to internal data structures (e.g., arrays)
  Frame deadlines

## Slide 13: Multimedia Application Characteristics
Cache
Data
Data
A
B
C
D
E
F
Block-partitioning algorithms
High spatial locality
Benefits from
large line sizes
Save energy by using
smaller cache sizes
Cache
Data memory references
to internal data structures
Save energy by using
smaller cache sizes
t1
t2
t3
t4
time
frames
Frame deadlines
Execution time must
not exceed deadline

## Slide 14: Phase-based Tuning Algorithm Overview
Phase
classification
Phase Pi
previously
characterized?
Get ConfigPi from
phase history table
Yes
Execute in
ConfigPi
No
Initialization
stage
Cache
configuration
adjustment stage
Store best ConfigPi in
phase history table
Deadline met/
cannot meet
deadline?
Yes
No
Determines initial
cache configuration
Hones initial
cache configuration
closer to optimal

## Slide 15: Initialization Stage
Minimize number of configurations explored/tuning overhead
  Determine initial configuration, ConfigPi_init for configuration adjustment stage
ConfigPi_init =
ConfigPi_pdm, if EDP[ConfigPi_pdm] < EDP[ConfigPi_msp]
ConfigPi_msp, if EDP[ConfigPi_msp] < EDP[ConfigPi_pdm]
Configuration estimation
algorithm
ConfigPi_pdm
ConfigPi_msp = ConfigPj, | D = min(D(Pi, Pj)), j = i – 1, i – 2, … i - n
Most similar phase’s
best cache configuration
phase distance
number of previously
characterized phases

## Slide 16: Cache Configuration Adjustment Stage
Iteratively tunes ConfigPi_init’s parameter values until best configuration is determined
Tune associativity
EDP increased or
all associativities?
EDP[ConfigPi] > 0.25*EDP[ConfigPi_base]
No
Tune line size
EDP increased or
all line sizes?
EDP[ConfigPi] > 0.25*EDP[ConfigPi_base]
No
Tune cache size
EDP increased or
all cache sizes?
No
Stop tuning
EDP[ConfigPi] ≤ 0.25*EDP[ConfigPi_base]
Explored from
smallest to largest
Explored from
largest to smallest
Explored from
largest to smallest

## Slide 17: Experimental Results

## Slide 18: Experimental Setup
Design space
  Level 1 (L1) instruction and data caches: cache size (2kB 8kB); line size (16B64B); associativity (direct-mapped4-way)
  Base cache configuration:
    L1 instruction and data caches: cache size (8kB); line size (64B); associativity (4-way)
13 benchmarks from Mediabench and Mibench suites
  Specific compute kernels
    E.g., JPEG compression and decompression, audio encoding and decoding, etc.
  Each workload represented a phase

## Slide 19: Experimental Setup
Simulations
  GEM5 generated cache miss rates
  McPAT calculated power consumption
    Energy delay product (EDP) as evaluation metric
      = system_power * (total_phase_cycles/system_frequency)2
Determined optimal cache configurations using exhaustive search
  Used lowest EDP cache configuration as optimal
Defined deadlines to represent different timing constraints
  Deadline-1: loose timing constraints, no specified deadline
  Deadline-2: stringent timing constraints, shortest execution time
  Deadline-3: 5% longer than shortest execution time
  Deadline-4: 10% longer than shortest execution time

## Slide 20: Results
Deadline-1: loose timing constraints, no deadline specified
  Savings calculated with respect to base configuration
  29% average energy and EDP savings overall
  1% average execution time degradation
  Optimal configurations determined for ten out of thirteen phases, remaining three within 1% of optimal
Chart: Execution time, energy, EDP normalized to the base configuration
| djpeg | cjpeg | jpegtran | rdjpgcom | wrjpgcom | mad | lame | mpeg2encode | mpeg2decode | epic | unepic | g721encode | g721decode | average
Execution time | 1.0378 | 0.99843 | 1.0265 | 1.0064 | 1.0069 | 1.0413 | 1.0133 | 1.004 | 1.0243 | 1.0066 | 1.0169 | 0.95094 | 0.94368 | 1.0059
Energy | 0.72195 | 0.6946 | 0.71411 | 0.72368 | 0.70043 | 0.74876 | 0.70492 | 0.69844 | 0.71253 | 0.69924 | 0.73123 | 0.68468 | 0.69646 | 0.71008
EDP | 0.74924 | 0.69351 | 0.73306 | 0.72834 | 0.70523 | 0.7797 | 0.71431 | 0.70123 | 0.72981 | 0.70385 | 0.74361 | 0.65109 | 0.65723 | 0.71463
29%
29%
-1%

## Slide 21: Results
Deadline-2: stringent timing constraints, shortest execution time
  Savings calculated with respect to base configuration
  1%, 11% and 12% average execution time, energy and EDP savings, respectively
  Energy and EDP savings as high as 32% and 35%, respectively, for g721encode
  Deadlines met for all phases
11%
12%
1%
Chart: Execution time, energy, EDP normalized to the base configuration
| djpeg | cjpeg | jpegtran | rdjpgcom | wrjpgcom | mad | lame | mpeg2encode | mpeg2decode | epic | unepic | g721encode | g721decode | average
Execution time | 1 | 0.98518 | 1 | 1 | 1 | 0.99932 | 1 | 0.99982 | 1 | 1 | 1 | 0.95094 | 0.94368 | 0.99069
Energy | 1 | 0.8832 | 1 | 0.72368 | 0.89591 | 0.82108 | 1 | 0.82242 | 1 | 1 | 1 | 0.68468 | 0.69646 | 0.88672
EDP | 1 | 0.87011 | 1 | 0.72834 | 0.89723 | 0.82053 | 1 | 0.82227 | 1 | 1 | 1 | 0.65126 | 0.65723 | 0.88054
Deadline-3 and -4 did NOT degrade energy and EDP savings from Deadline-1 results!!

## Slide 22: Results
EDP comparison to prior work (PDM) with Deadline-1
  Savings calculated with respect to base configuration
  PDM’s and our algorithm’s average EDP of 11% and 29%, respectively
  EDP savings increase as high as 62% for wrjpgcom
Chart: EDP normalized to the base configuration
| djpeg | cjpeg | jpegtran | rdjpgcom | wrjpgcom | mad | lame | mpeg2encode | mpeg2decode | epic | unepic | g721encode | g721decode | average
PDM | 0.82427 | 0.75454 | 0.8768 | 0.82726 | 1.888 | 0.77788 | 1.1266 | 0.82635 | 0.73921 | 0.72406 | 0.78304 | 0.73483 | 0.65723 | 0.8877
Algorithm | 0.74924 | 0.69351 | 0.73306 | 0.72834 | 0.70523 | 0.7797 | 0.71431 | 0.70123 | 0.72981 | 0.70385 | 0.74361 | 0.65109 | 0.65723 | 0.71463
29%
11%
18%
18% average EDP increase over PDM!!

## Slide 23: Conclusions
We presented a phase-based cache tuning algorithm for multimedia applications in embedded systems
  Leverages analytical phase based tuning methodology – Phase Distance Mapping (PDM)
    Fine-grained, low-overhead tuning
  Leverages multimedia applications’ characteristics
  Average EDP savings of 29%, execution time degradation of only 1% compared with default base configuration
Future work
  Evaluate algorithm in multilevel caches
  Tune other hardware that have significant impact on multimedia applications, e.g., clock frequency, instruction issue width, etc.

## Slide 24: Questions?