## Slide 1: Partially Reconfigurable System-on-Chips for Adaptive Fault Tolerance
Shaon Yousuf
Adam Jacobs
Ph.D. Students
NSF CHREC Center, University of Florida
Dr. Ann Gordon-Ross
Assistant Professor of ECE
NSF CHREC Center, University of Florida

## Slide 2: Introduction
Many space systems use remote sensing applications
  Gathers information about a target of interest from a distance
Gathered information requires processing
  Send data to ground station or other space systems using communication link
Modern remote sensing applications are complex
  Gathers a large amount of data
  Impractical to send all data through communication link
    System performance bottlenecked by limited communication bandwidth
  Solution: Pre-process data and transmit results
    On-board processing using system-on-chips (SoCs)
Preprocess Data
Limited Bandwidth
Notes: Est time for slide: 0:45 min
Total = 0:45 min

## Slide 3: SoCs for Space Applications
SoCs increase on-board data processing capabilities
  However, increases the system’s payload
  Optimized/customized SoCs for use in space (space SoCs) required
    Provide cost effective, high performance, and reliable data processing
  Traditionally, space SoCs consist of radiation hardened (rad-hard) devices
Specialized device enable reliable on-board data processing
Fixed/static design provide all the application’s required functionality all of the time
Specialized equals expensive
Increased payload
Rad-hard devices

## Slide 4: SoCs for Space Applications
Is there a better choice?
  Sure, why not use commercial-off-the-shelf (COTS) SRAM-based FPGAs
    Cheaper than rad-hard devices
    Allows reprogrammability (time multiplex hardware resources to reduce payload)
Is it that simple?
  Well, no
    In space, cosmic radiation corrupts FPGA SRAM!
    These are called single event upsets (SEU)s
FPGA
10111011
FPGA
01101100
Fault tolerance (FT) techniques used for reliability (provide redundant copies of required functionality)
Efficient SoC design to ensure a particular functionality along with required FT is available when required
Simple but Inefficient
Increased design complexity
COTS FPGA devices

## Slide 5: SoCs for Space Applications
So what do we do?
  Efficient system management by adapting to varying levels of radiation in space
    Same degree of FT (reliability) not required all the time
    Reconfigure FPGA to provide adaptive fault tolerance (AFT)
  Mitigate design complexity by designing a AFT base platform
    Enable rapid design and deployment of space applications
Low radiation orbit
High radiation Orbit
High radiation Orbit
High radiation Orbit
High reliability required
Low reliability will suffice

## Slide 6: AFT using FPGA Reconfiguration
FPGAs offer two reconfiguration (reprogrammability) methods
  Full reconfiguration (FR), which halts and reconfigures the entire FPGA
    Can impose significant performance overhead
  Partial reconfiguration (PR) halts and reconfigures a portion of the FPGA
    Mitigates FR performance issues by isolating reconfiguration to selected parts
PRR – Partially reconfigurable regions
Central Controlling Agent
ICAP
Mem controller
Module A
Module B
Module C
Static modules
Reconfigurable Modules (PRMs)
PRR 1
PRR 2
Static region
Static modules
Module: A & B
Modules: C & D
Module D
FPGA Fabric
Example with 2 PRRs

## Slide 7: Contribution
* A. Jara-Berrocal, A. Gordon-Ross, "VAPRES: A Virtual Architecture for Partially Reconfigurable Embedded Systems," Design, Automation & Test in Europe Conference & Exhibition (DATE), March 2010
In this work, we present an adaptive fault tolerant partially reconfigurable system-on-chip (AFT PR SoC)
  Leverages VAPRES*
    A Virtual Architecture for Partially Reconfigurable Embedded Systems
  Contains a data flow controller to manage data flow to and from PRRs
    Enables high SoC throughput by continuous data stream processing
  Contains a software-based AFT controller to vary the degree of FT
    Dynamically reconfigures the PRRs and changes the reliability mode according to the current orbital position
  The AFT PR SoC decrease payload and cost of space systems as compared to traditional static FT systems
  The AFT PR SoC can be leveraged as a base platform to deploy a multitude of different space applications

## Slide 8: Why VAPRES ?
MicroBlaze CPU
PR
Region 1
PR
Region 2
IO
Module
To IO
PLB Bus (other peripherals: SDRAM, UART)
PR Socket
GPIO Peripheral
PR Socket
PR Socket
ICAP
FSL
Fast
Simplex
Links
Switch 1
Switch 2
IF
IF
IF
IF
Slice macro
Regional clock buffer (BUFR)
MicroBlaze CPU
PR
Region 1
PR
Region 2
PLB Bus (other peripherals: SDRAM, UART)
GPIO Peripheral
PR Socket
PR Socket
PR Socket
FSL
Fast
Simplex
Links
IO
Module
To IO
Switch 1
Switch 2
IF
IF
IF
IF
ICAP
Independent clocks
Control functions
Reconfiguration
Data
Streaming data channels
VAPRES is a multipurpose, scalable, flexible architecture
  Flexible, scalable
    PRR count
    PRR size
    Number of FSLs per PRR/IOM
    MACS bandwidth
  Good platform for developing complex reconfigurable applications
Notes: Changes: Left side, bullet 2.1

## Slide 9: AFT PR SoC Design Consists of Two Steps
Data flow controller step
  Creates an HDL-based finite state machine to orchestrate the dataflow between the MicroBlaze and PRRs
Software-based AFT controller step
  Creates a C-based AFT controller module that allows the MicroBlaze to adaptively change the reliability mode

## Slide 10: Data Flow Controller
Idle
Read_Data
Read_Write_Data
Write_Data
Stall
If p_consumerfsl_rdy/
ce = 1, start = 1
If p_consumerfsl and rfd and done/
ce=1, start=1
If !p_consumerfsl_rdy
If p_consumerfsl and rfd and !done/
ce=1, start=1, p_consumer_en =1, p_consumer_data (32) = input_data (32)
If !p_producer_rdy and !rfd/
p_consumer_en=0
If dv and p_producer_rdy/
p_producerfsl_en = 1
p_producerfsl_data(32) = output_data(32)
If !p_producer_rdy/
ce= 0, start=0
If !p_producer_rdy /
ce= 0, start=0
If !p_producer_rdy /
ce= 0, start=0
If p_producer_rdy/ ce= 1, start=1
If !data_valid/ ce = 0, start = 0
If p_consumerfsl and rfd and dv and p_producer_rdy/
p_consumer_en =1, p_consumer_data (32) = input_data (32),
p_producerfsl_en = 1,
p_producerfsl_data(32) = output_data(32)

## Slide 11: Software-based AFT Controller
AFT controller brings efficient resource management to traditional fault tolerant (FT) systems
  Required FT level varies to match current orbital position’s radiation level
  Offers four reliability modes (software-based switching)
    Reliability mode switching depends on thresholds
  Required FT level dictates hardware task (PRMs) loading/unloading into PRRs
    Unused PRRs turned off to save power (power saving mode)
  Software voter detects anomalies and refreshes PRRs (configuration scrubbing) when errors detected (refresh mode)
MicroBlaze CPU
PLB Bus (other peripherals: SDRAM, UART)
GPIO
Peripheral
PR Socket
ICAP
Voter+Controller
FSL
Fast
Simplex
Links
PR
Region 1
PR
Region 2
PR
Region 3
PR Socket
PR Socket
Data
PR
Region 4
PR Socket
FFT
FFT
FFT
Matrix Multiply
Matrix Multiply
TMR – Triple modular redundancy
SCP – Self-checking pairs
ABFT – Algorithm-based fault tolerance
Reliability modes
  High reliability – TMR
  Medium reliability – SCP
  Low reliability – PRM loaded into single PRR
  Hybrid reliability
    Use low reliability mode for PRMs with ABFT
    Use medium/high reliability for PRMs without ABFT
Matrix Multiply
CORDIC
PRM – Partially reconfigurable modules

## Slide 12: Experimental Setup
Software
  Xilinx ISE design suite 12.4
  AFT VAPRES SoC compared to SoC without AFT
    Both SoCs have 4 PRRs
    PRRs reconfigured with 1k-point FFTs
    PRRs span 40 vertical and 21 horizontal configuration logic blocks (1,680 slices each)
  SoC without AFT always operates in TMR mode (worst-case condition)
  AFT SoC switches according to thresholds
    Low SEU rate threshold of 2.0 SEUs per day for switching between low to medium reliability
    High SEU rate threshold of 8.0 SEUs per day for switching between medium to high reliability
  Virtex-5 LX110T ISS orbit fault rates applied
Hardware
  XUPV5-LX110T board
* http://celestrak.com/NORAD/elements/stations.txt
** Quinn, H.; Morgan, K.; Graham, P.; Krone, J.; Caffrey, M.; , "Static Proton and Heavy Ion Testing of the Xilinx Virtex-5 Device," Radiation Effects Data Workshop, 2007 IEEE , vol.0, no., pp.177-184, 23-27 July 2007 doi: 10.1109/REDW.2007.4342561 URL: http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=4342561&isnumber=4342526
CRÈME96 Virtex-5 Weibull parameters** | 
Onset (um) | 0.5
Width (w) | 30
Power (s) | 1.5
Limit (um2) | 1.13E-7
CRÈME96 ISS (ZARYA) Orbit Parameters* | 
Apogee (km) | 355
Perigee (km) | 352
Inclination (º) | 51.6472
Initial Longitude (º) | 339.10
Initial displacement from ascending node (º) | 217.9038
Displacement of perigee from ascending node (º) | 185.0581
Virtex-5 LX110T ISS orbit fault rates calculated using crème tool (https://creme.isde.vanderbilt.edu)
ISS – International space station
Notes: Est time for slide: 0:20 min
Total = 10:50 min

## Slide 13: Virtex-5LX110T ISS orbit SEU rates
South Atlantic Anomaly (SAA)
Poles
Calculated using CRÈME 96 tool
Notes: Dr. George: incomplete, needs much work
Dr. Ann: Not sure about the title here. It says increased productivity, but this slide is about AFT. Not entirely what that work was targeted for.

## Slide 14: AFT PR SoC Resource Requirements and Analysis
Resource Type | 1-K point FFT Core | AFT PR SoC
Slice | 1, 680 | 12,351
BRAM/FIFO | 10 | 50
SoC operates at 100MHz
  71% of total device slices used
Normalized PRR resource utilization calculation
Symbol | Definition
Pnru | Normalized resource utilization
Pav | Total PRRs available
Preq | Number of PRRs required per PRM
Pused | Number of PRRs used per PRM
Pex | Number of extra PRRs used
Pfree | Number of free PRRs
Pusable | Number of usable free PRRs
where, , ,
and
Finally,
Notes: Est time for slide: 0:20 min
Total = 10:50 min

## Slide 15: AFT PR SoC Resource Utilization
100% PRR utilization
50% PRR utilization
Average 21% increase in PRR resource utilization over 24-hour period
Notes: Dr. George: incomplete, needs much work
Dr. Ann: Not sure about the title here. It says increased productivity, but this slide is about AFT. Not entirely what that work was targeted for.

## Slide 16: Conclusions and Future Work
Conclusions
  We designed and implemented an adaptive fault tolerant partially reconfigurable system-on-chip (AFT PR SoC) leveraging VAPRES
    The Virtual Architecture for Partially Reconfigurable Embedded Systems
  A novel MicroBlaze-based software controller (AFT controller) adapts the AFT PR SoC’s fault tolerance to changing space radiation levels
    Achieves higher resource utilization in comparison to a traditional triple modular redundancy (TMR)-based fault tolerant (FT) PR SoC
    Our results indicate the AFT PR SoC can achieve an average of 22% higher resource utilization in the International Space Station (ISS) orbit compared to a traditional FT SoC
  The AFT PR SoC is an ideal platform for space SoCs
    System designers can implement a wide variety of applications using the AFT PR SoC’s PRRs
Future Work
  Integrating an operating system in our space SoC to allow parallel software processes to control voting and reliability mode switching
  Upgrading the AFT PR SoC’s MicroBlaze processor with a LEON3FT fault tolerant processor to provide additional system reliability
  Using fault injection techniques to test our space SoCs robustnes
Notes: Est time for slide: 0:30 min
Total = 15:00 min

## Slide 17
QUESTIONS?
This work was supported in part by the I/UCRC Program of the National Science Foundation under Grant No. EEC-0642422. We also gratefully acknowledge tools provided by Xilinx.