## Slide 1: FTCA: On-Board Processing Design Optimization Framework
Dr. Alan D. George
Professor of ECE
University of Florida
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida
Dr. Ann Gordon-Ross
Asst. Professor of ECE
University of Florida
Nicholas Wulf
Research Student
University of Florida

## Slide 2: Outline
OBP Design Optimization Framework Overview
  Dependability and power evaluation metrics
  Hyperspectral imaging case study
Dependability Metric
  Space Orbit Overview
  Space radiation analysis with CREME96
  Atmospheric radiation
Power and Performance Metric
  Constrained linear optimization with linear programming

## Slide 3: Outline
OBP Design Optimization Framework Overview
  Dependability and power evaluation metrics
  Hyperspectral imaging case study
Dependability Metric
  Space Orbit Overview
  Space radiation analysis with CREME96
  Atmospheric radiation
Power and Performance Metric
  Constrained linear optimization with linear programming

## Slide 4: On-Board Proc. Framework
Goal: Provide theory for determining Pareto-optimal device & fault-tolerant (FT) strategy for on-board processing systems
  Focus on small satellites, UAVs, smart munitions, AUVs
  Generalized comparison framework deters ad hoc design methodology, leading to Pareto-optimal designs
Approach: Divide exploration space into its key components for study
  Device Set – Includes CPUs, DSPs, FPGAs, GPUs, & any Rad-Hard versions
  FT Strategies – Sacrifice resources for fault tolerance (may be app-specific)
  Mission Characteristics – Defines system’s environmental conditions
  Application Set – Includes most common kernels (e.g., space apps.)
  Analysis – Design evaluation metrics calculated from other components
    Is selected design acceptable?
    How does it compare to others?
Device Set
FT Strategy Set
Mission Characteristics
Application
Kernel Set
Analysis

## Slide 5: What is an FPGA?
Field-programmable gate arrays provide large amounts of logic resources connected with a complex, configurable routing network
  Logic resources: LUTs & FFs
  Routing resources: Switchboxes
  Specialized cores: BRAMs, DSPs, SERDES
FPGA configuration memories stores the current state of the device
  Modification of configuration memories effects the functionality of the device
Benefits of FPGAs over traditional processors
  Application-specific hardware enables efficient processing at low frequency and power
  Large logic fabric enables massive algorithm parallelism
  Run-time reconfiguration allows for time-multiplexing of multiple designs
Xilinx CLB Architecture
5

## Slide 6: Calculating Computational Density
Computational Density (CD) used to analyze device performance
  Developed within CHREC at the University of Florida
  Applicable to wide range of architectures (e.g., CPU, DSP, GPU, FPGA, etc.)
  Produces results in terms of operations per second
    Different CD result for each type of precision (e.g., bit, 8-bit int., 64-bit double)
    CD also depends on type of operation (e.g., add, multiply, divide)
Standard objective methodology for calculating CD on FPGAs
  Generate and analyze compute core on FPGA
    Perform twice for each core; one with and one without DSP resources
    Core must match desired precision & operation
  Collect data on resources used and max freq.
  Use optimal packing algorithm to determine maximum number of cores on device
  CD equals number of cores times worst clock rate from the list of cores used

## Slide 7: Framework Methodology
Designs evaluated according to two metrics
Power – power consumed by device
  Sensor data rate & application determine amount and type of required processing
  Device utilization is ratio of corresponding device CD to required processing
  FT strategy overhead increases utilization
  Linear interpolation between power range to find power consumption
Dependability – time between failures
  Device radiation characteristics and environment determine device upset rate
  Low utilization causes lower vulnerability
  FT strategies help to mitigate upsets
Dependability
72%
Consumed
Device
Power
Sensor
Utilization: 24%
Utilization: 72%
Device
TMR
100%
0%
50%
Static
Max
Utilization
Environmental Radiation (Particles / m2·ster·s)
Device Cross-Section (SEE / Particle·m2)
Power
LET
100
50
0
Device Upset Rate:
10 upsets/day
0.10
Only 72% of device is vulnerable
TMR protects against 99% of upsets
0.14
13.89
MTBF:
days
Sensor
Dependability
TMR = Triple-Modular Redundancy
CD = Computational Density

## Slide 8: HSI Case Studies
Hyperspectral Imaging (HSI) enables detection of key materials within a scene
  Detects intensities of hundreds of wavelengths for each pixel forming an image cube
  Compares characteristic spectrum of pixels to spectral signatures of desired materials
  Marks location of identified materials within the scene
Image cube too large for transfer to processing station due to limited bandwidth
Solution: perform computation in-situ and only transfer final results
Two HSI missions chosen as case studies for on-board processing
  Hyperion on EO-1 satellite requiring 2.2×109 32-bit integer MAC/s
  AVIRIS on ER-2 aircraft requiring 348×106 32-bit integer MAC/s
Detect
Compare
Identify
MAC = Multiply Accumulate

## Slide 9: Raw Results
Studied design combinations of 6 FPGAs and 3 fault-tolerant strategies
  Devices: 3 standard Virtexes, 2 low power Spartans, and 1 Rad-Hard SIRF
  Fault-tolerant strategies:
    No fault tolerance (NFT): 0% overhead and no added reliability
    Algorithm-based FT (ABFT): 10% overhead and significant added reliability
    Triple-modular redundancy (TMR): 200% overhead and strongest reliability
Power consumption and dependability metrics calculated for each design
FPGA = Field-Programmable Gate Array
Values predicted with linear regression on feature size in underlined italics

## Slide 10: Optimal Design Selection
Framework determines Pareto-optimal designs based on metrics
  Non-Pareto-optimal designs can be completely ignored
Constraints on metrics enforced to remove invalid designs
  Removes unreliable and/or power-hungry designs based on mission
Out of 18 designs, only 5 designs selected as optimal for each mission
  Designers decide which design is best based on desired tradeoffs
EO-1 Hyperion Satellite
ER-2 AVIRIS Aircraft

## Slide 11: Outline
OBP Design Optimization Framework Overview
  Dependability and power evaluation metrics
  Hyperspectral imaging case study
Dependability Metric
  Space Orbit Overview
  Space radiation analysis with CREME96
  Atmospheric radiation
Power and Performance Metric
  Constrained linear optimization with linear programming

## Slide 12: Radiation & Single-Event Effects
Radiation sources
  Galactic cosmic rays
  Solar flares and wind
  Trapped protons & heavy ions (Van Allen Belts)
Single-event effects (SEEs) are caused by energetic particles passing through Silicon
  SEU – soft errors; appear as transient pulses or bit flips in memory
  SEFI – soft error; causes entire device to stop functioning
  SEL – results in high operating, possible damage to the device
Effects of SEEs on FPGAs
  Configuration memory faults
    Routing faults– broken connections or short circuits
    LUT faults - change in logical functions implemented
    BRAM and FF faults – data errors in the running design
  Total Ionizing Dose (TID) limits component lifetime
    Silicon lattice damage
    Charge buildup within gate oxide
SEFI: single event functional interrupt
SEU: single event upset
MBU: multi-bit upset
SEL: single event latchup
12

## Slide 13: Various Orbits – LEO
Low Earth Orbit (LEO)
  Altitude: 160 - 2000 km
    Too much atmosphere under 200 km
  Trapped ion radiation from poles and South Atlantic Anomaly (SAA)
  Avg. upsets per day: <1 - 10
  A popular orbit for communications satellites
    Proximity to Earth means less energy to achieve orbit, less energy to communicate, and more detailed sensing
    Orbits may be sun-synchronous, but still orbit about once every 90 minutes, requiring a “constellation” network in order to provide continuous coverage
  Also the home of the ISS: ~350 km altitude
  Increasing space debris is a growing concern here
Low Earth Orbit
90-minute orbit
(ISS)

## Slide 14: Various Orbits – MEO & HEO
Medium Earth Orbit (MEO)
  Altitude: 2000 – 35,786 km
    Upper bound is Geostationary Earth Orbit (GEO)
  Trapped ion radiation in Van Allen belt is most intense here
    Greater than 2000 upsets per device-day in worst parts
  Home of GPS (12 hr period), Glonass (Russian), and Galileo (European)
  Includes Highly Elliptical Orbit (HEO)
    Molniya orbit was invented by Russians to observe high latitude regions
High Earth Orbit (HEO)
  Altitude: > 35,786 km (anything above GEO)
  Radiation from protons, heavy ions, and cosmic rays
    About 7 upsets per device-day around GEO
  GEO is useful for communications and weather satellites

## Slide 15: Various Orbits – Lagrangian Points
Special case of 3-body problem
  Discovered by Joseph Lagrange in 1772
Horseshoe Orbits
  Interesting but not really useful
L1 (Unstable)
  Useful for sun-observing satellites
L2 (Unstable)
  Sun and Earth on same side of satellite means only 1 side needs heat shield
  Useful for sensitive telescopes (James Webb & WMAP)
L3 (Unstable)
  Sun blocks communications with Earth; not currently used
L4 & L5 (Stable)
  These extremely stable orbits will allow the Solar Terrestrial Relations Observatory (STEREO) to capture 3D views of the sun; not currently used

## Slide 16: Space Radiation - CREME96
Model used to predict the effects of radiation on electronics
Requires the user to input several parameters
  Orbit
    Two-line elements (TLE) contain orbit parameters for specific satellites
  Solar conditions
    Cosmic radiation is at a maximum during solar minimum
  Shielding
    Satellite structure will usually provide some shielding
    Shielding can sometimes worsen things, causing a particle shower
  Device linear energy transfer (LET) characterization
    Specifies the likelihood of an upset occurring based on the amount of energy deposited by the intersecting particle

## Slide 17: CREME96 Example
A) Based on orbit and other input parameters, CREME96 predicts the amount, species, and energy of all ions passing through a unit area per unit time (flux)
B) Fluxes are modified based on sheilding
C) Fluxes are converted to LET specific to silicon
D) Inner product of environment & device LET gives upset rate

## Slide 18: Atmospheric Radiation
Radiation may still affect devices that are not in space
  Cosmic radiation is powerful enough to push through the magnetosphere and results in a neutron shower at higher altitudes
Neutron flux peaks around 60,000 ft
  This is where the cosmic rays have fully cascaded into a swarm of energetic neutrons that haven’t yet been absorbed by the air
Xilinx produces device neutron radiation characteristics in its Rosetta report, which can be used to determine upset rates

## Slide 19: Outline
OBP Design Optimization Framework Overview
  Dependability and power evaluation metrics
  Hyperspectral imaging case study
Dependability Metric
  Space Orbit Overview
  Space radiation analysis with CREME96
  Atmospheric radiation
Power and Performance Metric
  Constrained linear optimization with linear programming

## Slide 20: Improved CD Calculation
Old Method
  Pack device to its maximum to find max ops/cycle (1000 ops/cycle)
  Multiply this by limiting frequency of all used cores (150 MHz)
  1000 ops/cycle * 150 MHz = 150 GOPS
New Method
  Perform old method to find first CD
  Restrict use of core with limiting frequency and find new CD
  Continue removing limiting cores until design is impossible
  Use design that reported best CD
    800 ops/cycle * 200 MHz = 160 GOPS
EMPTY
Mult DSP
400 units
200 MHz
Add Logic
400 units – 300 MHz
50% Mult, 50% Add
Mult Logic
100 units – 150 MHz
Mult DSP
400 units
200 MHz
Add Logic
500 units – 300 MHz
50% Mult, 50% Add

## Slide 21: CD Packing Algorithm
Packing algorithm requires us to optimize CD while obeying several constraints
  Can’t use a negative number of resources or cores
  Can’t exceed the device’s resource limits when placing cores
  Must maintain a certain ratio between two or more groups of cores
This problem is ideally suited for linear programming, which is used to optimize a system of linear equations consisting of non-negative variables
  Developed in 1939 by Leonid Kantorovich to help Soviets in WWII by planning expenditures to reduce cost to Soviets and increase losses to the enemy
  Kept secret until 1947 when George Dantzig published the simplex algorithm
  Used postwar by many industries in their daily planning
Here’s a simple example using only 2 variables (x and y)
  Constraints: x ≥ 0, y ≥ 0, x + y ≤ 5, x ≤ 3, y ≤ 4
  Maximize z: z = 2x + y
  Constraints form a convex polytope
  Equation for z sets a gradient
  Only need to test the vertices (extreme points)

## Slide 22: CD Packing Algorithm Example
In this example, CD is calculated for the Virtex-6 LX75T-FF484-1 with a distribution of 50% multipliers and 50% adders and Int16 precision
These are our available cores and core/device resources used/available
Thus our equations are:
  AddLogic = x1 ≤ 0, AddDSP = x2 ≤ 0, MultLogic = x3 ≤ 0, MultDSP = x4 ≤ 0
  Distribution equation: x1 + x2 – x3 – x4 = 0
  Resource constraints (use slack variables to handle inequalities): 16x1 + 48x3 + sFF = 93120, 25x1 + 8x2 + 282x3 + 4x4 + sLUT = 46560, x2 + x4 + sDSP = 288
  CD minimizing equation: -x1 – x2 – x3 – x4 = -CD
Original matrix for simplex method
Simplex phase 1 finds first basic feasible solution (BFS)
Top row is non-positive. Final BFS. Results on right.

## Slide 23: Optimizing for Power
There’s only one solution for achieving the maximum CD, but possible infinite solutions for a lower target CD, so we can optimize for power in these cases
Thankfully, Xilinx and Altera power estimator tools assume dynamic power increases linearly with the number and frequency of each resource used
  Using these tools, we can find the power required per resource per cycle
  We can then use the resource count of each core to find it’s power/unit/cycle
  We can then modify our system of equations to lock CD and optimize for power
  CD/W can easily be found then for each CD
Legend
Int16 Int32 Float32 Float64
Target CD: 90
Target CD: 120

## Slide 24: Conclusions
Demand continues to grow for on-board processing
  Increasing need for autonomy in outer space and sensor processing for handling improved sensors
Increasing demand for space processing capabilities require innovative solutions to also satisfy the harsh constraints of space
The OBP Design Optimization Framework aids designers in handling all of these constraints simultaneosly
  Dependability is evaluated with CREME96 and vendor produced device datasheets
  Power and performance are evaluated with linear programming