## Slide 1: Building a RTOS for MPSoC Dataflow Programming
Jonathan David
2013 IEEE International Conference on Communications, pp.4373,4378, 9-13 June 2013
Osman Salem, Alexey Guerassimov, and Ahmed Mehaoua University of Paris Descartes – LIPADE Division of ITCE, POSTECH, Korea
Anthony Marcus and Borko Furht,
Department of Computer and Electrical Engineering and Computer Science, Florida Atlantic University

## Slide 2: The Need for Improvement
Multiprocessor System-on-Chip (MPSoC) designs are becoming standard in high performance DSP applications
  Zync
  Altera SoC
  ZigBee
Thus, being able load balance and make efficient use of parallel resources is of increasing importance
Need for a tool to ease MPSoC programming

## Slide 3: The Solution
Design of a real-time operating system capable of effectively managing resources
  Use of dataflow models shown to favor parallel algorithms
    Favors data locality
    Reduces multi-core scheduling constraints to data dependencies
Use of data flow graphs instead of thread declarations
  Execution handled by MPSoC RTOS
  Frees programmer from creating program primitives for task migration and synchronization

## Slide 4: How does it work?
Partitions each application between available cores
Parallelism of each application is stated inside of a dataflow graph
  Ensures good load balancing
  Reduces computation latency
MPSoC RTOS reuses C/C++ code for its actors
  Combines it with parameterized dataflow coordination language

## Slide 5: Highly dependent upon dataflow model!!!

## Slide 6: Dataflow Model
Well suited for applications based on a loop
  Telecommunications
  Video processing
Describes computation by splitting loop into actors
  Data exchanged through inputs/outputs only
  State of actor is not shared
Flow model is created before execution, and can be totally reconfigured once before starting a new executions

## Slide 7: Dataflow Model
Graph is represented by C++ objects
  Compile within dataflow management module
On each OS clock tick:
  Dataflow graph parameterized
  Temporary graph of execution obtained
  Each actor gets an RTOS task

## Slide 8: Dataflow Graph Management
An expansion is performed on the application
Dataflow graph transformed into temporary graph
  Each actor is executed only once in an iteration
  Temporary graph is dependent on parameter values that change between each iteration

## Slide 9: Dataflow Graph Management

## Slide 10: Expansion phase Can be performed in real time!!!

## Slide 11: Dataflow Graph Management
RTOS task is created for each actor
Tasks then scheduled on the cores of the MPSoC device
Alternate algorithms for dataflow management can be created, only restriction is that a dataflow graph can be produced

## Slide 12: Scheduling
Split into two phases
  Master/Slave Phase
  Symmetric Phase

## Slide 13: Master/Slave Phase
Master core executes dataflow graph management, posts actors to the slave cores, and finally posts actors to itself
Each core has a 1-place queue to receive an order to execute a task
  Message contains address of the task in shared memory
  Input/output buffer information contained
After first task dispatching is complete, all cores become pairs and the symmetric phase begins

## Slide 14: Master/Slave Phase

## Slide 15: Symmetric Phase
Each core can access the schedule function
  Mutex semaphores provided within library
Highest priority task executed first
Scheduler called in two scenarios
  Execution of task is preempted by higher execution task
  Task execution completes
If a core has no remaining tasks, the scheduler saves the current task’s context state and the core returns to its private memory

## Slide 16: Symmetric Phase

## Slide 17: Results
OS takes up a lot of space (more than 50%)!
Due to the size and task stacks allocated by kernel

## Slide 18: Results
Different number of actors for each iteration

## Slide 19: Results
Performance improves with number of cores
Definite diminishing returns
Shared memory accesses creates a bottleneck

## Slide 20: Shortfalls of the Study
Study is focused primarily on signal processing
Does not mention how the dataflow graphs are created, or how much time it takes (only mentions it falls within parameters for the tested algorithm)
Does not mention how much of a bottleneck is created by using one core as a master
No comparison against traditional/hand coded method

## Slide 21: Conclusions
Proposed MPSoC RTOS can ease difficulty of programming for modern day DSP applications
Increase in performance with number of cores
  Bottleneck with increased memory accesses
Large amount of memory occupied by proposed OS
Actors can be written in C or C++
Where is the competition?
  Can’t compare, does it result in a trade-off?

## Slide 22: Questions?

## Slide 23: R3TOS: Reliable Reconfigurable Real-Time Operating System
Jonathan David
2013 IEEE International Conference on Communications, pp.1720,1724, 9-13 June 2013
Mai Abdelhakim, Leonard E. Lightfoot, Jian Ren, Tongtong Li
Department of Electrical & Computer Engineering, Michigan State University
Air Force Research Laboratory, Wright-Patterson Air Force Base

## Slide 24: The Need for Improvement
FGPAs provide promising possibilities for the future as semiconductor manufacturing reaches its physical limits
  Obtain best performance per transistor count per unit of consumed energy
  Increase in reliability
  High amount of computation in given space and time

## Slide 25: The Solution
Use of online specialization
  Intelligent reuse of resources in the FPGA
  Architecture kept fault-free by reconfiguring around damaged areas of the chip
Maintain a “software look and feel” to avoid a collapse in productivity and cost
Satisfy requirements of high-performance, real-time, fault-tolerance necessary in applications

## Slide 26: RTOS != ROS

## Slide 27: Fundamental ROS Services
Software OS augmented with functions to manage reconfigurable hardware
Task loading
Memory management
Scheduling and allocation
Communications
  Hardware hardware
  Hardware software
Input/output
Accessible through AP, with runtime support

## Slide 28: R3TOS Foundations
Resource reusability and computation ephemerality
  Intensive use of fine-grained reconfiguration
Aims to keep resources available to any incoming task at any time
Circuits configured when required, then removed
  Clock distribution wires
  Task communication channels
Resources can be used for either computation or communication purposes

## Slide 29: R3TOS Foundations
Control logic to drive tasks is attach to their own circuitry, as opposed to predefined reconfigurable slots with fixed control logic and comm structures
  Self-contained, closed structures
  Fully relocatable within FPGA

## Slide 30: Task Control Logic (TCL)
Includes input data buffer, output data buffer, and hardware semaphore enable/disables computation
  Provides means to virtually lock physical data and control data of hardware tasks to logical positions in the configuration memory of the FPGA
Frees the allocation of a task from being constrained by communication interfaces during design time
  TCLs are accessible through the configuration interface of whichever memory position they are mapped to

## Slide 31: TCL Advantages
Number of tasks executed concurrently only limited by resources on the FPGA
Tasks can be allocated around damaged resource
Increased computation density
Complexity of allocation algorithms reduced
  No need to be aware of underlying implementation-related irregularities in the reconfigurable area
  No need to preserve static routes

## Slide 32: TCL Advantages
Tasks can be de-allocated quickly using multiple frame write configuration commands
  Simply blank an entire region
Each task can be clocked at its highest frequency, rather than running entire fabric on same clock
Device ages uniformly

## Slide 33: The Downsides
Bottleneck from the internal configuration access port leads to significant time overheads
Configuration of a hardware task delays its execution
Configuration of on-demand communication channels incurs an overhead greater than the time needed for created a virtual connection through a network-on-chip

## Slide 34: Computing Model
Task definitions and interactions described using parallel software syntax (POSIX Pthreads)
  Body of some tasks implemented in hardware
R3TOS addresses two main hardware tasks:
  Data-stream processing, to be used with data-intensive applications with regular dependencies
  Hardware-acceleration tasks
User relies on the R3TOS API to program their reconfigurable application
Execution of tasks controlled by main CPU

## Slide 35: Computing Model
The software microkernel (SWuK) interacts with the hardware microkernel (HWuK)
  SWuK schedules/executes software tasks and forwards hardware tasks to the HWuK
Hardware related services offered in the API are determined by the HWuK
  Scheduler server to schedule hardware tasks
  Allocator server manages FPGA resources
  Configuration manager to translate high-level operations into reconfiguration commands for the FPGA

## Slide 36: Computing Model

## Slide 37: General Architecture
A little bit complex, probably

## Slide 38: General Architecture
Three main parts
  HWuK
  Main CPU
  Memory

## Slide 39: Hardware Microkernel
Each component is implemented separately to allow for parallelism in the HWuK processes
  Allows for low runtime overhead and area overhead
  Main core of all HWuK components is the PicoBlaze
  Requires only 96 slices
HWuK components mastered by scheduler
  Allocator and configuration manager act as slaves
Communication between components managed by a very strict set of rules, overseen by two monitors (to detect malfunctions)

## Slide 40: R3TOS Main CPU
Xilinx on-chip processor (32-bit MicroBlaze soft-core) is used as main CPU
  Timer and interrupt peripherals included to expand functionality
Program executed by CPU is held in directly accessible program memory (BRAMs in FPGA)
Interfaced with the HWuK based on interrupts and shared memory

## Slide 41: Memory
Bitstream memory and main memory held on one external chip
  Data and code segments of software tasks
  Data segments and bitstreams of hardware tasks
  Bitstreams of the data relocating tasks
Lowest part of memory contains a pointer table, allowing the HWuK to know the exact location of each task bitstream

## Slide 42: Proof of Concept

## Slide 43: Proof of Concept

## Slide 44: Shortfalls of the Study
Has yet to be seen if the implementation is practical for most applications
Can’t be seen how execution times are effected
How difficult is coding?
Energy usage of device?
That’s is about it…the paper is pretty solid

## Slide 45: Conclusions
R3TOS allows for a viable, reconfigurable, real-time operating system
Many advantages gained by freeing hardware from static communication lines
  Better able to use resources
  Even wear over device
  Possible performance increases
Viability of design must wait for practical implementation, currently only proof of concept

## Slide 46: Questions?

## Slide 47: THANK you!