## Slide 1: Sensor Fault and Patient Anomaly Detection
Jonathan David
2013 IEEE International Conference on Communications, pp.4373,4378, 9-13 June 2013
Osman Salem, Alexey Guerassimov, and Ahmed Mehaoua University of Paris Descartes – LIPADE Division of ITCE, POSTECH, Korea
Anthony Marcus and Borko Furht,
Department of Computer and Electrical Engineering and Computer Science, Florida Atlantic University

## Slide 2: The Need for Improvement
Average lifetime has increased
  Advancement in medical procedures
  Technological advances
  Increased knowledge base
Unfortunate problem: Its hard to care for everyone!
  Increase in average lifetimes means an increase in the population
  Shortage of healthcare professionals

## Slide 3: The Solution
Wireless Body Area Networks (WBAN)
  Network of wireless sensors to relay patient information
  Uses accurate, high-throughput networks
  Allows patient greater freedom and mobility

## Slide 4: What can be measured?
Heart rate
Pulse
Oxygen saturation
Body Temperature
Respiration Rate
Blood Pressure
Blood Glucose
Galvanic Skin Response
It is quite comprehensive!

## Slide 5: How does it work?
Networked sensors transmit to central device
  Can be patients cell phone, base station in house, etc.
  Handles processing and storage
  Sends alarm upon detection of anomaly
Used on patients with chronic illnesses
Can be used to monitor patient recovery after surgical procedures

## Slide 6: Are there any problems? Are there ever not any? The sad truth of engineering

## Slide 7: Problems
Faulty measurements
Hardware failures
Security issues
Sensors have limits
  Reduced computational power
  Limited storage capacity
  Limited energy resources
  Passed to central device for processing

## Slide 8: Detect Faulty Measurements
Focus on what is correctible: bad readings
  A faulty reading can mean an error or that a patient is entering a critical state
  The differences are distinguished using historical data
  Achieved using an anomaly detection mechanism
    Suitable for WSNs given the lack of attack signatures
    Patterns checked against dynamically updated normal model
    Unfortunately, in the training phase it is difficult to find normal data to establish a normal profile

## Slide 9: How does the paper tackle this?
Use a J48 decision tree to detect abnormalities
Apply linear regression to find abnormal measurements in an abnormal record

## Slide 10: Use a what to do what?

## Slide 11: Decision Tree J48
Implementation of C4.5 decision tree
Classifies record and reduces temporal complexity
Attributes are stored in non-terminal nodes
Terminal nodes represent an outcome
An algorithm is used to obtain the gain ratio of each attribute, which allows for hierarchical distribution among the tree nodes

## Slide 12: Linear Regression
Predicts the current measurement for each parameter
Sends a trigger when current value is greater than the predicted value by a certain threshold
Correlation analysis conducted to detect faults

## Slide 13: Is it abnormal? If it is, Is it an error or a health issue?

## Slide 14: Why use this approach?
The purpose is to detect abnormal patterns
  Process needs to be real-time and must be fast
  Uses data passed to central device for processing
    Sensors don’t have the processing power or storage for this
J48 used because it is efficient at classification
  Easier to sort through large chunks of data
  Quicker identification of data that contains anomalies
Linear regression determines if it is an error
  If one anomaly, the value is replaced by predicted value
  It two anomalies, medical teams are alerted

## Slide 15: How well does it work?
Results focused on five vital signs
  Heart rate ϵ [80 – 120]
  Pulse ϵ [80 – 120]
  Respiration Rate ϵ [12 – 30]
  SpO2 (Oxygen Saturation) ϵ [90 – 100]
  Body Temp ϵ [36.5 – 37.5]
Based on two phases
  Training
    Machine learning methods used create model for data
  Detection
    Inputs classified as abnormal if they deviate from the model

## Slide 16: Results
Anomalies can be seen at approximately times .7 and 2.4
Two alarms are raised
  At .7, alarm due to abnormal pulse AND SpO2
  At 2.4, alarm due to highly irregular heart rate

## Slide 17: Results
Figure 5 uses methods proposed in paper
Figure 6 uses k-NN (k Nearest Neighbors)
  More computationally expensive
  Higher error than additive regression
Figure 7 uses a decision table
  Produces the worst results in all cases

## Slide 18: Results
Linear regression has lowest mean error
Approach achieves a high True Positive Rate with a corresponding low False Positive Rate

## Slide 19: Shortfalls of the Study
Does not mention what happens when data is continuously read as faulty
  May be indication of underlying health problem
  Indication that sensor needs to be replaced
Learning phase is glossed over
  Does it learn when patient is doing physical activity?
  How long is the learning phase?
Paper could use more fault tolerant methods
  Readings of same type from multiple sensors (TMR)

## Slide 20: Conclusions
The approach used in the paper performs well
  High True Positive rate
  Low False Positive rate
  Supposedly less computational power than other approaches
  Supposedly less storage used
Some areas of the study remain dubious
  Power comparisons?
  Computation time?
  Detection and replacement of faulty sensors?

## Slide 21: Questions?

## Slide 22: Architecture Design of Mobile Access WSNs
Jonathan David
2013 IEEE International Conference on Communications, pp.1720,1724, 9-13 June 2013
Mai Abdelhakim, Leonard E. Lightfoot, Jian Ren, Tongtong Li
Department of Electrical & Computer Engineering, Michigan State University
Air Force Research Laboratory, Wright-Patterson Air Force Base

## Slide 23: The Need for Improvement
WSNs impact on military and civilian applications
Need efficient and reliable communication over large-scale networks
  Energy constraints
  Trade-off between efficiency and throughput
SENMA (sensor networks with mobile access points)
  Mobile access units traverse network to collect data
  Improves energy efficiency of the sensors
    Improvement in terms of energy over ad-hoc
    Sensors do not perform energy-consuming routing functions
  Unfortunately, there is a large delay in data collection

## Slide 24: The Solution
Use mobile access coordinated wireless sensor networks (MC-WSN)!
Energy efficient, reliable, allows time-sensitive info
  Network is divided into cells
  Each cell is covered by one MA
  MA deploys, recharges, and replaces nodes
  Also replaces compromised nodes (enhanced security)
Data is sent to a cluster head in each cell
  Cluster head is always located at center of cell
  Easy data gathering (location is known, easy to find)

## Slide 25: Improvement over SENMA
Number of hops from any sensor to the MA is minimized to pre-specified number
  Set by network deployment and design topology
Delay is not based on speed of the MA!
  Only based on number of hops and wave speed
Energy consumption is also improved
  Determined by MA distance from nearest cluster head
  Independent of MA coverage area and node density
  Higher energy efficiency, lower delay times!

## Slide 26: Design of the Cells
Hexoganal cells
Each cell has one MA
Sensor nodes deployed, each group with a cluster head
One powerful center cluster head
Center cluster head communicates with the MA

## Slide 27: The Mobile Access Point
UAV capable of land travel
Multiple duties
  Deploys
  Replaces
  Recharges
  Collects data
Returns collected data to a base station
Only moves for data collection if routing path fails
  Communication with main cluster head and the nearest cluster head

## Slide 28: Main Features of MC-WSN
Resolves network deployment and extend lifetime
  MAs manage deployment of sensors and CHs
  Node signals MA when it is low on energy
Minimizes delay times
  Speed dependent on number of hops and wave speed
  MAs determine the topology of the network
Provide high energy efficiency
  Sensor nodes communicate to nearest cluster heads
  No inter-cluster routing necessary

## Slide 29: Main Features of MC-WSN
Enhanced network security
  Compromised sensors and cluster heads are replaced
  The MA itself roams the cell, keeping its location private
Enhanced resilience, reliability, and scalability
  Self-healing architecture
  Health relayed to MA by the central cluster head and/or nearest cluster head
  If routing paths fail, MA can roam cell to collect data

## Slide 30: Creating the Network
Form clusters
  CHs broadcast Hello message with ID and location
  Each sensor connects to nearest CH
Ring set-up (boundary)
  MA traverses the cell, broadcasts Start message to CHs
  MA denotes the cluster heads along its ring path
Discover links to ring
  CHs broadcast a message to find neighboring CHs
  Continues until all CHs find at least one neighbor

## Slide 31: Creating the Network
Discover links to the central cluster head
  CCHs broadcasts a signal to find neighboring CHs
  The signal is forwarded by the CHs until it reaches CHs on the ring
Establish links to the ring or central cluster head
  Cluster heads establish connections with the central cluster head or the closest cluster head
  The process is completed when the receiver successfully confirms a connection

## Slide 32: Data Gathering
Periodical sensing and collecting stages
  Sensors report information to the cluster heads
  Cluster heads report to other cluster heads or CCH
Transmission interference is avoided
  Sensors report in a given time slot
  Nodes of different clusters use different spreading codes
  Transmissions from sensors to CHs, between CHs, from CHs to the MA, and from the CCH to the MA all use different frequency ranges
MA sends a beacon signal, allowing CHs to communicate with it

## Slide 33: Results
Ring and CCH method produces lower average number of hops
Energy used by MC-WSN setup is orders of magnitude lower than SENMA setup

## Slide 34: CRAZY GAINS!

## Slide 35: Shortfalls of the Study
What happens if the MA fails?
  Data seems to only flow into the MA from CCH and the CHs, no check ups are performed on the MA
How much energy is needed to run the MA?
How practical is the MA?
  Is it feasible with todays technology?
    Complicated machinery
    Seems to be very expensive
  Is the energy saved by the network worth the cost of running the MA?

## Slide 36: Conclusions
MC-WSN provides multiple improvements over SENMA
  Huge reduction in energy consumptions
  Massive decrease in delay times
  Reliable, secure network
Unfortunately there are many questions
  Cost comparisons?
  Is the maintenance of the MAs worth the benefits?
  Practical to deploy with modern technology?
    If not now, when?

## Slide 37: Questions?

## Slide 38: THANK you!