## Slide 1: Real-Time Systems
Dave Ojika

## Slide 2: Image-Processing Semester Roadmap
Part I. Reconfigurable Systems
  Motivating research
  Current research
  Fast and Flexible High-Level Synthesis from OpenCL using Reconfiguration Contexts
Part II. Architectural Optimizations
  From OpenCL to High-Performance Hardware on FPGAs
  OpenCL for FPGAs: Prototyping a Compiler
Part III. Real-Time Systems
  Real-time Image Processing with Reconfigurable Hardware
  Gigapixel-size Real-time Interactive Image Processing with Parallel Computers

## Slide 3: Outline
General Background [10 frames]
Paper II
  Introduction
  Technological Driver
  Application
  Main Features
  Mechanism
  Design Implementation
  Results
  Conclusions
Paper I
  Introduction
  System Description
  Goal of Research
  Hardware Platform
  Hardware Library
  Application
  Results
  Conclusions

## Slide 4: Machine Vision
Machine vision or computer vision (CV) can substitute human vision for a number of application tasks such as
  Target tracking
  Robot guidance
  Tasks inspection
MSL
Autonomous operation aided by machine vision
  Real-time operation highly critical!

## Slide 5: Real-Time System in Machine Vision
Machine vision requires real-time capabilities; are often used in real-time applications
System extracts relevant information from an image through several processing steps
  Image acquisition 
    Input
  Image processing 
    *Processing
  Feature extraction 
    *Processing
  Decision making 
    Output
    *Processing: [enhancement, restoration, analysis, creation]
    [local maxima, etc.]

## Slide 6: Image Processing
Very important field in machine-vision
  OpenCV – image/video processing algorithms
Operations are difficult to achieve in real-time using software techniques
  Large amounts of data involved when dealing with high resolution images
Nevertheless, one of the most attractive areas for reconfigurable computing
Notes: This presentation is not about reconfigurable computing just yet…
  Reconfigurable computing and Real-time often go hand in hand
  FPGA (a kind of reconfigurable hardware) naturally makes real-time possible

## Slide 7: Reconfigurable Hardware
RC approach
  Custom-logic
    FPGA, ASIC
  map hardware to application
Traditional approach
  Fixed-logic
    CPU, DSP, GGPU
  map application to hardware
Reconfigurable circuits are advantageous
  Deliver hardware performance and software flexibility
  Re-programmability
  Price/performance benefits compared to ASIC
Notes: ASIC are somewhat fixed. FPGA are fully customizatble after fabrication Custom circuit unlike traditional approach that maps application to hardware GGPU are starting to have wide spread application not only for graphics processing

## Slide 8: Fixed-Logic in Real-Time Systems
Performance probably not as much compared to FPGA
  CPU
    Architecture: fetch, decode, …
    Limited parallelism: ILP, TLP
  GPU, DSP
    Throughput matches with FPGA
    Huge power consumption
However, its not business as usual…
  ARM: low-power CPU
  Intel Many-Core CPU: Xeon Phi
  Tesla GPU: Tesla & Tegra – massive parallelism with CUDA cores
  TI DSP: special-purpose Image/Video Processing ASICS (TI CorePac)
Notes: GPU, DSP rival FPGA in terms of performance but only at huge power consumption. Theses devices are power hungry

## Slide 9: Fixed-Logic in Real-Time Systems (cont.)
CPUs pure-software approach utilize fast clock (to deal with sequential operations) - are quickly inhibited by laws of physics
    However many advanced techniques: OOO, speculative execution, dynamic scheduling, branch prediction
        Not enough to solve problem of data-parallel image/video apps
    Multicore and many-core processors (SMP) have become almost the standard in high performance computing
        For many embarrassingly parallel apps, FPGA preferred
GPU and DSP have been traditional used for image/video processing, but are very power hungry
Focus on of this presentation is on use of reconfigurable hardware to maintain real-time constraints
Notes: So Reconfigurable hardware does seem promising for image processing, huh?
Lets see…

## Slide 10: Real-time Image Processing with Reconfigurable Hardware

## Slide 11: Introduction
A PCI-based system for image processing using hardware/software technique
  “PCI-based reconfigurable system for real-time image processing using reconfigurable hardware”
    Real-Time: focus of this whole talk
    Image Processing: choice domain application area
    Reconfigurable Hardware: choice architecture
    PCI: link between 2 and 3
    And, the rest is grammar…
Motivation
    Image processing app require huge amounts of data
    Software-based approach too difficult to achieve real-time
Notes:   We already gave motivation for domain application area and architecture (FPGA)
  sounds complicated? Not at all. Lets brake it down: PCI can be a bottleneck
  Why PCI?

## Slide 12: PCI Bus Interface
PCI provides a fast link between host system (hosting raw images) and reconfigurable hardware (processing these images)
To achieve real-time, need to minimize communication bottlenecks as much as possible
Other communication interfaces
    ISA (3~5 MB/s): being replaced by PCI
    USB
It is pretty much the standard for
host-accelerator interfacing
    Features many many generations with
    varying bandwidth and lanes
Notes: - “Avoid Bottlenecks Using PCI Express-Based Embedded Systems” - RTC Magazine (embedded systems technology

## Slide 13: System Description
HOT2-XL (a PCI board) used as co-processor for image processing
Environment based on library of hardware modules that implement a some of the most common operations in image processing
Also implemented, is a Visual C++ application in order to validate hardware design
System is an integrated hardware and software environment dedicated to processing images in real-time
  Software processes are executed by the CPU
  Hardware processes are implemented on the FPGA
    Essentially an area of hardware-software co-design
    A continuously growing area of research
      Deals with optimal solutions for partition a task into hardware and software domains
      Area, power, performance, etc. trade-offs
Notes:   How has reconfigurable hardware supported real-time image processing? Vega-Rodriguez et. all ( our friend, and his friends, at Univ Extremadura in Spain at their department de Informatica

## Slide 14: Goal of Research
Make real-time machine vision system suitable for both scientific purposes and commercial applications
  Maximize both flexibility and efficiency (throughput)
  Reduce cost
  A Parato-optimal design problem?

## Slide 15: Hardware Platform (Hot2-XL)
What is Hot2-XL board?
  Seem to have been used a lot by author
  Papers
    AN FPGA-BASED IMPLEMENTATION FOR MEDIAN FILTER MEETING THE REAL-TIME REQUIREMENTS OF AUTOMATED VISUAL INSPECTION SYSTEMS
    Cork stopper classification using FPGAs and digital image processing techniques
    An Optimized Architecture for Implementing Image Convolution with Reconfigurable Hardware
What makes platform unique?
  Not a lot of information found online about board
  Board costs $1995
Google search: ? 
Board Main features
    FPGA
    2 Fully independent 32-bit banks of RAM (4MB total)
    Configuration Cache Manager
Notes: Author Vega-Rodriguez
    Board from (from Virtual Computing Corporation)
What we certainly know:
  FPGA PCI-bus custom computing board
  Growing popularity for image processing apps
    Growing popularity for image processing applications (as a coprocessor) [year 2001]
    Features:
    2 Fully independent 32-bit banks of RAM (4MB total)

## Slide 16: Library of Hardware Modules
Collection of image processing algorithms in form of hardware modules
Consists of diverse categories of image processing operations
  Point, histogram, convolution, morphology, …
  16 modules completed
  Final purpose to combine modules along with software process into a hardware/software co-design environment aimed at machine vision application
Complement image (CI)
Binary contrast enhancement or Thresholding (BCE)
Histogram (H)
Brightness slicing (BS)
Vertical gradient filter (VGF)
Horizontal gradient filter (HGF)
Diagonal gradient filter (DGF)
Low-pass filter (LPF)
High-pass filter (HPF)
Laplacian filter (LF)
Histogram sliding and stretching or brightness contrast adjustment (HSS)
Binary erosion (BE)
Binary dilation (BD)
Gray-scale erosion (GSE)
Gray-scale dilation (GSD)
Median filter (MF)
    Hardware modules downloaded from host
    FPGA quickly reconfigured as required by application

## Slide 17: Library of Hardware Modules (cont.)
All hardware modules in VHDL models and schematics
  Models designed, simulated, refined and synthesized using Xilinx tools
Modules optimized for performance using several techniques
  Replication and pipelining
  Optimization of multiplier by means of adder trees (convolution)
  Reduction of sorting and selection network (median filer, gray scale morphological)
  Search for high regularity
  Re-utilization of common resources
Example
Median Filter
32 bit-words (4 8-bit pixels)
Replicated functional units
Re-use of common resources
Notes: filer applied to four pixels neighborhood simultaneously
  Computation of four pixels (P1, P2, P3, P4) performed in 2 stages (pipelined)
  Results in 4x acceleration of operation
    While stage 1 computes the pixels P1, P2 and P3 according to the three words read in the current clock cycle, stage 2 computes P4 and writes the resulting word associated with the three words read in the previous cycle.

## Slide 18: The PIHR Application
PIHR: Procesamineto de Imagenes mediante Hardware Reconfigurable
  Designed to validate library of hardware
Written in Visual C++
Operates on PC based-systems with Windows
Consists of:
  GUI application
  HOT2-XL board
  Hardware library of modules
  HOT Run-Time Reconfiguration

## Slide 19: How PIHR Works
Load, store, copy, paste and visualize bitmap
Select window with source image
Choose processing platform:
  software (CPU) or hardware (HOT2-XL)
Result: execution time
  hardware and software
For functional test, hardware and
software versions compared
Performance differences are also compared between both versions
  To get measurements, dimension of image and number of colors reported
  Number of pixels per millisecond is then obtained
Notes:   Can change clock frequency (360 KHz and 100 MHz of hardware version in order to evaluate offsets as a result of changes in clock frequency

## Slide 20: Configuration Manager
PIHR uses Configuration Manager; allows configuration of hardware modules
  Reduce configuration overload of frequently used modules
Onboard Configuration Cache maintains the list of hardware modules in the cache
  When configuration cache is full, application replaced modules based on LRU policy
    Potentially saves reconfiguration time of hardware modules that need to be programmed on the FPGA because the module will probably be in the cache

## Slide 21: Results
Almost all hardware modules admit maximum clock freq of 33 MHz
  Coincides with PCI bus speed/specification for a 32bit/33MHZ system
Complement image (CI)
Binary contrast enhancement or Thresholding (BCE)
Histogram (H)
Brightness slicing (BS)
Vertical gradient filter (VGF)
Horizontal gradient filter (HGF)
Diagonal gradient filter (DGF)
Low-pass filter (LPF)
High-pass filter (HPF)
Laplacian filter (LF)
Histogram sliding and stretching or brightness contrast adjustment (HSS)
Binary erosion (BE)
Binary dilation (BD)
Gray-scale erosion (GSE)
Gray-scale dilation (GSD)
Median filter (MF)
Notes: The operations are sorted in less to more execution time for the software version, and therefore in order of less to more complexity Operations sorted in less to more execution time for the software version, and therefore in order of less to more complexity
Maximum Frequency and Resource Utilizations obtained from Xilinx Foundation Series tools are synthesis, and are actual measurements on implementations (not estimations)
Almost all the hardware modules admit a maximum clock freq of 33 MHz Therefore a bandwidth of 132 Mbytes/sec bandwidth
 we can see that interface unit (PCI) is as important as the hardware itself. Usually the bottleneck

## Slide 22: Kernel Performance
GSE and GSD
  maximum freq decrease significantly almost by half
    Algorithm includes sorting and selection
    Circuits need great deal of logical resources to implement
      Increased # CLBs utilization in FPGA
CI
  Very simple operation - hardware implementation not advantageous (configuration time overload)
H
  Implementation carries out total of 8 sequential R/W operations for each word
      Multiple memory ops. occur sequentially
        Not taking advantage of the inherent parallelism
30 images of 640x480x256 each
Reconfiguration time: 440 ms
Time to process 30 images
  Hardware: 574 – 1578 ms
  Software: 150 – 84459 ms
    C++ compiler with optimization
    Pentium 2 @ 350 MHZ
    64 MB of RAM
Notes:   Incased circuits also result in great level of propagation delays (both logic and routing  increase min clock period, decrease max. clock freq

## Slide 23: Conclusion
PCI-based image processing system reconfigured in runtime to adapt to requirements of an application
  Reconfigurable hardware (HOT2-XL FPGA board) and library of hardware modules
Emphasis of hardware-software co-design, adding flexibility to the development process
  Able to explore design trade-offs trade-offs
Demonstrated effectiveness of parallelization techniques: replication, pipelining
  Achieve improved performance through efficient resource utilization
FPGA-based image processing applications show significant speedup compared to CPU software-based counterparts for complex algorithms

## Slide 24: Gigapixel-size Real-time Interactive Image Processing with Parallel Computers

## Slide 25: PiCEIS
What is it?
  Parallel Computation Environment for Imaging Science
  Image processing package designed for efficient execution on massively parallel computers
  Effective use of aggregate resources of the computing system
  Large and accurate production processing using existing of the shelf hardware
Goal:
  Reduce difficulty in writing scalable parallel programs
  Reduce time to add new functionalities
  Provide real-time interactive image processing

## Slide 26: Introduction
Large images are pervasive
  High-resolution and multi-spectral cameras from satellites, nuclear magnetic resonance
Some Hi-Res image sources
  IKONOS
  Digital imagery
  Space Digital imaging
  SPOT
Possible to process large images quickly & effectively
  Fundamental problems and requirements for improving processing of satellite images remain unchanged since the 60’s
    Spatial & spectral resolution, radiometric resolution, network and memory bandwidth constraints and display output requirements

## Slide 27: Technological ‘Driver’
More advanced satellites constantly put in place
  Post-processing beyond workstations and small shared memory imperative
High performance serial processing becoming pervasive with software and low cost high-end devices (Pentium4, Athlon, Itanium-2)
  Systems not sufficient enough to process large images
Specialized parallel hardware can handle large images
  Unusable for multiple applications due to large hardware/software development cost
Cluster of off-the-shelf hardware maybe cost effective – development of software still lagging

## Slide 28: Approach
Efficient and portable parallel programming methodology
  Processes images using commercial distributed shared-memory massively parallel computers
    IBM SP and Linux Cluster
  Portable library allows for shared memory operations
    In-core and out-of-core computations, visualizations, parallel I/O
Domain decomposition methodologies and software
  Solve partial differential equations, computation chemistry, parallel rendering
    Technique permits easy interface for processing tiles of images with user-specified routines as well as serial software: OpenCV, Python Image Library, Java toolkits
  Processor-specific, optimized low-level libraries used
    Vendor tools: Intel’s custom image processing lib; IBM’s ESSL lib

## Slide 29: Main Features
Data rearrangement and movement concern
  Can be time consuming to program; cause reliability concerns regarding message passing
  Can be alleviated using Global Arrays shared memory model
    Model has direct interface to ScaLAPACK, TOM and integral transformations (FFT)
Users can customize image-processing routine
  No knowledge of data distribution, memory hierarchies or underlying programming model required
Load balancing easily adapted to different scenarios
  Complexity of message passing moved to library level; handled by global arrays

## Slide 30: Mechanism
Complicated indexing task moved to Global Arrays
  Support for clusters of heterogeneous nodes, with different amounts of memory and processing power
  Used efficiently by allocating different sizes of data to each node
No special algorithm or code required
  Can perform dynamic load balancing by tracking computational time over key loops over a number of iterations

## Slide 31: Global Arrays Tools
Provides much of the underlying support for the parallelism in PiCEIS
  Memory Allocator:
    Access to local memory
  Global Arrays:
    Provide portable globally addressable shared-memory programming on distributed shared-memory computer
  Aggregate Remote Memory Copy Interface (ARMCI):
    Provide general purpose, portable and efficient remote memory copy operations (one-sided communication) optimized for noncontiguous (strided, scatter/gather, I/O vector) data transfer
  Parallel I/O (ParIO) and Disk Resident Array (DRA):
    Extend the shared memory model to disk
Notes: Global Arrays and ARMCI interoperate with
message passing interface (MPI) [16] for message passing
and can be considered an extension of MPI-2

## Slide 32: Global Arrays
Global Arrays supports the shared-memory model
  Allows nodes to share arrays between processes as if the memory is physically shared while providing separate mechanisms to access shared data

## Slide 33: ARMCI
ARMCI (through Global Arrays) provides programmer with simple routines to access and manipulate data
  Uses one-sided communication that allows for the overlap of computation and communication
  Platform-specific; uses all available resources to achieve best performance

## Slide 34: Design Implementation
Modular design
Three major components are driven by a script file read at runtime
  Which analysis algorithm to be displayed
  What device display will use
  How data to be read and written to disk

## Slide 35: Operation
Data is accessed and analyzed using Global Arrays and serial analysis algorithms; each serial algorithm derived from ComputeFunction
Data access implementation abstracted
  Stores data on disk

## Slide 36: Visualization and Display
Large distributed data makes gathering compute-intensive and time-consuming
  Output mechanism couples parallel processing with parallel rendering
IBM SP equipped with IBM Scalable Graphics Engine
  High performance graphics frame buffer directly connected to GigE network comm. switch fabric by 4 links (16 is the max)
Each link
theoretically capable of bandwidth of 45 megapixels
Notes: 24-bit color, full-motion, parallel image
output using the SGE has been benchmarked

## Slide 37: Performance & Experimental Result
IBM SP2
  Distributed shared-memory computer
  26 Quad-core nodes
  CPU is an IBM Power 3 processor @ 375 MHz
  Each node has 3 GB of memory
  input file is a Landsat 300 Mbyte image
HP Linux Cluster
  128-node/256 Itanium-2 processors (McKinley processors).
  1 Tflop peak theoretical performance
  1.5 Tbytes of RAM
  500 Mbyte Landsat image
Image converted to 8-byte floating-point
Two algorithms employed: Texture and Modified Radon Transform
Bump in timings due to a new, evolving system
Architecture by HP
Notes: 24-bit color, full-motion, parallel image
output using the SGE has been benchmarked

## Slide 38: Conclusion
Global Arrays tools key contribution to scalability
  Tools enable shared memory programming model with one-sided communication and async parallel I/O
An object-oriented framework
  Provides developers with an easier framework to develop scalable software for massively parallel computers
Performance numbers indicate we are approaching goal of real-time image processing of very large image files
  Goal to be ability to process large image files (greater than 75 megapixels) under 10 seconds
Future directions include analysis and viewing of 3-dimensional data

## Slide 39: Q&A

## Slide 40: Thank you