## Slide 1: Reconfigurable Computing
David Ojika

## Slide 2: What to Expect
Part I: Background
  Motivating research [10 mins]
Part II: Introduction
  Current research [10 mins]
Part III: Guest Paper
  Reconfigurable Computing [20 mins]
    Fast and Flexible High-Level Synthesis from OpenCL using Reconfiguration Contexts
      Reference I: Intermediate Fabrics: Virtual Architectures for Circuit Portability and Fast Placement and Routing
      Reference II: Design and Implementation of a Heterogeneous High-Performance Computing Framework using Dynamic and Partial Reconfigurable FPGAs
Q&A [10 mins]
Notes: This section: Reconfigurable Computing, encompasses all of these

## Slide 3
Three people were under an umbrella but never got wet!
How did they do it?
Notes: Quick brainteaser

## Slide 4
It never rained! ;)

## Slide 5: Reconfigurable Processing in Low-Power Programmable DSP
Part I: Background

## Slide 6: The People-Problem (Notional)
A computer named Robocomp
  To be launched to the moon
  Mission I: Acquire lunar samples:
    acoustics – analog signal
    oxygen and hydrological
    soil samples, etc
  Mission II: Process data on-the-fly
ACS
Robocomp-X
Robocomp
Robocomp
ACS: Adaptive Computing System

## Slide 7: Digital Signal Processing
Analog
Digital
Conversion
Acoustics Subsystem
- Multi-standard codec: MP3, AAC, WAV
- Fast sampling
Real-time playback
Low-Power!!!
Notes: Entire system could represent image or video processing. Signal processing encompasses both.

## Slide 8: 10 Minute Outline
Solutions to Low-Power Processing
Granularity of Programming Model
Granularity Models
Power Reduction Techniques
Multi-Granularity Architecture
  Multi-Granularity and Energy-Flexibility Gap
  Multi-Granularity Architecture Template
Experimental Examples
Conclusion & Future Work
Mission Success?

## Slide 9: Solutions to Low-Power Processing
Previous Approaches
  General Purpose (GP) processors with extend instruction set
  GP – Co-Processor structures
  Application Specific processors (ASIC)
  Processors with power-scalable performance
A Reconfigurable Architecture Solution
  Dynamic reconfiguration of hardware modules
  Match reconfiguration level (or architecture) with task
  A good matching ensures that only necessary computation fabrics are enabled and using up power
    How to define a good model for matching??

## Slide 10: Granularity of Programming Model
Programming model:
  Level of system reconfiguration chosen in accordance with the model of computation of the target task
Granularity:
  Digital composition of the building blocks of a computation – electrically and structurally
Energy
Utilization
Granularity
Computational
Complexity
task

## Slide 11: Granularity of Models
Stored-program
Dataflow
Datapath
Gate-level
Logic (gate) level
(Highest level of reconfiguration)
I. Stored-program model
(Zero level reconfiguration)
Notes: Two extremes

## Slide 12: Granularity of Models (cont.)
III. Datapath model
II. Dataflow model
Notes: Middle two

## Slide 13: Power Reduction Techniques
Operate at low voltage and frequency
  Power = Voltage^2 x Capacitive load x clock
Reduce energy waste on modules and interconnect
  Application-specific module
  Preserve locality in task algorithm
  Use energy on demand
  Static configuration – avoid extensive multiplexing

## Slide 14: Multi-Granularity Architecture
Energy
Utilization
Granularity
Computational
Complexity
task
ASIC FPGA CPLD Traditional
Processor
Programmable
domain
How to:
  Maintain programmability
  Make task more application-specific
  Big, big challenge!

## Slide 15: Multi-Granularity & Energy-Flexibility Gap

## Slide 16: Multi-Granularity Architecture Template
Components
  Satellites:
    Reconfigurable processing elements
  GP Processor:
  (general processor core)
  Communication Network
  Reconfigurable Bus

## Slide 17: Experimental Example
Traditional DSP
PL-DSP
Acoustics Subsystem
- Multi-standard codec: MP3, AAC, WAV
- Fast sampling
Real-time playback
Low-Power
Notes: We employ one of the previously described power-saving model

## Slide 18: Experimental Results
Energy versus concurrency
  Voice-Coder Processor: 1.5V, 0.6mm CMOS technology
    175 pJoule per MAC operation
    At max clock rate 30MHZ  5.7 GOPS/Watt
    Operation: Full-dot vector operation
    Total predicted power between 2 and 5mW

## Slide 19: Experimental Example II
CDMA Baseband Processor
  High performance Correlator
  Impossible to construct processor from functional modules
  Diminishing return, Amdahl's law
  Correlator Solution:
    Use of set of accumulators
    Removes need for multipliers
    Proposed by: Nazila Salimi -
    “CDMA Correlator Implementation in FPGA”
From Dr. Yutao He’s Note. Lecture Note 2

## Slide 20: Conclusion
Making an application configurable usually carries with it, large energy overhead
To minimize energy, applications must use the right model of computation for only the time period required.
Balance must be set for maintaining an optimal performance level against power dissipation
More research needs to be done in keeping energy dissipation low without sacrificing performance
 FPGA design automation research needs a new paradigm!

## Slide 21: OpenCL Benchmarking of Image Processing Applications on FPGA
Part II: Research

## Slide 22: Introduction
Modern HPC devices powerful but quite challenging for app designers
  Combination of disparate hardware and software programming models
  Portability of computation kernels often a challenge, coupled with need to maintain designers productivity
Image processing applications largely compute-intensive
  Naturally lend themselves to parallel computation due to their inherent data-parallel nature
  Produce vital results that are used to extract information and valuable for decision making
OpenCL framework enables architecture-independent programming while improving portability, performance and productivity
  Studies have shown trade-offs depending on application and architecture
  This study will comprise of a comparison and analysis of performance for several image processing dwarfs
    Study two main architectures: reconfigurable-logic device and fixed-logic device
    Implementations in both OpenCL and native device language (Verilog/VHDL and C/C++) will be compared based on real-time performance and power trade-offs
Notes: Increased interest from industry and CHREC members
Lots of ongoing research by vendors and in academia: Xilinx, Altera; Virginia Tech’s OpenCL & the 13 Dwarfs

## Slide 23: Approach
Kernel investigation
  Research image processing kernels and algorithm
    Determine amenability to OpenCL-based parallelization
Architecture study
  Altera Stratix-5 FPGA
    Study new device architecture
  Intel Xeon Phi Many-Core CPU
    Leverage previous experience from architectural capabilities of device
OpenCL kernel benchmarking
  Functional portability
    Performance compared to architecture’s native implementation
  Performance portability
    Performance across different hardware architectures
Kernel portability
  Map kernels to hardware
    Apply architecture-dependent optimizations
    Gather insights from kernel-architecture optimizations
Notes: Functional Portability: To what extent is OpenCL a suitable substitute for current programming standards. (by comparing with C/C++ and Verilog/VHDL).
Performance Portability: To what degree is OpenCL suitable as a single standard targeting multiple platforms. (by mapping to other architectures: Intel Xeon Phi).
Opencl Idea: Use all the available computing resources on device to make kernel run really fast

## Slide 24: Research Outline
Kernel
C++ Implementation
OpenCL Implementation
Reconfigurable-Logic Device
Fixed-Logic Device
Kernel Exploration
Research image processing kernels and algorithm that are highly amenable to parallelization
Serial Implementation
Leverage existing kernels and recast, or build from scratch
Test and validate
OpenCL Implementation
Convert code to OpenCL
Leverage OpenCL kernels: Vendors, Open-source (OpenDwarfs, et. al)
Device Porting
Kernel mapping
Device-specific optimizations
Insights and Conclusion
Experience accumulated from all levels
Performance and productivity evaluation; others, e.g. power
Kernel Layer
Implementation
Layer
Device Layer
Benchmarking

## Slide 25: System Architecture
Disparate FPGA and Many-Core architecture
  Will leverage RC Middleware
  Possibly, RDMA for Many-Core
Currently not truly heterogeneous – kernels not running concurrently
  Mix and match kernel/architecture can be complex
    All possibilities of cross-product of performance metrics with bandwidth required
      {Glops/s, … } x {L2, DRAM, PCIe, Network }  Requires comprehensive benchmarking
2 divergent architectures
  Reconfigurable-Logic: Stratix 5
  Fixed-Logic: Xeon Phi
Heterogeneous Architecture
  Compute-intensive tasks can be offloaded to accelerators

## Slide 26: Application Case Study
Edge Detection
  Set of mathematical operations that collectively aim to determine points in a digital image
  Vital algorithm in image processing and machine vision
    Feature detection & tracking
Benchmarking
  OpenCL-based kernel benchmarks
    Spatial domain: 2-D Convolution
    Frequency domain: 2-D FFT
Algorithm
  Sobel Filter
    Commonly used algorithm for edge detection apps
    Others: Canny, Kayyali
Dependency
Fig. 1: Application Structure
Fig. 2: Design Strategy
Notes: Algorithm:
The Sobel filter inherently exhibits parallelism that allows programmers to exploit ways of parallelizing the algorithm on different architectures.
It was the benchmark of choice for Rita Cucchiara and Massimo Piccardi in their evaluation of image processing on SIMD parallel machines [2]
Benchmarking:
will study, parallelize, map and where necessary, optimize

## Slide 27: Evaluation Method
Real-time performance metric
Human perception
SNR
Functional portability
Performance portability
Improvement over native lang.
Roofline Model or others
FPGA resource utilization
Realizable Utilization
Power metric
Notes: High-Level Combined Architecture-Application Evaluation Method. Architectural issues and application behavior exhibit a two-way interaction, with only a thin line of separation.
Functional Portability: To what extent is OpenCL a suitable substitute for current programming standards. (by comparing with C/C++ and Verilog/VHDL).
Performance Portability: To what degree is OpenCL suitable as a single standard targeting multiple platforms. (by mapping to other architectures: Intel Xeon Phi).
*Final real-time performance metric measured in frames/sec

## Slide 28: Current Milestones
Verification and Validation
  Two MATLAB-based models for validation of data from edge detection app
    Model A: Spatial Domain
      Sliding Window/direct pixel manipulation via convolution
    Model B: Frequency Domain
      Based on FFT, Dot-Product Multiply and Inverse FFT operations
[1] Cooley-Tukey FFT on the Connection Machine (1991)
Source
After edge detection
After normalization
1bit monochrome
2-D FFT OpenCL
  Initial run for single-precision 1024x1024 complex numbers
    Offline compilation of kernel for Altera FPGA
      Takes a very large amount of time as with traditional compilation methods
    Runtime API programming
      However, Online programming of FPGA with kernel binary fairly seamless
      Estimated resource utilization from tool
Serial 2-D FFT C++ implementation
  Based on Cooley-Tukey algorithm: O(nlogn) (Radix 2, for N = 2k)
    More general purpose and gives better scheduling [1]
  Implementation provided insights on algorithm and understanding of its parallelization technique
  Served as foundation for subsequent OpenCL-based implementation
  Why its so important:
    Employed in a large body of image, signal and video processing
      More investigation attached to appendix (appendixA.pdf)
Notes: Other FFT alorithms:
Stockham (Radix 2 , for N = 2k)
Sande-Tookey (Radix 2 , Decimation in Frequency, for N = 2k)
Bluesteins (Radix 2 , for any N) Stratix 5: 2D FFT (1024x1024 SP Complex)
Processing time = 5.2304ms
Throughput = 0.2005 Gpoints / sec (20.0476 Gflops)

## Slide 29: Future Work I
Notes: On the one side, kernel exploration and algorithm study completed Edge detection and SAD to be orchestrated in pipelined fashion (for either MPSD or MPMD) after insights from device-kernel benchmarking.
SAD: sum of absolute differences provides a simple way to automate searching for objects inside an image.
Unreliable due to the effects of contextual factors such as changes in lighting, color, viewing direction, size, or shape.
May be used in conjunction with other object recognition methods, such as edge detection, to improve the reliability of results.

## Slide 30: Future Work II
Notes: On the one side, kernel exploration and algorithm study completed Edge detection and SAD to be orchestrated in pipelined fashion (for either MPSD or MPMD) after insights from device-kernel benchmarking
Internship phone call from Intel about potentials of implementing iWarp within-the-rack.

## Slide 31: Fast & flexible high-level synthesis from opencl using reconfiguration contexts
Part III: Guest Paper

## Slide 32: What is RC?
We all know the gist!
Notes: Guess everyone here know what RC is.
- Architecture, benefits, etc

## Slide 33: RC is Challenging
Reconfigurable computing promising but design tools pose challenge to designers
Huge compilation time: synthesis P&R  mapping
  Design iteration difficult and productivity limited
  Runtime compilation difficult; contributes to niche FPGA usage
OpenCL enables high-level synthesis of FPGA
  Vendors adopting standard to alleviate steep learning curve associated with native language (VHDL/Verilog)
    Can be likened to Assembly vs C  only a small penalty in performance
    Altera, Xilinx. But other vendors with proprietary HLS: Xilinx, Convey
  Presents significant potential:
    Portability
    Productivity
    Performance

## Slide 34: OpenCL-Based Approach
On CPU and GPU, “online” compilation possible
When kernel changes, host simply loads a different kernel on accelerator: in ms
“OpenCL mainly used to program accelerators“
However, the case is different for FPGAs
  Kernel has to be re-compiled every time system changes
  Takes a huge amount of time: 8 hours to days
    Not a good idea for dynamic hardware, or even for a fixed instance of hardware!
  “Online” compilation not typically done
    Kernel pre-compiled “offline” into binaries and loaded as needed
Notes: this illustration is important to understand the following

## Slide 35: Limitations of OpenCL Approach
Current HLS approach conflict with mainstream OpenCL
Orders of magnitude FPGA compilation time
Limited support for changing/adding kernels after compilation
  Can PR in some way?  reconfiguration contexts
Reconfiguration Contexts
Key features
  Coarse-grain units instead of finer-grained LUTS
  Backend synthesis
    Thus, allowing use of (virtually) any OpenCL tool on the frontend
Advantages
  Compile kernel faster
  Change kernel online

## Slide 36: Backend Synthesis
Intermediate Fabrics (IF) – Leverages Dr. Stitt’s previous work
  See video online 
Summary
  1000X faster place & route compared to device vendors' tool
  21% increased FPGA resource utilization (drive logic)
  Uses coarse-grained resources implemented atop FPGA
    Avoids decomposing of circuits into finer grain LUTS
    Maps circuit unto app-specialized resources (FP, FFT)
Specializes IF for OpenCL
  Compliments existing OpenCL synthesis approach
    Enable fast compilation: compiling any kernel
    Enable fast reconfiguration: adding and changing kernels
  Automatically determines effective fabric architecture for given application (previous IF were manually designed)
Notes: …and FOR a given a given application, it automatically determines the efective fabric architecure

## Slide 37: Intermediate Fabric Optimality
Impossible to create optimal fabric for all combinations of kernels
  Context-design heuristics finds optimal IF
Intermediate Fabric
  1. Analyzes kernel requirements from application or domain
  2. Cluster kernels based on similarity into set of fabrics called reconfiguration contexts

## Slide 38: Reconfiguration Context (w/o IF)
Kernel-Specific accelerators (existing approach)
  Provides no support for kernels not known at system generation
    Limitation of existing OpenCL synthesis
  Example: context tasked with supporting three kernels
    Implements three kernel-specific accelerators
    Although, possibly more efficient than IF (as seen in pipelined archi.)
  Limited scalability due to lack of resource sharing across kernels

## Slide 39: Reconfiguration Context (with IF)
IF-Based Context
  Only common computational resources fixed during system generation
    Fixed resources: FFT, Mult, Accum, Sqrt
    Reconfigurable interconnection
  Provide flexibility to support kernels similar to one for which context was originally designed
    Important for iterative design development
    Versatile for changing system system requirements and workloads

## Slide 40: Reconfiguration Context in Operation
OpenCL Front-end
  Read source kernels
  Synthesize kernel into netlists (coarse-grained cores & controls)
IF Backend
  Read generated netlist
  Apply context-based heuristics (based on netlist clustering)
    Group netlist into sets of similar of resource requirements
    Design IF-based context for each set  reconfiguration context
FPGA Front-End
  Place and Routing
    Reconfiguration Context compiled into bitstreams using device-vendor tools

## Slide 41: Reconfiguration Context in Operation
Dynamic Operation
  While a context is loaded to FPGA
  Rapidly configure context to support different member kernels (kA, kB)
  Required kernel not in context:
    reconfigure FPGA with new context
  A new kernel added to system:
    Front-end tool: synthesize kernel
    Backend: Cluster kernel into existing an context
      Performs context PAR to create bitfile for kernel
Notes: ----- Meeting Notes (3/11/14 13:20) -----
Whilel context is loaded to FPGA… the IF rapid configures context to support different kernels.

## Slide 42: Context-Design Heuristics
Designing appropriate contexts most critical part of tool flow
  Main challenges of context-based design are:
    How many contexts to be created to support all the known kernels
    What functionality/resources to include in the context: DSP, FFT, etc.
    How to assign kernels to contexts
  Clearly an optimization problem!
    Maximize reuse of resources across kernels in a context
    Minimizing area of individual context
A well designed context seeks to:
  Minimize individual context area by minimizing number of resources reused across kernels in a context
  Helps design fit under area constraints
    Useful for scaling each context to increase flexibility and support similar kernels other than those known at compile time

## Slide 43: Heuristics Mechanism
Groups of kernels often exhibit similarity in their mixture of operation
  Example as seen in application-specialized processors in many domains
While computational resources are fixed, interconnection remains flexible
  Key enabler for IF-based context
  Heuristic considers functional similarity over any structural similarity
  Exploit of structural similarity between kernel (e.g to reduce interconnection area) an alternative clustering method
    Functional grouping still useful when cost of functional resources expected to be high than cost of interconnect
Notes: Heuristics can be quite complex

## Slide 44: Heuristics Mechanism
Ignores functional timing differences
  Assumes that differences are minimized through pipelining [2]
    Timing can be considered during grouping when timing pipelining isn't sufficient
      Using additional fmax dimension in a clustering heuristics
Contexts that minimally support one member of a group should support other members of the group
  Although each member might require different number of resources, or addition of other resources
  Identifying these groups is vital for designing contexts that are compatible with kernels similar to the kernels inside each group

## Slide 45: Heuristics Mechanism (IF)
Features identified using clustering heuristics in an n-dimensional feature space
  Feature space defined by functional compositions of system’s kernel netlist
  Example: given an application containing 2kernels – FIR and SAD
    Clustering would operate on SAD = <0.3, 0.0, 0.7> and FIR = <0.5, 0.5, 0.0> in the space <f_add, f_mul, f_cmp/sub>
K-means clustering used to group netlists in space
    Results to up to K sets of netlists for which individual contexts will be designed
    Heuristic can use resources requirement of core to estimate area required by each cluster
      K to be selected subject to user or system-imposed area constrains
    User may set select value for k so satisfy systems goals for flexibility

## Slide 46: OpenCL-IF Compiler
A custom tool based on Low-Level Virtual Machine (LLVM) and C frontend
First compiles kernel into LLVM’s intermediate representation
  Substitutes custom intrinsics for system system functions (e.g get_global_id)
Uses LLVM’s standard optimization parses
    Inlining auxiliary functions
    Loop unrolling
    Some common hardware-specific optimizations
Creates a control data flow graph (CDFG)
    Simultaneously maps LLVM instructions to compatible cores (specified in user-specified library)
    Cores may be added to library to enable limited application- and target-specific optimizations

## Slide 47: OpenCL-IF Compiler
DFGs independently scheduled and bound to final resources provided by the context using other approaches [2]
Resulting kernel netlist implemented on context through place & route
  Yields a context context bitsream for each kernel
At runtime, kernel executed after configuring its context with corresponding bitstream
  Execution mutually exclusive per context
A unique feature of OpenCL-IF is support for efficient data streaming from external memories
  Previous approaches implement kernel accelerators that comprise multiple pipelines competing for global memory through bus arbitration
    However some study addressed this memory bottleneck by using specialized buffers
Notes: Previous approaches implement kernel accelerators that comprise multiple pipelines competing for global memory through bus arbitration

## Slide 48: Experimental Setup
Evaluation of context-design heuristics
  Setup provides minimal guidance by using only framework’s known kernels
  Single framework for computer vision applications
    Multiple image-processing kernels executing in different combinations at different times
      Representative of stages in larger processing pipelines
  Evaluation Metrics
    Compilation time
    Area
    Clock frequency
FIR
Gaussian
Sobel
Bilinear
Threshold
Mean
Max
Min
Normalize
SAD
    10 OpenCL kernels
    Fixed-point and single-precision floating-points

## Slide 49: Results
Using 5 clusters provides significant 60% decrease in cluster size
  Flexibility in allowing implementation of different kernels under area constraints (by implementing context minimally)
Cluster size can increase (up to fabric capacity, or area constraint) if further flexibility is desired
  Provides better matching for underlying kernels
Different k values introduce trade-offs
  Can be beneficial in order applications depending on designer intent

## Slide 50
Comparison of compilation time, area, and clock frequency for OpenCL-IF reconfiguration contexts and direct FPGA implementations for a computer-vision application with k=5. Floating-point kernels are shown with an FLT suffix

## Slide 51: More Results
After context generation, reconfiguration context enabled compilation of entire system of kernels in 6.3s
  4211x faster than 7.5 hours required via ISE direct compilation to FPGA
Floating point kernels experience greater compilation speedup (6970x vs 1760x)
  More fine grained resources hidden by their context
Each kernel compiled at an average of 0.32 seconds
  Provides an estimate of the compilation time a new, context-compatible kernel
Clock overhead negligible on average
  Additional pipelining in fabric’s interconnect benefit some circuits
System require 1.8X additional area compared to implementing kernel directly
  Not necessarily an overhead due to significant added flexibility

## Slide 52: Configuration Time and Bitstream size
Context can be reconfigured with new kernel in 29.4 us
  On average, 144x faster than FPGA reconfiguration
  Enables efficient time-multiplexing of multiple kernels

## Slide 53: Conclusions
Introduced a backend approach to complement existing OpenCL synthesis using coarse-grained reconfiguration contexts
  Enabled 4211x faster FPGA configuration compared to device-vendor tools
  Cost overhead of 1.8x area overhead
Reconfiguration context context can be reconfigured in less than 29us to support multiple kernels
  While using slower FPGA reconfiguration context to load new contexts to support significantly different kernels
Clustering heuristics introduced to create effective contexts that group kernels into functional similarity
  Leverage previous work on intermediate Fabrics (IF) that supports requirements of each group

## Slide 54: Future Work
Evaluating other architectures for reconfiguration contexts
  Including more specialized (and less flexible) interconnects
Strategies for managing multiple context through partial reconfiguration and optimization enabled through runtime kernel synthesis

## Slide 55
Xie-Xie, Gracias, Namaste, Dalu, Thank you …
M i s s i o n A c c o m p l i s h e d ?!
Questions?
RoboComp-X