## Slide 1: Partial Reconfiguration Not just a half baked job of reconfiguring
Rohit Kumar
Research Student
University of Florida
Dr. Ann Gordon-Ross
Associate Professor of ECE
University of Florida

## Slide 2: Partial Reconfiguration is All Around Us
Changing situations…
…require part of the system to reconfigure on the fly

## Slide 3: Partial Reconfiguration is All Around Us
But, FPGA reconfiguration is disruptive
  Resets the device
  Lose all data
  Causes downtime
Downtime is dangerous

## Slide 4: Full Reconfiguration:
This is your FPGA
Task 1
Task 2
This is your
FPGA on PR
Task 1
Task 2
Static

## Slide 5: Why Partial Reconfiguration?
So what??
I’ll just put both tasks on the same device!
Sure, why not?
But, devices have limited space!
Not impressed
FPGA
Task 1
Task 2
Task 3
Task 4
Task 5
Task 6
Reason #1
Sharing many tasks on a single region saves area!

## Slide 6: Why Partial Reconfiguration?
I got it! I’ll just use PR on a tiny cheap FPGA and time- multiplex everything!
Okay, we’ll give you that one
But, it’s a trade off
  The more parallelism, the better the performance
  Plus, some tasks must be run in parallel
Reason #2
Using less area on a smaller device is less costly!

## Slide 7: Why Partial Reconfiguration?
So that’s it??
I pay a bunch more just to use less area?
Well, you know you could save power?
  Imagine you have two versions of a task
    High-performance version
    Low power version
  When performance is critical
    Load the high-performance version
  When performance is less critical
    Load the low-power one
Man, what a buzz-kill
FPGA
Reason #3
Replace tasks with low-power versions when possible!

## Slide 8: Why Partial Reconfiguration?
So what??
I’ll just use clock gating (CG) and dynamic frequency scaling (DFS), both of which are available for Xilinx FPGAs
Right… well… you see… actually….
Hmm…
Shut up

## Slide 9: Why Partial Reconfiguration?
Okay, but I’m not sold unless there are 4 reasons.
Did you know PR keeps your device safe in space?
  In space, cosmic radiation corrupts SRAM!
  These are called single event upsets (SEU)s
With PR, you can patch FPGA configuration memory
  Without turning off the device
  This is called “scrubbing”
But FPGA configuration memory uses SRAM!
FPGA
10111011
FPGA
01101100
Reason #4
PR keeps circuits safe in harsh environments

## Slide 10: So you wanna make a PR design…
First, we make partitions
  Partitions are like black boxes
    They start out empty
    Then we load modules
  Modules run tasks
  To change tasks
    Load a new module
    Old one is overwritten
Partition 1
Partition 2
The FPGA (not to scale)
a
b
a
f
f

## Slide 11: So you wanna make a PR design…
Modules have to fit like puzzle pieces
  Black boxes have a defined interface
  All modules must fit that interface
Where the ports are matters as well
  Ports must be in the same place for every module
  “Partition pins” are port location definitions
  They ensure connections are not broken during PR
Partition 1
Partition 2
The FPGA (not to scale)
a
b
a
f
f

## Slide 12: So you wanna make a PR design…
Quit sugar-coating it, sirs, I am not a child you know.
Oh, fine. This is what you’re going to learn today:
  Logically partitioning your application into modules
  Preparing your partitioned design in ISE
  Floor-planning the layout of your device in PlanAhead
  Implementing your design in PlanAhead
  Finding your inner child through meditation (time permitting)

## Slide 13: Step 1: Logical partitioning
Easy there buddy
Two components are mutually exclusive if
  Only one is used at a time
  One’s inputs don’t directly depend on the other’s outputs
Only mutually exclusive components share a partition
  So, before you can make your design…
  You must find as many of these as you can
The first step to make a PR design is breaking the application into sets of mutually exclusive components

## Slide 14: Step 1: Logical partitioning
Okay, lets do an example
This is an up/down counter
The add and the subtract
  …are mutually exclusive
  Only one is used
  They do not depend on each other
The store and the add
  …are not mutually exclusive
  The store depends on the add’s output
The add and subtract can share a partition
  The add forms one reconfigurable module
  The subtract forms another reconfigurable module
He’s still not reassured
Direction?
Direction = up
Result = 0
Result ++
Result --
Store Result
Get Direction
up
down
Direction = up
Result = 0
Result ++
count
Store Result
Get Direction
Result ++
PR!

## Slide 15: Now some cool stuff that our group has been doing in CHREC

## Slide 16: F4-13: Partially Reconfigurable System Development and Management
Number of supporting memberships: 1.5
Dr. Ann Gordon-Ross
Associate Professor of ECE
University of Florida
Rohit Kumar
Elizabeth Graham
Aurelio Morales
Shaon Yousuf
Zack Smaridge
Research Students
University of Florida

## Slide 17: F4-13: Goals, Motivations, and Challenges
    Optimize area, power, and performance
    Reduce design time effort
Goal
Increase reconfigurable computing (RC) system designer productivity
    Source code’s PR analysis aids design parameter selection
    PR isolates reconfiguration to portions of FPGA
    Enables resource time-sharing
    Leverage network of PR-capable FPGAs
    Leverage distributed resource management services
    Scripts and tools reduce manual design flow steps
Motivations
Partial reconfiguration (PR) enables area and power savings
  Distributed computing provides increased system computation capability
  Early design space pruning reduces design time
  Design automation enables rapid system implementation
    PR requires application- and device-specific, low-level knowledge
    Efficient design space exploration (DSE) for PR-centric system design
    Maintaining application data integrity across PR-centric distributed RC systems
Challenges
    Identifying automatable design flow steps

## Slide 18: F4-13: Approach
Alleviates tool flow overhead and reduces implementation effort
Enables load balancing across local and remote VAPRES nodes
Enables distributed processing and management across VAPRES nodes
Identifies resource- and performance-optimized PR architectures
Adapt system-wide version of DDRM for server/client
Leverage dynamic hardware task management tools
Design and test DDRM application
Node-Level
Distributed Resource
Management
Expand context save and restore (CSR) and hardware task relocation (HTR) features
Optimize CSR and HTR to maximize task throughput and resource utilization
Dynamic Hardware Task Management
Leverage PRML to generate PR applications from source code
Leverage high-level synthesis tools to generate VHDL code
Leverage intermediate fabrics1 and DAPR+2 for fast DSE
One-click PR Design Space Exploration
Design automation tool suite (DAPR++) to aid PR system design
Generates distributed RC system for increased computational capacity
Automated
Design
Implementation
PR-centric RC System Development
Task B
Task A
Task C
DAPR+ – Design Automation for PR FPGAs
DDRM – Distributed Dynamic Resource Manger
PRML – PR Modeling Language
1 Developed by F2-10
2 Developed by F4-11
DSE – Design Space Exploration

## Slide 19: Task A: PR Design Space Exploration Framework
Streamlined framework for rapid application partitioning, PR design space exploration, and implementation
Automatically generates PR application from non-PR high-level source code
Alleviates complexities in PR design implementation via automated tool flows
PR design space exploration
Low-level automated floorplaning and partitioned application’s area/ power/performance evaluation
Implementation
Automation and integration of vendor’s and various third-party tools
Framework components
Explores PR design space to find area/power/ performance optimized PR application
Automatically generates PR application from non-PR high-level source code
1 Published in FCCM’13
Partitioning
Automatic modeling and PR partitioning of application’s C source code via PRML1

## Slide 20: Task B: PR System Design Automation with DAPR++ Tool Suite
  DAPR++ tool suite aids designing RC systems using automation
Creates master and slave FPGA component layout tree
Creates FPGA VHDL black boxes for all components
DAPR++ Tool Suite
PR Architecture Generator
Network Generator
PR Task Manager
Throughput Profiler
Bitstream Manager
PRR Floorplanner
Automatically generates target device resource mapping
Heuristically floorplans PRRs and partition pins
Modifies bitstreams and enables task context save (CS) and context restore (CR)
Creates network protocols for master and slave FPGAs
Creates PR task reconfiguration schedules to reduce reconfiguration time
Records data packet transfer rates between master and slave FPGAs
CAW13
CAW13
CMW12
CAW13
Switch
Master FPGA
Slave FPGA 1
GPP
PRRs
Slave FPGA 2
PRRs
Notes: Click 1 (start of slide):
We know PR design is a complex to design process, so in order to alleviate this complicated design process, we introduce the DAPR++ tool suite.
Click 2:
The DAPR++ tool suite alleviates PR design by automation. DAPR++ tool suite aids PR system generation for an application using 6 useful tools:
Click 3:
A PR architecture generator that helps generate a PR architecture template and VHDL blackboxes for the PR application.
Click 4:
A PRR floorplanner that automatically generates the target architecture resource map and heuristically floorplans the application's PRRs.
Click 5:
A manager API that helps modify and manage bitstreams using context save and context restore hardware management tools
Click 6:
A network generator that generates data transfer protocols an Ethernet interfaces for the Architecture
Click 7:
A PR task manager creates task schedules that prioritize reducing reconfiguration delay in order to speedup overall application execution
Click 8:
A throughput profiler that records the application's throughput and reports this throughput data to PRML for architectural improvements.
Click 9:
For CMW 13, we developed the PR task manager tool and also enhanced the PRR floorplanner.

## Slide 21: Task C.1: Node-level DDRM
Node-level DDRM facilitates VAPRES network management
  Automatically manages task relocation
    Minimizes system delays caused by task relocation latency
  Uses custom node communication procedures
    Maintains global node execution status
  Task relocation circumvents node-level restrictions
    Individual nodes have limited resources and power
    Network nodes to leverage shared resource pool
  Example applications: sensor networks, target tracking
Node-level DDRM controls nodes’ task distribution
  Node is a client for local tasks, server for remote tasks
  Client determines new node and PRR for task execution
    Algorithm developed in system-level test version of DDRM
  Clients communicate with servers to locate new PRR and transfer PRM
    Created automated communication functions to coordinate inter-node transfer of bitstreams, context, test results, and node status
PRR – Partially Reconfigurable Region
PRM – Partially Reconfigurable Module
DDRM – Distributed Dynamic Resource Manager
DDRM
DDRM
DDRM
DDRM
DDRM
DDRM

## Slide 22: Task C.2: Hardware Task Management Tools
PRM – Partially Reconfigurable Module
VAPRES – Virtual Architecture for Partially Reconfigurable Embedded Systems
DSP – Digital Signal Processing
BRAM – Random Access Memory Block
PRR – Partially Reconfigurable Region
VAPRES node
PRR
1
M2
PRR1
M1
PRR1
On-chip CSR
VAPRES node
PRR
2
PRR
1
M3
PRR2
merged
M1
PRR2
M1
PRR2
M2
PRR1
M1
PRR1
On-chip HTR
Experimental results on XUPV5 board
  Linear growth rate in CSR execution times w.r.t. number of PRM flip-flops
  HTR execution times
    Linear growth rate for context save (CS) and context restore (CR)
    Non-linear growth rate for task relocation (TR)
  System designers can trade off PRR size/granularity and CSR/HTR execution times based on application requirements
New CSR and HTR features
  Supports DSPs/BRAMs/LUTRAMs and multiple PRR rows/columns
  Reduced execution times
Distributed processing and load balancing tools for networked VAPRES nodes
  Portable across different FPGA architectures
  On-chip context save and restore (CSR) and hardware task relocation (HTR) software
    PRM execution state retained on PRM preemption
    Enhances task switching in PR-capable FPGAs
    Suitable for autonomous, multitasking PR systems
Notes: Great animations!