## Slide 1: Design and hardware implementation of chaotic encryption scheme in real time embedded systems
Authors:
Amit pande and joseph zambreno
Publication :
Signal Processing and communication
conference, 18-21 july, 2010

## Slide 2: Intro to cryptography
Confidentiality
End-Point Authentication
Message Integrity
secure
sender
secure
receiver
channel
data, control messages
data
data
Alice
Bob
Trudy
Notes: Confidentialiyy: only sender, intended receiver should “understand” message contents : sender encrypts, receiver decrypts
End-Point Authentication: sender, receiver want to confirm identity of each other
Message Integrity: sender, receiver want to ensure message not altered (in transit, or afterwards) without detection

## Slide 3: Types of Cryptography
Crypto often uses keys:
  Algorithm is known to everyone
  Only “keys” are secret
Public key cryptography
  Involves the use of two keys
Symmetric key cryptography
  Involves the use one key
Hash functions
  Involves the use of no keys
  Nothing secret: How can this be useful?

## Slide 4: Symmetric key cryptography
symmetric key crypto: Bob and Alice share same (symmetric) key: K
e.g., key is knowing substitution pattern in mono alphabetic substitution cipher
Q: how do Bob and Alice agree on key value?
plaintext
ciphertext
K
S
encryption
algorithm
decryption
algorithm
S
K
S
plaintext
message, m
K (m)
S
m = KS(KS(m))

## Slide 5: Breaking an encryption scheme
Cipher-text only attack: Trudy has cipher text that she can analyze
Two approaches:
  Search through all keys: must be able to differentiate resulting plaintext from gibberish
  Statistical analysis
Known-plaintext attack: Trudy has some plaintext corresponding to some cipher text
  eg, in monoalphabetic cipher, trudy determines pairings for a,l,i,c,e,b,o,
Chosen-plaintext attack: Trudy can get the ciphertext for some chosen plaintext

## Slide 6: Ciphers- Overview
Symmetric key cipher
Secure only for a fixed length of bits
Same key to encrypt all blocks, degrades security
Data encryption standard(DES), Advanced Encryption Standard (AES), developed by IBM
Encrypt individual bits
Starts with a secret key (seed)
Generate keying stream
ith bit of keying stream is a func of the key & the first i1 ciphertext bits
Combine stream with plain text to form cipher text(usually XOR)
Block
Stream
Ciphers

## Slide 7: What does a good cipher do?
Large key to resist brute-force search
Resistant to attacks
Lesser hardware resources
High throughput
Size of the enciphered text should be no larger than the original message
Discretisation needs to be addressed (short cycle length, non ideal distribution, correlation)

## Slide 8: Proposed model
Construction of a chaotic encryption stream cipher
Cipher uses a Pseudo-random sequence generator based on Modified logistic map
Hardware implementation in FPGA
Proposed cipher gives 16 bits of encrypted data/cycle
Embedded devices with tight constraints (power consumption, hardware resources)

## Slide 9: Chaotic Systems
Sensitive dependence on initial conditions
Fulfil the Shannon requirements of confusion and diffusion
Continuous time chaotic systems require repeated resynchronisation to match the phase at encoding and decoding ends
Discrete chaotic systems behave as private key encryption algorithms and can be implemented in fixed point hardware.
Notes: In Shannon's original definitions, confusion refers to making the relationship between the ciphertext and the symmetric key as complex and involved as possible; diffusion refers to dissipating the statistical structure of plaintext over bulk of ciphertext. This complexity is generally implemented through a well-defined and repeatable series of substitutions and permutations.

## Slide 10: Logistic Map
Xn+1 = λLM*xn (1-xn)
A simple model of resource-limited population growth
Dependent on value of λLM-growth rate
λLM ≈3.57 is the onset of chaos
beyond 3.57 exhibit chaotic behaviour
Islands of stability

## Slide 11: Histogram for 50000 samples using LM with initial seed=0.100010
a) λLM =3.61
b) λLM =3.91
c) λLM =4
d) λLM =3.83
Islands of stability
range(0,1) symmetric distribution around 0.5
Interval of great sensitivity to initial conditions

## Slide 12: Modified logistic map
Xn+1 = λLM*xn (1-xn) + μ
xn ∈ [α,1-α], α<0.5
Maxima occurs at xn = 0.5, Max value=λ/4+μ
Minima occurs at xn = α or 1- α,
min value= λ*α*1- α + μ
Solving yields :λ=4/(1-2α) & μ=α(2α-3)/(1-2 α)
End result: Flatter symmetric distribution for all values of α
Avoids any islands of stability

## Slide 13: Histogram for 50000 samples using MLM with α values corresponding to
λLM =3.61
λLM =3.91

## Slide 14: Quantization
xn quantized to obtain 16 bit value
Xn represented in fixed point as
Yn restricted to the least significant 16 bits
Many to one quantization
bn obtained for random feedback scheme
  bn = {an-1} ie the MSB

## Slide 15: Pseudo Random Sequence
zn =yn ⊕ yn-1 ⊕yn-2
No linear correlation between yn and zn
Statistical de-correlation makes it difficult to trackback yn

## Slide 16: Masking and random feedback
Cn = Pn ⊕ Zn ⊕ Fbn
  Cn - cipher text,
  Pn – plain text,
  zn – pseudo random sequence,
  Fbn – random feedback input from the past cipher text
Fbn = {Cn-1 when bn =0, Cn-2 when bn =1}

## Slide 17: How secure is this model?
Difficult to predict key value XORed to the plain text
Sequences zn and yn are linearly uncorrelated
Yn is obtained by sampling xn , which is used to iterate the chaotic map.
Chaotic map more sensitive to the MSB than to the LSB, so will become difficult to track back xn
100 iterations of the MLM to allow diffusion of initial key bits and parameter values(though 20 is sufficient)

## Slide 18: Hardware implementation
Fixed point implementation(more efficient in hardware)
Bit width of plain and cipher text is 2 bytes
64 bits fixed point precision is chosen (x(i), λ, μ)
α (0,0.375) in fixed point with 0 int bits and 64 fract bits
λ(4,16)
μ (-3,-15.0975)
Effective key space : 2125

## Slide 19: Hardware specifications
Virtex 6 XCVLX75TL FPGA using Xilinx11.0
Optimization
  Add two pipelining stages to the multiplier
  Single DSP slice can perform 25*18 bits multiplication
  For 64*64 bits multiplication 12 slices needed.
  But due to truncation of 64 bits , optimization possible

## Slide 20: Implementation of chaotic stream cipher
Xn-1
Xn-1 *(1-xn-1)
Xn-1*(1-xn-1)* λ
Xn-1*(1-xn-1) * λ
+ μ
Xn
Yn
Cn =Yn⊕Yn-1⊕ Yn-2
Zn=Cn⊕Pn ⊕FBn

## Slide 21: Resource utilisation
 | Orig. design | opt . design
Clock frequency (MHz) | 69 | 93
No DSP48EI slices | 23 | 16
No. slice registers | 228 | 160
No. slice LUTs | 354 | 643

## Slide 22: Shortfalls of the paper
Logistic map is very basic type of chaotic map
Synchronization problems not discussed( message loss during any transition period)
MLM was not tested using crypt attacks, chosen-plain text and chosen-cipher text attacks

## Slide 23: Conclusion
Chaotic stream cipher based on Modified Logistic Map
Secure against plain text attacks
Hardware implementation of proposed scheme achieved clock frequency of 93 MHz
Suitable for real time embedded applications.

## Slide 24: Questions???