## Slide 1
Research highlighted in this presentation was supported by CHREC members and by the I/UCRC Centers Program
of the National Science Foundation under Grant Nos. EEC-0642422 and IIP-1161022.
28th Annual AIAA/USU Conference on Small Satellites, 05AUG14
Investigators and Students
Dylan Rudolph, Christopher Wilson, Jacob Stewart, Patrick Gauvin, Alan George, Herman Lam, Gary Crum, Mike Wirthlin, Alex Wilson, Aaron Stoddard
Research Partners
University of Florida (lead), NASA Goddard, Brigham Young University, NASA Kennedy, Honeywell, Space Micro, and growing!
CHREC Space Processor
A Multifaceted Hybrid Architecture for Space Computing

## Slide 2: Introduction and Background
James MacKinnon

## Slide 3: Major Challenges for Space
Research focus on Advanced Space Computing
  New concepts, methods, and technologies to enable and deploy high-performance computing in space
Why is it necessary and important?
  Escalating demands for sensor-data processing
    Downlink bandwidth to Earth is extremely limited
    Sensor data rates are dramatically increasing
    Post processing is not as viable
  Escalating demands for autonomous processing & control
    Autonomy requires high-speed computing for decision-making
    Severe propagation delays for human in-the-loop for commands

## Slide 4: Space Computing Requirements
Embedded space environments have strict requirements and restrictions
  Performance (throughput and real-time)
  Size, Weight, Power, and Cost (SWAP-C)
  Reliability (device lifetime and radiation effects)
    Single-Event Effects
    Total Ionizing Dose
Next-generation satellites and spacecraft will require high-performance processing
  Traditional radiation-hardened general-purpose processors unable to keep up
    Honeywell RHPPC: .08 GOPS*
    BAE Systems RAD750: .266 GOPS*
    Zynq 7020: 324.15 GOPS*
Low Power
Low Cost
Speed
Depend-ability
Lifetime
*GOPS for 8-bit Integer Operations c/o Device Metrics

## Slide 5: Goals, Motivations, Challenges
Goals: Explore innovative strategies, architectures, and systems for hybrid space computing
Motivations: Space computers with radiation-hardened processors will be unable in some cases to meet demands of future missions
  Managing platforms with limited size, weight, power, and cost (SWaP-C) budgets while providing high performance and high reliability
  Research needed to explore hybrid methods featuring COTS processors, augmented with fault tolerance in various forms, & supported by RadHard
Challenges: Concept of hybrid space computers is relatively new and untested, requiring thorough research and analysis for deployment
  Space systems are complex, time-consuming, and arduous to develop
  Analytical research is needed to explore design approaches
  Experimental research is needed to evaluate design approaches
COTS = commercial off-the-shelf
RadHard = radiation-hardened

## Slide 6: Featured Technology
Field Programmable Gate Array (FPGA)
  Large amount of logic resources and specialized design units connected with a complex and configurable routing network
  Lower frequency and power over conventional CPU
  Massive algorithm parallelism for immense speedup
System-on-Chip (SoC)
  Integrated Circuit that combines many processing technologies into a single chip
  Xilinx Zynq 7020
    Dual ARM Cortex-A9 processors
    NEON SIMD engines
    Low-power 28nm Artix-7 FPGA
  Some applications are control-flow oriented and better suited for CPUs

## Slide 7: Flight Hardware
Jacob Stewart

## Slide 8: CHREC Space Processor (CSP)
Goal: Create a high-performance and reliable space computing platform
  Expand CSP to fulfill a variety of demands in space computing
System Overview
  Multifaceted hybrid space computer
    Hybrid system (COTS + RadHard technology)
    Hybrid processor (multicore + FPGA subsystems)
Mission Development
  Auxiliary flight hardware and test equipment
    Backplane and Power/Interface boards
  Reusable mission software
    CFS/cFE with Wumbo
  Space applications
    Image processing (enhancement and compression)
Project Leads: Jacob Stewart & Patrick Gauvin
NAND Flash
Power Circuit
Watchdog/Reset
Zynq - 7020
DDR3 SDRAM
RSA Reliable Bootstrap
ECC
FPGA Scrubbing
Project conducted in collaboration with NASA Goddard, BYU, NASA Kennedy

## Slide 9: CSPv1 Dual Format
COTS (Testing) Board (COTS+FTC)
Hybrid (Flight) Board
(COTS+RadHard+FTC)

## Slide 10: CSPv1 System Description
Reference Slide
Requires 3V3 and 5V0, other voltages generated on-board
  1.7 – 3.5 W depending on maximum load state
160-pin Samtec Searray connector (no other I/O)
  60 High-Speed FPGA I/O pins
  26 High-Speed ARM I/O pins
Watchdog circuit based around Intersil supervisor
Other information:
  50-60 grams loaded
  1U form factor (10x10 cm)
  62 mil thickness, 12-layer PCB
  2x256MB DDR3 RAM

## Slide 11: COTS+RH+FTC on CSPv1
FTC = Fault-Tolerant Computing
Variety of mechanisms
  Dual ARM A9/Neon cores
  External watchdog unit to monitor Zynq health and reset as needed
  RSA-authenticated bootstrap (primary, secondary) on NAND flash
  ECC memory controller for DDR3 within Zynq
  ADDAM middleware with message, health, and job services
  FPGA configuration scrubber with multiple modes
  Internal watchdogs within Zynq to monitor behavior
  Optional hardware, information, network, software, and time redundancy
RadHard
NAND flash
Power circuit
Reset circuit
Watchdog unit
COTS
Zynq-7020 hybrid SoC
  Dual ARM A9/Neon cores
  Artix-7 FPGA fabric + hard IP
DDR3 memory
Reference Slide

## Slide 12: Camera Link
Uses 11 LVDS pairs
  4 Data and 1 clock pair feed a SERDES core on the FPGA
    80 MHz reference clock deserializes data at a 7:1 ratio
    Max throughput of 240 MB/s
  4 are dedicated to camera control
    Used for triggering and setting exposure
    Length of control pulse determines shutter exposure time
  2 are low speed serial UART links
    Configures all other camera controls
    Examples of controls include:
      Pixel bit depth
      Analog and digital gains
      Image testing modes
      Trigger mode selection

## Slide 13: Overall Architecture
Camera
SERDES
AXI-Stream Converter
UART
Image Processing
Pipeline
VDMA
DDR3
CSP
Deserialized Data
AXI-Stream
AXI-HP

## Slide 14: Image Processing
Xilinx provided licenses for their video processing IP core library
Current cores being used:
  Bayer Interpolator
    Accepts the 12-bit per pixel filtered data and interpolates it into RGB
  Image Enhancement
    Edge detection and smoothing
    Useful for reducing noise
  Colorspace Conversion
    RGB to YCrCb
      Conversion required by other cores

## Slide 15: Flight Software
Joseph Kimbrell

## Slide 16: Software Suite
Flight Software Development (cFE)
  File upload and download capability
  Telemetry output and command ingest
  Full testbed for evaluating new commands
Applications and Interface Design
  NEON-accelerated image processing
    STAR, Jpeg Compression, Edge enhancement, 2-D Convolution, and Thumbnailer
  Image download via SpaceWire
STAR – Surface Threshold Average Rater
FPGA Fabric
FPGA Cores
Communication Interfaces
Partial Reconfiguration Region
FPGA Cores
Processing System
Wumbo GNU/Linux
Reliable Bootstrap
Kernel Modules
Core Flight Executive
Comm. Interfaces
Partial Reconfig. Controller
Hardware Accelerated Applications
Aerospace Middleware Applications
AXI-4 Bus

## Slide 17: ARM Software Reliability Assurance
Master device in system – ARM processor
  Connected to system non-volatile memory
  Configures and initializes FPGA
Critical to ensure device boots up properly
  Use Zynq’s built in RSA authentication features to verify boot images
  Redundant boot images
Caches can trigger interrupts on parity failure

## Slide 18: FPGA Software Reliability Assurance
Configuration scrubber uses readback strategy
  Continuously reads configuration data
  Compared to golden frame stored in main memory
  Overwrites configuration frame with golden frame contents if error detected
PR Support
  Scrubber paused during partial reconfiguration
    Otherwise, reconfiguration would be reverted
  Golden frame updated before resuming

## Slide 19: System Reset Methodology
CSP uses multi-level heartbeat
External heartbeat connected to internal heartbeats
  ARM (Application health information)
  FPGA hardware elements
Internal monitors attempt to reset failed elements
  External heartbeat fails if this process also fails

## Slide 20: Core Flight Executive
Integrate with NASA Goddard’s reusable flight software framework
  Open source version available at SourceForge
  Perform local device management, software messaging, & event generation
Core Components
  Core Flight Executive (cFE): Mission-independent software services
  Core Flight System (CFS): Applications and libraries running on cFE
Software Bus
cFE Core
Stored Commands
Health & Safety
Scheduler
File Manager
Other Apps
Watchdog
Camera Support
Time Sync
Image Self Check
Scrubber
PR
Error Logging
SpaceWire
cFE Core
CFS Apps
Mission Apps
Core Flight System
Notes: Supporting abstraction and utility services
  Connected via Software Bus
File Manager
  Processes ground commands
Health and Safety
  Application and event monitoring, watchdog servicing, execution counter reporting, CPU aliveness indication
Housekeeping
  Packet-driven telemetry message builder
Stored Commands Task
  Receives commands from ground
Scheduler
  Generates messages when specified

## Slide 21: NASA Missions for CSPv1
Two confirmed for NASA Goddard
  CSP featured as new technology for space computing
NASA technology mission
  STP-H5/ISEM on ISS – late 2014 delivery
  Two CSPv1 computers working in tandem
  SpaceWire, Camera Link, reconfiguration
NASA science mission
  CeREs Cubesat – early 2015 delivery to NASA
  Heliophysics experiment in LEO
  One CSPv1 computer for on-board processing
Additional missions in planning
  TechCube 1
  Escape

## Slide 22: Artist Illustrations (c/o NASA)

## Slide 23: Conclusions
Major challenges lie ahead
  Escalating app demands in harsh environment
  Tightening constraints of platform, budget, process
  Necessitates adeptly doing more with less
CHREC Space Processor
  Focus upon reconfigurable space computing
    Adaptive (performance, reliability, power) for mission needs
  Focus upon multifaceted hybrid computing
    Agile mix of COTS + RadHard + FTC; fixed & reconfigurable
  Focus upon scalable building blocks
    Address needs of small, large, & clustered spacecraft

## Slide 24: Questions and Shortfalls
Hardware
  No explicit experimentation process for hardware reliability (e.g. TID part lifetime)
  Untested in actual flight environment
Software
  Doesn’t address drawbacks of disabling FPGA scrubber during PR
    Downtime could miss errors from SEUs
    Suggestion: PR needs to be done very fast
  Could use data to validate software reliability choices

## Slide 25: Questions?