## Slide 1: Space Communications: Congestion Control Methods
joe Kimbrell
James mackinnon
Jacob stewart

## Slide 2: Paper Selection
Panigrahi, B.; Yanxiao Zhao; Sohraby, K., "Deep space autonomous network using reverse channel for congestion control," Electro/Information Technology (EIT), 2013 IEEE International Conference on, vol., no., pp.1,6, 9-11 May 2013. doi: 10.1109/EIT.2013.6632720
Ravandi, M.G.; Mortazavi, M.; Ghorshi, S., "CPM: A congestion control method for interplanetary network," Electrical and Computer Engineering (CCECE), 2014 IEEE 27th Canadian Conference on, vol., no., pp.1,5, 4-7 May 2014 doi: 10.1109/CCECE.2014.6901050

## Slide 3: Deep Space Autonomous Network
Using Reverse Channel for congestion control

## Slide 4: Communications Beyond Earth
Three major challenges faced by communication systems in deep space
  Long propagation delays between source and destination
    Range from tens of minutes to hours
      Example – Communications between Earth and Mars ranges from 8.5 to 40 minutes
    Long distance makes conventional transport protocols impractical
      ACK/NACK are inefficient
  Intermittent connectivity
    Planets’ positions vary with time
    Line of sight required for communication between nodes
  Limited buffer size on intermediate nodes
    If node buffer is full, incoming data packets are dropped
      Source node gets no feedback about packet loss
    Proposed modifications to TCP protocols difficult to implement

## Slide 5: Deep Space Autonomous Network
Communications beyond Earth form store-and-forward Deep Space Autonomous Network (DSAN)
  Integration of multiple independent networks
    Sensor arrays, space stations, colonies, etc.
Example – Sending data from Mars to Earth
  Messages collected from surface sensor network on Mars and stored in gateway
  Messages delivered to and stored in intermediate node
  Messages delivered to Earth

## Slide 6: Novel Approach
Utilize long delay channel as memory resource for congestion control
  Overflow packets transmitted back to source instead of being dropped
  Continues to send packets back and forth until destination accepts data
  Probability of packet loss significantly reduced
  Indirectly provides feedback on congestion status at destination
    Source takes measures to control packet flow if data returned
      Tells planet sensors to slow down transmission
      Stores sensor data and slows transmissions (rate control)
Simulation results verify reverse channel with rate control outperforms traditional approach
  Energy consumption
  Number of retransmissions per packet

## Slide 7: Considerations for a System Model
Two-hop DSAN system model
  Source, relay node, destination
Reverse channel proposed in addition to regular forward channel
  Destination sends packets back to source if buffer full
Source and relay nodes maintain queues
  Source queue larger than relay queue
Destination buffer may lack storage
  Connection to next destination unavailable or if incoming traffic exceeds outgoing traffic
Returned packets join incoming traffic at source to retransmit
  As opposed to dropping packets at destination
Source responds to returned packets
  Control rate of data flow to reduce congestion

## Slide 8: Assumptions for the Study
Nodes assumed static
  Planet mobility slow compared to packet transmission time
  Once line of sight between nodes established, remains for period of time
Control Case
  No ACK mechanism
    If packet dropped at destination, source unaware
  Dropping of packets at destination only due to lack of buffer space
    Assume all else is ideal
      No channel error
      Low SNR
      Made possible by using high transmission power at source

## Slide 9: No Reverse Channel
General Case in which there is only packets travelling in the forward direction
  Typically in the direction of Earth due to large amounts of sensor data being
Distance between nodes is vast and delay times long
  Prevents the use of a normal ACK/NACK protocol
  Sender is ignorant of any packet loss at receiver
  Loss severely degrades throughput
Sender transmits multiple redundant copies of a packet to ensure it arrives
  Packets are spaced to avoid overflows
  Consumes more energy per packet
  Trades efficiency and speed for fault tolerance

## Slide 10: Reverse Channel
Retransmit packets if relay node packet buffer is full
  Uses the time the packets are “in flight” as a form of storage
  Packets are bounced back and forth until they are accepted at relay
A separate connection called a downlink channel
  Operates at a separate frequency from the uplink/forward channel
Two major benefits
  Ensures a much lower rate of packet loss
  Enables the source gateway to control the flow of packets into the system

## Slide 11: Reverse Channel With Rate Control
Basic principal is the same as without rate control
Rate Control provides congestion mitigation by slowing transmit of packets
  When the relay starts to receive duplicated packets it slows transmission
  Rate at which transmission is slowed is called alpha
  Alpha is varied depending on the rate of received duplicates
Data rates reduced in two ways
  Configures the sensors to reduce capture rate
  Stores packets from sensors and releases them at a slower rate
Storing packets uses energy
  The energy used for storage is usually less then the energy used for transmission

## Slide 12: Energy Consumption
Packet transmission energy consumption usually greater than packet storing
  Deep space communication use high gain amplifiers
  Transmission amplification power usage can reach into the 10’s of watts
Storing energy requirements can become significant in deep space scenarios
  Extremely long delays lead to long buffering periods
  Storage requires power sources to be maintained
Many factors can determine storage energy
  System configurations
  Hardware specifications
  Operating system
  Memory management algorithms

## Slide 13: Energy Consumption Metrics
Energy is a vital resource on space missions
Is reverse channel congestion control worth the cost?
Two main metrics:
  Energy consumption per successful packet
    Called Ec
    Takes into consideration both cost of transmission and storage power consumption
  Average number of retransmissions per successful packet
    Called Na
    A measure of how many times a packet is retransmitted before acceptance
    Retransmissions count in both directions
Simulation is used to estimate these values

## Slide 14: Simulation Overview
Comparisons made between multiple packet management methods
  No Reverse Channel
    If the relay node buffer is full, packets are dropped
    Source node transmits K=3 redundant packets for each original packet
  Reverse Channel (with no rate control)
    If the relay node buffer is full, packets are sent back through the reverse channel; however, the source node does not slow down packet transmission speed
  Reverse Channel (with rate control)
    If the relay node buffer is full, packets are sent back through the reverse channel and the source node slows down by a factor of alpha

## Slide 15: Simulation Parameters
Base assumptions for simulations
  Two-hop model
    Source node transmits to relay node which transmits to the final destination
  Channel Characteristics
    Source – Node propagation delay of 400s
    Direct channel data rate of 100kbps
    10 KB packet sizes
  Relay Node Characteristics
    Average packet arrival time of 1s
    Queue size of 50 packets
    Packet Relay speed of
  2000 steady state observation period of the simulation
  High power () 30 GHz (Ka-Band) transmissions
    Retransmissions will not be caused by poor reception

## Slide 16: Simulation Results Number of retransmissions
Verbal Insight
  Reverse channel with rate control requires the least amount of retransmissions for this system
  Without rate control, the reverse channel is less effective at limiting retransmissions for this system
  The lack of a reverse channel requires 3 retransmissions per packet and therefore is the most costly

## Slide 17: Simulation Results Average Energy Consumed per Successful Packet – Transmission
Verbal Insight
  Reverse channel with rate control requires the least amount of energy per packet
  Without rate control, the reverse channel is less effective at limiting energy used per packet
  The lack of a reverse channel requires 3 retransmissions per packet and therefore is the most costly in terms of energy used

## Slide 18: Simulation Results Average Energy Consumed per Successful Packet – Storage
Verbal Insight
  For the low storing energy cases, reverse channel with rate control saves the most energy
  For the higher storing energy case, the lack of a reverse channel decreases the power used on storage
  No clear indication of what point is the crossover

## Slide 19: Simulation Results Average Energy Consumed per Successful Packet – Transmission
Verbal Insight
  With varying relay node data rates, the reverse channel with rate control performs the best
  At higher data rates, all of the reverse channel methods merge

## Slide 20: Simulation Results Average Energy Consumed per Successful Packet
Verbal Insight
  All reverse channel methods drop no packets
  Lacking a reverse channel, packets are dropped due to the data rate of the relay node being too low

## Slide 21: Control Packet Mechanism
Congestion control method for interplanetary network

## Slide 22: Introduction
Interplanetary network (IPN)
  Network providing communication and navigation services for spacecraft
  Difficulties arise with the distance and variability between transmissions
  Each node operates as a point to point communication node
  TCP/IP does not fit well with IPNs due to intermittent connectivity, long delays, and high bit error rates
  A new TCP is required for deep space communication networks

## Slide 23: IPN Architecture
Networks that operate independently and communicate with one another
1. IPN Backbone Network
2. IPN External Network
3. PlaNetary Network
  3a. PlaNetary Satellite Network
  3b. PlaNetary Surface Network

## Slide 24: IPN Backbone and External Networks
IPN Backbone Network
  Provides infrastructure for communications between –
    Earth-based operations
    Ground stations on planets and moons
    Satellites and relay stations
  Includes data links between elements with long-haul capabilities
IPN External Network
  Consists of groups of spacecraft between planets, sensor clusters, space stations
  Some nodes have long-haul capabilities

## Slide 25: PlaNetary Network
Comprised of PlaNetary Satellite Network and PlaNetary Surface Network
Consists of –
  Satellites orbiting planet
  Rovers and mission elements on surface
Implemented on any planet to provide interconnection and cooperation among satellites and surface elements

## Slide 26: PlaNetary Satellite Network
Satellites circling planets provide relay services
  Between Earth and planet
  Communication and navigation services to surface elements
  Some surface elements can communicate with satellites
    Receive data and commands
Includes links between orbiting satellites
Includes links between satellites and surface elements
Composed of satellites in multiple layers
Location management of PlaNetary Surface Networks

## Slide 27: PlaNetary Surface Network
Provides communication links between high power surface elements
  Rovers and landers
    Communicate with satellites
Provides power-stable wireless backbone on planet
Includes surface elements that don’t communicate with satellites directly
  Organized in clusters
  Spread out in ad hoc manner
Requires special protocol stack to meet requirements of each sub-network
  Must work with terrestrial networks to connect to terrestrial internet

## Slide 28: Control Packet Mechanism (CPM)
Reliable transfer method for IPN in backbone network
  Purely rate controlled method
  Uses a series of informational packets to determine transfer rate
Method supports connection between single sender and receiver
  Ex: ground station to space station or between relay links
  Intermediate devices are receiver of previous sender and sender for next receiver
Relay links act as store-and-forward routers
  Susceptible to packet loss and congestion
  Congestion can lead to increases in delay and packet retransmissions
CPM can help to avoid congestion problems

## Slide 29: Control Packet Mechanism (CPM)
CPM is based around a packet based transmission scheme
  Packets are transmitted together as a logical unit called a frame
  Frames also contain data that will be used to shape the connection
Handshakes are used to initialize connection
  Uses SNACKs instead of ACKs
  SNACK is a selective negative acknowledgment
    Reduces congestion in the reverse link
    Fewer SNACKs than ACKs
    Saves energy by virtue of there being fewer of them
Error rates in the link can be estimated from ratio of SNACKs to total packets

## Slide 30: Method of Operation – Phase 1
Source sends two identical handshake packets consecutively to receiver
  Duplicate packets ensure a low probability of a loss
Once the receiver gets the handshake it starts transmitting data frames
  Initially the frames are limited to 5 packets
    Small number of packets are because the link quality is unknown
  Data frames contain information about receiver
  This first burst is called the Information Packet 0 (IP0)
Source uses IP0 to calculate free buffer size
  CFBS = FBS – NIF*(Frame Size)
    CFBS – Current Free Buffer Size
    NIF – Number of Interval Frame
Total time in phase 2RTT

## Slide 31: Method of Operation – Phase 2
Starts after T > 2RTT
Each side of the transmission sends information packets in their frames
  Additional information now in these packets
    They still contain the free buffer space
    Additionally contain SNACKs
Sender and receiver keep track of packets sent in frames
  SNACKs indicate lost packets
  SNACKed packets are retransmitted
Parameter called Error Link is calculated from information packets
  This parameter is used to tune connection speed to
    Minimizes packet loss and congestion

## Slide 32: Error Link
Important parameter for adjusting network
Calculated using:
  EL = (Numbers of lost packets)/(Number of Packets in Frame)
The number of lost packets is determined by the information packet
  SNACKs correspond to lost packets
Error Link is used to calculate the size of the next frame
  Care is taken to ensure the size of the next frame is not larger than the FBS

## Slide 33: Congestion Control
Occurs when the forward and reverse links when the buffer is full in the receiving or transmitting node, respectively
  Because of the high and variable distance between transmission points knowing the congestion is very difficult
  The question becomes, “How do we detect the congestion?”
Two methods presented for congestion control
  Block out
  Frame lost and InP lost

## Slide 34: Congestion Control
Block Out
  When the error link goes above 50% it indicates that 50% of the packets must be retransmitted
  Sender stops transmitting for a set period of time
  Sender will begin transmitting once the error link goes below 50%
Frame lost and InP lost
  Sender enters a timeout period
  Begins retransmission frame if after 2RTT of the sending frame it has not received its InP
  Benefit of not wasting time before retransmitting

## Slide 35: Results - Setup
Simulation Configuration
  Discrete time simulation to represent discrete events in space communications
  Simulation based on OMNeT++4
    C++ simulation library with discrete, component-based, modular simulation capabilities
  Network Configuration
    Earth Ground station (source) transmits to earth orbiting satellite
    Deep space communication from earth orbiting satellite and Mars orbiting satellite
    Mars Ground station (sink) receives data from Mars orbiting satellite
  Scenario
    10GB of data to be transmitted from Earth Ground station to Mars ground station
    Buffer sink is equal to 10MB

## Slide 36: Results – Congestion
Verbal Insight
  A correctly sized sink buffer results in no congestions
  Higher data rates lead to more congestion
  Negative values indicate congestion as well as the packet being dropped
Overhead
  CPM does not increase any overhead because it doesn’t change the sending patterns
  The reverse link uses SNACKs instead of ACKs

## Slide 37: Shortfalls
DSAN
  Priority of retransmitted packets not discussed
  Claims alternate TCP protocols are difficult to implement without backing this up
  Simulations limited in scope
    Assumes an ideal environment – need future work with channel noise and other nonidealities
CPM
  Paper was very poorly edited, and had a large amount of grammatical mistakes
  It made several unsubstantiated claims
  Graph was missing axis labels, which made it hard to understand