## Slide 1: Reconfigurable Computing
Methods for Increasing Portability and Productivity
Joe Kimbrell
James MacKinnon
Jacob Stewart

## Slide 2: Paper Selection
Kirchgessner, R.; George, A.D.; Lam, H., “Reconfigurable computing middleware for application portability and productivity,” Application-Specific Systems, Architectures and Processors (ASAP), 2013 IEEE 24th International Conference on , vol., no., pp.211,218, 5-7 June 2013 doi: 10.1109/ASAP.2013.6567577
Vuletic, M.; Pozzi, L.; Ienne, P., “Programming transparency and portable hardware interfacing: towards general-purpose reconfigurable computing,” Application-Specific Systems, Architectures and Processors, 2004. Proceedings. 15th IEEE International Conference on , vol., no., pp. 339,351, 27-29 Sept. 2004 doi: 10.1109/ASAP.2004.1342483

## Slide 3: Reconfigurable Computing
Middleware for Application Portability and Productivity

## Slide 4: Introduction
Advantages of reconfigurable devices
  Flexibility for application specific tasks
    High performance, low power
Difficulties of using reconfigurable devices
  Lack of standardization between platforms
    Difficult to port code
    Vendor specific cores

## Slide 5: Possible Solution - HLS
High-level synthesis (HLS)
  Reduce the difficulties of FPGA development
  Encounter the same lack of portability
    HLS tool must support various platforms
      Impulse-C: per-platform support packages
      ROCCC: per-platform application cores
  FPGA device development outpaces tool development
  HLS tools must make assumptions which decreases efficiency of generated core

## Slide 6: RC Middleware (RCMW)
Designed to enable more portability
  User specifies required resources and interfaces via XML at design time
    Including number, type, size, and data types of each resource
  RC Middleware toolset creates a portable hardware and software interface
  Portability is no longer a concern as the interface can be generated for many different devices

## Slide 7: Related Work
RCMW is a complementary technology to other FPGA abstraction methods
  Intermediate Fabrics – coarse grained logic blocks that increase FPGA compile times
  FPGA-on-FPGA overlays – provides compatibility between devices without requiring bitfile recompilation
  OpenCL and Liquid Metal (Lime)
    High-level programming models focusing on improving portability

## Slide 8: Approach
RCMW composed of three layers
  Translation Layer
    Converts platform-specific resource interfaces to a standardized RCMW interface
  Presentation Layer
    Uses the RCMW interface to provide user specified resource requirements
  Application Layer
    Final interfaces allow user to develop application without platform dependencies

## Slide 9: Translation Layer (HW)
Converts vendor-specified physical interfaces to an RCMW-standardized interface format
  Including interfaces for inter-FPGA communication, memories, and host communication
RCMW-standardized interface can then be integrated further in the Presentation layer
Exposes FPGA block RAM on the device
  Allows for the user to implement lower-latency OCM

## Slide 10: Presentation Layer (HW)
Converts standardized physical resources into resources usable by the application
  Consulting the RCMW IP database
    Contains components for arbitration, interface conversion and controllers, and multiplexing
Variable number of interfaces can be provided in FIFO or burst mode
Configured via XML framework
  Interfaces, pin assignments, and timing constraints

## Slide 11: Presentation Layer (HW) Resource Arbitration
Resource Arbitration allows for multiple interfaces to map to a single physical interface
  Bandwidth to support multiple interfaces
  Coordinated via arbitration controller
    Ready-to-send (RTS) and clear-to-send (CTS) signals
RTS signal
  Asserted when a configurable number of bytes remains in the buffer, indicating the controller is ready to access memory
CTS signal
  Asserted when the interface takes control of the physical memory bus
  De-asserted when the interface gives up control of the physical memory bus

## Slide 12: Application Layer (HW)
Provides application-specific hardware interfaces required by the user
Interface provided in the form of a top-level entity
No knowledge required of underlying hardware

## Slide 13: Software Abstraction Implementation

## Slide 14: Software Abstraction
Provides object-oriented API based on C++11
  C++11 used for improved threading and memory management
  Standardized register and memory interfaces

## Slide 15: Translation Layer (SW)
Standardized interface exposed through Board class
Each platform has subclass in board to implement –
  Blocking reads/writes
  Non-blocking reads/writes
  Board enumeration
  Bitfile initialization
Memory and FPGA objects inside board represent physical components on platform
Implemented using vendor-specific API or RCMW-specific driver interface

## Slide 16: Presentation Layer (SW)
Generated as subclass of RCMW application class
Application class encapsulates instances of resource interface objects requested in the XML specification
At runtime –
  Loads bitfile
  Initializes memory interfaces (calls bind)
  Runs user code (calls execute)
Resources automatically released at end of execution

## Slide 17: Application Layer (SW)
Implemented by application class
Only need to build app in execute stub
Improves productivity
  Thread-safe timing library

## Slide 18: RC Middleware Toolset
Handles generating presentation layer
  Maps application resources onto platform resources
Three-step generation
  Parsing XML description
  Mapping application to platform resources
  Generates HDL/C++ for interfaces
    Structural HDL generated for hardware instances
    Application class software created in C++
    Makefile also generated to ease compilation

## Slide 19: RC Middleware Tool Flow

## Slide 20: Mapping
Most complex step in presentation layer generation
  Determines locations of memory and FIFO resources
Mappings vary greatly between target platforms
Iterates through all application to physical mappings
  Evaluates with cost function
    Lowest cost mapping gets used
    Cost function based on number of IP instances and metadata information
  Metadata about interfaces used to help evaluate cost
    Maximum operating frequency
    Device resource utilization reports

## Slide 21: Experimental Results

## Slide 22: Experimental Setup
Three different platforms were used for testing
  GiDEL PROCStar III
    Altera Stratix III FPGA
    4 GB DDR2 and 256 MB SDRAM per FPGA
  GiDEL PROCStar IV
    Altera Stratix IV FPGA
    8 GB DDR2 and 512 MB SDRAM per FPGA
  Pico Computing M501
    Xilinx Virtex-6
    512 MB DDR3 per FPGA

## Slide 23: Experimental Setup
Software used:
  Quartus II v11.1 for Altera bitfile generation
    Used GiDEL drivers for PROCStar board tests
  Xilinx ISE 14.1 for Xilinx bitfile generation
    Used with Pico boards
  GCC with C++11 support using –O3 optimizations
    Used for compiling the RCMW’s software API

## Slide 24: Performance Analysis
Native and RCMW implementations compared
Performance overhead was analyzed in two ways
  Read and Write performance
    Measured by timing memory transfers from the host and FPGA
    Tested with a variety of data sizes
  Area overhead
    Measured using post-fit component device utilization summary generated by Quartus and ISE

## Slide 25: Performance Analysis
Greatest overhead occurred between the host and external memory
  PROCStar III was the worst at 80% overhead
    Overhead was caused by RCMW’s additional features
    Thread-safety mainly to blame
  M501 has thread-safety built in
    Performs better than both other boards
Transfer size had large effect on overhead
  Overhead approaches zero for large transfer sizes
Overhead increased transfer time by microseconds

## Slide 27: Area Analysis
Area split up into three categories
  RCMW
    Logic overhead of middleware components
  Application
    Area usage dedicated to implementing benchmark
  Vendor IP
    Consists of vendor supplied IP such as memory controllers, FPGA to host interface (PCIe), PLLs, etc
RCMW typically took less than 1% of total fabric area
  This can vary depending on the number of interfaces

## Slide 29: Productivity Analysis
Split into three metrics
  Software lines of code (SLoC)
  Hardware lines of code (HLoC)
  Total development time
Each benchmark was ported to the hardware platform from existing OpenCores IP
  Same developer worked on all the benchmarks
  This ensured number of lines of code stayed consistent

## Slide 30: Productivity Analysis
RCMW required much less development than native
GiDEL (Altera)
  65% less SLoC
  41% less HLoC
  53% less development time
Pico (Xilinx)
  66% less SLoC
  59% less HLoC
  69% less development time

## Slide 31: Portability Analysis
RCMW makes it possible to easily port projects between diverse hardware platforms
RCMW toolset executed only once per platform
Architectural differences did affect performance
  Benchmarks requiring more memory interfaces like image segmentation ran better on GiDEL hardware
  Pico hardware supported a newer PCIe standard which increased the speed of the host-FPGA connection

## Slide 32: Overall Performance

## Slide 33: Conclusions
Drastically decreased the amount of time/coding required for the development
Increased the portability of FPGA apps between hardware platforms
Allows developer to code from an application centric viewpoint and not worry about low level hardware

## Slide 34: Future Work
Larger case study to fully evaluate RCMW productivity
  Variety of developers and applications needed to fully flesh out the effectiveness of the middleware
Vendor specific IP cores hurt portability
  Work is needed to be able to enable interoperability of vendor cores like memory and interface controllers

## Slide 35: Programming Transparency and Portable Hardware Interfacing
Towards General-Purpose Reconfigurable Computing

## Slide 36: Introduction
Two main types of computation
  Temporal computation
    Computation running on general processors
    Most common
  Spatial computation
    Computation in specifically-designed hardware for a particular application
    Application specific

## Slide 37: FPGA Pros and Cons
Pros
  FPGAs provide flexibility for spatial tasks without developing ASICs
    ASICs even more expensive, not reprogrammable
  Allow for design growth of unit through re-programmability
Cons
  Higher unit cost for FPGAs compared to processors
    Reduces large-scale production abilities
  Slower clock speed than processors and ASICs

## Slide 38: Reconfigurable System-on-Chip
Lack of unified programming methodology
  Increases difficulty of software development
No standardized interfaces for hardware accelerators
  Makes portability difficult
Must be easier to program and more portable
  Make RC systems better for general-purpose computing

## Slide 39: Microprocessors vs RC Devices
Microprocessors
  Easily programmed and run on abstraction layers
    OS, libraries, virtual machines
    Hide platform specific details
RC devices
  Software and hardware need to be written and interfaced
  Exposed platform-dependent communication details to programmer
    Difficult to manage
    Less portable

## Slide 40: Goal
New programming paradigm for RC devices
  Decoupled from underlying platform
    App-level programmers don’t have information about hardware
    Hardware designers not exposed to interfacing details
      Don’t know where data to be processed is located
  Underlying architecture provides abstraction layer to fit between hardware and software design
    Supports programming model
    Abstraction layer provides transparency and uses standard interfacing between software and hardware

## Slide 41: Transparent Programming Model
Application Programmers
  Code high-level concepts without knowledge of underlying platform
    Could be sequential or parallel code
  Authors considered parallel multithreaded model
    Shared memory paradigm

## Slide 42: Multithreaded Programming Model
Co-routine execution – First approach to multithreading without system-level support
Common multithreading supported by abstraction layer
  Ignores existence of hardware threads
Extended multithreading supports seamless integration of hardware threads
  Programming transparent
  Interfacing portable

## Slide 43: Extended Abstraction
Multithreaded apps achieved through coroutine execution
Abstraction layer of libraries/OS support currently used for thread management
  Doesn’t cover possibility for hardware threads
  Non-standardized communication and interfacing
    Bad for hardware accelerators
  Solution – Extend thread abstraction layer
    Provide support for standard integration of hardware threads
    Threads communicate over standardized interfaces
    Normal abstraction layer still in place

## Slide 44: Designing Portable Software Architectures

## Slide 45: Software Threads
Underlying Goal: Portability
General Guidelines
  Software thread should interface with virtualization layer and not hardware accelerators directly

## Slide 46: Hardware Threads
Underlying Goal: Portability
General Guidelines
  Hardware thread should interface with virtualization layer and not main memory directly
Interconnect accessible via communication assistants

## Slide 47: Architectural Effects
Portable code that abstracts the underlying hardware from the application designer
Paper explicitly does not address resource management, just portability

## Slide 48: Software – Hardware Interaction
Software initiates execution and passes parameters through virtualization layer to hardware accelerator
Hardware Accelerator accesses memory and synchronizes with other system components through communication assistant
Address translations and memory copies go through virtualization layer
Acceleration core passes result back, control is returned to the software thread

## Slide 49: Software – Hardware Interaction

## Slide 50: Virtualization Layer - Outsides
Software Threads
  Abstracted via thread libraries and system software
  Designed by application developers to accomplish task
Hardware Threads
  Abstracted via Communication Assistants
    Perform address translation and network interfacing
  Designed to accelerate software tasks

## Slide 51: Virtualization Layer - Insides
Inner abstraction to coordinate thread libraries with communication assistants
Perform memory translations between software threads, hardware accelerators and local/central memory
Perform additional processing, prefetching, or other advanced data management techniques

## Slide 52: Advanced Techniques

## Slide 53: Dynamic Optimizations
Multiple layers of abstractions decreases efficiency
Virtualization layer can be used for optimization
  Layer could detect memory access patterns
  Use this information to perform prefetching
  Hides communication latency
Can be used for detecting sequential data accesses
  E.g. Supplying data in advance for a Vector Addition

## Slide 54: Automated Synthesis
High level language concepts hard to map to hardware
Pointers complicate hardware synthesis
  Virtualization layer allows generation of memory addresses as they are
Recursion handled by hardware thread calling itself
  Virtualization layer decides dynamically what to do
    If accelerator supports recursion then it runs as is
    If not then the layer will call a software equivalent of the hardware thread

## Slide 55: Flexible Software Migration
Allows runtime software to hardware migration
Can add abstraction layers such as JVM
Conserves “compile-once-run-anywhere” principle

## Slide 56: Real Implementation

## Slide 57: Programming
Virtualization layer simplified using sequential execution model
  Eliminates memory consistency problems
Layer implemented as Virtual Memory Window (VMW)
  Main function initializes data and passes virtual pointers to hardware accelerator
  Utilizes standardized OS services to call accelerator
  Switches back to software after hardware execution
  Obscures all communication details

## Slide 58: Architecture
Software runs on ARM processor
Accesses memory through AMBA bus
Hardware accelerator core instantiated into FPGA and accessed via Window Management Unit (WMA)
WMU
  Acts as communication assistant for hardware core
  Translates virtual addresses to physical addresses

## Slide 59: Results
Ran multimedia benchmark ADPCM Decode
  Measured execution time
    Pure software
    Typical coprocessor (Directly programmed from user app)
    VMW-based version of coprocessor
Significant improvement with the VMW version
  Typical coprocessor achieved 20x speedup
  VMW-based version
    w/o prefetching 15x speedup
    w/ prefetching 23x speedup

## Slide 60: Results
Manage Time – Time required manage WMU
Copy Time – Time required to copy pages to/from main memory
Sleep Time – Time while VMW manager sleeps waiting for WMU

## Slide 61: Conclusion
Authors address problems that plague every RC system
  Lack of standardization for programming
  Lack of standardization for hardware designing
Brings RC closer to general purpose computing needs
  Model suppresses difference between software and hardware from the viewpoint of the programmer
  Virtualization layer abstracts platform details
Despite overhead virtualization layer can be a big benefit
  Overhead actually can be leveraged to optimize on the fly
Presented case study of a real reconfigurable system

## Slide 62: Shortfalls
Middleware
  Case study was limited to one developer
  Only mentions the problems with Vendor IP even though this is a huge problem for portability
Portability
  Only tested on one kernel so ADPCM Decode might be an outlier
  Paper spent a lot of time explaining basic programming concepts

## Slide 63: Questions?