## Slide 1: On-Chip Control Flow Integrity Check for Real Time Embedded Systems
Fardin Abdi Tahi Abad, Joel Van Der Woude, Yi Lu, Stanley Bak Marco Caccamo, Lui Sha, Renato Mancuso, Sibin Mohan
2013 IEEE 1st International Conference on Cyber-Physical Systems, Networks, and Applications (CPSNA)
Presented by
Aishwarya Dhandapani
Taru Doodi

## Slide 2: Setting the Scene… (1/2)
Why real-time systems are more vulnerable?
  Susceptible to attacks over the internet/network
  Life-critical and safety-critical applications run on these systems
How are they vulnerable?
  Buffer Overflow
  Code Injection
  Return-into-libc
  Return-oriented-programming
Characteristics of a good security system
  Minimum predictable overhead
  Minimum hardware complexity

## Slide 3: Setting the Scene… (2/2)
Attack model considered
  Attacker has networked access to the system
  Physical attacks/tampering NOT considered
Other Prerequisites
  Safe and trusted initialization of the system
  Network connection is established after bootstrap sequence is complete

## Slide 4: System Architecture
On-chip Control Flow Monitoring Module (OCFMM) is placed on the same chip as the processor
It is isolated from the rest of the system
OCFMM has direct access to the Program Counter (PC) and Instruction Register (IR)
Accessing the PC and the IR does not require additional instructions to be executed on the processor

## Slide 5: How does it work?
Defining Code Blocks
Control Flow Graph Extraction
Error Detection

## Slide 6: Defining Code Blocks
Scan the entire binary executable to identify code blocks
  Code block is a basic unit of control flow
  Longest sequence of instructions contained between two control flow statements
Assign an unique Block ID to each code block
  Conditional Branches : ‘Yes’ block and ‘No’ block identified and destination addresses stored
  Unconditional Jumps : destination address is stored
  Hardware stack used to push and pop destination addresses
Depth First Search starting at the main function is used to generate CFG

## Slide 7
How does it work?
Defining Code Blocks
Control Flow Graph Extraction
Error Detection

## Slide 8
Control Flow Graph Extraction

## Slide 9
How does it work?
Defining Code Blocks
Control Flow Graph Extraction
Error Detection

## Slide 10
Error Detection
Program flow is compared to the CFG
When the execution begins, the block ID of the block containing the main function is fetched. Subsequent blocks follow
CFG profiles for next blocks are fetched while the current block is being executed in the processor. This minimizes overheads
The module ensures that the execution remains within the CFG profiles of that block.
An error flag is raised when a deviation is detected
Appropriate action can be taken by the system/administrator in case of an error
Stack module implemented in hardware is used to handle unconditional jumps

## Slide 11: Predictable Overhead
The CFG is generated only once, before the system is initialized for the first time. This is a non-recurring cost
When a block is very small, the time taken to load the block information is longer than the execution time of the block itself and hence will cause the execution to be halted
However, each block has a predictable upper bound on the halting time. This helps the system designer reconsider task execution times
    Where, ei is the minimum execution time of the ith instruction in the block
    m is the access time of OCFMM memory
    nk is the number of instructions in the kth block

## Slide 12: Experiments and Evaluation
The embedded processor was implemented on a Xilinx Virtex-5 LXT FPGA.
The control module was implemented on the FPGA fabric through a LEON3 soft core processor
  LEON3 is a 32-bit synthesizable version of SPARC v8 processor
The OCFMM did not dedicated have external memory which restricted the size of the CFG and hence the embedded application
Two tests were performed
  Modified binary with a PID temperature controller
  Overwriting return address from stack
Both tests proved successful. Error flag was raised when the CFG did not match with the executing binary

## Slide 13: Future Work
Implementing a dedicated external memory to the OCFMM.
Implementing CFG profile caching mechanism to mitigate profile fetching overhead for smaller blocks
Although the overhead is predictable, the implementation is incomplete and hence would require a comprehensive overhead measurement method
More research is required to prevent state variables from being over written due to buffer overflow
Protection against data errors has not been addressed

## Slide 14: Conclusion
The proposed on-chip control flow monitoring module enforces control flow integrity in real-time embedded systems
It is suitable for simple embedded systems that have strict timing requirements
The proposed solution can be extended to complex embedded systems with an external memory unit
This technique does not require any changes to the existing code thereby allowing to be compatible with legacy code
This technique was able to detect and protect against return-into-libc, return-oriented-programming and code injection.

## Slide 15: Questions?