## Slide 1: Schedule-Aware and Compression-Aware Dynamic Cache Reconfiguration in Real Time Embedded Systems
Shreya sriperumbuduri
Siddharth ambadasu
Jayalakshmi muthiah

## Slide 2: Introduction
Design and Optimization in Real time systems
  Energy Constrained – Battery operated
  Time Constrained
    Hard task deadlines
      – Tasks must complete execution by their deadlines in order to ensure correct system behavior
      – Example: Safety-critical systems
    Soft task deadlines
      – These systems remain effective even if their deadlines are not guaranteed to be met.
      – Minor deadline misses may lead to temporary service or quality degradation, but will not lead to incorrect behavior
      – Example: Gaming, multimedia, housekeeping devices
  Some common Optimization techniques in Real time systems
  Processor idle time (slack time) – uses Dynamic Power Management (DPM) techniques to put the system to sleep when idle.
  Dynamic Voltage Scaling (DVS) methods – reduce the clock frequency such that tasks execute slowly without violating their deadlines
  Dynamic Reconfiguration of the cache hierarchy

## Slide 3
Dynamic cache reconfigurations
    Promising for improving energy and performance
    Hard to implement in real-time systems
    Dynamic computation is expensive
    Dynamic reconfiguration leads to timing uncertainty
Propose a scheduling-aware dynamic cache reconfiguration technique to generate significant energy savings in soft real-time systems by exploiting static analysis during runtime.
Dynamic Cache Reconfiguration

## Slide 4
Real Time Scheduling Techniques
Commonly used scheduling techniques
    Earliest Deadline First (EDF) scheduling
      Dynamic scheduling algorithm
      Places processes in a priority queue
      Whenever a scheduling occurs, queue will be searched for the process closest to its deadline – this process is next to be scheduled for execution
    Rate Monotonic (RM) scheduling
      Static scheduling algorithm
      Priorities are assigned on the basis of cycle of duration of the job – the shorter the cycle duration is, higher the job’s priority

## Slide 5
Cache in Real Time Systems
  Challenges of using caches in Real Time Systems
    Difficulties due to the unpredictability imposed on the system
    Scheduling algorithms have difficultly calculating WCET for tasks
  Techniques to overcome the scheduling difficulties
    WCET analysis - a static, design time analysis of tasks in the presence of caches to predict cache impact on task execution times
    Cache locking - useful cache lines are “locked” in the cache when a task is preempted so that these blocks will not be evicted to accommodate the new incoming task
    Cache partitioning - cache is partitioned into reserved regions, each of which can only cache data associated with a dedicated task
    Cache-related preemption delay analysis - tight delay estimation so that prediction accuracy is higher than in traditional WCET analysis.

## Slide 6
Reconfigurable Cache Architectures
  Reconfigurable cache architecture – as proposed by Zhang et al
    imposes no overhead to the critical path
    the cache tuner consists of small custom hardware or a lightweight process running on a coprocessor, which can alter the cache configuration via hardware or software configuration registers
    four separate banks, each of which acts as a separate way
    Way concatenation - logically concatenates ways - enables configurable associativity
    Way shutdown - shuts down ways to vary cache size
    Configurable line size, or block size - setting a unit-length base line size and then fetching subsequent lines if the line size increases

## Slide 7
Determining Best Cache Configuration
  Dynamic Analysis - cache configurations are evaluated in system during runtime
    Limitation - imposes unpredictable performance or significant energy overhead
  Static Analysis - non-intrusive – most appropriate for real-time systems
    Application-based tuning - alternatives are explored and the best cache configuration is selected for each application in its entirety
    Phase-based tuning - best cache configuration is selected for each phase of execution within an application
    Best cache configuration may be stored in a look-up table or encoded into specialized instructions
  Previous methods focus solely on energy savings and not deadlines, which are imperative in real-time systems.

## Slide 8
Reconfigurable Cache Architecture - Overview
  An efficient and near optimal strategy for cache tuning based on static program profiling for both statically and dynamically scheduled real-time systems
  statically executes, profiles, and analyzes each task intended to run in the system
  Information obtained in the profiling process - utilized to make reconfiguration decisions dynamically
  Example:
    Assume a system with two tasks, T1 and T2.
    Traditionally, the system will use a base cache configuration – Cachebase

## Slide 9
Overview (Contd..)
  Each task into 2 phases – Each phase of each task has a different optimal cache configurations
  Phase1 - starts from the beginning to the end
  Phase2 - starts from the half position of the dynamic instruction flow (midpoint) to the end
    Cache1T1,Cache2T1,Cache1T2,Cache2T2 - represent the optimal cache configurations for phase1 and phase2 of task T1 and task T2, respectively

## Slide 10
Overview (Contd..)
    T2 arrives (at time P1) and preempts T1
    Traditional Approach - the system executes using Cachebase exclusively
    With Reconfigurable Cache
      the first part of T1 executes using Cache1T1
      Cache1T2 is used for execution of T2
      When T1 resumes at time point P2, the cache is tuned to Cache2T1 - since the actual preemption point is closer to the midpoint compared to the starting point
      Note: the actual preemption point of T1 is not exactly at the same place where we pre-computed the optimal cache configuration (midpoint).
Reduces energy consumption up to 74% without introducing any performance
penalty

## Slide 11
Phase-based Optimal Cache Selection
    A task is divided by n potential preemption points (0, P1, P2 … Pn-1)
    A phase is the period of time between a predefined potential preemption point and task completion - also called partition points
    Each phase has its optimal cache configuration (C1, C2 … Cn) - Performance-optimal and energy-optimal
    A static profile table is generated for each task

## Slide 12
  Potential preemption points may not be the same as actual preemption points
    They are used for cache configuration selection.
  Partition granularity - the number of dynamic instructions between partition points - determined by dividing the total number of dynamically executed instructions by the partition factor
  Partition factor determines the potential preemption points and resulting phases
    Large partition (finer granularities) factor leads to large look-up table
    Not feasible due to area constraints
    Large partition factor may not save more energy
    Partition factor around 4 to 7 is profitable
  A static profile table is generated for each task - stores the potential preemption points and the corresponding optimal cache configurations for each task
Phase-based Optimal Cache Selection

## Slide 13
Scheduling-Aware Cache Reconfiguration
    Statically scheduled systems
    Arrival times, execution times, and deadlines are known a priori for each task
    Statically profile energy-optimal configurations for every execution period of each task without violating any task deadlines
    Dynamically scheduled systems
    Task preemption points are unknown
    New tasks can enter the system at any time
    Conservative approach
    Aggressive approach

## Slide 14
Conservative Approach
    Energy-optimal cache configuration with equal or higher performance than base cache
    Nearest-neighbor
    Use the nearest partition point to decide which cache configuration to tune to
    Static Profile table (a)
    (EOi(n/p)) represents deadline-aware energy-optimal configuration for partition phase n/p in task i.
    n/p – nth phase in a set of p phases
    TIN - total dynamic instruction count executed in a single run of that task.
    Task list entry (b)
    Runtime information – Arrival time (Ai), Deadline (Di) and remaining number of dynamic instructions (RIN)
    Information used by both the scheduler and the tuner
  When a newly arrived task begins execution, the deadline-aware energy-optimal cache configuration (EOi(0/p)) is obtained from the task list entry, and the cache tuner adjusts the cache appropriately.

## Slide 15
Aggressive Approach
    Energy-optimal cache configuration & Performance-optimal cache configuration
    Includes their execution time as well.
    Ready task list (RTL) – in addition to task list
    Contains all the tasks currently in the system
    Static Profile table (a)
    Energy - optimal configuration
    Performance -optimal configuration
    Approximate execution time for each configuration
    Task list entry (b)
    Runtime information – Current Phase indicator (CPi)
EO, EOT, PO, and POT stand for the energy-optimal cache configuration, the energy-optimal cache configuration’s execution time, the performance-optimal cache configuration, and the performance-optimal cache configuration’s execution time, respectively.

## Slide 16
Aggressive Approach
    When task T is the only task in the system
    Always tune to energy-optimal cache if possible
    When task T preempts another task
    Run schedulability check
    Discard the lowest priority task if absolutely necessary
    Tune to energy-optimal cache
    If all other tasks in RTL can meet their deadlines using their performance-optimal caches
    When task T is preempted by another task
    Calculate and store runtime information (RIN, CP)

## Slide 17
Experimental Setup
    SimpleScalar to obtain simulation statistics
    Used external I/O (eio) trace file, checkpointing and fast forwarding to generate static profile table
    Energy model
    Calculates both dynamic and static energy consumption, memory latency, CPU stall energy, and main memory fetch energy.
    Dynamic energy consumption was updated for each cache configuration using CACTI 4.2
    Benchmarks – EEMBC and MediaBench
    Reconfigurable cache Configuration - four-bank cache of base size 4 KB, which offers sizes of 1 KB, 2 KB, and 4 KB, line sizes ranging from 16 bytes to 64 bytes, and associativity of 1-way, 2-way, and 4-way.
    Base cache configuration - a 4 KB, 2-way set associative cache with a 32-byte line size

## Slide 18
Energy Savings (Instruction Cache)
28% average energy savings using conservative approach
51% average energy saving using aggressive approach

## Slide 19
Energy Savings (Data Cache)
17% average energy savings using conservative approach
22% average energy saving using aggressive approach

## Slide 20
Hardware Overhead
    Profile Table stores 18 cache configurations
    Synthesized using Synopsys Design Compiler
    Assumed lookup frequency of one million nanoseconds
    Table lookup every 500K cycles using 500 MHz CPU
    Average energy penalty is 450 nJ
    Less than 0.02% of overall savings (2825563 nJ)

## Slide 21: Compression Aware Dynamic Cache Reconfiguration (CACR)

## Slide 22
Code Compression in Embedded Systems
    Major Design Constraints in Embedded Systems: Memory and time
      Cost & size of the system
      Power Consumption
    DCR may increase the execution time – not desirable in real time systems
      Code compression with cache reconfiguration resolves timing constraints by effectively shrinking the program size – fits critical portion of application into a smaller cache

## Slide 23
Code Compression Techniques
    Traditional Dictionary Based Code Compression
    Hamming Distance Base Code Compression
    Our Approach : Bitmask Based Code Compression
      Compression Algorithm
      Decompression Mechanism

## Slide 24
Traditional Code Compression Methodology

## Slide 25
Compression Ratio
Compression Ratio
Smaller compression ratio is better
Compression Ratio = Compression Program Size
Original Program Size

## Slide 26
Compression Techniques
    Dictionary-based approach
      Good Compression Ratio
      Fast decompression Scheme
    Hamming Distance Approach
      Limited: profitable only upto 3 bitmasks
    Our approach
      Use bitmasks to maximize matching patterns
      Improve compression ratio even further

## Slide 27
    Original Code Size – 80 bits
    Compressed Code Size – 62 bits
    Dictionary Size – 16 bits
    Compression ratio – (62+16)/80 = 97.5%
Traditional Dictionary Based Code Compression

## Slide 28
Hamming Distance Compression
    Improved Dictionary-based approach
    Compression ratio depends on number of bit changes during compression
    Compression ratio – 95%
Encoding scheme for incorporating mismatches

## Slide 29
Bit-mask based code Compression
    Increased matching patterns
    Data compressed using bitmask requires 8 bits
    Compression ratio – 80%
    Challenges: Bitmask selection and dictionary selection
    The mapping of old addresses (in the original uncompressed code) to new addresses (in the compressed code) is kept in a jump table.
Example of a compressed word

## Slide 30
Compression Aware DCR - Algorithm

## Slide 31
Performance – Energy Consumption Trade-off
– Anagram Benchmark
Pareto optimal alternatives are connected using dashed lines

## Slide 32
Placement of Decompression Unit
    Pre-cache placement – memory contains compressed code – instructions are stored in cache in uncompressed form
      Has little effect on energy and performance of cache
    Post – cache placement - the decompression unit is placed between cache and processor thus both memory and cache contain compressed instructions.
      The best choice to achieve maximum performance as well as minimum energy consumption.
      However, post-cache placement can introduce significant performance overhead to the system.

## Slide 33
The impact of pre-cache placement of decompression
engine on cache energy – djpeg benchmark

## Slide 34
Experimental Setup
    Benchmarks
      jpeg, djpeg, epic, adpcm (rawcaudio and rawdaudio), g.721 (encode, decode) benchmarks from the MediaBench
      dijkstra, patricia, crc32, bitcnts from MiBench
    Code Compression Techniques - bitmask-based, dictionary-based and Huffman code compression
    Dictionaries of sizes - 1 KB, 2KB, 4KB, and 8 KB.
    Three mask sets - one 2- bit sliding, 1-bit sliding and 2-bit fixed, and 1-bit sliding and 2-bit fixed masks.
    Dictionary-based and Huffman compression - 0.5 KB, 1KB, 2KB, 4KB, and 8 KB dictionary sizes with 8 bits, 16 bits and 32 bits word sizes were used
    Best choice – dictionary size of 2 KB and word size of 16 bits.
    Code compression is performed offline
    ECOFF (Extended Common Object File Format) header files provided in SimpleScalar toolset - compressed code back into binary files so that they can be loaded into the simulator.
    Cache configurations same as in DCR

## Slide 35
Performance-Energy consumption tradeoff for compressed and uncompressed codes using rawcaudio (adpcm-enc) benchmark

## Slide 36
Energy Savings
    Instruction cache subsystem – 10% - 76% with an average of 52% - utilizing only DCR
    BMC + DCR – energy savings upto 48% on top of 10% - 76% obtained only by DCR – without performance degradation
    Our Approach – average 65% energy savings

## Slide 37
Performance Improvements
    DCR alone – 11% performance loss on average
    BMC + DCR – 75% performance improvement (g721_enc)

## Slide 38
Conclusion
    Dynamic cache reconfiguration is a promising approach to improve both energy consumption and overall performance.
    65% reduction on average in overall energy consumption of the cache subsystem as well as up to 75% performance improvement in embedded systems when code compression is integrated with DCR.
    FUTURE WORK
      Hard real-time systems
      Multi-core and multi-processor systems
      Optimal mask and dictionary selection techniques
    Gaps in the paper
      How partition factor is determined during static profiling?
      Working of the decompression unit is not explained