## Slide 1: FPGA Glitch Power Analysis and Reduction
Vibhav Kundalia Niharika Chatla
UFID – 31561935 UFID - 90431959

## Slide 2: FPGA – Field Programmable Gate Arrays
Used for Implementing Digital Systems
  Pros
    Flexible
    Low time-to-market
  Cons
    Power Consumption (upto 10x more power than equivalent ASIC design)

## Slide 3: FPGA Architecture
Island-style architecture
  Logic blocks connected through programmable routing network
Look-up-tables (inside logic blocks)
  L-input LUT can implement k variable logic functions and requires 2^k configuration bits
  Hardware implementation of truth table

## Slide 4: Power in FPGAs
Static Power
  Current leakage in transistors
Dynamic Power
  Signal transition for 0 to 1 or 1 to 0
    Functional transition
      Necessary for correct operation of circuit
    Glitch
      Transitions that arise from unbalanced delays to the inputs of a logic gate
      Doesn’t affect the functionality of a synchronous circuit but has significant effect on power
      4-73% of total dynamic power, average 22.6%

## Slide 5: Glitch Example

## Slide 6: Glitch Reduction in FPGAs
Algorithms that attempt to balance delays
  Technology mapping stage
    Mapping based on glitch-aware switching activities
  Routing stage
    Faster arriving inputs delayed by extending path
  Architectural level
    Programmable delay elements
  All incur area or performance overhead
Flip-flop insertion/pipelining
  Break up deep combinational logic paths into stages of pipeline
  Fewer logic levels reduces opportunity for imbalanced delays
Hazard-free logic synthesis techniques
  Change don’t-care values to reduce glitches

## Slide 7: Dynamic Power of FPGA
Terms
  n : number of nets in circuit
  Si : switching activity of net i
  Ci : capacitance of net i
  f : frequency of circuit
  Vdd : supply voltage
The glitch reduction algorithm aims to lower the switching activity as a means of reducing dynamic power

## Slide 8: Proposed Solution
Glitch reduction algorithm based on don’t-cares
  Selects don’t-care output values of LUTs in such a way that reduces glitches
  Performed after placement and routing
  Uses timing simulation data for guidance
  No area or performance overhead
  Inspired by hazard-free logic synthesis techniques for asynchronous circuits

## Slide 9: Don’t-cares in Logic Circuits
Entries in truth table where output can be set as either logic-0 or logic-1 without affecting correctness of circuit
Two categories
  Satisfiability don’t-cares (SDCs)
    Particular input pattern can never occur on inputs
  Observability don’t-cares (ODCs)
    Output cannot propagate to circuit’s primary outputs

## Slide 10: Don’t-care Analysis
ABC logic synthesis network
  Developed at UC Berkeley
  Boolean satisfiability (SAT)-based complete don’t-care analysis that determines don’t-care minterms
  Utilizes miter circuit to find don’t-cares
    If C(x) = 0, y is don’t care minterm of LUT f

## Slide 11: Glitch Power Analysis
Examined amount of glitch power dissipated by 20 MCNC benchmark designs
Experimental setup
  Altera Quartus 10.1
  65nm Stratix III devices
ModelSim 6.3e used for functional and timing simulation using 5000 random input vectors
Dynamic power computed using Quartus PowerPlay
Glitch power
  dynamic power(timing simulation) – dynamic power (functional simulation)

## Slide 12: Glitch Power Analysis
Percentage of dynamic power from glitches
  Range: 5.8-45.4%
  Average : 26.0%
Percentage of LUT input states that are don’t-cares
  Range: 0.8-37.2%
  Average: 15.1%

## Slide 13: Glitch Reduction Algorithm
Inputs
      Placed and Routed Netlist
      Value change dump file(VCD)
The algorithm iterates through each LUT in the netlist from shallower to deeper ones.
For each LUT
      Compute the don’t cares of the LUT
      Scan the input vectors
      Set the values of the don’t cares.

## Slide 14: Glitch Reduction Algorithm
Computing the don’t-cares for a LUT
      ABC’s SAT-based don’t-care analysis is used
Scanning the input vectors
      Voting mechanism
Set the value of don’t cares and update the netlist
      Set to the value with more votes
      Netlist is updated before proceeding to the next LUT
      The functionality of the circuit should be guaranteed.

## Slide 15: Input Vector Scan
The sequence of local input vectors to the LUT extracted from the VCD file.
The input vectors are examined in order.
Whenever an input vector corresponding to a don’t care is reached
      check for the closest care states in the past and future of the don't care input vector.
      cast the vote for 0 or 1 based on these care states if they are same.
      Otherwise, no vote is cast.
Vote count is maintained for each don't care in a LUT.

## Slide 18: Iterative Flow
Run the simulation using the modified circuit after glitch reduction.
The algorithm is repeated iteratively.
Runtime of algorithm is less.

## Slide 19: Experimental study
Experimental Setup
      20 MCNC benchmark circuits
      Quartus II 10.1
      Altera Stratix III 65nm FPGA family
      Modelsim SE 6.3e
For each circuit
      5000 random input vectors are applied
Combinational equivalence checking is used after the glitch reduction step.
Three passes of the optimization loop are performed.
Power measurements performed by Quartus Powerplay.

## Slide 20: Results
Dynamic Power reduction in comparison with baseline settings
    Average : 4%
    Peak : 12.5%
Glitch Power reduction
    Average : 13.7%
    Peak : 49%
Dynamic power reduction optimized vs worst-case settings
  Average : 9.8%
  Peak : 30.8%

## Slide 21: Power & don’t-care ratio vs Fanout
Relationship between don’t cares, power and fanout presents a challenge to glitch reduction algorithm.
Increase in fanout increases the average dynamic power of the FPGA due to increase in capacitance.
High fanout signals have fewer don't cares in their driving LUTs than low fanout signals.
Signals consuming most power are poor targets for glitch reduction techniques based on don't cares.

## Slide 22: Power vs Average Voltage Bias
Vote bias is defined as the percentage of votes that were cast for the most popular setting.
There usually exists a highly preferable setting for a particular don’t-care minterm in a LUT.
Observations suggest that don’t-care logic values can be selected with a high degree of confidence.

## Slide 23: Conclusions
Glitch power is a significant portion of total power.
    can be reduced using don't care based optimizations.
As glitch reduction technique performed after placement and routing, it has no effect on circuit area.
Future work
  Integrate algorithm into power-aware FPGA CAD Flow.
  To investigate whether other stages of CAD flow could improve algorithm effectiveness.