## Slide 1: Comparative Analysis of Present and Future Space Processors with Device Metrics
Tyler M. Lovelly
Ph.D. student
University of Florida
Kevin Cheng
M.S. student
University of Florida
William Garcia
B.S./M.S. student
University of Florida
Dr. Alan D. George
Professor of ECE
University of Florida
This work was supported in part by the I/UCRC Program
of the National Science Foundation under Grant Nos. EEC-0642422 and IIP-1161022

## Slide 2: Papers of Interest
J. Richardson, S. Fingulin, D. Raghunathan, C. Massie, A. George, and H. Lam, “Comparative Analysis of HPC and Accelerator Devices: Computation, Memory, I/O, and Power,” Proc. of High-Performance Reconfigurable Computing Technology and Applications Workshop (HPRCTA), at SC’10, New Orleans, LA, Nov 14 2010
Lovelly, T.M.; Bryan, D.; Cheng, K.; Kreynin, R.; George, A.D.; Gordon-Ross, A.; Mounce, G., "A framework to analyze processor architectures for next-generation on-board space computing," Aerospace Conference, 2014 IEEE , vol., no., pp.1,10, 1-8 March 2014 doi: 10.1109/AERO.2014.6836387

## Slide 3
Introduction & Background

## Slide 4: Introduction
Space computing presents unique challenges
  Harsh and inaccessible operating environment
  Severe resource constraints – power, size, weight
  Stringent requirements for performance and reliability
Increasing need for high-performance space computing
  Escalating demands for real-time sensor and autonomous processing
  Limited communication bandwidth to ground stations
  Legacy space processors that cannot meet performance requirements
    Generations behind commercial-off-the-shelf (COTS) processors
    Based upon architectures not particularly suited to needs of space computing
Quantitative and objective analysis of processor architectures
  Device metrics analysis based on architectural capabilities
  Broad and diverse set of architectures under consideration
    Targeting space processors and low-power COTS processors (≤ 30 W)

## Slide 5: Space Processors
Radiation-hardened (RadHard) processors for high reliability
Outcomes of radiation-hardening
  Cumulative effects
    Total-Ionizing Dose (TID) ≥ 300 krad(Si)
  Single-Event Effects (SEEs)
    Immunity to Single-Event Latchup (SEL), Upset (SEU), Functional Interrupt (SEFI)
  Performance and power
    Slower operating frequency, reduction in cores or execution units, increased power
Techniques for radiation-hardening
  Radiation-hardening by process
    Insulating oxide layer used in process
  Radiation-hardening by design
    Specialized circuit-layout techniques
  Radiation-hardening by architecture
    Fault-tolerant computing strategies

## Slide 6: Framework to Analyze Processors

## Slide 7: Dwarfs/Benchmarking
What key benchmarks are of interest for space computing?

## Slide 8: Device Metrics
Suite of quantitative and objective metrics developed by NSF CHREC Center at University of Florida [1-2]
  For comparative analysis of broad and diverse set of processors
    Central processing units (CPUs)
    Digital signal processors (DSPs)
    Field-programmable gate arrays (FPGAs)
    Graphics processing units (GPUs)
    Hybrid combinations of above (often SoCs)
  Highly useful for first-order analyses and comparisons
    Study broad range of devices with metrics to determine best candidates
    Later, study best candidates more deeply with selected, optimized benchmarking
  Different methods used for fixed- and reconfigurable-logic devices
Metrics data collected from architectural features of device
  Determined from vendor-provided information and tools
    Experimental testbed in lab is not required for metrics analysis
[1] J. Williams, A. George, J. Richardson, K. Gosrani, C. Massie, H. Lam, “Characterization of Fixed and Reconfigurable Multi-Core Devices for Application Acceleration,” ACM Transactions on Reconfigurable Technology and Systems (TRETS), Vol. 3, No. 4, Nov. 2010, pp. 19:1-19:29.
[2] J. Richardson, S. Fingulin, D. Raghunathan, C. Massie, A. George, and H. Lam, “Comparative Analysis of HPC and Accelerator Devices: Computation, Memory, I/O, and Power,” Proc. of High-Performance Reconfigurable Computing Technology and Applications Workshop (HPRCTA), at SC’10, New Orleans, LA, Nov 14, 2010.

## Slide 9: Device Metrics Analysis
Analyzing performance (GOPS) and power (GOPS/W)
  Computational Density (CD) measures theoretical performance
    Reported in giga-operations per second (GOPS)
    Calculated separately for varying data types
      8-bit, 16-bit, and 32-bit Integer (Int8, Int16, and Int32)
      Single-precision and double-precision floating point (SPFP and DPFP)
    Determine operations mix (additions, multiplications, etc.) based on target apps
  CD per Watt (CD/W) measures performance scaled by power
Analyzing memory and input-output bandwidth (GB/s)
  Internal Memory Bandwidth (IMB) measures throughput between processor and on-chip memory (cache or BRAM)
  External Memory Bandwidth (EMB) measures throughput between processor and off-chip memory (DDR2, DDR3, etc)
  Input-Output Bandwidth (IOB) measures throughput between processor and all off-chip resources (DDR, GigE, PCIe, GPIO, etc.)

## Slide 10
Device Metrics Examples

## Slide 11: Device Metrics: CPU Analysis (1/2)
Example: Freescale P5040 (RadHard RAD5545)
  COTS counterpart of RadHard RAD5545 CPU from BAE Systems
  Fixed-logic CPU: 2.2 GHz, 49 W, quad-core, no SIMD engine
Calculating CD and CD/W
  Each core contains
    3 integer execution units 1 floating-point execution unit
      Can issue 2 instructions each cycle
  Calculate operations/cycle for each data type
    Int8: 2 ops/cycle Int16: 2 ops/cycle Int32: 2 ops/cycle
    SPFP: 1 op/cycle DPFP: 1 op/cycle
  CDInt8,Int16,Int32 = 4 cores × 2.2 GHz × 2 ops/cycle = 17.6 GOPS
  CD/WInt8,Int16,Int32 = 17.6 GOPS / 49 W = 0.36 GOPS/W
  CDSPFP,DPFP = 4 cores × 2.2 GHz × 1 ops/cycle = 8.8 GOPS
  CD/WSPFP,DPFP = 8.8 GOPS / 49 W = 0.18 GOPS/W
Operations mix of 50% add, 50% mult

## Slide 12: Device Metrics: CPU Analysis (2/2)
Calculating IMB, EMB, and IOB
  Each core contains
    L1 data cache: 8-byte bus L1 instr cache: 16-byte bus L2 cache: 64-byte bus
  Total of 2 DDR3 controllers: 8-byte bus; 1600 MT/s
  IMBL1data = 4 cores × 2.2 GHz × 8 bytes = 70.4 GB/s
  IMBL1inst = 4 cores × 2.2 GHz × 16 bytes = 140.8 GB/s
  IMBL2 = 4 cores × 2.2 GHz × 64 bytes = 563.2 GB/s
  EMB = 2 DDR3 × 8 bytes × 1600 MT/s = 25.6 GB/s
  IOB = DDR3 + 10GigE + 1GigE + PCIe + SATA2.0 + GPIO
  = 25.6 GB/s + 5 GB/s + .5 GB/s
  + 8 GB/s + .3 GB/s + 8.8GB/s = 48.2 GB/s
Based on optimal SerDes lane config.
Assumes 100% cache hit rate

## Slide 13: Device Metrics: FPGA Analysis (1/2)
Example: Xilinx Virtex-5 FX130T
  COTS counterpart of RadHard Virtex-5QV FX130 FPGA from Xilinx
  Reconfigurable-logic FPGA: different methods required for metrics [3]
Calculating CD and CD/W
  FPGA logic resources
    Look-up tables (LUTs), Flip-flops (FFs), Multiply-accumulate units (DSPs)
  Generate and implement compute cores on FPGA with vendor tools
    All combinations of operation and data types: with and without DSP resources
    Collect data on resource usage and max. operating frequencies
    Linear-programming algorithm optimally packs cores onto FPGA
    Max. cores = max. ops/cycle (with pipelined cores)
  Use vendor-provided tools for power estimation
    Calculate dynamic power based on resource usage for cores
  CDInt8 = 2358 ops/cycle × 0.353 GHz = 833.2 GOPS
  CD/WInt8 = 833.2 GOPS / 16.53 W = 50.42 GOPS/W
[3] N. Wulf, J. Richardson, and A. George, “Optimizing FPGA Performance, Power, and Dependability with Linear Programming,” Proc. of Military and Aerospace Programmable-Logic Devices Conference (MAPLD), San Diego, CA, April 9 - 12, 2013.
Same process used for all data types
Operations mix of 50% add, 50% mult

## Slide 14: Device Metrics: FPGA Analysis (2/2)
Calculating IMB, EMB, and IOB
  298 Block RAM units (BRAMs): 9-byte bus, 2 ports, 0.266 GHz operating frequency
  5 DDR2 controllers: 8-byte bus, double data rate, 0.266 GHz operating frequency
  840 GPIO pins: 0.8 Gb/s data rate
  20 RocketIO GTX transceivers: 6.5 Gb/s data rate
  IMBBRAM = 298 BRAMs × 0.266 GHz × 9 bytes × 2 ports = 1430.04 GB/s
  EMB = 5 DDR2 × 0.266 GHz × 8 bytes × 2 (double data rate) = 21.33 GB/s
  IOB = DDR2 + GPIO + RocketIO GTX transceivers
  = 21.33 GB/s + (840 pins × 0.8 Gb/s)
  + (20 transceivers × 6.5 Gb/s) = 121.58 GB/s
Based on max. packing of memory controllers

## Slide 15
Benchmarking Examples

## Slide 16: Benchmarking: P5040 (1/2)
Matrix multiplication of two matrices
  Generated results for various data types, problem sizes, # cores
  Estimated RAD5545 performance based on reduced frequency
Max performance of ~0.61 GOPS
Performance analysis
  Scales down with higher precision
    Exception: Int32/Int64 slower than SPFP due to larger output matrices
  Very high parallel efficiency; approaching linear speedup
Max performance of ~3.09 GOPS
Speedup consistent for all data types

## Slide 17: Benchmarking: P5040 (2/2)
Convolution of matrix with Sobel filter
  Generated results for various data types, problem sizes, # cores
  Estimated RAD5545 performance based on reduced frequency
Performance analysis
  Scales down with higher precision
    Slower GOPS than matrix multiplication
    More overhead from indexing matrices
  Moderate parallel efficiency with peak performance at 4 cores
Supports higher sizes than matrix multiplication
Max performance of ~0.84 GOPS
Max performance of ~0.17 GOPS

## Slide 18
Current Research Data

## Slide 19: Space Processor Comparisons (1/2)
RadHard
COTS counterpart to RadHard Xilinx Virtex-5QV FX130
COTS counterpart to RadHard BAE Systems RAD5545
COTS device in CHREC Space Processor (CSP)
Results displayed in logarithmic scale
COTS counterparts to RadHard
COTS being deployed in space
RadHard data unavailable; loss in performance is expected
FPGAs give high CD and CD/W for all data types
Many-core CPU gives high integer CD, but low CD/W
DSP gives high floating-point CD and CD/W
Older RadHard CPUs greatly outperformed
COTS device in Space Micro Proton400k
FPGA gives better CD and CD/W than CPU

## Slide 20: Space Processor Comparisons (2/2)
BRAMs in FPGAs give much greater IMB than caches
RadHard
COTS counterparts to RadHard
COTS being deployed in space
After FPGAs, multi-core and many-core CPUs give high IMB
Older RadHard CPUs greatly outperformed
Highest EMB and IOB given by FPGAs
Multi-core and many-core CPUs give high EMB and IOB
EMB based on controller for external L2 cache
Results displayed in logarithmic scale
RadHard data unavailable; loss in performance is expected
No controllers for external memory

## Slide 21: RadHard vs. COTS Counterparts (1/2)
COTS vs. RadHard
COTS vs. RadHard
COTS vs. RadHard
COTS vs. RadHard
RadHard version achieves ~30% of original CD
Less integer and floating-point units
Less cores, but adds floating-point units
RadHard version achieves ~14% of original CD/W
RadHard version achieves ~49% of original CD/W
Results displayed in logarithmic scale
RadHard version achieves ~33% of original CD
RadHard version achieves ~28% of original CD
RadHard version achieves ~73% of original CD
RadHard version achieves ~31% of original CD/W
RadHard version achieves ~29% of original CD/W

## Slide 22: RadHard vs. COTS Counterparts (2/2)
COTS vs. RadHard
COTS vs. RadHard
COTS vs. RadHard
COTS vs. RadHard
No L2 cache
Only supports external L2 cache
Changes in IMB for RadHard versions largely consistent with changes in CD
Exception is RADSPEED, which achieves ~93% of original IMB
No controllers for external memory
EMB based on controller for external L2 cache
Changes in EMB for RadHard versions is consistent with changes in IMB
Results displayed in logarithmic scale

## Slide 23: RadHard vs. COTS Comparisons (1/2)
Results displayed in logarithmic scale
RadHard CPU
RadHard DSP
COTS CPU
COTS CPU + DSP
COTS FPGA
COTS CPU + GPU
RadHard CPU gives ~2-17% of integer CD and ~2-28% of floating-point CD of leading COTS devices
RadHard DSP gives ~0.4-6% of integer CD and ~13-80% of floating-point CD of leading COTS devices
RadHard CPU gives ~2-9% of integer CD/W and ~1-17% of floating-point CD/W of leading COTS devices
RadHard DSP gives ~0.8-5% of integer CD/W and ~9-68% of floating-point CD/W of leading COTS devices

## Slide 24: RadHard vs. COTS Comparisons (2/2)
Results displayed in logarithmic scale
RadHard CPU
RadHard DSP
COTS CPU
COTS CPU + DSP
COTS FPGA
COTS CPU + GPU
RadHard CPU gives varying % of IMB of leading COTS devices
~18% for CPU, ~12% for DSP,
~1% for FPGA, ~39% for GPU
RadHard DSP gives small % of IMB of leading COTS devices
~3% for CPU, ~2% for DSP,
~0.2% for FPGA, ~6% for GPU
RadHard CPU gives varying % of EMB/IOB of leading COTS devices
~24/33% for CPU, ~29/31% for DSP,
~9/4% for FPGA, ~60/67% for GPU
RadHard DSP gives varying % of EMB/IOB of leading COTS devices
~27/22% for CPU, ~24/29% for DSP,
~8/3% for FPGA, ~50/63% for GPU

## Slide 25: Appendix: Device Metrics Data
 | Processor | Type | CD (GOPS) |  |  |  |  | CD/W (GOPS/W) |  |  |  |  | IMB (GB/s) |  |  | EMB (GB/s) | IOB (GB/s)
 |  |  | Int8 | Int16 | Int32 | SPFP | DPFP | Int8 | Int16 | Int32 | SPFP | DPFP | L1 cache | L2 cache | BRAMs |  | 
RadHard | Honeywell HXRHPPC | CPU | 0.080 | 0.080 | 0.080 | 0.080 | 0.080 | 0.011 | 0.011 | 0.011 | 0.011 | 0.011 | 1.280 | 0.000 | 0.000 | 0.000 | 0.160
 | BAE Systems RAD750 | CPU | 0.266 | 0.266 | 0.266 | 0.133 | 0.133 | 0.053 | 0.053 | 0.053 | 0.027 | 0.027 | 3.192 | 0.000 | 0.000 | 1.064 | 1.592
 | Aeroflex/Gaisler GR712RC | CPU | 0.080 | 0.080 | 0.080 | 0.025 | 0.025 | 0.053 | 0.053 | 0.053 | 0.017 | 0.017 | 4.800 | 0.000 | 0.000 | 0.400 | 1.213
 | Boeing MAESTRO | CPU | 101.920 | 50.960 | 25.480 | 12.740 | 12.740 | 4.591 | 2.295 | 1.148 | 0.574 | 0.574 | 101.920 | 50.960 | 0.000 | 8.320 | 15.070
 | BAE Systems RADSPEED | DSP | 17.708 | 17.708 | 10.119 | 70.832 | 35.416 | 1.181 | 1.181 | 0.675 | 4.722 | 2.361 | 14.912 | 7.456 | 0.000 | 6.990 | 14.185
COTS counterparts to RadHard | Freescale PowerPC603e | CPU | 0.266 | 0.266 | 0.266 | 0.266 | 0.266 | 0.076 | 0.076 | 0.076 | 0.076 | 0.076 | 4.256 | 0.000 | 0.000 | 0.000 | 2.128
 | IBM PowerPC750 | CPU | 0.800 | 0.800 | 0.800 | 0.400 | 0.400 | 0.170 | 0.170 | 0.170 | 0.085 | 0.085 | 9.600 | 0.000 | 0.000 | 3.200 | 4.000
 | Tilera TilePro64 | CPU | 358.400 | 179.200 | 89.600 | 0.000 | 0.000 | 15.583 | 7.791 | 3.896 | 0.000 | 0.000 | 358.400 | 179.200 | 0.000 | 22.400 | 29.150
 | Freescale P5040 | CPU | 17.600 | 17.600 | 17.600 | 8.800 | 8.800 | 0.359 | 0.359 | 0.359 | 0.180 | 0.180 | 211.200 | 563.200 | 0.000 | 25.600 | 48.200
 | Clearspeed CSX700 | DSP | 24.000 | 24.000 | 13.714 | 96.000 | 48.000 | 2.400 | 2.400 | 1.371 | 9.600 | 4.800 | 16.000 | 8.000 | 0.000 | 7.500 | 21.500
 | Xilinx Virtex-5 FX130T | FPGA | 833.200 | 416.300 | 89.680 | 80.230 | 17.530 | 50.420 | 23.810 | 6.088 | 5.754 | 2.025 | 0.000 | 0.000 | 1430.042 | 21.334 | 121.584
COTS being deployed in space | Freescale P2020 | CPU | 4.000 | 4.000 | 4.000 | 8.000 | 8.000 | 0.615 | 0.615 | 0.615 | 1.231 | 1.231 | 176.000 | 80.000 | 0.000 | 8.000 | 10.620
 | Xilinx Zynq-7020 (CPU) | CPU | 32.020 | 16.010 | 8.000 | 8.000 | 2.670 | 57.610 | 16.720 | 6.860 | 6.860 | 2.290 | 53.360 | 10.670 | 0.000 | 10.664 | 11.030
 | Xilinx Zynq-7020 (FPGA) | FPGA | 292.130 | 135.990 | 39.340 | 30.740 | 10.460 | 88.260 | 57.140 | 15.130 | 10.060 | 4.210 | 0.000 | 0.000 | 1154.387 | 6.400 | 53.050
 | Xilinx Zynq-7020 (Hybrid) | CPU+FPGA | 324.150 | 152.000 | 47.340 | 38.740 | 13.130 | 72.350 | 42.820 | 12.560 | 9.160 | 3.590 | 53.360 | 10.670 | 1154.387 | 42.656 | 89.670
COTS | Intel Atom Z2760 | CPU | 144.000 | 72.000 | 36.000 | 21.600 | 7.200 | 48.000 | 24.000 | 12.000 | 7.200 | 2.400 | 18.800 | 7.200 | 0.000 | 6.400 | 9.192
 | Intel Core i7-4610Y | CPU | 594.600 | 316.200 | 177.000 | 124.800 | 78.400 | 51.704 | 27.496 | 15.391 | 10.852 | 6.817 | 742.400 | 92.800 | 0.000 | 25.600 | 64.100
 | TI OMAP4460 | CPU | 146.170 | 73.090 | 36.540 | 36.140 | 12.000 | 77.420 | 38.710 | 19.360 | 19.140 | 6.360 | 120.000 | 36.000 | 0.000 | 6.400 | 11.710
 | Tilera TILE-Gx8036 | CPU | 486.000 | 270.000 | 162.000 | 54.000 | 54.000 | 16.200 | 9.000 | 5.400 | 1.800 | 1.800 | 1152.000 | 576.000 | 0.000 | 12.800 | 45.920
 | Freescale MSC8256 | DSP | 24.000 | 24.000 | 12.000 | 12.000 | 6.000 | 3.974 | 3.974 | 1.987 | 1.987 | 0.993 | 192.000 | 96.000 | 0.000 | 12.800 | 17.940
 | TI KeyStone-I TMS320C6678 | DSP | 960.000 | 480.000 | 240.000 | 160.000 | 80.000 | 47.291 | 23.645 | 11.823 | 7.880 | 3.940 | 960.000 | 160.000 | 0.000 | 12.800 | 33.860
 | TI KeyStone-II 66AK2H12 | CPU+DSP | 1459.200 | 729.600 | 364.800 | 198.400 | 99.200 | 67.280 | 33.640 | 16.820 | 9.150 | 4.570 | 1049.600 | 176.000 | 0.000 | 28.800 | 48.220
 | Xilinx Spartan-6Q LX150T | FPGA | 590.400 | 185.100 | 37.960 | 21.220 | 7.859 | 60.580 | 22.460 | 5.947 | 3.889 | 1.467 | 0.000 | 0.000 | 675.360 | 24.000 | 57.800
 | Xilinx Artix-7Q 350T | FPGA | 1245.000 | 939.100 | 163.300 | 134.200 | 45.520 | 75.490 | 52.650 | 13.730 | 8.930 | 3.721 | 0.000 | 0.000 | 3598.614 | 16.000 | 75.600
 | Xilinx Kintex-7Q 410T | FPGA | 2295.000 | 1696.000 | 380.600 | 224.300 | 91.950 | 74.280 | 51.360 | 18.030 | 8.715 | 3.500 | 0.000 | 0.000 | 6555.268 | 42.667 | 184.292
 | Xilinx Virtex-7Q X980T | FPGA | 4356.000 | 2186.000 | 890.500 | 539.600 | 207.200 | 75.130 | 48.310 | 14.790 | 8.763 | 3.469 | 0.000 | 0.000 | 12368.430 | 89.600 | 417.425
 | Altera Stratix III EP3SL150 | FPGA | 1115.000 | 329.700 | 87.100 | 69.430 | 21.550 | 37.470 | 16.460 | 5.332 | 2.575 | 1.264 | 0.000 | 0.000 | 2020.140 | 38.400 | 64.800
 | Altera Stratix IV EP4SGX230 | FPGA | 2563.000 | 811.500 | 258.100 | 153.000 | 60.550 | 99.320 | 41.230 | 15.040 | 5.995 | 2.694 | 0.000 | 0.000 | 6906.600 | 44.800 | 87.900
 | Altera Cyclone V GXFC9E6 | FPGA | 1113.000 | 358.800 | 81.530 | 94.170 | 31.810 | 138.300 | 65.970 | 18.170 | 8.645 | 3.463 | 0.000 | 0.000 | 3843.000 | 32.000 | 51.813
 | Altera Arria V GXFB7K4 | FPGA | 3329.000 | 1197.000 | 310.000 | 260.700 | 97.100 | 131.800 | 70.330 | 20.610 | 8.607 | 3.481 | 0.000 | 0.000 | 9656.000 | 44.800 | 103.800
 | Altera Stratix V GXEBBR1 | FPGA | 7885.000 | 1999.000 | 499.000 | 461.300 | 140.600 | 168.900 | 69.100 | 19.230 | 8.669 | 3.063 | 0.000 | 0.000 | 15840.000 | 44.800 | 191.125
 | Xilinx Zynq-7045Q | CPU+FPGA | 1896.020 | 719.810 | 269.200 | 194.100 | 65.270 | 70.640 | 44.690 | 12.250 | 7.930 | 3.170 | 53.360 | 10.670 | 4493.863 | 34.110 | 126.630
 | Altera Cyclone V SoC SXFC6D6 | CPU+FPGA | 454.800 | 149.500 | 40.990 | 45.960 | 13.840 | 104.480 | 44.560 | 13.230 | 8.510 | 3.030 | 74.000 | 14.800 | 1754.550 | 46.930 | 69.180
 | Altera Arria V SoC SXFB5H4 | CPU+FPGA | 3168.400 | 1170.200 | 294.200 | 246.900 | 91.290 | 125.680 | 65.960 | 19.300 | 8.520 | 3.400 | 64.000 | 0.000 | 9128.000 | 53.330 | 107.960
 | NVIDIA Tegra 3 | CPU+GPU | 265.984 | 137.984 | 73.984 | 73.984 | 25.600 | 132.992 | 68.992 | 36.992 | 36.992 | 12.800 | 240.000 | 25.600 | 0.000 | 10.680 | 118.400
 | NVIDIA Tegra 4 | CPU+GPU | 473.980 | 261.180 | 154.780 | 109.180 | 30.400 | 94.800 | 52.240 | 30.960 | 21.840 | 6.080 | -- | -- | 0.000 | -- | --
 | NVIDIA Tegra K1 | CPU+GPU | 697.600 | 440.000 | 311.200 | 256.000 | 44.400 | 139.520 | 88.000 | 62.240 | 51.200 | 8.880 | 358.400 | 36.800 | 0.000 | 13.854 | 22.550
Notes: Slide 8: Justin
Requesting a minimum of 3 memberships, directly correlating to how many platforms and benchmarks we can do

## Slide 26
Conclusions & Future Research

## Slide 27: Conclusions and Future Research
Conclusions
  Device metrics provides powerful 1st order evaluation
    Lower cost
    Much less time to analyze
  Benchmarking is used for more detailed analysis
    Cost of acquiring testbeds
    Time and cost spent to develop benchmarks for specific architectures
  Leveraging both provides valuable insight
Future Research
  Profile operations mixes of more space dwarfs
    Perform device metrics with resulting operations mixes
    i.e. 20% ADD, 30% DIVIDE, 50% MULT (a.o.t 50% ADD / 50% MULT)
  Benchmark more COTS devices & extrapolate to RadHard
    i.e. Scale by clock speed and power
Notes: Slide 8: Justin
Requesting a minimum of 3 memberships, directly correlating to how many platforms and benchmarks we can do

## Slide 28
Notes: Slide 8: Justin
Requesting a minimum of 3 memberships, directly correlating to how many platforms and benchmarks we can do