## Slide 1: Time-Triggered Ethernet: Concepts and Switch Design
Andrew Mortellaro
William Garcia

## Slide 2: Literature Survey
Kopetz, Hermann; Ademaj, A.; Grillinger, P.; Steinhammer, K., "The time-triggered Ethernet (TTE) design," Object-Oriented Real-Time Distributed Computing, 2005. ISORC 2005. Eighth IEEE International Symposium on , vol., no., pp.22,33, 18-20 May 2005
Steinhammer, K.; Grillinger, P.; Ademaj, A.; Kopetz, Hermann, "A Time-Triggered Ethernet (TTE) Switch," Design, Automation and Test in Europe, 2006. DATE '06. Proceedings , vol.1, no., pp.1,6, 6-10 March 2006

## Slide 3: Problem
Real-time systems depend a deterministic communications architecture
The open-nature of Ethernet makes guaranteeing strict temporal properties difficult
Unification is imperative
  Support for real-time and non-real-time applications
  Specialized communications solutions are costly
    Chip mask development
    Software-tool development
  Generic unified platform supported by COTS components would significantly reduce cost

## Slide 4: Time-triggered protocol
Developed by Real-Time Systems Group
Supports bandwidth up to 25 Mbits/sec
NEXT-TTA Project
  Implemented TTP on COTS Gigabit Ethernet
  COTS Ethernet switch unpredictable in nature
  Disappointing resource utilization
Applications in the aerospace, railway, and automotive domains

## Slide 5: Time-Triggered Ethernet (TTE)
Unifies real-time and non-real-time traffic
Distinguishes between two traffic types:
  Event-triggered (ET) – standard traffic handled by existing IEEE Ethernet standards
  Time-triggered (TT) – temporally guaranteed traffic for safety-critical configurations
TTE aims to handle both traffic types over single communications architecture

## Slide 6: TTE Requirements
Certification
  Most demanding requirement
  Need for correct operation in all fault scenarios
  Repartitioning into fault-containment regions (FCRs)
Legacy Integration
  Portability of existing Ethernet applications
  No changes in software or hardware
Deterministic Message Transfer
  Small delay and minimized jitter
Fault-Tolerant Global Time
  Tantamount to safety-critical applications

## Slide 7: TTE Requirements
Strong Fault Isolation
  Physical Proximity fault toleration: distributed system
  Elimination of error propagation
Consistent Diagnosis
  Correct nodes should agree on “up” and “down” nodes
  Important for reconfiguration and recovery
Scalability
  Higher speeds (10 Gigabit/sec)
  Number of system controllers

## Slide 8: TT vs. ET systems
Event-triggered
  Action is started for a significant non-temporal event
  Can occur outside or inside the computer
  Examples: state change, interrupt firing
Time-triggered
  Action is started for a significant temporal event
    Real time reaches a predefined instant, or trigger value
    Trigger value has a period and phase
  Occurs inside the distributed computer system
  Example: command and control, telemetry

## Slide 9: Event vs. State Messages
Event messages are event-triggered (Ethernet)
State messages are time-triggered (TTE)

## Slide 10: Dependable Real-Time Systems
Dependable services demand redundant resources and a voting mechanism
Deterministic multicast transmission
  The jitter, or difference between maximum and minimum delay, is a priori known characteristic parameter
    Assures timeliness with a bounded latency
  The receive order of messages is same as send order
    Important for a TMR system
  If the send instances of multiple messages are the same, then an ordering will be established a priori
    Ensures conflict resolution

## Slide 11: Open vs. Closed World Systems
Open-World Systems
  Unknown number of clients compete for a server
  Critical Instant: when all clients request server simultaneously
  Guaranteed real time performance not guaranteed
  Ex: the Internet
Closed-World Systems
  Limited number of clients known a priori
  Clients cooperate to establish a coordinated schedule
  Server meets all requests within specified temporal bounds

## Slide 12: Global Sparse Time
Time-triggered system must contain global time base
  Periodic synchronization of node’s local clock
Dense time base
  Events may occur at any instant in timeline
Sparse time base
  Events may occur within an active interval π
  Silent interval Δ between any two active intervals

## Slide 13: Time Format
Characterized by granularity and horizon
  Granularity: minimum interval between ticks of digital clock
  Horizon: the instant when time will wrap around
64-bit binary time format
  Fractions of a second: 24 negative powers of 2
  Full seconds: 40 positive powers of 2

## Slide 14: Periods
Restricted to positive and negative powers of 2
  Theoretically 64 different period durations
  Period Bit: bit that specifies duration of period
Custom Implementation
  16 different period choices from 2 seconds to 60 μseconds
  Phase bits: twelve bits to right of period bit
  Example: period of 1/24 with phase 1/26 + 1/211

## Slide 15: Principles of Operation
Standard Configuration
  Standard Ethernet controllers
  TT Ethernet controllers
  Single switch
Fault-tolerant Configuration
  Safety-critical TT Ethernet controller (two port)
  Two independent switches
  Switches monitored by two independent guardians

## Slide 16: TT Ethernet Systems
Standard Configuration Fault-tolerant Configuration

## Slide 17: The TT Ethernet Switch
Event-triggered messages
  Stored in an ET-message queue of switch
  Forwarded to specified receiver if outgoing channel free
  Switch clears channel for incoming TT messages, then retransmits ET message once TT message terminates
Time-triggered messages
  Delayed and then forwarded to addressed receivers
  Clearance delay: time needed to clear transmission path for preempted ET message (4 μseconds in custom design)

## Slide 18: The TT Ethernet Controller
Event-triggered messages
  Conform to IEEE Ethernet standard
  COTS Ethernet controller can process TT message
Time-triggered messages
  For every new message type (period ID), allocate a local message-buffer with current version of state message
  Outgoing message remains in buffer until phase bits of global time match those of the period ID
  Incoming message overwrites current contents of the controller local message buffer

## Slide 19: TT Ethernet Message Format
Since message type name is part of a TT message, host connected to COTS Ethernet controller can process message

## Slide 20: Message Categories
ET Message
  Handled in full conformance with IEEE Ethernet standard
Free-Form TT message
  ET messages in the way of FFTT message will be preempted
  Used in systems without clock synchronization
TT startup message
  Initial synchronization, setup of startup phase
TT synchronization message
  Maintain clock synchronization during operational phase
Unprotected TT message
  Not protected by a guardian; intended for multimedia applications
Protected TT message
  Protected by guardians; intended for safety-critical applications

## Slide 21: Safety-Critical TT Ethernet Systems
Safety-Critical TT Ethernet Controller
  Three ports: one to host, two to independent switches
  TT message header contains membership vector, period counter, and signature of scheduler
The Guardian
  Connected to switch by Ethernet port and set of parallel wires
  Parallel wires observe and disable inputs and outputs of switch
  Has knowledge of schedule of PTTMs
Fault-Tolerant Clock Synchronization and Startup
  Combination of distributed fault-tolerant clock state synchronization algorithms and central rate correction algorithm

## Slide 22: TT Ethernet Switch Architecture
Features
  Classification of ET and TT packet traffic
  Constant, a priori known transmission delay for TT traffic
  Memory-less transmission path for TT traffic
  Preemption of ET packets
  Retransmission of preempted ET packets
  ET packet handling according to Ethernet standard
Implementation
  Custom board based on Altera EP1C20 FPGA
  Eight-port Ethernet PHY transceiver
  Exchanged data are Ethernet layer 2 packets

## Slide 23: TT Ethernet Switch Functionality
Each TT packet takes same route through FPGA
Supports only 100 Mbit/sec
  Field communication systems
Input Shift Register
  Extracts source and destination
  Length must be less than that of minimum frame length (~26)
ET-Buffer
  Three modes
    Normal read/write operation
    ET preemption or packet collision
    Buffer overflow
Multiplexor
  Each is connected to all destination shift registers
  Control module sets MUX to direct packet to respective output register

## Slide 24: TT Ethernet Switch Experiment
Cluster of 4 nodes
  Three nodes with TTE Controllers (transmit TT messages)
  One node with Ethernet Controller (broadcasts ET messages)
TT Ethernet frames sent periodically
  Based on configuration file stored at each node
  5 different configurations; TT periods from 7.8 ms to 2 s.
  Receiver expects TT message within time interval:
    : precision of global time
    : propagation delay from sender i receiver j
  Lost frames are received outside time window
TTE Controller
  Implemented on single-board computer “net4801”
  Linux OS with real-time application interface (RTAI)

## Slide 25: TT Ethernet Switch Results
Data gathered for 20 runs, 33000 TT messages
Δ: maximum difference between expected and actual frame arrival time
Experimental Results
  TTE Switch showed no frame loss and lower Δ than that of COTS switch
  COTS Switch showed frame loss for ET messages and higher Δ than TTE

## Slide 26: Conclusion and Opportunities
Conclusion
  Time-Triggered Ethernet Design
    TTE is a unified communication architecture for non-real-time and real-time apps
    Unification makes system design less costly
  Time-Triggered Ethernet Switch
    Transmission delays and jitter for COTS switch not satisfactory
    Preemption enables constant TT transmission delay and bounded jitter
Opportunities
  Results from TTE Design Paper
    Group was currently implementing design on FPGA modules
  Switch validation results for a safety-critical TTE configuration
    Results were for a standard configuration
    Reliability estimates would be useful for evaluating fault-tolerance

## Slide 27: Questions?