## Slide 1: HW/SW Codesign Techniques for Dynamically Reconfigurable Architectures
Authors: Juanjo Noguera & Rosa M. Badia
Presented by: Derrick Gilland
Course: EEL 6935 (Spring 2009)

## Slide 2: Outline
Introduction
Definitions
Codesign Methodology
Proposed Architectures
Optimization Algorithms
Experiments & Results
Conclusions

## Slide 3: Introduction
Apply HW/SW codesign techniques to dynamically reconfigurable logic (DRL) devices
  Major challenge is reconfiguration latency
Conventional HW/SW codesign approaches fail to consider features of DRL devices
  Do not take into account flexibility of DRL
    Multiple configurations
    Partial & run-time reconfiguration, etc.
Need new methodologies/algorithms

## Slide 4: Paper’s Contributions
HW/SW methodology with dynamic scheduling using DRL architectures
Novel approach to dynamic DRL multicontext scheduling
HW/SW partitioning algorithm for dynamically reconfigurable architectures

## Slide 5: Definitions
Reconfiguration contexts
  Temporal exclusive segments
DRL multicontext scheduling
  Finds an execution order for a set of tasks that minimizes the application execution time

## Slide 6: Definitions
Discrete Event Class (DEC)
  Concurrent process type with certain behavior
Discrete Event Object (DEO)
  Concrete instance of a DE class
State
Behavior
Input Event
Output Event
DEC
S1
DEC
DEO1

## Slide 7: Definitions
Event Stream (ES)
  List of events ordered by tag
Discrete Event Functional Unit
  Physical component where an event can be executed
(Tag, DEC, DEO, V)
(Tag, DEC, DEO, V)
(Tag, DEC, DEO, V)
-
+
(Tag, DEC, DEO, V)
DEC2
S1

## Slide 8: Codesign Methodology
Application
Stage
Static
Stage
Dynamic Stage
Discrete Event System Specification
Design Constraints
HW/SW Class Partitioning
Discrete Event Class & Object Extraction
DE Class Estimation
SW Synthesis
HW Synthesis
DRL
Multi-Context Scheduling
HW/SW Scheduling

## Slide 9: Architecture 1: Shared Memory
CPU
System RAM
HW/SW & DRL
Multi-Context Scheduler
Event Stream RAM
DRL Context (Class) RAM
DRL Cell0
DRL Cell1
DRL CellN
Object State RAM
DRL Array
Object Bus
System Bus
Class Bus
Event Bus
I/O0
I/OL

## Slide 10: Architecture 2: Local Memory
CPU
System RAM
HW/SW & DRL
Multi-Context Scheduler
Event Stream RAM
DRL Context (Class) RAM
DRL Cell0
DRL Cell1
DRL CellN
Object State RAM
DRL Array
System Bus
Class Bus
Event Bus
I/O0
I/OL
Object State RAM
Object State RAM

## Slide 11: Dynamic DRL Management
Event driven scheduler
  One event at a time
  Can be modified for parallel processing of events
    Not considered by paper
Manages class & object switching
  Class switching can be done while event executes
  Uses class switch (reconfiguration) prefetching
Controls all DRL cells & CPU transitions

## Slide 12: DRL Cell State Diagram
Object Switch
Waiting
Execution
(A)
(F)
(G)
(E)
(H)
(I)
(C)
(D)
(B)
Parallel to Current Event
Idle
Class Switch
Waiting for Current Event to Finish
Serial to Current Event

## Slide 13: Algorithms for Shared Memory Optimization
HW/SW Partitioning Algorithm
  Sorts DE classes by execution time
  Most time consuming DE classes mapped to HW
    Area constrained
    Resource constrained
DRL Multicontext Scheduling Algorithm
  Minimizes class switching overheads

## Slide 14: DRL Multicontext Algorithm
Executed at end of processing current event, but concurrently with next event
Uses expected active DE classes and associated tags within event window (EW)

## Slide 15: DRL Multicontext Algorithm
Two possible cases
Case 1: No DRL cells available
  Selects 1st DE class (DEC1) in EW that is not loaded
  Compares to loaded DE class (DEC2) that is required latest
  If DEC1 is needed before DEC2 then DEC1 is loaded in place of DEC2
    Otherwise no reconfiguration occurs

## Slide 16: DRL Multicontext Algorithm
Case 2: K DRL cells available
  Processes entire event window from beginning
  If DE class not loaded in DRL cell, then that DRL cell is reconfigured
  Stops once all DRL cells are loaded

## Slide 17: Algorithms for Local Memory Optimization
Differences from Shared Memory
  HW/SW Partitioning Algorithm
    Decides which DRL cell will always execute events of each class
  DRL Multicontext Algorithm
    Mapping between classes/objects and DRL cells is fixed at compile-time
      i.e. DEC1 must always be loaded in DRL3, but DEC1 is not always loaded
Rest of algorithms are similar

## Slide 18: Improvements to HW/SW Partitioning
HW based prefetching technique which overlaps execution & reconfiguration
Goal: maximize # of DE classes mapped to HW while…
  Meeting memory and DRL area constraints
  Average execution time for all classes in HW is less than average SW execution time
    Factors in probability of how often DE class will be used
Obtains initial solution & iteratively improves

## Slide 19: Improvements to HW/SW Partitioning
Initial solution
  Obtained using previous algorithm except some classes classified as SW due to limited resources
Iterative solution
  Uses list of classes sorted by execution time
  Tests improvement to average HW time vs. average SW time if class moved to HW
  Continues until optimal solution found

## Slide 20: Improvements to HW/SW Partitioning
Goal: minimize reconfiguration latency by reducing # of reconfigurations performed
Solution: Class Packing
  Goal: Pack HW classes into minimum # of reconfiguration contexts (i.e. several classes into single DRL cell)
  Packed according to DRL area
  Uses left-edge algorithm for optimal results

## Slide 21: Evaluation of Improved Algorithm
Simulation examples (subset of full datasets)
  Example 1 & 2
    Have 7 DE classes
    E1’s area facilitates class packing while E2 does not
  Example 3 & 4
    Have 8 DE classes
    E3’s difference between HW & SW execution time is not significant while E4’s is

## Slide 22: Evaluation of Improved Algorithm
Chart: Simulation Examples Performance Evaulation
| 1.0 | 2.0 | 3.0 | 4.0
ALL_SW | 117000 | 124000 | 85000 | 115000
ALL_HW | 24000 | 24000 | 24000 | 24000
Tr=2000 | 44000 | 50000 | 57000 | 50000
Tr=500 | 32000 | 32000 | 37000 | 32000

## Slide 23: Conclusions
All HW Implementation vs. Improved HW/SW Partitioning & DRL Multicontext Algorithms
  No significant difference in execution time
All SW Implementation significantly slower than all other implementations (even when SW class execution time similar to HW)
  Due to HW/SW communication overhead
Optimal event window size is # of DRL cells + 1
  DRL reconfigurations can overlap CPU executions