## Slide 1: A Self-Tuning Cache architecture for Embedded Systems
Chuanjun Zhang, Frank Vahid and Roman Lysecky
Presented by: Wei Zang
Mar. 29, 2010

## Slide 2: Outline
Introduction
Configurable cache architecture
  Associativity: Way concatenation
  Cache size: Way shutdown
  Line size: line concatenation
  Way prediction
Energy Evaluation
Self-tuning strategy
Experiment results
conclusions

## Slide 3: Outline
Introduction
Configurable cache architecture
  Associativity: Way concatenation
  Cache size: Way shutdown
  Line size: line concatenation
  Way prediction
Energy Evaluation
Self-tuning strategy
Experiment results
conclusions

## Slide 4: Introduction
Why configure cache?
  Caches often consume about half of a microprocessor system’s power
  Customized cache can improve performance, reduce power
In embedded systems
  An embedded system may execute one application forever
  Complicated programs have different cache requirements over time – adapt to program phases
What cache parameters?
  Total size
  Line size
  Associativity

## Slide 5: Introduction
Challenges:
  Architecture that can configure size, line size and associativity to application
  Drawbacks in using simulation to determine the best cache:
    Simulation tool setup is very hard
    Simulation is extremely slow
    Simulation uses a fixed set of input data during execution, cannot capture actual run-time behavior where the data changes dynamically
  Drawbacks in exhaustively searching all possible cache configurations:
    May involve too many configurations
      The number quickly increases when other components within the system are configurable (level2 cache, bus, etc.)
    Too many cache flushes, very time and power costly
  Propose a method of dynamically tuning cache in efficient manner

## Slide 6: Outline
Introduction
Configurable cache architecture
  Associativity: Way concatenation
  Cache size: Way shutdown
  Line size: line concatenation
  Way prediction
Energy Evaluation
Self-tuning strategy
Experiment results
conclusions

## Slide 7: Associativity: Way Concatenation
index
data output
critical path
6x64
6x64
a31 tag address a13 a12 a11 a10 index a5 a4 line offset a0
data array
Trivial area overhead
No performance overhead
reg1
reg0
c1
c3
c0
c2
Configuration circuit
c1
c0
tag address
c0
c1
mux driver
line offset
c2
6x64
6x64
c3
c2
c3
6x64
6x64
tag part
32 bytes
2^6 sets
tag

## Slide 8
reg1
reg0
c1
c3
c0
c2
Configuration circuit
a31 tag address a13 a12 a11 a10 index a5 a4 line offset a0
bank1
bank2
bank3
bank4
Reg0 =1; Reg1 =1
Four-way
c0, c1,c2,c3 = 1
All banks are active
Given an address, four banks are selected as four ways, no matter what is a11 or a12

## Slide 9
reg1
reg0
c1
c3
c0
c2
Configuration circuit
a31 tag address a13 a12 a11 a10 index a5 a4 line offset a0
bank1
bank2
bank3
bank4
Reg0 =0; Reg1 =0
Direct mapped
C0 = !a11 !a12
C1 = !a11 a12
C2 = a11 !a12
C3 = a11 a12
Concatenate address
bank1
bank3
bank2
bank4
!a11 !a12
a11 !a12
!a11 a12
a11 a12
Given an address, only one bank is selected according to a11 a12:
a11=0, a12=0, select bank1
a11=0, a12=1, select bank3
a11=1, a12=0, select bank2
a11=1, a12=1, select bank4

## Slide 10
reg1
reg0
c1
c3
c0
c2
Configuration circuit
a31 tag address a13 a12 a11 a10 index a5 a4 line offset a0
bank1
bank2
bank3
bank4
Reg0 = 0; Reg1 =1
Two-way
C0 = !a11
C1 = !a11
C2 = a11
C3 = a11
concatenate address in two banks
bank3
bank4
bank1
bank2
a11
!a11
2-ways
Given an address, only two banks are selected
according to a11:
a11=0, select bank1 and bank2 to realize 2 ways
a11=1, select bank3 and bank4 to realize 2 ways

## Slide 11: Configurable cache architecture
W1
Four Way Set Associative(Base Cache)
W2
W3
W4
W1
Two Way Set Associative
W2
W3
W4
W1
Direct mapped cache
W2
W3
W4
Way Concatenation
W1
Shut down two ways
W2
W3
W4
Gnd
Vdd
Bitline
Bitline
Gated-Vdd
Control
Way Shut down:
Use sleep transistor method (Powell et. al. ISLPED 2000)
Reduce static power
Reduce dynamic power by accessing fewer ways
Counter
bus
One Way
16 bytes
4 physical lines are filled when line size is 64 bytes
Off Chip Memory
(Zhang et. al. ISVLSI 03)
Way prediction unit can be turned on/off.
Line Concatenation

## Slide 12: Benefits of a configurable cache
  Cfg is for configurable cache tuned to the best configuration for each benchmark
  Energy is normalized to the cnv4w32
  Average of over 40% memory access energy saving

## Slide 13: Outline
Introduction
Configurable cache architecture
  Associativity: Way concatenation
  Cache size: Way shutdown
  Line size: line concatenation
  Way prediction
Energy Evaluation
Self-tuning strategy
Experiment results
conclusions

## Slide 14: Computing Total Memory-Related Energy
Considers CPU stall energy and off-chip memory energy
  Excludes CPU active energy
  Thus, represents all memory-related energy
energy_miss = k_miss_energy * energy_hit
energy_static_per_cycle = k_static * energy_total_per_cycle
(Vary the k’s to account for different system implementations)
energy_dynamic = cache_hits * energy_hit + cache_misses * energy_miss
energy_miss = energy_offchip_access + energy_uP_stall + energy_cache_block_fill
energy_static = cycles * energy_static_per_cycle
energy_mem = energy_dynamic + energy_static
Underlined – measured quantities

## Slide 15: Outline
Introduction
Configurable cache architecture
  Associativity: Way concatenation
  Cache size: Way shutdown
  Line size: line concatenation
  Way prediction
Energy Evaluation
Self-tuning strategy
Experiment results
conclusions

## Slide 16: Cache Self-tuning Hardware
Self-tuning method
  Incorporates a cache parameter tuner on a SoC platform
  Detect the lowest energy dissipation cache parameters
  The tuner sits to the side and collects information used to calculate the energy
Mem
Processor
D$
I$
Tuner

## Slide 17: Designing a Search Heuristic: Evaluating Impact of Cache Parameters
  Total cache size has the biggest average impact on energy and miss rate
  Then cache line size (Data address tend not to have strong spatial locality compared with instruction addresses)
  Least impact: associativity

## Slide 18: Search heuristic
Initial: 2K_1W_16B, without way prediction
Search cache size from 2K, to 4K to 8K bytes
Search cache line size from 16B to 32B to 64B
Search cache associativity from 1W to 2W to 4W
Decide weather to use way prediction
Search Cache Size
Search Line Size
Search Associativity
Way prediction if more than 1 way
  Suppose there are n configurable parameters, each has m values.
  Total m^n different combinations
  This heuristic only search m*n combinations at most
  Time complexity
  Search all space: O(m x n x l x p)
  Heuristic : O(m + n + l + p)

## Slide 19: Outline
Introduction
Configurable cache architecture
  Associativity: Way concatenation
  Cache size: Way shutdown
  Line size: line concatenation
  Way prediction
Energy Evaluation
Self-tuning strategy
Experiment results
conclusions

## Slide 20
  On average 5 searching instead of 27 total searching
  2 (mpeg2 and pjpeg) out of 19 benchmarks miss the lowest power cache configuration.

## Slide 21: Outline
Introduction
Configurable cache architecture
  Associativity: Way concatenation
  Cache size: Way shutdown
  Line size: line concatenation
  Way prediction
Energy Evaluation
Self-tuning strategy
Experiment results
conclusions

## Slide 22: Conclusions
A highly configurable cache architecture
  Reduces on average 40% of memory access related energy
A self-tuning mechanism is proposed
  A special cache parameter explorer
  A heuristic algorithm to search the parameter space
Thank you!