## Slide 1: Challenges In Embedded Memory Design And Test
History and Trends In Embedded System Memory

## Slide 2: Ideal Memory: Yesterday, Today And Tomorrow
1980 – 1990: The Stand-Alone Chip
Three Main Types:
  SRAM
  DRAM
  Flash EEPROMs

## Slide 3: 1980-1990: The Stand-Alone Chip
SRAM – The “S” is for “Static”
  6T variety used in handheld systems due to:
    Low standby power
    Wide noise margin
    Ease of use
  4T variety typically used for cache, especially for systems using mostly DRAM

## Slide 4: 1980-1990: The Stand-Alone Chip
DRAM – The “D” is for “Dynamic”
  Must be refreshed periodically because the bits are stored with a capacitor, which leaks current
  Small cell size and high density made them ideal for larger memory systems.
  However, slower performance typically required the use of an SRAM cache
  Higher power consumption due to the need for refreshing, not suitable for handheld embedded systems.
Notes: Mention that Flash was used for non-volatile applications like a BIOS

## Slide 5: 1990-2000: Memory Integrated With Logic
From 1990-2000, logic began to be integrated onto memory chips
Sub-micron processes increased logic speed, requiring faster memories
Also provided room for logic on the memory chip, allowing them to be synchronous
Refresh circuitry for DRAMs now located on chip, allowed them to operate in an SRAM socket (P-SRAM, “P” stands for “Pseudo”)

## Slide 6: 2000-2005: Scaled Embedded Memory
Era of true embedded memory begins
100’s of millions of gates on a chip allows for a large portion of chips to contain memory that are functionally not a memory
Embedded memory has different characteristics than standalone memory:
  Wide on-chip buses + parallelism
  High-speed operation not as important
Commercial IP becomes equivalent of a memory standard

## Slide 7: The Product Perspective: Trends in SoC Design
Memory content in SoC increasing dramatically from year to year.
Memory either organized as large chunks of “hand optimized” blocks or smaller memories generated by compilers.
Re-used logic and memory blocks exceed number of newly designed functions
  Why? Designs are stable faster allowing device manufacturers to meet a faster market window

## Slide 8: Product Perspective: Trends in SoC Design
Notes: Now finding everything from large caches to small local storage. Can be optimized for speed, low power, etc.

## Slide 9: Advantages and Challenges To Embed Memories
Why embed all this memory?
If tailored properly you can achieve:
  Improved performance
  Lower power consumption
  On-demand memory activation / refined stand-by modes
  Higher bandwidth
  Package cost reduction and overall cost reduction
  Generalized form factor / board space advantages

## Slide 10: Advantages and Challenges To Embed Memories
BUT: Drawbacks vs. using multiple chips
  Increased development complexity
  Memories need to be area optimized
  Need new design methodologies
  Need new testing methodologies
  Higher mask cost
  Higher effort to ramp one complex product
  Decreased flexibility and extendibility
Notes: The real big challenge beomes how to partition the system and implement a cost-optimized solution in time

## Slide 11: Implementation of Embedded Memory Devices: A Case Study
Need to develop a communication device with the following requirements:
  Doubled Functionality
  30% Performance Gain Compared To Multi-Device Solution
  Power must be optimized so that the device still fits into its former package

## Slide 12: Implementation of Embedded Memory Devices: Case Study
Only solution was to embed all memory:
  Multi-chip failed: Off-chip driver for the larger memories absorbed 30% of power budget alone
  Need a customized floor plan where logic placement was optimized with respect to memory location.
  I.E. More than just sticking a big blob of SRAM on the chip somewhere

## Slide 13: Implementation of Embedded Memory Devices: Case Study

## Slide 14: Embedded Memory Test and Repair: Trends and Challenges
Today’s SoCs have moved from being logic-dominant to memory dominant
More memory needed for today’s memory hungry applications
Aggressive design of embedded memories leads to greater manufacturing and field reliability problems than any other part of the chip
Overall yield thus relies heavily on the memory yield, significantly affecting cost

## Slide 15: Embedded Memory Test and Repair: Trends and Challenges
Yield can be improved by offering redundancy in memories
Requires determining the adequate type and amount from memory design techniques and failure history
Further, need ability to detect where defects occur and knowledge of how to then incorporate redundant elements
Test and Repair
Power-Up Soft Repair

## Slide 16: Manufacturing Cost
Traditional approach of Test-and-Repair requires extensive equipment and can contribute as much as 40% of the overall manufacturing cost of a chip
Need to keep these costs down especially for high-volume consumer electronics or anything that is particularly cost-sensitive.

## Slide 17: Time-To-Volume
Time-To-Volume is the time it takes a design to become sufficiently mature such that it can be manufactured in high volume at lower cost
Dependent upon two factors:
  Initial SoC design time
    Re-use of proven IP cores
  Production ramp-up time
    Yield optimization: detect, analyze and correct problems

## Slide 18: Time-To-Volume
Time-to-market pressure may require a shortened ramp-up period
Can minimize TTV if yield optimization starts before ramp-up period
  Memory IP cores need to be tested in silicon and optimized beforehand to improve yield once incorporated into an SoC: “Silicon-Proven IP”
  Memory IP should already include all necessary diagnosis and failure analysis functions which can then be used during ramp-up
  Memory repair functions need to be designed together with the system as a whole to simplify the SoC ramp-up.

## Slide 19: Questions