## Slide 1: Comparative analysis of High Level Programming for Reconfigurable Computers: Methodology and Empirical Study
Wen-qian Wu
EEL 6935

## Slide 2: Contents
Reconfigurable Computing (RC) design flow
1
High level language (HLL) based design
2
Metrics of HLL and quantification
3
Experiment and result
4

## Slide 3: RC design flow
Reconfigurable Computing system takes the advantage Hardware (e.g. FPGA) acceleration
Two main mechanisms for acceleration:
  Loop unrolling and pipelining
Not all computations are fit for FPGA
  Control intensive application
  Floating point operations
  Data transfer overhead
RC system is naturally a hybrid system which consists both software and hardware
Programming SW in C/C++/Java, HW in VHDL/Verilog
HW and SW partitioning
Notes: HW/SW处可以加一副图！

## Slide 4: HDL OR C
HDL is not so friendly
  Ratio of VHDL to C developers 1: 10000
  Function is dependent on architecture, not portable
  Tedious, slow development cycle…
Most application developers are willing to give up some performance and chip utilization in exchange of productivity
High-level design tools are hence raised!

## Slide 5: High Level design flow
High level design flow
Describing HW using HLLs is possible, and has been tried in several commercial products, such as Xilinx Forge, Celoxica Handel-C, Impulse-C, Mitrion-C, DSPLogic, etc.
HDL
Netlist
Bitfile
Processor
FPGA
RT Synthesis
Physical Design
Technology Mapping
Placement
Routing
High-level Synthesis
C/C++, Java, Simulink, etc
Notes: Fig from RC!

## Slide 6: High Level Language (HLL)
Benefits of HLL
  Allow mathematicians and computer scientists to develop entire applications without relying on hardware designers.
  Substantially increase the productivity of the design process.
Challenges of HLL
  Able to compile high level description to HDL
  Mutually synchronization and data transfer between microprocessor and FPGA
  Facilitate HW and SW co-simulation and code reuse
This paper review 3 HLLs
  Impulse-C (C-based)
  Mitrion-C (C-based)
  DSPLogic (graphical-based)

## Slide 7: High Level Language (HLL) – cont.
Why choosing the 3 HLLs for studying
  1) Fully developed HLL tools with variable platform supporting.
  2) Each one wants to reach broader audience of potential RC users.
  3) Each one has different and distinct vision on how to realize its goal.
    Impulse-C: Imperative programming
    Mitrion-C: Functional programming
    DSPLogic: Schematic programming

## Slide 8: Impulse C
Translate C code to HDL
  A subset of ANSI C
  Pragma
  pipelining and scheduling features may
  be controlled at the level of your C
  source code through the use of certain
  predefined pragmas, like co pipeline,
  co unroll, etc.

## Slide 9: Impulse C
Built-in communication
  Separate processes are made
  for the SW (CPU) & HW (FPGA)
  Communication via co stream
  Synchronization via co signal
HW/SW co-simulation
  Test vector is generated automatically
  when performing C level simulation.
  The test vector is used for writing testbench for HDL
Notes: According to the previous presentations, HW/SW partitioning is at task level and can be performed dynamically. But when using HLL, the partitioning is at process level and as a designer, you must keep in mind that which process can take the advantage of HW acceleration and tag that process as HW process.

## Slide 10: Mitrion C
Mitrion-C programming language is an implicitly parallel with syntax similar to C
Focus on parallelism and data-dependencies.
  Any operation may be executed as soon as its data dependencies are fulfilled.
Software written in the Mitrion-C language is compiled into a configuration of Mitrion Virtual Processor (MVP)
  MVP is a fine-grain, massively parallel, reconfigurable soft processor.
The configuration of MVP will be downloaded to FPGA.

## Slide 11: Mitrion C
Mitrion-C programming flow:

## Slide 12: DSPLogic
DSPLogic provides RC toolbox
  Offers a graphical (as well as text based) programming environment
  Based on Xilinx System Generator for DSP package.
Enable the use of MATLAB/Simulink package
Blocks both from RC toolbox and Xilinx System Generator are used to create a Data Flow Graph.
Notes: Try to find a graph…

## Slide 13: HLL Metrics
How to evaluate HLL?
  Metrics: easy-of-use, efficiency
Easy-of-use
  In terms of total acquisition time + total development time
  Acquisition time is dependent on the type of paradigm being adopted
  Development time depends on both the paradigm and the application being developed
  Also affected by programming model explicitness
    The more explicit the programming model is, the more architectural details needs to be handled, the longer for both acquisition time and development time will be
  User/developer previous experience also needs to be considered
Notes: In RC application, programming model typically determines whether the programmer can control data transfers between the FPGA and the onboard memory, the FPGA and the microprocessor memory, and the FPGA and the microprocessor.

## Slide 14: HLL Metrics
Efficiency
  Ability to extract the maximum possible parallelism/performance with the lowest cost
  In terms of end-to-end throughput, maximum achievable frequency and resource usage
  Again, the user/developer experience should be taken into consideration

## Slide 15: Quantification
Easy-of-use
  Average ease-of-use factor:
is the average acquisition time of a reference language (usually VHDL)
is the difference of acquisition time between reference language and one HLL
Assumption: the number of user included in the experiment, the number of applications considered, the number of language for each paradigm and the number of platform being used as testbed should be as large as possible to achieve accurate result.

## Slide 16: Quantification
Efficiency
  Average efficiency factor of language x relative to a reference language, e.g. VHDL
Average ease-of-use factor ranges from 0 to 1
  0 represents a language which is most difficult to use like VHDL
  1 represents the easiest-to-use language
Similarly, average efficiency factor ranges from 0 to 1
  0 represents least efficient language
  1 represents most efficient language like VHDL

## Slide 17: Applications
4 workload were selected for implementation on Cray-XD1
  Pass-through
    Reads input data from the uP and sends it back.
    Purpose: measure the overhead of each HLL by the simplest application
  Discrete wavelet transform (DWT)
  Data encryption standard (DES) algorithm
  DES breaking

## Slide 18: Cray-XD1 platform
General structure of the XD1:
  One chassis houses 6 compute cards
  Cards are connected via RapidArray
  switch fabric
  2 AMD Opteron uP, 2 RapidArry
  proceesor and 1 FPGA accelerator
  on each compute card
XD1 development flow

## Slide 19: Result 1
Easy-of-use in terms of acquisition time

## Slide 20: Result 2
Efficiency and development time

## Slide 21: Result 3
Tools Efficiency vs. Easy-of-use

## Slide 22: Result 3 – cont.
Tools Efficiency vs. Easy-of-use

## Slide 23: Conclusions
A formal methodology and framework is established to evaluate different high level programming paradigms for RC application
The metrics we devised were easy-of-use, and efficiency of generating hardware characterized by high throughput at the lowest cost of resource usage
Encouraging:
  preliminary results achieved by HLL are close to manual HDL
  The SW to HW porting becomes considerably easier and more efficient with every new release
Lesson learned:
  Optimized hardware is not the same as software optimization
  Some hardware knowledge is still needed for performance optimization, for creating a new platform wrapper, etc.
  Debugging hardware is another major problem. Tracing is difficult since the internal VHDL signals are unknown.

## Slide 24
Thank You !
Questions?

## Slide 25: Reference
[1] W. Luk, N. Shirazi, and P.Y.K. Cheung, Compilation Tools for Run-time Reconfigurable Designs, IEEE symposium on Field-Programmable Custom Computing Machines, FCCM 1997; 56-65
[2] K. Comptoon, S. Hauck, Reconfigurable Computing: A survey of Systems and Software, ACM Computing Surveys 34 (2) (2002) 171-210
Impulse C – “Impulse Accelerated Technologies” website available at http://www.impulsec.com/
Mitrion website available at http://www.mitrion.com
DSPLogic website available at http://www,dsplogic.com
Crat website available at http://www.cray.com