## Slide 1: Execution Context Optimization for Disk Energy
Jerry Hom
Ulrich Kremer
Subramanian Srinivasan
Mahesh Sukumar
Notes: There are several reasons why power consumption is an area of concern for PC users.
The first is that the amount of power needed by the hard disks must be provided for when specifying the power supply (although modern systems with one hard disk don't generally need to worry about this).
The second is that the start-up power requirements of hard disks exceed their normal requirements and must be given special consideration in systems with multiple storage drives.
The third is that more power consumption, all else being equal, equates to more heat dissipated by the drive.
The final one is environmental: the trend is towards systems that use less power just for the sake of using less power!

## Slide 2: Introduction
Power, energy and thermal concerns have constrained embedded system designs.
In many mobile systems, the disk/memory is among the top energy consumers.
Notes: One important hurdle continues to block the widespread acceptance of these miniature hard disks in mobile devices: power consumption.
Recent studies have demonstrated that a small form-factor disk, such as the IBM Microdrive, may consume 5-10 times more power than its Flash memory counterparts
Self-Monitoring, Analysis, and Reporting Technology, or S.M.A.R.T. (sometimes written as SMART), is a monitoring system for computer hard disks to detect and report on various indicators of reliability, in the hope of anticipating failures.

## Slide 3: Introduction (Contd.)
This paper introduces a framework to make programs aware of and adapt to their runtime execution context.
Although this research focuses on disk, the energy optimizations and analysis may be applied to other resources which support multiple low power operational modes for energy conservation.

## Slide 4: HDDs VS SSDs
Top Power and Energy consumers : System’s Display, Processor and Disk.
Flash memory: A serious contender in the mobile storage area, mainly for energy considerations.
Choice between HDDs and SSDs reduce to a product design trade-off for performance, energy and cost.
Example: Apple iPod classic
Notes: The iPod Classic (Costs $249 as of now compared to >$400 for just a 160GB SSD drive) which functions mainly as a media player, opts for disk storage up to 160 GB. Mobile phone platforms could feasibly use disk instead of Flash storage, combining general purpose computing with large capacity storage.

## Slide 5: Previous Optimizations
Many previous optimizations for disk energy have assumed Uni-Programming environments.
Not so practical! Let us see why….

## Slide 6: Uni-Programming problems
• CPU must wait for I/O instructions to complete before proceeding
• I/O instructions are very slow as compared to compute instructions

## Slide 7: Multi-Programming advantages
When one job waits for I/O, the processor can switch to another job (interleave I/O and computing.)
• Increased throughput
• Increased system utilization
Notes: Previous research for disk energy management have generally focused on uni-programming models of execution. Yet most general purpose systems actually use multi-programming to run multiple programs concurrently.
Operating systems use short time slices to give the illusion of simultaneous execution. The OS mediates among programs when they access various resources, such as the memory and network, giving the illusion of a virtual computing system.
The computing paradigm allows a programmer to develop a program without worrying about interference from other programs. In turn, compilers apply optimizations on a program without worrying about how they affect other programs.

## Slide 8: Multi-Programming

## Slide 9: Energy-Aware Compilers
An energy-aware compiler can reshape a program to enable and exploit idle periods.
Disk requests should be clustered to maximize idle time and provide opportunities for hibernating the disk.
The strategy works well in uni-programming but may lead to poor overall results in multi-programming.

## Slide 10: Hibernation
A physical resource can hibernate only when there are no queued requests for a sufficient amount of idle time.
Example:
Suppose two programs are accessing a resource. In the worst case, their accesses alternate such that the resource repeatedly wakes up and hibernates.
Notes: They would do better by adapting the hibernation policy threshold or coordinating their accesses. A limited notion of optimizing programs together was introduced to cluster disk requests.
Disk hibernation strategies calculate a hibernation or break-even threshold as a function of a disk's physical characteristics.

## Slide 11: Paper’s main theme
Explores the opportunities for disk energy optimizations in execution contexts.
Conducted a user study to gain insight into actual program usage profiles and serve as a guideline for optimization.
Usage profiles are modeled as a finite state machine where a state represents an execution context.
The opportunity for saving disk energy is closely associated with a particular execution context and the interaction between programs.
Notes: Execution Context: A set of running programs.
Transition: A transition between states means a program was started or exited.

## Slide 12: Paper’s contributions
A user study to identify program usage patterns, quantify the available opportunity for optimization, and provide evidence in support of execution context optimization.
Language extensions {STREAMED, BUFFERED, SYNC_RECV, SYNC_SEND} to categorize program disk request interactions.
Notes: Measured results from a Hitachi disk showed a range from -33% to 63% energy savings.

## Slide 13: Paper’s contributions (continued…)
A measurement and evaluation infrastructure using a compiler and runtime system approach to implement execution context optimizations. The infrastructure allows for repeatable, interactive experiments.
Physical measurements and evaluation of eight programs in ten execution contexts. An energy model estimates disk energy savings based on disk access patterns.

## Slide 14: Sample user session trace
Bold numbers indicate order of transitions.
Italic numbers indicate the time in seconds spent in that state.
Note that F is the start (42) and end (297) state.
Notes: The user started by launching Sftp (F), Firefox (W), and OpenOffice (O) in that order. After nearly three minutes in the execution context FWO, the user exited W and O in quick succession but remained in F for another five minutes before exiting. The popular states, FWO and F, dominate the overall active time and represent the opportunity.

## Slide 15: Benefits of execution contexts
Having opportunity is not enough. Realizing the benefits of execution context optimization depends on people's actual activity.
If a user is idle in any execution context, then maximum energy is saved without anything special. Hence, programs within an execution context may have large opportunities, but the benefits vary according to user activity.
Benefits are evaluated by examining a variety of common applications and their interactions within a diverse set of execution contexts.

## Slide 16: Opportunity
Most people do not keep large numbers of programs running due to resource constraints of the system such as memory.
The opportunities for execution context optimizations are inherent in the particular combination of programs.
Example:
Applications which access the disk sparingly, such as a calculator, will have little opportunity.
Conversely, streaming applications are characterized by periodic disk accesses and receive the greatest benefits from these optimizations.
We want to investigate how often these opportunities occur.

## Slide 17: Compiler Run-Time framework
File Descriptor Attributes
Synchronization mechanism
File-level buffer
Notes: The compiler aspect of our framework consists of new keywords in the form of file descriptor attributes.
The attributes categorize a program's disk requests, and the interaction of these requests across programs can be used to synchronize disk accesses.
The buffer enables clustering of disk requests within a program while synchronization clusters disk requests across programs.
All test programs are written in C and C++. OpenOffice and Firefox also have extra modules written in Java, but they were disabled.

## Slide 18: File Descriptor Attributes
A file descriptor may be tagged with one of four attributes:
SYNC_SEND, SYNC_RECV, BUFFERED, and STREAMED.
The keywords inform the compiler as to how the program intends to access the file and the level of interaction with other programs.
Notes: The SYNC_SEND attribute may be used by practically all programs which have any amount of disk activity. Participation in the synchronization protocol is optional but helpful to other applications. For example, a web browser can notify other programs about disk activity by sending a message after it has read from or written to its disk cache.
The SYNC_RECV attribute is special among the keywords because it needs extra code by the programmer to take full advantage. This attribute means a program can take useful action when receiving a synchronization message. For example, a text editor with auto-save may decide to save early, in combination with another program's disk access, when receiving a message.
The BUFFERED attribute is useful for programs which access large data files sequentially but not periodically in time. For example, a postscript document can be reasonably large, and a user may read through the document page by page. When the buffer's data is consumed, the buffer prefetches data to refill itself. Disk accesses are effectively clustered at buffer refill points.
The STREAMED attribute is useful for programs which also access large data les sequentially and do so periodically. Some streaming applications, such as audio and video, are also referred to as real-time, meaning that they try to meet minimum performance goals by skipping ahead if computation lags too much.

## Slide 19: Runtime
The compiler must determine where a program's logical I/O operation ends, but finding the end of a logical operation via static analysis is an un-decidable problem.
Notes: Synchronization points should be placed at the end of a logical I/O operation. Finding such points is an un-decidable problem.
If a loop iteration takes longer than the disk's hibernation threshold, then Case 1 is appropriate. If a loop iteration takes shorter, then a second attempt would look at the loop surrounding the I/O calls and then decide Case 2 would be better. Yet Case 2 misses the perspective that the loop may be enclosed within another loop.

## Slide 20: Setup and Implementation
Hardware
Software:
Optimization Stages
Notes: A Tektronix TDS3014 oscilloscope with a Hall effect current probe is attached to the wire supplying current to the disk. The host computer supplies power at a constant five volts; therefore, measuring the supply current readily translates into the disk's power consumption.
The Travelstar product line is commonly referred to as laptop class disks. They are designed for smaller form factors and better energy efficiency than desktop class disks. If we had tested on a desktop disk, energy savings from our techniques would have been even greater. Although our user study tracked program workloads on desktop machines, we expect to see similar workloads on laptops and emerging general purpose handheld systems.
The write cache has a choice of policies, write-through or write-back, to affect data safety and performance. The write-through policy uses synchronous writes meaning that data is written to disk immediately and ensures safety at the cost of performance. The write-back pol-
icy uses asynchronous writes by buffering data and flushing to disk only when necessary.

## Slide 21: Hardware
The host computer has an AMD Athlon processor at 1.2GHz with a default workstation installation of Red Hat 9 Linux.
The computer features a Hitachi Travelstar E7K60 as our target disk.

## Slide 22: Software
The software test suite includes interactive programs such as a web browser.
The key for such programs is user interaction such as clicking on a link or typing a web address.
Unfortunately, user interaction lends poorly toward repeatability for experiment testing .
Fortunately, the X Window System contains extensions, RECORD and XTEST.

## Slide 23: Optimization Stages
A Low Level Virtual Machine (LLVM) compiler infrastructure is used to implement code transformations in various passes.
Among its many features, LLVM extends gcc with a new intermediate representation, an analysis and optimization framework, and several back-ends including portable C.
Notes: Since LLVM can emit C source code, we preferred to perform source to source code transformations, then compile normally without changing the build system. However, this approach also limits our implementation for inter-procedural analysis. LLVM is designed to perform inter-procedural
analyses during the linking phase when all object code is available for inspection.

## Slide 24: Implementation steps for Optimization Stages
Notes: Stage 1 is used only for SYNC_SEND and SYNC_RECV attribute types.
Stage 2 can accept results from Stage 1 to mark synchronization points.
Stage 2 then inserts code to implement program synchronization, buffers, and disk profiling.

## Slide 25: Experiments
Investigate the energy and performance impact of execution context optimizations on disk accesses from concurrently running programs.
The experiments were devised by using Xnee to record a session and replay it repeatedly while measuring disk energy consumption.
Notes: GNU Xnee is a suite of programs that can record, replay and distribute user actions under the X11 environment. Think of it as a robot that can imitate the job you just did. GNU Xnee is licensed under GNU GPLv3

## Slide 26: Results
The experiments show that with mostly interactive programs such as WP (firefox, xpdf), the opportunity for energy savings is small. Conversely, streaming programs such as AF (mpeg123, sftp) offer plenty of opportunity for savings.
Some contexts have moderate opportunity for savings, such as AWT (mpeg123, firefox, emacs), though the actual activity did not demonstrate all of the potential savings.
Notes: W->Web Browser (firefox)
P ->PDF Viewer (xpdf)
A ->Audio player (mpeg123)
F ->(s)FTP Client (sftp)
T ->Text Editor (Emacs)

## Slide 27: Results (continued …)
Using the write-through policy, the average savings was 21% with a range of 3% to 63%. Using the write-back policy, the average savings was 8% with a range of -33% to 61%.
Notes: The write cache has a choice of policies, write-through or write-back, to affect data safety and performance. The write-through policy uses synchronous writes meaning that data is written to disk immediately and ensures safety at the cost of performance. The write-back policy uses asynchronous writes by buffering data and flushing to disk only when necessary.
The negative results under the write-back policy are due to the write semantics our techniques employ.

## Slide 28: Energy Model
Notes: Our optimizations save disk energy via two forms of clustered disk accesses. User level file buffers cluster accesses from each program while synchronization clusters accesses across multiple programs. Both forms appear identical to the physical disk and are modeled as operational power
modes over time.
Intuitively, the energy savings comes from eliminating wakeup (E >) and hibernate (E <) transitions and combining the active periods together.
Energy saved is proportional to the transition costs of a given disk. Laptop class and smaller disks are designed for fast transitions with lower energy costs then desktop or server class disks.

## Slide 29: Summary
A disk request classification system in the context of a compiler and runtime framework to implement optimizations for disk energy consumption was introduced.
The measured energy savings are in proportion to the opportunities available (up to 63%) and can be substantially greater over previous best optimizations.
The overhead from these optimizations impacts performance by less than 1%.
Lastly, simple model to estimate energy savings was formulated based on a disk's specifications, a disk access profile, and expected program interactions.

## Slide 30: Future Work
Our user study does not delve deeply enough to characterize user activity and formulate representative traces. A more detailed user study is a monumental task left for future work.

## Slide 31: Questions …