## Slide 1: Software / Hardware Partitioning Techniques
SHaPES: A New Approach

## Slide 2: Background
The allocation of a system’s functionality into hardware and software components has a significant impact on total system cost.
Partitioning algorithms usually target one of the following types of systems:
  Single-processor, single-ASIC (or FPGA) SOC
  Multiple processing element (PE), distributed heterogeneous system

## Slide 3: Background
The three main sub-problems that must be solved when determining the hardware-software partitioning of a system:
  Functional Clustering – cluster system functionality into a set of tasks
  Allocation – allocate a task to either hardware or software
  Scheduling – schedule tasks to ensure correct timing
These problems are independent

## Slide 4: Background
These are hard problems!
  Allocation and scheduling are NP-hard
  There’s an exponential number of different possible clusters
Huh?
  NP-hard means superpolynomial time (e.g. O(2^N))
  We’ll have to use a heuristics based approach if we want to get a solution in our lifetime

## Slide 5: Background
Heuristic-based solutions have their own problems
  Random Search: takes a long time
  Iterative Improvement: quality of final solution proportional to quality of initial revision
  Constructive: yields good solutions, good execution time, etc., but scheduling is a bi-product, not the main focus.

## Slide 6: Who you gonna call?
SHaPES
“Software-Hardware Partitioning For Embedded Systems”

## Slide 7: Formulating The Problem
This approach assumes a single microprocessor and single ASIC SOC as the target platform
Looks at the partitioning problem as a real-time scheduling problem… we’re scheduling a set of periodic and sporadic tasks
Tasks are implemented either completely in hardware or software

## Slide 8: Formulating The Problem
Implementation Costs We Care About:
  Hardware Area
  Power Consumption
  Timing Constraints
But, a scheduling problem can’t model size and power constraints!

## Slide 9: Formulating The Problem
Hard-timing constraints modeled as follows:
  Processing Time (pj): How long it takes a task to execute on the microprocessor uninterupted
  Release Time (rj): The earliest moment as which a task can begin execution
  Deadline (dj): The time by which the task should be completed
  Weight (wj): The importance of a task

## Slide 10: Formulating The Problem
Under this model, all tasks start out initially in software. Rejecting a task implies it should be implemented in hardware.
Since hardware is always assumed to be fast-enough for a task, you could cheat and reject all tasks, but that’s not realistic

## Slide 11: Formulating The Problem
Violations are modeled as “costs;” the further past the deadline a task completes and the higher the weight of the task, the higher the penalty
Delegating a task to hardware is also modeled as a cost, called the “rejection cost,” represented by ej

## Slide 12: Formulating The Problem
Thus, the crux of the problem is:
Partition the set of tasks such that the sum of costs incurred by overtime software tasks and the rejection costs incurred by implementing a task in hardware are minimized

## Slide 13: Formulating The Problem
But, sometimes a task has to wait around for other tasks to complete before they can start!
These dependencies are accounted for and are referred to as “precedence constraints” in the paper.

## Slide 14: Solving The Scheduling Problem
Scheduling a set of jobs to minimize overall tardiness is an old problem (older than you)
Some simple approaches are:
  Earliest Due Date (EDD)
  Shortest Processing Time First (SPT)
This paper, however, uses ATC or Apparent Tardiness Cost

## Slide 15: Solving The Scheduling Problem
Tasks are scheduled in non-increasing priority with priority defined as:

## Slide 16: Solving The Scheduling Problem
Note that the formula includes the processing time of the subsequent task
Thus, that value is replaced with kp, where p is the average execution time, and k is a look-ahead factor whose value depends on how many tasks are completing late.

## Slide 17: Solving The Scheduling Problem
ATC dispatching is basically a proportion of the weight to the execution time, scaled by how much time you still have to schedule the task
Thus, the priority of a task increases the closer you are to its deadline
Good News: The algorithm still works pretty well even if your processing time estimates contain errors (but that’s another paper)

## Slide 18: Dealing With Idleness
Basic Idea: ATC designates a task that should be run next, but its release time has not yet been reached. The system will have to sit idle until that time is reached.
Solution: Scale the priority of a task proportional to this idleness:

## Slide 19: Rubber Hits The Road
Start with all tasks initially in software partition
At a given time t, take the task with the largest ATC
Multiply its weight by its tardiness (completion time – deadline)
If the above cost is greater than its rejection cost, reject it to hardware and pick another task

## Slide 20: Rubber Hits The Road
Repeat this until you have an ordered set of software tasks, and a set of tasks that have been rejected to hardware.
Re-run the algorithm for the hardware tasks with appropriate processing times.
If you have no rejected hardware tasks, you’re done!
If you do have rejected hardware tasks, you need to pick different hardware and start over.

## Slide 21: Questions