## Slide 1: Comparing Three Heuristic Search Methods for Functional Partitioning in Hardware-Software Codesign
Theerayod Wiangtong, Peter Y. K. Cheung and Wayne Luk
Presented by: Wei Zang
Mar.17, 2010

## Slide 2: Outline
Introduction of HW/SW partitioning
Heuristic Search Methods
  Genetic algorithm
  Simulated annealing
  Tabu search
Processing time – System cost
Experiment results
Conclusions

## Slide 3: Outline
Introduction of HW/SW partitioning
Heuristic Search Methods
  Genetic algorithm
  Simulated annealing
  Tabu search
Processing time – System cost
Experiment results
Conclusions

## Slide 4: Introduction of HW/SW partitioning
Common case
  Implement performance critical code in FPGA
  Implement everything else on microprocessors
Definition
  Given an application, hw/sw partitioning maps each region of the application onto hardware (custom circuits) or software (microprocessors) under design constraints
Possible Goals
  Meet design constraints (performance, power, size, cost, etc.)
  Maximize performance
  Minimize power for a given performance constraint
Exploration searches partition space for a optimal partition
  NP complete/NP hard(Reconfigurable hardware) problem
  Heuristic method to generate near-optimal solution

## Slide 5: Outline
Introduction of HW/SW partitioning
Heuristic Search Methods
  Genetic algorithm
  Simulated annealing
  Tabu search
Processing time – System cost
Experiment results
Conclusions

## Slide 6: Genetic Algorithm
Based on Darwinian natural evaluation and selection. Solve optimization problems (Video)
Four main operations:
  Evaluation
    Use fitness function
  Selection
    Select the parents to breed a new generation
    Features in parents represented by chromosome, made by genes. Each capture a desirable features
  Crossover
    Randomly divide each parents chronmosome into two sets of geanes and then mix them – help to transmit good features into next generation
  Mutation
    Occasionally modify a gene
    To avoid being trapped in local minima

## Slide 7
The number of genes in a chromosome of each individual is equal to the number of tasks or functional blocks
A gene is encoded as “0” if the task is implemented in software; “1” if it is mapped to hardware
Begin
Get input parameters:
pop size, # generations
Initialize population
Reach # of desired generations
Evaluation
Cal cost fun and fitness fun
Selection
Crossover
Mutation
End

## Slide 8
Fitness function
  Define the cost of the number:
  Fitness
Crossover
  Two surviving parents generate two children to maintain population size
Mutation
  Randomly flipping individual bits in the child chromosome with a small probability value(less than 0.01)

## Slide 9: Simulated Annealing
Search feasible solutions in optimization problems (video)
Can avoid being trapped in local minima
  Hill-climbing algorithm always choose the best solution in the neighborhood, miss better solution further away
  SA accepts an inferior solution in the neighborhood according to an acceptance probability function
Annealing process
  The acceptance probability function is set high at the beginning
  Gradually reduced to zero
Cooling schedule
  Predefined threshold, a solution is arrived
  Too fast, algorithm stop early at some local minimum
  Too slow, algorithm jump more or less randomly for a long time before settling to a solution

## Slide 10
Dcost < 0?
Generate a neighboring solution (Sneigh) randomly
Compare diff of cost function
Dcost = cost(Sneigh)–cost(Snow)
Snow=Sneigh
Update temp use cooling schedule
Meet terminating condition?
End
q= random(0,1)
q<exp
(-Dcost/T)?
Cooling schedule
Neighborhood search: randomly changing one state bit in the solution (and obey the area constraint)
Cost is a direct function of processing time
Acceptance probability for a more costly neighboring solution:
Loop terminate when
  New temperature reaches Tstop
  No improvement over the last 500 iterations.
Begin
Get input parameters:
Tstart, Tstop, area constraint
Initialized solution (Snow)

## Slide 11: Outline
Introduction of HW/SW partitioning
Heuristic Search Methods
  Genetic algorithm
  Simulated annealing
  Tabu search
Processing time – System cost
Experiment results
Conclusions

## Slide 12: Reference architecture
Timing model
  Communication time
  Execution time on HW/SW
  Configuration time if reconfigurable HW
    Only consider ASIC or FPGA without reconfiguration (all hardware tasks are bounded to on-chip hardware)
Execution on SW & HW
  SW processor can execute only one task at a time
  HW can execute multiple tasks concurrently;
  HW and SW can work in parallel
Transmit data between tasks can only use read or write shared or local memory
  Memory acts like a medium; Prevent loss of data while waiting
Bus conflicts -> waiting time
  SW tasks have higher priority in using shared bus since hardware is generally faster
  One has the minimum use of bus is allocated first
shbus
Software processor
Hardware ASIC/FPGA
Shared memory
Local
memory
Shared memory
swbus
hwbus

## Slide 13: Example
Processing time: Sum the worst-case time at each precedence level

## Slide 14: Outline
Introduction of HW/SW partitioning
Heuristic Search Methods
  Genetic algorithm
  Simulated annealing
  Tabu search
Processing time – System cost
Experiment results
Conclusions

## Slide 15: Experimental setting
Input parameters for each algorithm are carefully selected by several pre-simulations to get the most promising value
Test on randomly generated task graphs with a uniform distribution and commonly encountered structures
Parameters used

## Slide 16: Experimental results
TS provide the shortest processing time and the lowest search time
SA is better than GA in most cases

## Slide 17: Outline
Introduction of HW/SW partitioning
Heuristic Search Methods
  Genetic algorithm
  Simulated annealing
  Tabu search
Processing time – System cost
Experiment results
Conclusions

## Slide 18: Conclusions
Combines HW/SW partitioning and scheduling to minimize processing time
Compare three popular optimization algorithms
  Genetic algorithm – demands more memory to stoe information of large number of solutions
  Simulated annealing – better than GA in most cases; more memory efficient
  Tabu search – provides higher quality results in shorter time than both GA and SA; more memory efficient
Future work
  Now only use simulated inputs in task graphs
  Need to be verified on real hardware-software systems by using realistic benchmarks