## Slide 1: Context-Aware Wireless Sensor Networks for Assisted Living and Residential Monitoring
Anthony D. Wood, John A. Stankovic, Gilles Virone, Leo Selavo, Zhimin He, Qiuhua Cao, Thao Doan, Yafeng Wu, Lei Fang, and Radu Stoleru
University of Virginia
Network, IEEE , vol.22, July-Aug. 2008
Presented By:
Sidhartha
Rahul

## Slide 2: Agenda
Need for assisted living environments
Introduction to AlarmNet
Contributions of AlarmNet
Related Work
Architecture
  Circadian Activity Rhythm
  SenQ
  Context Aware Power Management
  Dynamic Privacy Management

## Slide 3: Need for Assisted Living Systems
Aging Population
Rising cost of medical care
Shortage of full time medical professionals
Expense of high end of medical devices
Human Error in collecting data

## Slide 4: Introduction
Key features of AlarmNet
  a novel system for assisted living and residential monitoring
  Two-way flow of data and analysis between the front and back-ends to enable context-aware protocols
  Circadian Activity Rhythm analysis
  SenQ query protocol
  Context-aware power management
  Dynamic privacy policies

## Slide 5: Contributions: AlarmNet
Extensible heterogeneous network middleware
  Addresses challenges of ad hoc wide scale deployment
  Integrates embedded devices, back-end systems, online analysis, user interfaces
SenQ query protocol
  Efficiently streaming online sensor data to system and users
Context-aware protocols using two-way network information flow
  Environmental, system, resident data flow into the back-end
  Circadian activity rhythm (CAR) analysis feeds back into the system to enable smart power management
  Dynamic alert-driven privacy tailored to an individual’s activity patterns

## Slide 6: Related Work
University of Rochester’s Smart Medical Home
  Five-room lab outfitted with infrared sensors, computers, biosensors, and video cameras
MIT’s PlaceLab
  One bed-room condominium fixed with sensors
Code-Blue at Harvard
  Pre-hospital and in-hospital emergency care and disaster response
AlarmNet combines the ubiquitous sensing of PlaceLab with the medical focus of CodeBlue
  An assisted-living context where long-term behavior and pathologies are learned

## Slide 7: The AlarmNet Architecture
Heterogeneous devices in a common system-level architecture
  Mobile body networks
  Emplaced sensors
  AlarmGate applications
  Back-end programs
  User interfaces

## Slide 8: Circadian Activity Rhythms
Measures rhythmic behavioral activity of residents and detects changes within these patterns
Supports context-aware protocols based on learned activity patterns
  Smart heterogeneous power management
  Dynamic alarm-drive privacy
Graphs provide information about activity patterns
  Sleep-wake cycle
  Medical hints about ADLs of the resident
Any Statistically significant deviations from learned patterns are displayed as alerts in the GUI and sent to the AlarmGate application

## Slide 9: Circadian Activity Rhythms

## Slide 10: Query Management: SenQ
Multilayer embedded query system
Enables user-driven and peer-to-peer in-network query issue by wearable interfaces
Streaming queries and Snapshot queries
Spatial and temporal aggregation and filtering to reduce the energy consumed by communication

## Slide 11: Query Management
SenQ to support query management and meet requirements
  Reconfigurable in-network sensing and processing
  Dynamic query origination by embedded devices
  High-level abstraction for expressing queries
Queries uniquely identified by <source ID, query ID> tuples
Nodes register with nearest gateway upon powerup
  Provide device type, sensors and h/w ID
  Assigned dynamic network ID
Query Manager main point of
access for user interface
  Translates between higher-level
  query abstractions and SenQ
  protocol
Dynamic semantic binding

## Slide 12: Context Aware Power Management
CAPM dynamically chooses power management operations to provide good sensing service with less energy
  Based on administrator directives
  Rely on context awareness
Triggers power management
operations when condition of
context policy met
Priorities used to rank importance
of commands
Context-aware power manager in
Alarm-Gate application core of
CAPM
  Outputs - Set of power management commands for each sensor device in AlarmNet

## Slide 13: Dynamic Context-Aware Privacy
Framework to protect privacy & still support timely assistance to residents
  Dynamically adjustable to context
  Allows data access authorization
  to be evaluated at runtime
  Adaptable to emergencies
Privacy policies at different levels
of granularity
Privacy management framework
three functional components
  Context Manager
  Request Authorizer
  Auditor

## Slide 14: Conclusions
AlarmNet - A wireless sensor network system designed for long-term health monitoring in assisted living environments
System operation adapts to the individual context and behavior patterns of the residents
Feed back to influence power management and privacy policy enforcement
System supports a diverse collection of sensors, user interfaces, and power and privacy policies