## Slide 1: Attacks and Defenses of Wireless Sensor Networks
Jason Li
Jeremy Fowers

## Slide 2: Agenda
Background Information
Wireless sensor network characteristics
General sensor network security mechanisms
DoS attacks and defenses
  Physical layer
  Link/MAC layer
  Network layer
  Transport layer
  Application layer
Questions

## Slide 3: Denial-of-Service in Wireless Sensor Networks: Attacks and Defenses
David R. Raymond, Scott F. Midkiff
Virginia Tech University
Raymond, D.R.; Midkiff, S.F.; , “Denial-of-Service in Wireless Sensor Networks: Attacks and Defenses,” Pervasive Computing, IEEE, vol. 7, no. 1, pp. 74-81, Jan.-March 2008

## Slide 4: Background Information
Expansion of WSN applications highlight the need for better security
  Medical monitoring
  Homeland security
  Industrial automation
  Military applications
Computer and network security aim to provide
  Confidentiality: prevent unauthorized access
  Data integrity: communications are unaltered and not repeated
  Service availability: authorized parties can access on request

## Slide 5: Denial of Service (DoS)
DoS attacks target service availability
  Problematic for many network types
  Prevents communication between devices
  Disables a targeted device
Denial-of-sleep
  Specific to energy-constrained embedded systems
  Motes commonly sleep their power-hungry radios
  Attacks force radios to remain active
  Can reduce battery life by orders of magnitude

## Slide 6: WSN Characteristics
Weaknesses of WSNs
  Limited processing capability and memory
  Inability to secure wireless medium
  Sensors are vulnerable to physical tampering
  Face attackers who aren’t limited by resources
  Limited and often non-replenishable power supplies

## Slide 7: General Security Mechanisms
Security Protocols for Sensor Networks
TinySec
IEEE 802.15.4 or ZigBee specifications

## Slide 8: Security Protocols for Sensor Networks (SPINS)
Characteristics of SPINS
  Broadcast authentication
  Two-party authentication
  Data confidentiality
Symmetric vs. public-key cryptography
  Uses shorter encryption keys and requires less computation
  Data freshness for unicast messages
    Antireplay counters are incremented when packet is sent or received
    Transmits a calculated message authentication code
    Packet drops if authentication fails and requires expensive recovery
    Unrealistic for memory-constrained sensor nodes

## Slide 9: TinySec
TinySec characteristics
  Packet authentication and encryption
  Included in TinyOS version 1.1
  Low overhead
    Authentication increases per packet power consumption by only 3 percent
    Encryption increases per packet power consumption by only 10 percent
  Supports network-wide, cluster-wide, pair-wise encryption keys
Limitations
  Doesn’t protect against message replay
  No specific protection against resource consumption attacks

## Slide 10: ZigBee
Details physical and MAC layer requirements for wireless radios
Provides hardware support for data confidentiality by use of AES encryption
Advanced Encryption Standard
  State-of-the-art symmetric cryptography protocol
  Access control
  Data encryption
  Packet authentication
  Optional antireplay counters
Attacks on ZigBee
  Same-nonce attack1 to break confidentiality by using same encryption key

## Slide 11: DoS attacks and defenses
We restrict the Open System Interconnect model down to 5 layers from 7
  Physical layer
  Link/MAC layer
  Network layer
  Transport layer
  Application layer
Analyze each for attacks and potential defenses

## Slide 12: Physical Layer - Jamming
Jamming-primary physical attack
  Constant: high power, random noise
  Deceptive: high power, sends byte traffic
  Random: low power, sleeps to save energy
  Reactive: low power, jams in response to traffic
Problem: simple radios have limited spectrum
  Cannot use classic spread-spectrum technique
Defense: detect and sleep
  Secondary defense: detect and reroute

## Slide 13: Physical Layer – Tampering
Physical attack on the node itself
Problem: nodes often deployed in unsecured areas
No way to prevent for sure, defenses include:
  Camouflage
  Tamper-proof packaging
  Redundant nodes
  Tamper reaction (fire safe)

## Slide 14: Link Layer Attacks
Attack MAC protocols operating the link layer
  Collision: identical to jamming
  Interrogation: constantly request-to-send
  Packet replay: record legitimate traffic and replay
Problem: Very susceptible to DoS because MAC controls power-hungry radio HW
  Reduces battery life by orders of magnitude

## Slide 15: Link Layer Defenses
Link-layer authentication
  Ensure communication with trusted parties
  Problem: replaying trusted communication
Antireplay support
  Ensure packets are only sent and received once
  Problem: checking for replays still uses energy
Jamming detection
  Sleep to counter stream of replayed messages

## Slide 16: Network Layer Attacks
Attack the routing protocol between nodes
Hello flooding
  Nodes send “hello” to one-hop network
  Attacker replays “hello” with high power antenna, creates false one-hop network
  Doesn’t require encryption breaking
  Defense: pairwise authentication, geographic routing (both very expensive)

## Slide 17: Network Layer Attacks cont.
Head node volunteering
  Nodes cluster to save power, use one head node
  Attacker volunteers to be head node, drops packets
  Defense: None suitable for embedded so far

## Slide 18: Network Layer Attacks Cont.
Homing Attacks
  Analyze traffic for special nodes (cluster heads, key managers)
  DoS special nodes to shut down entire network
  Defense: header encryption, dummy packets (obscure network traffic)
Black Hole Attack
  Become part of many routes, drop all packets
  Defense: authentication, antireplay

## Slide 19: Transport Layer
TCP manages end-to-end connections
  Uses memory to store state information
Flooding attack
  Open many connections to overflow state buffer
  Defense: SYN cookies (client maintains state)
Desynchronization attack
  Sends bogus sequence numbers or controls flags
  Defense: authentication

## Slide 20: Application Layer
Attack by sending large amounts of stimuli
  Applications are controlled by stimuli
    i.e. send alert for motion detection
  Causes large amounts of network traffic
  Defense: filter data alerts, limit alert rate
Network-programming attack
  Nodes can be reprogrammed in the field
  Attack by sending false program
  Defense: break program into parts, each part has hash of next part

## Slide 21: Application Layer cont.
Path-Based DoS
  Forward packets all the way to base station
  Use network bandwidth, node energy
  Defense: authentication and antireplay

## Slide 22: Conclusion
Encryption and authentication defend against many attacks
  Jamming detection also necessary
Low overhead antireplay protocol needed
Denial of Sleep attack must be taken seriously
Any questions?