## Slide 1: Icap Controller for high-reliable internal scrubbing
Quinn Martin
Steven Fingulin

## Slide 2: Motivation
Field-programmable gate arrays (FPGAs) perform well in space
  Low non-recurring engineering (NRE) costs compared to application-specific IC (ASIC)
  Good performance per watt compared to microprocessor
  Reconfigurability
However, they are susceptible to radiation effects
  Generally more susceptible than ASIC
  Can cause unpredictable behavior or system failure
Therefore, want develop efficient ways to improve reliability of FPGA-based systems in space

## Slide 3: Radiation Effects on Electronics
Single event effects – trapped protons and heavy ions in space/upper atmosphere can affect electronic operation when they encounter device
  Single event latchup (SEL) – Event that causes a certain overcurrent condition that can permanently damage device
  Single even upset (SEU) – Event that results in the change of a flip-flop value
  Single event transient (SET) – Event that results in a pulse through the circuit. If latched, becomes an SEU.
  Single event functional interrupt (SEFI) –
  Event that results in interruption of basic
  device function. Usually requires a full
  reset to repair.

## Slide 4: Field-Programmable Gate Arrays
Reconfigurable field-programmable gate arrays (FPGAs) provide a fabric that can be used to implement arbitrary digital logic
Configuration (logic and routing information) is stored in SRAM cells
SRAM is highly susceptible to SEUs
Some radiation-hardened FPGAs are available, but cost up to 100x more than equivalent commercial off-the-shelf (COTS) part

## Slide 5: Configuration Memory Scrubbing
Scrubbing corrects SEUs in configuration memory
  Takes advantage of reconfigurability of FPGA to repair upsets quickly after the occur
  Uses redundant configuration data
Scrubbing can not correct user flip-flop values or SETs
  Must use other fault-tolerant techniques like triple-modular redundancy (TMR) or algorithm-based fault tolerance (ABFT)
Two main scrubbing strategies
  Blind scrubbing: Write over all configuration memory periodically or continuously with a “golden copy” stored externally
  Readback scrubbing: Read the configuration memory and only correct when upset detected
    Detection commonly done using Cyclic Redundancy Check (CRC) or Hamming error correction code

## Slide 6: Internal vs. External Implementation
External scrubbing
  Traditional method of scrubbing the FPGA uses an external, usually radiation-hardened, microcontroller or one-time-programmable (OTP) FPGA
Internal scrubbing
  Takes advantage of internal configuration access port (ICAP) to implement the scrubbing controller in the FPGA fabric

## Slide 7: Internal Configuration Access Port (ICAP)
Internal Configuration Access Port (ICAP) provides direct access to FPGA configuration data from user logic designs
Built into Virtex-II and above FPGAs from Xilinx
Can be used to partially reconfigure the device
Uses the SelectMAP interface
  A parallel interface to the configuration logic
  Gives access to special device registers
  Allows addressing of individual configuration
  frames (sets of 41 32-byte words) for read or
  write

## Slide 8: FRAME_ECC Primitive
Fixed logic primitive built into Virtex-4 and above
Works in conjunction with 12-bit single error correction, double error detection (SECDED) Hamming code stored in the frame during configuration
Calculates error syndrome on frame data that is read back through ICAP
Readback and repair must be done in user logic

## Slide 9: PicoBlaze Processor
Used in this system to handle control of the scrubber (Figure 5)
  Performs “run” scan until it detects an error
  Then performs “walk” to correct the error
A small 8-bit processor
Fetches instructions and data from a small block RAM (BRAM) on the FPGA

## Slide 10: High Reliability Scrubber
Internal ICAP scrubber is susceptible to SEUs
  Upset could jeopardize device configuration
Two methods to make scrubber more reliable
  Triple Modular Redundancy (TMR)
  BRAM scrubbing

## Slide 11: Triple Modular Redundancy (TMR)
Triplicate each component and use voting to verify correct operation
  Two of the three modules would need to be corrupt to give incorrect output
Feedback TMR
  Uses voters on the feedback loops within the circuit
  Reduces number of single points of failure
BL-TMR tools used to apply TMR
  ICAP, Frame ECC, PicoBlaze program BRAM not triplicated due to resources

## Slide 12: Block Memory Scrubbing
BRAM contents change during operation so BRAMs cannot be scrubbed with “golden” copy
Three types of BRAMs in design
  PicoBlaze processor’s stack, scrath pad, store, and register memory
  DMA BRAM
  PicoBlaze program BRAM
BRAM scrubber algorithm
  Data at address AddrB is read from each of three BRAMs using second data port
  Data is voted on then sent as dataIn back to each BRAM
  If an error is found, then WEB (write enable) is set
  Address is incremented, repeat

## Slide 13: Radiation Test
Goals
  Demonstrate a working scrubber in an environment where upsets are present
  Determine amount of reliability provided by TMR and memory scrubbing
  Identify ways of improving reliability and on-line functionality of the circuit
Avnet Virtex-4 LX-25 evaluation board
  Aluminum shield protects components other than FPGA
UART cable connects host PC to PicoBlaze processor for status information
Two designs used
  First design used internal scrubber circuit, but no TMR
  Second design did make use of TMR
    TMR design did not triplicate clock or UART

## Slide 14: Radiation Test
The test program consisted of:
  PicoBlaze detecting and correcting errors
  UART communication
  Read/Write configuration registers
  Transmit BRAM data to host computer
One inch aluminum shield protects all of the board except FPGA
Proton beam set to 63 MeV

## Slide 15: Results
Average of 24.75 Multiple Bit Upsets (MBUs) per failure for design two (TMR protected)
Average of 10.68 MBUs per failure for design one (no TMR)
1.7% of all upsets were MBUs
Types of failures:
  Program crash
  Invalid response from UART
  Repeat FAR (Frame Address Register) and/or syndrome values/sets of values
  Failure during reconfiguration
  Errors present at end of test
45.45% of tests on TMR design failed
74.19% of tests on design without TMR failed

## Slide 16: Results and Conclusions
TMR design was 3.6x less likely to fail than unmitigated design
TMR design also tolerated more MBUs
Single points of failure introduced at UART and communication points
Able to detect, but not fix MBUs
Future work will reduce amount of single points of failure and attempt to correct multiple bits within a frame