## Slide 1: Ground Target Following for Unmanned Aerial Vehicles
Jason Li
Jeremy Fowers

## Slide 2: Agenda
Introduction
Hardware Configuration
Software Configuration
Vision-Based Ground Target Following
  Target Detection
  Image Tracking
  Target Following Control
Experimental Results
Questions

## Slide 3: A Robust Real-time Embedded Vision System on an Unmanned Rotorcraft for Ground Target Following
Feng Lin, Xiangxu Dong, Ben Chen, Kai-Yew Lum, Tong Lee
National University of Singapore
Lin, F.; Dong, X.; Chen, B. M.; Lum, K.-Y.; Lee, T. H.; , "A Robust Real-Time Embedded Vision System on an Unmanned Rotorcraft for Ground Target Following," Industrial Electronics, IEEE Transactions on , vol.59, no.2, pp.1038-1049, Feb. 2012

## Slide 4: Introduction
Increasing interest in UAVs
  Industrial surveillance
  Agriculture
  Defense and security
Vision payload
  Search and rescue
  Target detection and tracking
  Surveillance

## Slide 5: More Advanced Functions?
Applications and advancements
  Vision-aided flight control
  Terrain mapping
  Navigation
Vision System Design/Implementation
  Hardware system
  Real-time software system
  Mission-based vision algorithms

## Slide 6: Description of Application
Autonomous Flight Control
  Locates target
  Tracks target
  Vision feedback for flight control
  Maintains relative distance

## Slide 7: Hardware Configuration
Visual Sensor
  30g, 380 TV line resolution, 40˚ field of view
Image Acquisition Module
  720x576, multiple inputs, 30 FPS
Vision Processing Module
  Two separate for vision and flight control

## Slide 8: Hardware Configuration
Pan/Tilt Servo Mechanism
Wireless Data and Video Link

## Slide 9: Software Configuration
CAM
IMG
SVO
COM
USER
Additional systems: SAV and MAIN

## Slide 10: Vision-Based Target Following
Many options available
  Template matching, background subtraction, optical flow, stereo vision, feature based
Authors chose feature detection + tracking
Get target position with vision + nav sensors

## Slide 11: Target Following
Follow a predefined target, ie toy car
Step 1 is Target Identification
  Segmentation
  Feature Extraction
  Pattern Recognition
Discussion tuned to Embedded Systems
  Math has been glossed over
  Embedded compromises highlighted

## Slide 12: Segmentation
Separate objects from background
  Assume brightness constant with viewing angle
  Assume target has a distinct color distribution
Convert to hue-saturation-value
Filter by color threshold
Morphological operations
Contour Detection
Segmented Image

## Slide 13: Feature Extraction
Find distinguishing characteristics in objects
Geometric Features
  “Four lowest moment invariants”, “Object compactness”
Color Features
  Create color histogram for each object
Dynamic Features
  Distance from object to expected target location

## Slide 14: Pattern Recognition
Identify target from segmented objects
Bayesian function + a priori knowledge
Pre-filter: remove objects that contradict a priori knowledge
Discriminant Function: select object with the highest probability of being the target
  Takes training data, extracted features as input

## Slide 15: Image Tracking
Follow target through frames once identified
Hierarchical system of trackers
Only use complex if simple fails

## Slide 16: Image Tracking cont.
Model-based Image Tracking
  Predict location of target, estimate likelihood target is present
  Low computational overhead, failure prone
Mean Shift Algorithm
  Determine if the target is still in the image
  More powerful, much more expensive

## Slide 17: Target Following Control
Instruct the pan/tilt servo and UAV navigation
Camera is pointed to center the target
UAV maintains specified distance from target
The calculation itself is outside the scope of this lecture

## Slide 18: Experimental Results
Vision-based servo following

## Slide 19: Experimental Results
Relative distance estimation

## Slide 20: Experimental Results
Vision-based target following

## Slide 21: Conclusions
Design and implementation of vision system for UAV
Automatically detect and track target
Guide UAV to follow motion of target
Further research

## Slide 22: Questions?