## Slide 1: HOME AUTOMATION NETWORKS
Oliver Pankiewicz
EEL 6935
Embedded Systems
10-25-11

## Slide 2
My Background
Applications
Home Automation Protocols:
  Insteon
  Z-Wave
  ZigBee
  X10
  Wi-Fi
Network Layers
Comparisons
Outline

## Slide 3: My Background
Oliver Pankiewicz
  Electrical engineer
  Live in Orlando
  Work at Kennedy Space Center since 2003
  NASA contractor
  Ground support equipment design
  Interests in home automation

## Slide 4
Wireless Home Automation Networks: A Survey of Architectures and Technologies
Research and Design of Smart Home System Based on ZigBee Technology
Home Area Network Technology Assessment for Demand Response in Smart Grid Environment
Other Sources:
  Z-Wave Node Type Overview and Network Installation Guide
  Insteon Compared
Papers

## Slide 5
Light Control
Security
HVAC
Smart Grid
Sensors
Door Locks
Windows
Power Outlets
Home Theater
Scenarios
Home Automation Applications

## Slide 6
Home Automation Diagram

## Slide 7
Ad-Hoc network
Independent devices
Self-routing
Healing properties
Increased reliability
Mesh Networking

## Slide 8
ZigBee
Z-Wave
Insteon
HomePlug
X10
Wavenis
6LoWPAN
WiFi
Home Automation Protocols

## Slide 9
Dual mesh network
  Powerlines
  RF
Advantage of using home’s existing powerline infrastructure
Powerline phase issue
ISM frequency at 904 MHz
RF issues:
  Interference from other wireless devices
  Interference from walls and objects
Insteon

## Slide 10
Insteon Network

## Slide 11
Peer-to-peer network
No master controller
Simulcast transmission method
Any device can be a sender, receiver, or repeater
Max 3 hops, 4 total transmissions.
Sends RF signals and through powerline
No collision avoidance
Insteon Details

## Slide 12
24 bit packet
Sent at zero crossing
13 kbps
Uses rolling codes for encryption
Standard message = 120 raw bits
Extended message = 264 raw bits
RF uses FSK
Powerline uses BPSK
Insteon Signals

## Slide 13
Insteon Powerline Packets

## Slide 14
Insteon RF Packets

## Slide 15
Z-Wave Alliance
9.6 to 200 kbps
908 MHz in U.S.
868 MHz in Europe
New 2.4 GHz
90’ to 300’ range
232 nodes max
Master and slave architecture
Uses mesh networking
BPSK
Collision Avoidance
Random back off times
Z-Wave

## Slide 16
Controllers:
  Host routing tables for mesh network
    Used to calculate best route for a signal to get to a slave
  Routes retransmitted by slave nodes
  Only one primary controller
    Can include/exclude devices
    Manage allocation of Node Ids
  Secondary controllers get copies of routing tables
Slave Devices
  Do not compute routing tables
  Can store routing tables
  Act as a repeater
Z-Wave Devise Types

## Slide 17
Z-Wave Routing Example

## Slide 18
Z-Wave Packets

## Slide 19
ZigBee Alliance
Based on IEEE 802.15.4
Design goals:
  Wireless networks
  Low data rates
  Self organizing mesh networks
  Low power
Released in 2005
ZigBee

## Slide 20
IEEE 802.15.4
915 MHz and 2.4 GHz in U.S.
868 MHz and 2.4 GHz in Europe
Supports up to 64,000 nodes
Mesh networking
128 Bytes packet size
20/40/250 kbps data rate
10 to 100 meter range
Uses CSMA/CA
128 bit encryption keys
ZigBee Details

## Slide 21
ZigBee Coordinators
  Controller
  Discovers other devices
  Stores security information
  One per network
ZigBee Router
  Can pass data from other devices
ZigBee End Device
  Low capabilities
  Can’t relay data
ZigBee Device Types

## Slide 22
ZigBee Software Layer

## Slide 23
ZigBee Packet
Preamble
Start of
Packet
Delimiter
PHY
Header
PHY Service
Data Unit (PSDU)
PHY Packet Fields
Preamble (32 bits) – synchronization
Start of Packet Delimiter (8 bits)
PHY Header (8 bits) – PSDU length
PSDU (0 to 1016 bits) – Data field
6 Octets
0-127 Octets

## Slide 24
Powerline networking
Designed in the 1970’s
Max 256 devices
16 Command codes
60 bps
No acknowledgments
No security
X10 Details

## Slide 25
Insteon compatible with X10
Manchester coding
Insteon starts 800us before X10
Zero crossing
60 bps
X10 Signals

## Slide 26
Start Code (4-bit)
House Code (8-bit)
Key Code (10-bit)
X10 Packet

## Slide 27
IPv6 over Low power Wireless Personal Area Network
Use existing internet network infrastructure
IPv6 packets on top of IEEE 802.15.4 network
Issues:
  IPv6 not designed for sensor networks
  1280 byte IPv6 packets
  127 byte IEEE 802.15.4 frames
  40 byte IPv6 header
6LoWPAN

## Slide 28
Physical Layer Comparison

## Slide 29
Link Layer Comparison

## Slide 30
Communication Comparison

## Slide 31
Network Layer Comparison

## Slide 32
Application Layer Comparison

## Slide 33: Questions?
Please post any questions on Sakai
Notes: Nembus Home Automation aims to bring home automation to the masses and capture a significant portion of the multi-billion dollar industry. Nembus will accomplish its goals by focusing on the comprehensive customer experience through:
Creating easy-to-use apps for smartphones, media boxes, and HDTVs.
Building a social network where customers connect with home automation installers, find home automation products, and get questions answered.
Designing a home automation-focused media box with easy-to-setup hardware.
Creating an HTN professional certification program that trains electricians how to install and wire home automation hardware.
Nembus Home Automation is seeking $500,000 to complete product development. The majority of the funding will be used for salaries, hardware prototyping, and research and development. The $500,000 will support Nembus until month thirteen when Nembus’ products are ready for production.