## Slide 1: ROBTIC : On chip I-cache design for low power embedded systems
Varun Mathur
Mingwei Liu

## Slide 2: I-cache and address tag
Instruction cache has
Large chip area
High access frequency=>switching power
Example:
Direct mapped I-cache
1024 entries (=>1024 one way sets)
32 bit data per entry (=>four 8 bit instructions per entry)
32 bit PC address
So,
10 bit index
2 bit block offset
Therefore, 32-(10+2) = 20 bit tag
Cache area taken by tag = (20/(20+1+32)) = 37.7%
Larger the cache tag => more area and power consumption.

## Slide 3: Previous work
a filter cache or L0-cache
tag comparison before data fetch
buffer the address of the previously hit cache line (non-branch or un-taken)
use a couple of the least significant bits of the tag for comparison
Reduced One-Bit Tag Instruction Cache (ROBTIC)

## Slide 4: Their work is directed at:
Application programs have a lot of loops.
Loops have high temporal and spatial locality.
Exploit this locality to reduce tag size.

## Slide 5: Standard cache size for ROBTIC:
Wide range of benchmarks surveyed.
Apps most time within certain loop blocks.
90% of loops have < 30 instructions.
ROBTIC’s standard capacity = 32 inst
Enough to capture most of temporal and spatial locality.

## Slide 6: ROBTIC Archetecture

## Slide 7: Cache tag size v/s cache memory coverage
Tag : identifies which memory location stored at particular cache location
Cache memory coverage : cache mappable address space of main memory.

## Slide 8: Features of ROBTIC:
Direct mapped
Each cache entry contains :
Cache line (data)
1 bit tag
Valid bit
Cache size extensively reduced
Due to 1 bit tag, cache operational control unit reqd.
Performance retained.
Reduced size + maintained performance=>reduced power consumption

## Slide 9: Cache tag size v/s cache memory coverage
FULL TAG = FULL MEMORY COVERAGE

## Slide 10: Cache tag size v/s cache memory coverage
Reduced TAG = PARTIAL MEMORY COVERAGE
Only segments of memory mapped at a time.
Mappable regions distinguished by CC-index.

## Slide 11: Ideal scenario

## Slide 12: Reality : Ping-Pong effect
Consider the case of block B2.

## Slide 13: Overlapped Dynamic Cache Coverage Control
Dynamically shift cache coverage in overlapping manner.
Some of the previously mapped addresses survive.
Again consider the case of Block B2.

## Slide 14: Cache operation control flow:
Three states:
Cache coverage shift
Shift when PC moves out of current coverage.
Invalidate
Always shift by cache size.
Cache flush
If Jump or Branch offset > cache size
Normal cache access

## Slide 15: Cache coverage shift and shift detection
Method 1 : Range gauge
Disadvantages
2 registers (full tag size)
2 comparators (full tag size)
Neutralizes savings from 1 bit tag.

## Slide 16: Method 2 : with gray encoding
Only need to differentiate between 3 regions.
Least two significant bits of tag sufficient.
Called local cache coverage position (CC-lpos).
Range checking will not work.
2 bit CC-lpos (p1p0) -> gray code value (g1g0)
Adjacent coverage regions differentiated by a bit in (g1g0) called common value bit (CVB).
Its value is called common value(CV).
CVB and its CV uniquely identify 4 consecutive regions.

## Slide 17
For current cache coverage :
CVP = ~(g1 xor g0) = ~p0
CV = g0 = p1 xor p0
Hardware cost : does not increase with tag size, one 2 bit reg, one 2 bit B2G conv, one 2x1 mux and 1 bit comp.

## Slide 18: Experimental Results:
Results of Cache Coverage Shift implementation

## Slide 19: Experimental Results:
Comparison of ROBTIC with PTC-5

## Slide 20: Experimental Results:
Comparison of standard & custom ROBTIC designs

## Slide 21: Limitations and future work:
On a jump instruction, the cache is flushed irrespective of the offset.
For future work, they want to investigate multi-way associative structure in ROBTIC.