## Slide 1: Run-time reconfiguration for automatic hardware/software partitioning
Tom Davidson, Karel Bruneel, Dirk Stroobandt
Ghent University, Belgium
Presenting: Steven Fingulin, Quinn Martin

## Slide 2: Run-time Reconfiguration
FPGAs store configuration data in SRAMs
  Allows configuration to be changed during run-time
  Can change functionality quickly without needing to restart
Parameterisable configurations
  FPGA configuration where bits are expressed as Boolean functions rather than Boolean values
  Allows for one configuration to represent several designs
  Previous reconfiguration techniques required all possible configurations externally

## Slide 3: TMAP Tool Flow
TMAP tool flow is a modification of traditional FPGA mappers
  Inputs are either parameters (change slowly) or regular signals (change frequently)
TMAP generates parameterisable configuration based on the design
  For different parameter values, a new configuration must be generated
    User specifies which signals are parameters by annotating VHDL
  After generating a new configuration, the FPGA can be reconfigured
    Only values in truth tables (LUTs) can be reconfigured
    Prevents need to place and route entire design
  This overhead of generating new configurations and applying them is application dependent
    Usually on the order of milliseconds

## Slide 4: Advanced Encryption Standard (AES)
AES specifies how to encode 128-bits of data using a specific key-value
Data Encoding
  128-bits split to 16 bytes
  Each byte is assigned a location in 4x4 state matrix
  Byte transformation are performed in rounds according to current RoundKey
    SubBytes
    ShiftRows
    AddRoundKey
    MixColumns
  RoundKey changes every round

## Slide 5: AES Continued
Key Expansion
  Used to generate keys for each round of the algorithm
  Input Key is used for first round
  Three operations
    Rcon(i) – constant value dependent upon i
    SubWord() – applies Rijndael S-box transformation
    RotWord() – Cyclic rotate word 8 bits left
  Full explanation is beyond scope of this presentation

## Slide 6: Automatic Hardware/Software Partitioning
Most research is focused on system level and algorithm aspects of HW/SW partitioning
Goal of TMAP tool flow is to optimize hardware design and automatically partition HW and SW components
  Frequently changing inputs lead to static segments of configuration and coded in hardware
  Parameter inputs change more slowly and can be computed by software
    Configuration manager (CM) such as PowerPC processor will compute values to complete FPGA configuration

## Slide 7: Hardware/Software Boundary
Conventional HW/SW partitioning
  Does not use Run-time reconfiguration
    Hardware must be general for different parameter values
  All operations dependent upon Parameters are computed in SW
    Software writes values to registers for HW to read
Run-time reconfiguration
  Can alter configuration memory (LUT values) rather than write to registers
  Hardware circuit can be more specialized and faster

## Slide 8: An Example: k_AES
Manually partitioning AES would naturally lead to encoding in HW and key generation in SW
Authors write implementation: k_AES
  Pipelined chain of 10 rounds that implements encoding
  Combinatorial 10 k_rounds that perform key expansion
  128-bits of encoded data output each clock cycle
  Design is not optimized for simplicity
TMAP tool flow applied to design
  Key for encoding is selected as parameter

## Slide 9: Results for k_AES
For k_AES, there is a fairly large area gain (20.3%)
  k_AES algorithm is fairly easy to parition
  Converted key input (parameter-dependent) part to software
Also must consider reconfiguration penalties
  Several milliseconds to load new FPGA configuration
  Memory to store bit files
Manual partitioning showed .7% gain over TMAP
  Minimal effort to partition this application manually
  Motivation to see if other less clearly partitioned applications see performance gains

## Slide 10: Comparison to other implementations
k_AES algorithm also compared to open-source cores
  Crytopan
    More sequential than k_AES (state machine)
    Same throughput (128 bits/cycle)
    Less resource usage before HW/SW paritioning because already hardware optimized
    Smaller gains because less parallelizable
  Avalon_AES
    Even more sequential than Cryptopan
    However, 10x lower throughput
    Hard to compare designs because they are both Pareto optimal
TMAP gains are small
because of low levels of
parallellism

## Slide 11: Other Applications
From k_AES, we see that real gains can be achieved with TMAP
  TMAP is fast and automatic, works well for algorithms with clear partitioning
  Nearly as good as manual partitioning
Not every app has a clear hardware software boundary
  Will explore the effect of using TMAP on some of these cases
Two case studies
  Triple DES Encryption
  Quadratic

## Slide 12: Triple DES
Basic symmetric key encryption/decryption scheme using Data Encryption Standard (DES)
  Encrypts with key 1, decrypts with key 2, then encrypts with key 3
  Extra steps add layers of additional security
TMAP able to improve area usage by 28.7% over hardware-only implementation
  From 3584 to 2552 LUTs
Main design effort in finding
parameters

## Slide 13: Quadratic
Quadratic polynomial solver
  Solves an equation of the form ax2+bx+c
Easily parameterizable
  Coefficients are parameters
  Therefore easy to partition using TMAP
Not easily partitioned manually
  Unclear how coefficients map to partitioning with design-space exploration
TMAP sees area gain of of 21.9%
  Partly due to run-time reconfiguration advantage

## Slide 14: General Guidelines
Parameter selection the most important choice for TMAP
  Other than parameters, tool flow is fully automatic
Implementation choices greatly affect partitionability
  k_AES saw large gains, but not Cryptonpan or Avalon_AES
  Since parameter-dependent parts are optimized in hardware by design-space exploration, they should be as parallel as possible
  Often in conflict with traditional hardware-optimized designs that are largely parameter independent

## Slide 15: Conclusions/Thoughts
TMAP tool flow successful at automatic hardware/software partitioning
  Can reduce FPGA resource utilization by 20%
  Highly dependent on parameter and implementation choices
  Still needs an expert user
Reconfiguration time penalty should be explored more thoroughly
No specifics on FPGA/microprocessor platform used for implementation
  Maximum frequency consideration could offset gains

## Slide 16: Questions?