## Slide 1: A Generalized Framework for System-Wide Energy Saving in Hard Real-Time Embedded Systems
Gang Zeng, Hiroyuki Tomiyama, Hiroki Takada
Graduate School of Information Science, Nagoya University
Tohru Ishihara
System LSI Research Center, Kyushu University
Presenters: Quinn Martin, Steven Fingulin

## Slide 2: Introduction
Power and energy consumption a major concern in embedded systems
  Battery lifetime
  Cooling costs
  Reliability
Three main approaches for energy savings
  Dynamic Hardware Resource Configuration (DHRC)
  Dynamic Voltage Frequency Scaling (DVFS)
  Dynamic Power Management (DPM)
Real-time systems in particular have a good chance of benefitting from these techniques
  Typically have “slack” as a consequence of deadlines

## Slide 3: Dynamic Hardware Resource Configuration (DHRC)
Attempts to dynamically tune processor resources in order to be more efficient, thus saving power
  Adaptive branch predictor
  Selective cache way (associativity)
Performance is heavily application-dependent
  A technique may be effective for some applications but not for others
  An application with random branch behavior would not benefit from a dynamic branch predictor, and may actually suffer

## Slide 4: Dynamic Voltage Frequency Scaling (DVFS)
Lowers voltage and frequency to save power
  Dynamic power for CMOS is P = ACV2F
  Proportional to frequency and square of voltage
  Easy to predict effect on power consumption
Embedded processors often have several voltage and/or frequency levels
  Can use digitally-controlled oscillators and dividers to provide different clocks to different part of the chip
Generally has similar effectiveness on different applications

## Slide 5: Dynamic Power Management (DPM)
Transfers a device in idle state to a low power or “sleep” mode
Applies not only to the microprocessor/microcontroller, but also to external peripherals (e.g. memories)
Challenging to balance power savings with performance degradation incurred from transferring to and from low power mod
  Often takes time and energy to sleep and wake
  Must decide which of potentially several low power modes to use

## Slide 6: Motivation/DEPS
Since each of these technologies contributes to power savings, why not combine them?
  Evaluating the effectiveness of such a scheme has been difficult, especially for hard real-time systems
Energy savings in the processor does not necessarily indicate energy savings in the system
  Must consider the entire system when evaluating power

## Slide 7: DEPS Framework
Three Layers
  Power-controllable hardware
  Power-aware software
  Power analysis tools
Implemented in the scheduler of the real-time OS
Software-centric approach to power optimization offers greater flexibility than traditional hardware-centric approach

## Slide 8: System Model
Includes a processor
  Configurable core and cache for DHRC
  Capable of DVFS
Also includes a memory
  Demonstrates system aspect of framework
  Capable of DPM

## Slide 9: Problem Formulation (1)
Consider n periodic real-time tasks Γ = {τ1, τ2, ..., τn}
Each task τi has a period Pi and mi effective DEPS configurations denoted Ci1, Ci2, …, Cim.
Each configuration Cij has an associated energy-time relation that can be represented by (Tij, Eij).
  Tij is the worst-case execution time (WCET)
  Eij is the energy consumption
A hyperperiod = LCM(P1, P2, …, Pn)
  Essentially the fundamental period of all tasks
The problem is finding the optimal DEPS configuration for each task such that energy usage over a hyperperiod is minimized

## Slide 10: Problem Formulation (2)
In English: Minimize energy of all the tasks over a hyperperiod (1) subject to either Rate Monotonic (2) or Earliest Deadline First (3) scheduling
Selecting the optimal configuration is NP-hard – was solved using linear programming

## Slide 11: Static Scheme Implementation
Find the set of effective DEPS configurations (those with lowest power for their execution time)
Find the energy time relations for these configurations
Solve the optimization problem described previously using linear programming or similar method
Store the derived optimal configurations into a configuration table
The OS scheduler uses the table to load the best configuration for the currently scheduled task
Off-line
On-line

## Slide 12: Case Study/Simulation Setup
Energy savings possible highly dependent on employed technologies
Simulation case study performed using a SimpleScalar/ARM-based power analyzer, Sim-Panalyzer

## Slide 13: Simulation of Static Scheme
Ran two benchmarks on the simulation setup – g3fax and V42
As expected, DEPS can save much power when CPU utilization is low
Static DEPS is more effective than DVFS or DHRC alone by about 14%, and dynamic DEPS is more effective than static

## Slide 14: Conclusions/Comments
DEPS is a useful framework for improving performance of embedded hard real-time systems
Future work will apply DEPS to use on a multiprocessor
Dynamic DEPS and the DPM memory aspect of the static DEPS system was explored in the paper but not covered due to time
Since performance is so application dependent, comparison against a larger set of benchmarks would have added validity to the work
“System” element of the framework is weak – only one off-chip component is included

## Slide 15: Questions?
Please post on the discussion topic on Sakai. Thanks!