## Slide 1: Reconfigurable Computing
Jason Li
Jeremy Fowers

## Slide 2: Speedups and Energy Reductions From Mapping DSP Applications on an Embedded Reconfigurable System
Michalis D. Galanis, Gregory Dimitroulakos, Costas Goutis
University of Patras
Galanis, M.D.; Dimitroulakos, G.; Goutis, C.E.; , "Speedups and Energy Reductions From Mapping DSP Applications on an Embedded Reconfigurable System," Very Large Scale Integration (VLSI) Systems, IEEE Transactions on , vol.15, no.12, pp.1362-1366, Dec. 2007

## Slide 3: FPGA-Based Embedded Motion Estimation Sensor
Zhaoyi Wei, Dah-Jye Lee, Brent Nelson, James Archibald, Barrett Edwards
Brigham Young University
Zhaoyi Wei, Dah-Jye Lee, Brent E. Nelson, James K. Archibald, and Barrett B. Edwards, “FPGA-Based Embedded Motion Estimation Sensor,” International Journal of Reconfigurable Computing, vol. 2008, Article ID 636145, 8 pages, 2008. doi:10.1155/2008/636145

## Slide 4: What is Reconfigurable Computing?
  Architecture that adapts to specific application
  Processing unit coupled with reconfigurable hardware
  After execution, reconfigures hardware for next task
Implementing circuits without fabricating device

## Slide 5: Introduction
Reconfigurable Hardware combined with µP
  µP => noncritical control intensive
  Hardware => kernels
Coarse-grained reconfigurable arrays (CGRA)
  Array of processing elements (PEs)
  Word-level parallelism

## Slide 6: Introduction
Seven DSP benchmarks
  Three 32-bit ARM processors
  Two CGRA architectures
Application Speedup
Energy Consumption vs µP/VLIW system

## Slide 7: Architecture Overview
µP with instruction memory for storing program code
CGRA with memory for complete configuration
Shared data RAM used for communication
Load data into PEs
PE array with bus connecting rows and columns
Manages CGRA execution; set by µP

## Slide 8: Design Flow Outline
Distinguish kernel from non critical
SUIF2 and MachineSUIF compiler
Loop Unrolling
Scheduler exploits ILP

## Slide 9: Experimental Setup
CGRA1 = 4x4 array, CGRA2 = 6x6
  150 MHz
  CGRA1 power consumption is 154.5 mW
  CGRA2 power consumption is 258 mW
ARM7
ARM9
ARM10
133 MHz, 26.6 mW
325 MHz, 195 mW
250 MHz, 112.5 mW

## Slide 10: Experimental Results - Mapping
When II = MII, performance is
optimal
Optimum performance in 19/23
Average CGRA utilization is
13.3 IPC or 83.1%
71.7% usage in CGRA2

## Slide 11: Experimental Results - Speedup

## Slide 12: Experimental Results - Speedup
Speedups range from 1.81 to 3.99
ARM7 = 2.86, ARM9 = 2.74, ARM10 = 2.57
  ARM7 has highest CPI
Speedups are all close to ideal
  CGRA2 is only 6% less

## Slide 13: Experimental Results - Energy
Energy Estimation
  Timeproc = noncritical software
  TimeCGRA = kernel execution time
  Pmem_icon = shared data RAM and interconnection power consumption

## Slide 14: Experimental Results - Energy
ARM coupled
with 4x4 CGRA 
ARM coupled
with 6x6 CGRA 

## Slide 15: Experimental Results – vs. VLIW
CGRA1 is used due to greater energy savings
Compared to µP coupled with eight-issue VLIW

## Slide 16: Experimental Results – vs. VLIW
Avg speedup
  2.71 compared to 2.53
Avg Energy Savings
  57.2% compared to 55%

## Slide 17: Conclusion
Significant speedup and energy reductions
  Compared to pure software implementation
  Compared to VLIW system
Reconfigurable Computing Application
  Optical Flow using FPGA

## Slide 18: FPGA-Based Embedded Motion Estimation Sensor
Zhaoyi Wei, Dah-Jye Lee, Brent Nelson, James Archibald, Barrett Edwards
Brigham Young University
Zhaoyi Wei, Dah-Jye Lee, Brent E. Nelson, James K. Archibald, and Barrett B. Edwards, “FPGA-Based Embedded Motion Estimation Sensor,” International Journal of Reconfigurable Computing, vol. 2008, Article ID 636145, 8 pages, 2008. doi:10.1155/2008/636145

## Slide 19: Optical Flow
Measure the motion of pixels between consecutive frames
  Performed on images’ brightness pattern
  Major implications for 3D vision, UAVs
Applications:
  Navigation, moving object detection, motion estimation, structure from motion, time-to-impact

## Slide 20: Optical Flow

## Slide 21: Real-time Optical Flow
Notoriously difficult to execute in real time
  CPU is too slow, parallelism necessary
  GPU acceleration works, not embedded friendly
FPGAs ideal for embedded optical flow
  Low power + fast parallel processing
  Attempted in many previous works

## Slide 22: Embedded Optical Flow
Previous embedded work made compromises
Algorithm limitations
  Ideal algorithm: iterative steps
  Ideal hardware: data parallel or pipelined
Resource limitations
  Smoothing important, expensive

## Slide 23: Algorithm (Math Alert)
The next slide has all of the equations
Use it to get an idea of the computational load
Refer to the paper to learn details

## Slide 24: Algorithm
Averaged gradient =
  Mask: d = (1 -8 0 8 -1)
Outer product (3x3) O =
Gradient Tensor (3x3) T =

## Slide 25: Algorithm Cont.
Optical Flow: pixels/frame =
  ti are elements of T
Smooth Optical Flow

## Slide 26: End Math Zone

## Slide 27: Smoothing Masks
Filter every stage to improve accuracy
ci is 3x3 spatial, mi is 7x7 spatial
wi is 5x5x3 temporal (3 frames)
  Accessing previous frames very expensive
  First paper to do this in HW
  Greatly improves accuracy

## Slide 28: Hardware Structure
SRAM
Derivative Module
Optical Flow Module
High Speed Bus (PLB)
Note: Reduced system diagram
Camera
SDRAM

## Slide 29: Derivative Module
Camera
SRAM
SDRAM
Temporal Gradient
Spatial Gradient
gt(t)
gx(t)
gy(t)
frame(t-1)
frame(t-2)
frame(t-3)
frame(t-4)
frame(t)

## Slide 30: Optical Flow Module

## Slide 31: Hardware Platform
  Virtex-4 FX60 FPGA, 100 MHz Clock
  32Mb SDRAM, 4 Mb SRAM
  2x built in 400 MHz PowerPC cores
CMOS Camera, 30 FPS 640x480

## Slide 32: Testing
Camera data for frame rate
MATLAB simulation for accuracy

## Slide 33: Results
Achieved 15 FPS
  Suitable for some UAV apps
Accuracy 2x better than previous work
  Authors: 6.7o
  Previous: 12.7o
  SW: 1.0o
Importance of temporal smoothing
  10.6o without it