## Slide 1: Topic 2: Communications (Short Lecture)
Jorge J. Gómez

## Slide 2: The Flooding Time Synchronization Protocol
Miklós Maróti, Branislav Kusy, Gyula Simon, Ákos Lédeczi Institute for Software Integrated Systems, Vanderbilt University Proceedings of the 2nd international conference on Embedded networked sensor systems (SenSys '04)

## Slide 3: Introduction
Typical sensor network applications need time synchronization
  Doesn’t need to be as heavy as distributed computing world
  Better precision leads to better, more consistent, sensing
Examples
  Target tracking
  Surveillance
  Battlefield monitoring
  Counter-sniper systems
Target platform is Mica2
  7.37 MHz processor
  4kB RAM, 128kB flash
  433 MHz radio (38.4 kbps, 500 ft range)
  TinyOS operating system
    Allows application developers to override OS operations like scheduling and radio communication

## Slide 4: Approaches to Time Synchronization
Network Time Protocol (NTP)
  Most widely adopted protocol
  Used primarily in data centers
  Accuracy in order of milliseconds
    In DSNs, non-determinism of wireless communications add substantial imprecision
Popular DSN time protocols
  Reference Broadcast Synchronization (RBS)
    A reference message is broadcast, nodes timestamp the receipt
    Nodes exchange time-stamp of reference message in order to sync
    Large message overhead for communicating local time-stamps
  Timing-sync Protocol for Sensor Networks (TPSN)
    Builds a spanning tree of the network topology
    Pairwise message exchange on edges, always syncing to root node
    Does not handle clock drift and topology changes
The proposed protocol: FTSP
  Uses less messages than TPSN
  Handles clock drift between synchronization periods

## Slide 5: Uncertainties in Radio Message Delivery
Non-deterministic delays in wireless communications limit the precision of any time protocol
Sources of uncertainty can be classified as
  Send time– time to assemble a message and issue the request to the MAC layer
  Access time– delay of waiting for the medium to become free
  Transmission time– time it takes to send the message
  Propagation time– time it takes a bit to arrive at the receiver
  Reception time– same as transmission time but at receiver

## Slide 6: Uncertainties cont.
Sources of uncertainty cont.
  Interrupt handling time– delay from radio issuing an interrupt and the CPU responding
  Encoding time– time taken to transform bit stream to wireless pattern
  Decoding time– time taken to transform wireless pattern to bit stream
  Byte alignment time– time required to align sender’s bit stream at the receiver
Table outlines magnitudes and distributions
  We see that send/receive and access time are biggest issues

## Slide 7: Flooding Time Synchronization Protocol
Intro
  Assume each node has local clock
    Can have drift due to crystal’s timing errors
  Nodes can communicate over wireless link to some neighbors
    Unreliable but error corrected
  FTSP synchronizes one sender to multiple receivers
    Single message MAC layer time-stamped at sender and receiver
    Linear regression used to compensate for clock drift between sync periods
Time-stamping
  Multiple time-stamps are generated as byte boundaries pass
    Interrupt handling time–minimum of these stamps
    Encoding/decoding time– average of the time stamps
    Alignment time– calculated from transmission speed and byte offset
  With 6 time stamps used to calculate single error corrected final time stamp
    Errors on Mica set-up was 1.4μs (average), 4.2μs (max)

## Slide 8: Clock Drift Management
Crystals in Mica can drift 40μs per second
  If we wanted μs precision, sync period would have to be less than one second
  Assume drift is linear provided short-ish sync period
Using linear regression of previous time offsets we can predict clock drift
Tested linear properties of drift in following experiment
  Off-line linear regression of time stamps
    Ideal case, not practical
  Last 8 points used for on-line calculation
    Re-sync period of 30s or 300s
    Shorter period only marginally better
  Requires re-sync (see →)

## Slide 9: Multi-hop Time Synchronization
In practical DSNs network radius is larger than single radio’s range
  Multiple nodes will need to broadcast reference times
FTSP’s solution
  Root node is reference
  A node is synchronized if enough sync periods have been gathered
  Synchronized nodes can broadcast synchronization messages
Subtleties
  Synchronization message format
    Contains timestamp, root ID, and sequence number
    Sequence number is set and incremented by root and used to handle redundant synchronization
  Managing redundant information
    Regression table needs 8 entries
      New entry can only come from (rootID >= myRoot && seqNum > highestSeqNum)
    Longer period of time contained in regression table leads to better regression results
  Root election
    Root is node with smallest ID in the network
    Possibility of multiple roots in network but if message received with root ID lower than node ID, that node stops claiming to be root
  Convergence
    Choice of synchronization period is a tradeoff between power consumption, accuracy, and speed of convergence

## Slide 10: Experimental Set-up
Set-up
  60 nodes with software implemented topology shown here
    Topology meant to mimic multi-hop real-life network, but all nodes in experimental set-up need to be in range of metric gathering station
  Root node (ID1) is in center, back up (ID2) is on edge
  Parameters tuned to 30 second re-sync and 3 minute root declaration
Script for graph on next slide
  A) All motes turned on at 0:04
  B) At 1:00 root was turned off causing ID2 to become root eventually
  C) For 15 minutes, starting at 2:00, nodes were reset randomly on a 30 second period
  D) At 2:30 all odd node IDs were turned off
  E) At 3:01 all odd nodes were turned back on
  F) At 4:02 the experiment was ended

## Slide 11: Results

## Slide 12: Discussion and Comparison to Previous Approaches
When experiment starts, large percentage of nodes declare themselves root, no real sync
  Eventually, system converges
    Took 14 minutes (idealized result would have been 9-12 minutes)
During election of new root, error stays low
  Nodes declare themselves new root but do not throw out their regression tables
  This voting round only took 6 minutes
Errors under root ID2 were greater than under root ID1
  First network is 60-mote, 6 max hop to root
  Second network is 59-mote, 11 max hop to root
  Average per-hop error only increased from 0.5μs to 1.6μs
TPSN and RBS algorithms were tested in a two-node experiment on identical hardware
  16.9 and 29.1μs average errors compared to 3μs in FTSP case
  Message overhead also much less than RBS, slightly less than TPSN

## Slide 13: Applications and Conclusions
Used in real-world test experiment: Counter-sniper sensor network
  60 motes with special FPGA-accelerated acoustical sensing algorithm
  Repeated tests of 4-8 hours with fluctuations in humidity and temperature affecting clock drift
  No FTSP metrics collected but application was successful and performance did not degrade over time
Further Improvements
  Perform examination of scaling to thousands of nodes
  Improve convergence by using two different broadcast periods (remember trickle?)