## Slide 1: Topic 3: Aero-space Applications (Short Lecture)
Jorge J. Gómez

## Slide 2: A Distributed Routing Algorithm for Datagram Traffic in LEO Satellite Networks
Eylem Ekici, Ian F. Akyildiz, Michael D. Bender Georgia Institute of Technology and National Security Agency IEEE/ACM Transactions on Networking April 2001

## Slide 3: Introduction
Satellite networks meet specialized communications needs of business, government, and individuals
  Next-Generation Internet (NGI)
    Rural, remote, and inaccessible areas
    Flexible bandwidth on demand
    Trivial to add new users
Satellite networking is very challenging
  Satellites move causing changes in network topology
  Distinction between logical and physical locations of satellites with respect to ground stations (destination)
    Satellites move with respect to each other and with respect to their final, logical destination on the ground
This work extends existing datagram routing algorithms
  Distributed algorithms to find minimum propagation delay paths
  Off-line (pre-launch) calculations not required
  No overhead because no topology information needs to be exchanged between satellites

## Slide 4: Satellite Network Architecture
Satellite Networks in LEO composed of
  N – polar orbits (planes)
  With M satellites per orbit
Inter-satellite distances
  Constant within a plane (intra-plane links)
    North-south routing
    Length computation can be done off-line
  Changes between planes (east-west routing)
    Length varies but can be calculated easily
    Inter-plane links are shorter the closer to the poles they get
    Inter-plane links are shut down while crossing the poles because neighbors change locations
Routing is done with respect to logical locations
  Logical location (base state) has one satellite associated with it at a time

## Slide 5: Satellite Network Architecture cont.
Definitions
  Neighbors
    Each satellite has two inter-plane neighbors (up, down) and two intra-plane neighbors (left, right)
  Eastern and Western Hemispheres
    The boundary where a satellite moving north has a neighbor to its west moving south (called seam) separates the logical east and west
  Initial Alignment
    When all satellites are over logical locations and all inter-plane links are parallel to the equator
  Horizontal Ring
    The satellites on the same latitude in initial alignment make up a horizontal ring
    The horizontal rings closest to the polar regions are said to be at LATmin
  Multi-hop path
    Any source-destination satellite pair can be connected by a multi-hop path
    Total propagation delay– the delay over a multi-hop path
    Minimum propagation delay path– the multi-hop path that minimizes total propagation delay for a given source-destination pair

## Slide 6: Datagram Routing Algorithm
Satellite network can be considered a spherical Manhattan Network
  Special care taken with polar regions where only north-south links are active
Strict Manhattan Networking is sub-optimal
  Inter-plane links further north are shorter and therefore have shorter inter-plane delays
Decision map created to decide whether to pass over pole to get to destination
  Two equations presented which serve as decision metric for the north direction in LATmin horizontal ring
  Logically, delay of going strictly horizontally is greater than going north twice and finishing the rotation in opposite hemisphere

## Slide 7: Datagram Routing Algorithm cont.
First step: Direction Estimation
  Assume all links have equal delay and position is over logical locations
  Output of this step is two directions dv and dh with three possible values each {-1, 0, 1} for up/right, no change, or down/left
  Simple look up table created for every destination
Second step: Direction Enhancement
  Considers output of last step but relaxes assumption of equal delay links
  Simple rules for enhancement
    If in polar region, take dv as dh is unavailable
    If in LATmin, prefer dh unless polar crossing is shorter (decision map)
    Anywhere else, compute minimum delay based on simple equation set
  Outputs preferred direction and secondary direction in case of congestion or faults
Third step: Congestion Avoidance
  Take secondary direction if output buffer in preferred direction is larger than preset metric
  Resulting path will still be minimum-hop but may not be minimum-delay

## Slide 8: Datagram Routing Algorithm cont.
Fault-tolerance
  If currently in polar region and north neighbor failed, send back
  If satellite in primary direction failed, use secondary
  If satellite in primary direction failed and no secondary direction identified send in a direction orthogonal to primary
Time and space complexity
  Packet forwarding decision is O(1)
  Connectivity and lookup tables are of size M2xN2

## Slide 9: Performance
In all experiments constellation is 12 planes with 24 satellites per plane
  Results based on all possible source-destination pairs
  Comparisons based on Bellman’s algorithm O(N3) max O(N*log(N)) average
Path Optimality
  Authors made assumption that all routing happens with satellites positioned over logical locations
  Effect of deviating from that assumption is minimal
    Max deviation from results of Bellman’s is 0.35% with direction enhancement stage turned on
    Constantly 8% without direction enhancement
    Enhancement phase is critical in the algorithm for minimum delay paths

## Slide 10: Performance cont.
Effect of satellite failures
  Percent deviation from optimal studied versus latitude of failed satellite
    Longitude of satellite follows the same pattern
  Deviation falls from 6.25% to 4.4% while moving north from equator
    Links get shorter
  When the satellite is in LATmin the deviation increases to 15%, 16% for satellites in the polar region
    Failures inside of next to polar region causes the packets to be sent back to satellites outside that region
    Increases the difference in the propagation delay
  The increases in this case are still minimal
    Satellite failures are rare and typically short lived

## Slide 11: Performance cont.
Typical propagation delay values
  Real-life scenario of packets travelling from continental North America (40N, 120W) to Central Europe (55N, 12E)
    Satellite constellation is identical to the other experiments
    All satellites ~1375 km above the surface
  We start with initial alignment of the satellites and examine the change in propagation delay over each quarter of the movement period
    Bellman’s algorithm yields values between 43.5 and 47.1 milliseconds one way, while this algorithm deviates from that by less than a millisecond at the worst case

## Slide 12: Conclusions
Introduced a datagram routing algorithm for LEO satellite networks
  Algorithm is distributed
  Routing decisions are made on a per packet basis
The generated paths are loop free and shown to be durable
  Satellite movements have negligible effect on optimality
  Protocol can route around failures with minimal performance degradation
  Can avoid congested satellites using only local data
Viable routing algorithm for satellites providing Next Generation Internet