## Slide 1: High Performance Cache Replacement Using Re-Reference Interval Prediction (RRIP)
Aamer Jaleel, Kevin B. Theobald, Simon C. Steely Jr. , Joel Emer
Intel Corporation
The ACM IEEE International Symposium on Computer Architecture (ISCA) conference,
June 19–23, 2010, Saint-Malo, France.
Chien-Chih(Paul) Chao
Chih-Chiang(Michael) Chang
Instructor: Dr. Ann Gordon-Ross

## Slide 2: Agenda
Motivation
Background
  Least Recently Used (LRU) policy
  Dynamic Insertion Policy (DIP)
  Least Frequently Used(LFU) policy
Re-Reference Interval Prediction (RRIP)
  Not Recently Used policy
  Static RRIP
  Dynamic RRIP
Experimental Methodology
Results and Analysis
Conclusion

## Slide 3: Cache Replacement Policies
Cache stores the frequently required data
Discard items to make room for the new ones when cache is full.
http://i.crn.com/enc/CACHEMEM.GIF
Notes: Knowledge based on “Memory Hierarchy”
“The Librarian Example”
Cache memory stores the data items that are frequently required by the processor
When the cache is full, the algorithm must choose which items to discard to make room for the new ones

## Slide 4: Motivation
Efficient last-level cache(LLC) utilization
  Avoid long latency cache misses to main memory
Need a practical cache replacement policy that is not only thrash-resistant but scan-resistant
Notes: LLC, also called as the L3 cache as we know

## Slide 5: Background
LRU Replacement Policies
DIP (Improvement of LRU)
Cache Access Patterns
LRU/ LFU Hybrid replacement policy
Comparison of DIP and Hybrid(LRU/LFU)
Improving LLC performance by targeting cache blocks that are dead upon cache insertion
Notes: Both industry and academia have produced an impressive amount of research work dedicated to improving the performance of replacement policies. While we cannot describe all replacement policies that exist in the literature,
summarize prior art that most closely relates to improving LLC performance by targeting cache blocks that are dead upon cache insertion.

## Slide 6: LRU Replacement Policies
Least Recently Used(LRU)
  LRU Chain: LRU / MRU
  Re-Reference Interval Prediction (RRIP) chain
  Good with high data locality
  Bad performance when re-references only occur in the distant future.
Near-immediate
Distant
Notes:   It is a commonly used cache replacement policy
  Re-Reference Interval Prediction (RRIP) chain that represents the order in which blocks are predicted to be re-referenced

## Slide 7: Dynamic Insertion Policy(DIP)
Improves LRU replacement by dynamically changing the re-reference prediction
Both DIP and LRU are failed t0 make accurate predictions when mixed re-reference patterns occur
  Scan: a burst of references to data whose re-reference interval is in the distant future
Notes: improves LRU replacement in situations where the re-reference interval is in the distant future by dynamically changing the re-reference prediction from a near-immediate re-reference interval to a distant re-reference interval.
A scan is any sequence of one-time use requests

## Slide 8: Cache Access Patterns
Recency-friendly Access Pattern
Thrashing Access Pattern
Streaming Access Pattern
Mixed Access Pattern

## Slide 9: Cache Access Patterns (cont.)
Recency-friendly Access Pattern

## Slide 10: Cache Access Patterns (cont.)
Thrashing Access Pattern

## Slide 11: Cache Access Patterns (cont.)
Streaming Access Pattern

## Slide 12: Cache Access Patterns (cont.)
Mixed Access Pattern

## Slide 13: LRU / LFU Replacement Policy
Least Frequently Used(LFU)
  frequently accessed : near-immediate future
  infrequently accessed : distant future
  Measured by counter
Features:
  DIP: Thrash-resistant
  LRU/LFU: Scan-resistant

## Slide 14: Comparison of DIP and Hybrid(LRU/LFU)

## Slide 15: Re-Reference Intervall Prediction
Not Recently Used (NRC) replacement policy
Static RRIP
  SRRIP with Hit priority
  SRRIP with Frequency priority
Dynamic RRIP
Behavior for a Mixed Access Pattern
Experimental methodology and Results
  Simulator
  Benchmark

## Slide 16: NRC replacement policy
Motivation
  LRU cannot perform to mixed access patterns
  Chained-based LRU is impractical for highly associative caches
The nru-bit
  Value of ‘1’ implies was recently used and is predicted to be re-referenced in the near-immediate future
  Value of ‘0’ implies was not recently used and is predicted to be re-referenced in the distant future

## Slide 17: Static RRIP
Motivation
  One bit of information is not enough
  NRU cannot identify non-scan blocks in a mix access pattern
M-bit Re-Reference Prediction Values (RRPV)
  2M possible RRPV eables intermediate re-reference intervals predicton
Hit Priority (HP)
  Updates RRIP to be near-immediate on a hit
  Prioritize replacement of blocks with no hits
Frequency Priority
  Decrementing the RRPV register on cache hits
  Prioritize replacement of blocks with infrequently re-ref

## Slide 18: Behavior of LRU
Mixed Access Pattern
a1, a2, a2, a1, b1, b2, b3, b4, a1, a2
Cache Hit:
  Move block to MRU
Cache Miss:
  Replace LRU block
  Move block to MUR

## Slide 19: Behavior of NRC
Mixed Access Pattern
a1, a2, a2, a1, b1, b2, b3, b4, a1, a2
Cache Hit:
  Set nru-bit of block to ‘0’
Cache Miss:
  Search for first ‘1’ from left
  If ‘1’ found go to step (5)
  Set all nru-bits to ‘1’
  Go to step (1)
  Replace block and set nru-bit to ‘0’

## Slide 20: Behavior of 2-bit SRRIP with HP
Mixed Access Pattern
a1, a2, a2, a1, b1, b2, b3, b4, a1, a2
Cache Hit:
  Set RRPV of block to ‘0’
Cache Miss:
  Search for first ‘3’ from left
  If ‘3’ found go to step (5)
  Increment all RRPVs
  Go to step (1)
  Replace block and set RRPV to ‘2’

## Slide 21: Dynamic RRIP
Motivation
  SRRIP does not thrash-resistant
Bimodal RRIP (BRRIP)
  Similar to Bimodal Insertion Policy of DIP
  Insert majority of cache blocks with distant re-ref
  Insert infrequently with a long re-ref interval
Set Dueling
  Choose between scan-resistant SRRIP and thrash-resistant BRRIP by using two Set Dueling Mointors
  Use a single policy selection counter

## Slide 22: Experimental Methodology
Simulator
  CMP$IM
  4-way out-of-oreder
  128-entry reorder buffer
  3 level cache hierarchy
Benchmarks
  5 workloads from SPEC CPU2006
  9 “real world” workloads
    PC Games
    Multimedia
    Server

## Slide 23: Results of SRRIP-FP
Reduces MPKI by 5-18%
Outpeform LRU by an average of 2.5%

## Slide 24: Results of SRRIP-HP
Reduces MPKI by 5-15%
Outpeform LRU by an average of 5%

## Slide 25: SRRIP-HP Sensitivity to Cache size
SRRIP is insensitive when M>3
Wider RRPV retain blocks for longer periods
2-bit or 3-bit RRPV is sufficient to be scan-resistant

## Slide 26: DRRIP Performance
Improve avg 5% above SRRIP

## Slide 27: Comparing to Other Policies
Base on single-core processor with 16-way 2MB LLC
RRIP requires less hardware than LRU yet outperform LRU on average
RRIP requires 2.5X less hardware than HYB

## Slide 28: Conclusion
RRIP predicts intermediate re-ref between near-immediate and distant re-ref interval
SRRIP needs only 2-bit for scan-resistant
DRRIP for both scan-resistant and thrash-resistant
SRRIP and DRRIP outperform LRU by an average of 4% and 10%