## Slide 1: Hiding cache miss penalty using priority based execution for embedded processors
Varun Mathur
Mingwei Liu
Sanghyun Park, Aviral Shrivastava and Yunheung Paek

## Slide 2: Motivation
Disparity between memory & processor speeds keeps increasing.
30-40% of instructions access memory.
Processor time wasted waiting for memory.

## Slide 3: Solution
Multiple issue
Value prediction
Out of order execution
Speculative execution
Problem:
Only suited for high end processors
Significant power & area overhead
Most embedded processors:
Single issue
Non-speculative
Alternative mechanisms reqd to hide memory latency with minimal power & area overheads

## Slide 4: Their technique at a glance
Compiler classifies instructions into high and low priority.
Processor executes high priority inst.
Execution of low priority inst postponed.
Low priority instructions are executed on a cache miss.
Hardware reqd:
Simple reg renaming mechanism
Buffer to keep state of low priority inst.

## Slide 5: Priority of instructions
High priority instructions are reqd to continue :
Instruction fetch
Data transfers
Therefore, high priority instructions are:
Branches
Loads
Instructions feeding high priority instructions
All others are low priority.

## Slide 6: Steps involved in determining priority
Mark loads & branches.
Mark instructions that generate source operands of marked instructions.
Mark conditional inst that marked inst are control dependant on.
Loop between step 2 and 3.
Marked instructions are high priority, rest low priority.

## Slide 7: Example

## Slide 8: Scope of their analysis
Considers only instructions in loops.
First execute all high P instructions of the loop.
Once done, execute pending low P instructions.
Cannot wait till another cache miss, since cache misses rare outside loops.
ISA enhancements :
1 bit priority info
Special flushLowPriority instruction

## Slide 9: Execution model
Two execution modes:
High priority
Low priority
Only high P executed.
Low P inst, operands renamed and queued in a ROB
When cache miss, switch to low P mode
Execute low P instructions
If cache miss resolved -> high P mode
If all low P executed and still cache miss unresolved -> high P mode

## Slide 10: Reasons for performance improvement
Number of effective instructions in a loop reduced=>loop executes faster
Low P inst executed on cache miss=>utilisation of cache miss latency

## Slide 11: Architecture
Architecturally similar to Out of order execution with compiler support.
Requires full reg renaming capability.
P : 1 bit priority indicator
Rename table : mapping info from real reg -> rename reg
Rename manager : insts in ROB renamed dynamically suing info from table
Priority selector : decides exec mode of processory

## Slide 12: Experimental setup
Use Intel Xscale microarchitecture:
Single fetch, single decode, single issue
7 stage out of order pipelined processor
32K 32 way Icache & Dcache
Experiments done on, innermost loops of several multimedia apps.
Specifically, 4 multimedia apps
H.264 decoder from MediaBench
2 checksum benchmarks from MiBench
3 kernels for swim from SPEC2000
3 benchmarks from DSPstone
Why were these benchmarks chosen ?
Important kernels of multimedia apps
Have non-negligible cache miss penalty due to data intensive calcs

## Slide 13: Effectiveness of priority based execution
ROB = 100 entries
GSR shows most improvement
17% avg reduction in exec time

## Slide 14: Reduction in memory stall time
Laplace benchmark interesting
So even if there is not much scope for improvement, this method can hide significant portions of memory latency.

## Slide 15: Varying ROB size
Saturates after ROB size = 100.
Because Intel Xscale avg mem latency = 75 cycles.

## Slide 16: Power & performance tradeoffs
Performance better than 1F1D1I
Performance better than 2F2D2I
Worse than 2F2D2I out order, but lot smaller power consumption

## Slide 17: Future work
Measuring effectiveness of this technique on high issue processors.
Questions ?