## Slide 1: Designing VM Schedulers for Embedded Real-Time Applications
Alejandro Masrur, Thomas Pfeuffer, Martin Geier, Sebastian Drössler and Samarjit Chakraborty
Institute for Real-Time Computer Systems, TU Munich, Germany
Realia Tec GmbH, Garching, Germany
Presented by Steven Fingulin

## Slide 2: Introduction
In embedded systems, many applications may exist in the same system
  In automotive industry, many Electronic Control Units (ECUs) to control each application
  Increases cost and may have redundant hardware that is underutilized
Virtual machines provide isolation between separate applications
  If one program crashes, it won’t affect others
  More critical applications such as airbag deployment and anti-lock brakes can be separated from radio or A/C systems
Every operation must go through the VMM or hypervisor before executing on hardware

## Slide 3: Introduction
Scheduling on VM requires hierarchical scheduling
  VMs must be scheduled onto processors at VMM level
  Tasks must be scheduled inside of each VM
Deadline-monotonic (DM) scheduling – tasks are assigned priorities based on their deadlines
Rate-monotonic (RM) scheduling – shorter jobs have higher priority
Tasks on VMs are scheduled with DM
VMs on the VMM are scheduled with RM

## Slide 4: Related Work
Analysis of hierarchical scheduling by Deng and Liu using Earliest Deadline First (EDF)
Kuo and Li performed similar analysis with RM and EDF
  Stricter assumption of periods equal to deadlines
PShED framework allows servers to update their priority according to deadline of current task
Shin and Lee present VM scheduling with periodic fixed CPU times for each VM
VM literature mainly analyzes performance and fairness of scheduling

## Slide 5: Models and Notation
T denotes a set of sporadic independent tasks
Task Ti has deadline di, worst case execution time ei and minimum inter-release time pi
V denotes the set of all VMs Vl in the system
  Each VM has a time slice sl and a period pl
Tasks and VMs are sorted by priority(Ti has higher priority than Ti+1)

## Slide 6: Requirements for a VM
Execution length – largest time interval that it takes a VM to execute a single time slice
Assume that scheduling all VMs is feasible
  Vl can first finish executing sl time units as early as possible
  All higher priority VMs are then released together with the next execution of Vl
These assumptions follow that the VM’s schedule time sl must be greater than the worst case execution time of the task associated with the smallest deadline: sl ≥ el,min
Vl’s execution length
Worst-case response time for Vl

## Slide 7: Scheduling on a VM
Each application (composed of several real-time tasks) should run on its own VM
All of the tasks in a VM can run on the same processor
  If only one VM allocated to a processor, then the tasks can be scheduled if sl ≤ pl
If wi ≤ di, then the tasks are able to be scheduled and will meet deadlines
Worst-case execution demand of a task

## Slide 8: Guarantee of Task Meeting Worst-Case Deadline
kl,i is number of complete periods that pass between when a task can start and its deadline
min(s1, α(ti-kl,i*pl) function is time in last period of deadline
wi

## Slide 9: Design of Highest-Priority VM Scheduler
VMs are scheduled under RM, so period determines priority of each VM
Highest priority VM is V1 with minimum deadline d1=p1 and worst case response s1
Eq 9 is used to find s1 that enables scheduling of V1
Eq 10 is derived by setting min(s1,t1-k1,i*p1) to 0 and substituting di-(p1-s1)/p1 for ti
s1 must be smaller than p1

## Slide 10: VMs with Lower Priority
Shortest deadline of any task in Vl determines priority of Vl
pl = dl,min + sl –wl : derived from combining equations 2 and 1
Same equation as highest priority can be employed to solve for sl
By approximating α(t), a faster method can be used that requires less iterations to solve (appendix slide)
The complexity of calculating slice times is pseudo-polynomial

## Slide 11: VM Scheduler

## Slide 12: Case Study
Electronic Stability Control (ESC)
  Improves steering by minimizing skidding and blocking
  Two real-time tasks: T1 and T2
Engine Management (EM)
  Computes best ignition point after each revolution in the engine
  Three real-time tasks: T3, T4, T5
Xen hypervisor used for scheduling
Intel Core 2 Duo @ 2.16 GHz

## Slide 13: Case Study
Network Interface Controller (NIC) assigned to an unprivileged domain in Xen to interface VMs to communication network
Sensors are connected to a bus with an Ethernet network listening via a gateway
Design cases analyzed:
  Each real-time task has its own VM
    Inefficient due to memory overhead
    Higher utilization (more control over slice and period)
  Each application is run on a VM

## Slide 14: Network Domain
Network domain exists between VMs and bus so it must be highest priority
  Has its own time slice and period, sN and pN
Number of packets limited by speed at which they are sent and number of tasks that can send them
  sN ≥ n * eN : eN is worst-case processing time of a packet
  n=5 and eN=0.06ms therefore sN=0.3ms

## Slide 15: Network Domain
Worst-case response time used to determine pN
  domN receives message and uses up its time slice
  Relays message to V1 and must wait for response
  pN must be large enough that all tasks can process a packet
pN = d1,min-sN : since d1,min=2.5, pN=2.2ms

## Slide 16: Design Cases
Case A (Task Domains):
  DM policy sets T1 as highest priority and T5 as lowest
  Period set to period of the task
  Slice set to execution time of the task
  System and schedule are feasible
Case B (Application Domains):
  ESC tasks: T1 and T2 on one domain
  EM tasks: T3, T4, and T5 on separate domain
  Network and EM share one core, ESC gets the other

## Slide 17: Design Case B
Electronic Stability Control
  Period of ESC: pESC = d1 = 2.5ms
  Time slice of ESC: sESC ≥ e1 = 1ms
  Equation 5 and 10 applied to calculate sESC so that it accounts for execution of T2
  sESC = 1.5ms
Engine Management
  Must share time with network VM so it is lower priority
  sEM = 3.85ms and pEM = 6.7ms

## Slide 18: Results
Remote PC simulates input
20k packets sent for each point on curve

## Slide 19: Results and Conclusion
For ESC tasks T1 and T2, no real difference between design A or B
  Can meet deadline up to 70 and 50% respectively
EM task T3 always makes deadline
EM task T4 makes deadline up to 65% higher priority tasks
EM task T5 meets deadline up to 80%
  Design A is better for below 35%
Presented method for real-time scheduler in VM systems
Compared case of task-dedicated VMs vs. application-dedicated

## Slide 20: Appendix