## Slide 1: Topic 1: Sensor Networks (Long Lecture)
Jorge J. Gómez

## Slide 2: Trickle: A Self-Regulating Algorithm for Code Propagation and Maintenance in Wireless Sensor Networks
Philip Levis, Neil Patel, Scott Shenker, and David Culler University of California, Berkeley Published in 2004 USENIX/ACM Symposium on Networked System Design and Implementation

## Slide 3: Introduction
Sensor networks
  Made up of large numbers of small, resource-constrained nodes called motes
  Operate unattended for long periods of time
Sensor networks need to evolve
  Code can be changed during the lifetime of the network
  New code must be propagated to all the nodes
Networking is expensive
  High energy transmitters drain the battery of the mote
  Constant communication means lower lifetime of a network
Two conflicting goals
  Changes to running code need to disseminate quickly
  Maintaining consistent code should have close to zero cost
Notes: Unattended in buried an active burrow or implanted in a tag on an animal
Networking hardware is generally simple, 10s of Kbps. Single packet sent uses the same power as executing a thousand instructions

## Slide 4: Introduction cont.
Authors present Trickle: an algorithm for code propagation and maintenance
Draws on two major areas of research
  Controlled, density-aware flooding research for wireless and multicast networks
  Epidemic and gossiping algorithms for maintaining data consistency in wired, distributed systems
It has been observed that transmitted code is generally very small
  Verbose code needs demands concise representations
Basic overview of Trickle
  Uses polite gossip: if a node hears gossip with the same metadata as its own, it will not gossip and if it hears old gossip it will broadcast new code
  Nodes dynamically adjust gossiping attention spans in order to reduce overhead

## Slide 5: Methodology
Three platforms to investigate the Trickle algorithm
  High-level, abstract simulation
  TOSSIM, a bit-level simulator for TinyOS
  Actual TinyOS mica2 nodes deployed in a lab
    900 MHz radio, 128KB D+I memory, 4KB of RAM, 7MHz, 8 bit μC
    Effective bandwidth is 40, 36-byte, packets per second
Abstract simulation
  Quickly evaluates changes in the algorithm and its parameters
  Just an event queue that outputs transmission amount and has various input parameters
    Run duration
    Boot time
    Uniform packet loss rate
TOSSIM
  Compiles from TinyOS code, simulating complete programs
  Includes a CSMA MAC protocol
  Model a network as a directed graph
  Can simulate bit errors and hidden terminal problem
  Uses a statistical packet loss rate as shown here

## Slide 6: Trickle Overview
Two goals: propagation and maintenance
  Propagation should be quick
  Maintenance should cost very little
    Cannot be free because you must communicate in order to tell if code is stale
  Assumes reprogramming events are uncommon
    O(minutes)
  Assumes nodes can succinctly describe their code
    Can tell if stale with metadata contained in a single packet
Two states for a cell (neighborhood): everyone is up to date, or the need for an update is detected
  Detection can occur if a node broadcasts old data or if a node receives newer data
Communication can be either transmission on reception
  Allows to scale
  Communication rate can be kept independent of node density
    Amount of bandwidth used in a cell is independent of cell size
  Conserves bandwidth and power

## Slide 7: Maintenance
Each node maintains a counter, , a threshold, , and a timer, , in the interval
  is a small, fixed integer
  is uniformly distributed in its range and can be varied
  When a node hears identical gossip, it increments
  At time , if , the node will broadcast its code
  When the interval of size completes, and are reset
  If a node with code hears a gossip of , it broadcasts a code update to that node
  If a node with code hears code , it broadcasts its code in order to receive an update
Performance
  Each node broadcasts at most once per period
  In perfect conditions (lossless, non-interfering motes) there will be transmissions per cycle
  If there are multiple cells, , each with nodes, this will go up to transmissions -- regardless of
  Random selection of ensures even distribution
  Expected latency for detection is
Assumptions!!!

## Slide 8: Maintenance cont.
Maintenance in the presence of loss
  Packet loss is common
  For a given loss rate, number of transmissions grows with
  This logarithmic scaling is impossible to escape
    Increase represents the worst case, expected case must transmit more to meet requirements
    Some nodes miss an update and need it to be repeated
Maintenance without clock synchronization
  Clock sync is a network intensive, expensive ordeal
  Causes a short-listen problem
    A subset of nodes have small
    With sync’d clocks the shortest of the set will quiet the rest
  Short listen problem causes transmissions to go up with all of which are redundant
  Solution is a listen-only period, reducing the redundancy significantly
    is now selected in the interval
Notes: Why not have a longer listen-only period: breaks down in the nominal case

## Slide 9: Maintenance cont.
Multiple Cells
  TOSSIM used to simulate larger systems
  Hidden node problem accounted for
  Scales as expected when hidden node problem ignored
    Scales poorly with high density systems if not ignored
      Result of limitation of the CSMA protocol

## Slide 10: Load Distribution
Shown that Trickle imposes low system overhead
  But is the overhead spread evenly
Results of a TOSSIM simulation show that load is correctly distributed
  Simulation of 400 mote network in a 20x20 grid with 5 ft spacing
  Transmissions per interval are uniformly distributed
    Any non-uniformity can be attributed to statistical variation
  Receptions are evenly distributed everywhere except in the edge of the grid
    Edges have less multi-cell interference
      Motes in center has 4x the neighbors and multiple cells it can hear
      Motes in edges can hear very few cells

## Slide 11: Propagation
Trickle can use the maintenance system to rapidly propagate code
  Large was shown to reduce maintenance cost
  However for fast code propagation, a low is desired
Trickle dynamically varies in order to reduce overhead while still maintaining consistent code
  has a lower bound and upper bound
  Whenever expires without an update, it doubles until it reaches
  When a node installs an update, is reset to
Nodes gossip more frequently when a change occurs
  New information is dissemenated quickly
  Once code is installed in most nodes, gossiping dies down

## Slide 12: Propagation Results
Notes:   TL: Simulation of 400 mote network in a 20x20 grid with 5 ft spacing (spacing, Th) no real consistent tradeoff b/w th and effectiveness
  BL: (a) shows hidden node effect
R: Nineteen nodes actually deployed tl=1s th=60s. RC is 40 experiments, avg is dotted. LC is distribution, long tail b/c of loss and exp scaling of tau, ramp up due to granularity of timers, could actually be artifact

## Slide 13: Discussion
Trickle is small
  70B of RAM, 2.5KB of machine code which can be optimized by 30%, low duty cycle
Assumes nodes are always on
  Not true of energy conserving motes that power cycle
  TDMA schemes can be used to schedule Trickle times
Trickle could be used to disseminate any kind of data
  Designed for code propagation but only assumptions were low frequency and small size
  Could limit propagation scope by adding predicates to broadcast data
    Good for data replication among only a cell

## Slide 14: Conclusions
Using dynamic and listen-periods, Trickle effectively balances the need of quick propagation and low maintenance overhead
Simple mechanism means low resource overhead
In one empirical experiment, Trickle imposed an overhead of 3 packets per hour but reprograms the system in less than 30 seconds with no intervention from the user

## Slide 15: A Key-Management Scheme For Distributed Sensor Networks
Laurent Eschenauer and Virgil D. Gilgor University of Maryland Published in 2002 Proceedings of the 9th ACM Conference on Computer and Communications Security

## Slide 16: Introduction
Distributed Sensor Networks (DSNs)
  Battery powered, resource constrained
  Limited mobility after deployment
  Large scale (tens of thousands of nodes)
  May be deployed in hostile environments
  Networks are self healing; they allow nodes to join and leave freely
  Subject to capture or manipulation by adversaries
Communication security constraints
  Typical sensor nodes lack computational power
  Typical asymmetric cryptosystems are impractical due to high computation
    Energy required to complete a 1024-bit RSA is 2 orders of magnitude greater that a 1024-bit AES
  Symmetric-key ciphers, low-energy authenticated modes, and hash functions become the tool of choice for protecting communications
Key Management constraints
  Traditional, internet-style key exchange based on a trusted third party is impractical due to limited communication range
  Key pre-distribution
    Single mission key would mean a compromised system if one node was captured
    Pair-wise private keys would require (n-1) keys stored per node, n(n-1)/2 keys in the DSN

## Slide 17: Overview of the Basic Scheme
Key distribution
  Pre distribution
    Generate a large pool of keys (100K-1M)
    Draw k keys out of the pool without replacement for each node’s key ring
    Load key ring on to memory of each sensor
    Save a key identifier for each key ring on a trusted controller
  Shared-key discovery
    Every node discovers its neighbors and with which neighbors it shares keys
      Key identifiers can be broadcast in plaintext
      Or broadcast the identifiers k times, each encrypted with a certain key
    This phase establishes the topology as seen by the DSN where a link is made only if the two nodes are in range and share a key
  Path-key establishment
    Assigns a path-key to pairs of sensor nodes in range of each other that do not share a key but are connected through other nodes
    Uses left over keys in key ring
      Key ring is statistically over provisioned
      k chosen to allow for extra keys for revocation, node joins, and path-key establishment

## Slide 18: Basic Scheme cont.
Revocation
  When a node is compromised assume the key ring is compromised
  Controller node broadcasts a revocation message containing a signed list of keys compromised
    Signed with key generated in pre-distribution for node-controller communication
  Nodes verify list, remove keys
    Links may disappear so shared-key discovery and path establishment need to be restarted
  Revocation only affects a small set of the global key space but all links of the compromised node
Re-keying
  If keys in a node expire, nodes self revoke their keys
    Very inexpensive, can just message affected nodes
  Not very common as key lifetime usual exceeds node lifetime
Sensor node capture
  Two levels of attack: data manipulation and physical control
  Sensor data manipulation is hard to detect without off-line, computationally-intensive algorithms and can only be solved with redundancy
  Physical control of a device can lead to sleep-deprivation attacks and could give away the key ring
    Shielding of nodes can be used to detect tampering and trigger key ring erasure
    Even if node lacks shielding, key-ring algorithm will only give away k keys where
      Mission key scheme gives away all nodes
      Pair wise key scheme results in n – 1 keys compromised

## Slide 19: Analysis
Using graph theory we can determine what p, the probability two nodes share a key, needs to be in order to have the system be connected
  Degree of a node, d, is the number of edges a node has
    When p is zero, the graph does not have any edges
    When p is one the graph is fully connected
  Using results from graph theory we can find p as shown here
    To increase probability by an order we need an increase of 2 in node degree
How to choose k and P, the key ring size and key pool?
  p limited by wireless effects (cell size)
  Deterministic equation can be derived for p given P and k as shown

## Slide 20: Simulations
Network of 1k nodes simulated
  Average density of 40 nodes per cell
Average path length affected by k
  Small k means two nodes may miss to share a key and therefor need to find an alternate, longer path
  These long paths are only used once
Number of hops is to reach a neighbor is very small for large enough k
We can also see that only 50% of keys are used to secure links, 30% protect only one link, 10% two, etc.
  Compromise of one key ring leads to compromise of a link with those probabilities

## Slide 21: Conclusions
Presented a novel key-management scheme for large DSNs
  Approach is simple to avoid computational overhead while deployed
  Technique is scalable and flexible
    Tradeoffs can be made between memory overhead and connectivity
  Security is better than traditional schemes