## Slide 1: Tyler Lovelly, Donavon Bryan, Andrew Milluzzi EEL6935 - Embedded Systems Seminar Spring 2013
Topic: Aerospace Applications
02/07/13

## Slide 2: Pulling the Pieces Together at AFRL
Wegner, Peter M.; Kiziah, Rex R.; "Pulling the Pieces Together at AFRL", 4th Responsive Space Conference, April 24–27, 2006, Los Angeles, CA

## Slide 3: Introduction
AFRL Space Vehicles Directorate pushing technology to enable rapid satellite development and launch
  Minimal cost and response time emphasized
Lead to heavy investment in new technologies for rapid spacecraft design and integration
Experiments to demonstrate capabilities
  TacSat Missions
  Test beds and simulations

## Slide 4: Operationally Responsive Space
Joint effort between several DoD agencies to provide cheap and rapidly deployable space capabilities
Plans laid out in Space Science and Technology Vector-2
  Total mission cost <$30M
  Less than one year development time
  Launch in 6 days from call-up
  Rapid integration with new technologies with new plug-n-play standards
  Small operator crews (<4 people)

## Slide 5: Filling the Gaps
Few options considered for Responsive Space
  On-orbit storage of spacecraft
    Deemed prohibitively expensive
  Ground storage of spacecraft
    Adopted cost effective solution
Technological advancements often outpace the rate of spacecraft development
  Need way to rapidly develop spacecraft and integrate new technology
RSATS- Responsive Space Advanced Technology Study
  Investigated technologies to develop these capabilities
  Proposed plug and play architectures utilizing “internet-like” data-bus architectures
  Identified key technologies to be developed
    Communications for tactical tasking and data dissemination
    Miniaturized spacecraft components and payloads
    Rapid deployment tools
    Modular plug and play spacecraft architectures and components

## Slide 6: Spacecraft Plug-n-Play Avionics
Responsive capability through network structure
  Similar to the internet
  Plug-n-Play structure
    Standard Interfaces
    Modular components
  Low-data-rate systems
    SPA-U – similar to USB 1.1
  High-data-rate systems
    SPA-S – similar to European Spacewire
Notes: SPA = Spacecraft Plug-n-Play Avionics

## Slide 7: Spacecraft Plug-n-Play Avionics
Support for:
  Data transport
  Power delivery
  Synchronization
  Single point ground connection
  Self descriptive ‘hooks’
Features added to existing standards
  28 V power
  Synchronization pulse (1 per second)
  Test interface

## Slide 8: Satellite Data Model
Components can share resources and data without needing to be programmed
  XML Transducer Electronic Data Sheet (xTEDS)
    Identifies device
    Identifies resources for device
  Devices can post data to network, SDM will route it, using xTEDS to other parts of the network

## Slide 9: Responsive Space Test-bed
Responsive Satellite Cell
  Mock of system to demo real-time operation
  Hardware-in-the-loop simulation
Satellite Design Tool
  Design satellite based on mission characteristics
  ‘Wizard’ approach
Ground Control Station and 6-DoF Simulator

## Slide 10: Extending Plug-n-Play
Moving from avionics to structural elements
Leveraging SBIR grants to get additional systems for SPA
  Generate a ‘PnP Catalog’
Increase autonomous operation of satellites
  Fault detection
  Reconfiguration based on goals
  Collaborative decision making between satellites
Notes: SBIR = Small Business Innovative Research

## Slide 11: Operational Experimentation
TacSat-2
  Low Earth Orbit (LEO)
  Specific Emitter Identification (SEI)
    Downlink in same orbit pass
  Common Data Link (CDL)
  On-Orbit Checkout Experiment (OOCE)
  Autonomous Tasking Experiment (ATE)
TacSat-3
  Low-cost Hyperspectral Imager (HSI)
    HSI analysis of a given region for specific objects
    Returns tagged image
  2nd generation CDL radio
Notes: SBIR = Small Business Innovative Research

## Slide 12: Modeling Simulation & Analysis
On-orbit experimentation is critical step
Tech. must provide cost-effective military benefit
Modeling Simulation and Analysis (MS&A)
  Provides initial military benefit analysis
TacSat-2/TacSat-3 analyzed with MS&A
  Provide useful/timely info to warfighters
  Unpredictable overflight time & innovative
  sensors counter enemy CC&D measures
  Gives field commanders significant advantage
Notes: SBIR = Small Business Innovative Research

## Slide 13: Conclusions / Future Research
AFRL chartered to develop new tech for future national security needs
New series of tech & experiments on space-craft
  Provides tactical warfighter real-time info
  Can be rapidly tailored for new technologies
  Fast time to place into orbit
  Tasked directly from tactical theater, returns valuable info
AFRL pursuing Responsive Space tech & space-craft
  Robust Plug-n-Play hardware & software
  Small, lightweight, low-cost components
  Ground-based & space-based experiments, test beds, analysis
  Operational experimentation with TacSat-2/TacSat-3
Notes: SBIR = Small Business Innovative Research

## Slide 14: Development of the Malleable Signal Processor (MSP) for the Roadrunner On-Board Processing Experiment (ROPE) on the Tacsat-2 Spacecraft
R.L. Coxe, et al; "Development of the Malleable Signal Processor (MSP) for the Roadrunner On-Board Processing Experiment (ROPE) on the Tacsat-2 Spacecraft", 2005 MAPLD International Conference, September 7-9, 2005, Washington D.C.

## Slide 15: Introduction
Malleable Signal Processor (MSP)
  Reconfigurable computing engine.
  Five radiation-tolerant Virtex-II FPGAs
Roadrunner On-Board Processing Exp. (ROPE)
  Multispectral Imaging (MSI) payload
  AFRL TacSat-2 satellite
DoD Responsive Space Initiative

## Slide 16: Development Plan
Air Force Research Lab: Space Vehicles
  Phase I Small Business Innovation Research (SBIR)
  Physical Sciences Inc. (PSI)
MSP requirements
  Pipelined radiometric calibration
  JPEG image compression
  Anomaly detection on multispectral imagery
  Rapid prototyping
  On-demand functional upgrades

## Slide 17: Responsive Space
Air Force Responsive Space Initiative
  Demonstrated in TacSat missions
  6-12 months development time
  <3 years lifetime
  Stored to orbit in <1 week
  Modular design methodologies, standard interfaces
  Collection/downlink of mission data in single pass
  Dynamic re-tasking
  “faster-cheaper”

## Slide 18: ROPE Payload
Roadrunner On-Board Processing Exp. (ROPE)
  Real-time, MSI processing system
Major components
  Wide-field MSI unit
  MSP
  Fusion Processor (FP)
  8GB solid-state buffer

## Slide 19: Malleable Signal Processor (MSP)
Five radiation-tolerant Virtex-II FPGAs
Military/industrial temperature grade COTS
MicroBlaze soft processor in Service FPGA
  Software adjustable parameters
Radiation-tolerant configuration PROMs
MSP FPGA logic resources
MSP Flight Eng. Model

## Slide 20: Malleable Signal Processor (MSP)
Operational modes or “personalities”
  Personality #1: 16:1 Lossy JPEG
  Personality #2 : 4:1 Lossy JPEG
  Personality #3: Calibration
  Personality updates possible from ground
Single-Event Upsets (SEUs)
  SRAM-based FPGAs vulnerable
  Data errors, functional failures
  MSP/ROPE has no TMR, bitstream scubbing
  FP reconfigs/power-cycles MSP after 100ms timeout

## Slide 21: System Development Issues
Responsive Space is “wave of the future”
  TacSat-2 one of the first missions
Integration of hardware was major hurdle
Third-party IP cores used
  Xilinx: COREGEN & MicroBlaze
    No major problems, new Xilinx ISE release solved issues
  Amphion Semiconductor: Lossy JPEG core
    Required much time/effort, ambiguous docs & timing data
  Birger Engineering: Lossless JPEG core
    Never met timing, removed from project

## Slide 22: Conclusions
Malleable Signal Processor (MSP)
  Five radiation-tolerant Virtex-II FPGAs
Roadrunner On-board Processing Exp. (ROPE)
  Multispectral Imaging (MSI) payload
TacSat-2 mission for AFRL Space Vehicles
  Air Force Responsive Space Initiative
  “faster, cheaper, and good enough”

## Slide 23: Further Research
MSP supports rapid-prototyping of reconfig. computing apps without hardware modification
  Sonar beamforming
  Other pipelined FFT processing applications
  Real-time Hyperspectral Imaging (HSI)
  More sophisticated anomaly and edge detection
  Neural computation engines
Further fault-tolerance for SEU mitigation
  Triple Modular Redundancy (TMR)
  FPGA bitstream scrubbing

## Slide 24: Achieving Multipurpose Space Imaging with the ARTEMIS Reconfigurable Payload Processor
Troxel, I.A.; Fehringer, M.; Chenoweth, M.T.; , "Achieving Multipurpose Space Imaging with the ARTEMIS Reconfigurable Payload Processor," Aerospace Conference, 2008 IEEE, vol., no., pp.1-8, 1-8 March 2008

## Slide 25: Introduction
ARTEMIS: Advanced Responsive Tactically Effective Military Imaging Spectrometer
  Payload for the TacSat-3 mission
Features hybrid processing power, general purpose processor board and FPGAs
Design focused on flexibility, reusability, fault tolerance

## Slide 26: ARTEMIS Processor Architecture
Four types of boards constitute ARTEMIS
  Power Supply
    Receives 28V from spacecraft, regulates and distributes to other boards
  Universal Power Switch
    Relays commands for sensor power management
  G4-based single-board computer (G4-SBC)
  Responsive Avionics Reconfigurable Computer (RA-RCC)

## Slide 27: G4-SBC
Includes MPC7457 processor, memory controller, and support FPGA
  Support FPGA provides fault tolerant memory interfaces, and external bus communication
  External interfaces
    RS422 LVDS
    cPCI
    SpaceWire
    GigE
Primary payload controller
  Controls external spacecraft interfaces
  Manages data up/down links
  Orchestrates data processing

## Slide 28: RA-RCC
Controls sensor functionality, mass data storage, performs on-board processing of sensor data
4 total FPGAs
  Actel RTAX2000
    Provides PCI interface to backplane and between other FPGAs
    Controls FPGA scrubbing
    Controls storage devices and UPS serial interface
  3 Xilinx V4 LX160
    adaptable high-speed mezzanine interface
    Highly customizable interconnects to sensors, mission flexibility
Flexibility designed for fault tolerance and reusability

## Slide 29: Reconfigurability for Fault Tolerance
Mezzanine I/O cards provide redundancy in sensor communications
  Varying degrees of redundant links can be established

## Slide 30: Fault Tolerance
Scrubbing configuration memory
  Handled by Rad-hard controller
Many options for triple modular redundancy in the RA-RCC
  Mezzanine cards can interface to external rad-hard voter
  Distributed voting
  Dedicated voter unit on COP
  Selective TMR

## Slide 31: TacSat-3 Mission
Operational from May 19 2009- Feb. 15 2012
Joint AFRL and NRL effort
Primary focus was autonomous HIS processing
  Handed over to Air Force in 2010
  First satellite to provide recon within 10 minutes of passing

## Slide 32: Conclusions/ Future Work
Mezzanine interface decouples sensors and processors
  Allows for reuse in future generations
Fault tolerant architecture achieved with commercial components
Upgrades and future missions with ARTEMIS planned

## Slide 33: Tactical Satellite 3 CDL Communications, a Communications Link for Mission Utility
Galindez, Richard; Davis, Thom; , "Tactical Satellite 3 CDL Communications, a Communications Link for Mission Utility," Military Communications Conference, 2007. MILCOM 2007. IEEE , vol., no., pp.1-6, 29-31 Oct. 2007

## Slide 34: Introduction
Common Data Link
  Wideband communications waveform
  Launched in December 2006 with TacSat-2
    274 Mbs down
    200 Kbs up
    12” parabolic antenna for ground communication
    Horn antenna for rover communication
  MMA originally for F-16
    Not suited for LEO
Notes: Microwave Modem Assembly

## Slide 35: Background on CDL
Common Data Link (CDL)
  History
    Started in 1979 with Interoperable Data Link (IDL)
    In 1988 the Assistant Secretary of Defense ordered development of common communication architecture for all DoD services
      Decision based on success of IDL
  Full duplex, jam resistant spread spectrum signal
    Digital microwave system

## Slide 36: The Difference of Space
Space is much harsher environment than Earth
  Temperature swings
  Limited power
    Separate power for Tx/Rx
  Size and weight restrictions
    The bigger an object and the heavier, the more it costs to launch
    No gases/liquids for heating/cooling
    Not likely to be fixed
  Fault-tolerance
    Electronic failure
    Radiation
Notes: Photo from NASA: http://www.nasa.gov/images/content/429961main_cubesat_1.jpg

## Slide 37: Operational Responsive Space
Tactical Satellites (TacSats)
  Low cost
  Small
  Rapid response
  Not a perfect system
    Learning platform
    2 years to launch vs. 5+ years for conventional

## Slide 38: Need for CDL in Space
Existing Infrastructure
  CDL is military standard
  Existing ground stations
    Multiplex with airborne systems
Reduced Lifetime Costs
  No need to purchase new system for communication
  Only one system to support
  Parts can be reused between systems

## Slide 39: Example
Ground uplinks collection task
TacSat-3 Moves to target position and collects data
  Data is processed and sent back to earth
TacSat-3 waits for new task
  Raw data is sent down when it has next opportunity

## Slide 40: TacSat-3 Part Analysis
Radio Frequency Assembly
Parabolic Antenna
  Special modifications required to ensure stability in temperature swing
Horn Antenna
Microwave Modem Assembly
  More than 12,000 parts
    1,000 active parts
    350 unique parts
Limits on Tin, Zinc, and Cadmium
  Some connectors had to be modified to get around Cadmium restriction

## Slide 41: Radiation
Total Ionizing Dose is less than 70 rad
  Not considered a significant risk to electronics
Single Events harder to estimate
  Figure 4. shows lower high energy particle interference with 41⁰ vs. 60⁰
  System only on for 45 minutes per day
    System also powers down over South Atlantic Anomaly

## Slide 42: Summary and Conclusion
TacSat-3 is an agile development approach to satellites
Validated solutions to many of the problems that come with using terrestrial systems in space
System leverages hardware reuse while still ensuring operation in space
Paper does not go into exact details of success
  No discussion on tests performed and observed performance