## Slide 1: Energy Optimization Techniques: FPGA Glitch Reduction
Patrick Cooke and Elizabeth Graham

## Slide 2: Field-Programmable Gate Arrays
Used to implement digital systems
  Pros
    Flexible
    Low time-to-market
  Cons
    Consumes up to 10x more power than equivalent ASIC design
      Barrier for power-sensitive applications

## Slide 3: FPGA Architecture
Island-style
  Logic blocks connected by programmable routing network
Look-up-tables (LUTs)
  k-input LUT supports k variable logic functions and requires 2k configuration bits
  Hardware implementation of truth table

## Slide 4: Power in FPGAs
Static power
  Current leakage in transistors
Dynamic power
  Signal transition between logic-0 and logic-1
    Functional transition
      Necessary for correct operation of circuit
    Glitch
      LUT output transition due to unbalanced delays at inputs
      4-73% of total dynamic power
      Average of 22.6%

## Slide 5: Glitch Example
Unbalanced Delays
Balanced Delays

## Slide 6: Glitch Reduction Techniques
Algorithms that balance delays
  Technology mapping stage
    Mapping based on glitch-aware switching activities
  Routing stage
    Faster arriving inputs delayed by extending path
  Architectural level
    Programmable delay elements
  All incur area or performance overhead
Flip-flop insertion/pipelining
  Fewer logic levels reduces opportunity for imbalanced delays
Logic manipulation algorithms
  Change don’t-care values to reduce glitching

## Slide 7: FPGA Glitch Power Analysis and Reduction
Warren Shum and Jason H. Anderson
University of Toronto
Department of Electrical and Computer Engineering
Published in ISLPED 2011

## Slide 8: Proposed Solution
Glitch reduction optimization algorithm based on don’t-cares
  Selects don’t-care output values of LUTs in such a way that reduces glitching
  Performed after placement and routing
  Uses timing simulation data for guidance
  No area or performance overhead
  Inspired by hazard-free logic synthesis techniques for asynchronous circutis

## Slide 9: Don’t-cares
Entries in truth table where output can be set as either logic-0 or logic-1 without affecting correctness of circuit
Two categories
  Satisfiability don’t-cares (SDCs)
    Particular input pattern can never occur on inputs
  Observability don’t-cares (ODCs)
    Output cannot propagate to circuit’s primary outputs
SDC
ODC

## Slide 10: Dynamic Power Model
Variables
  n : number of nets in circuit
  Si : switching activity of net i
  Ci : capacitance of net i
  f : frequency of circuit
  Vdd : supply voltage
Algorithm focuses on switching activity

## Slide 11: Removable Glitch
0

## Slide 12: Don’t-care Analysis
ABC logic synthesis network
  Developed at UC Berkeley
  Boolean satisfiability (SAT)-based complete don’t-care analysis
    Determines don’t-care minterms
  Utilizes miter circuit to find don’t-cares
    If C(x) = 0, y is don’t care minterm of LUT f

## Slide 13: Motivational Experiments
Examined amount of glitch power dissipated by 20 MCNC benchmark designs
Experimental setup
  Altera Quartus 10.1
  65nm Stratix III family
ModelSim 6.3e used for functional and timing simulation
  5000 random input vectors
Dynamic power computed using Quartus PowerPlay
Glitch power = dynamic power(timing) – dynamic power(functional)

## Slide 14: Motivational Results
Percentage of dynamic power from glitches
  Range: 5.8-45.4%
  Average : 26.0%
Percentage of LUT input states that are don’t-cares
  Range: 0.8-37.2%
  Average: 15.1%

## Slide 15: Glitch Reduction Algorithm
Inputs
  Placed and routed netlist
  Value change dump (VCD) file
    Results of timing simulation
Algorithm progresses from shallower levels of LUTs to deeper ones
In each level, LUTs examined in descending order of power consumption

## Slide 16: Glitch Reduction Algorithm
For each LUT in netlist
  Compute don’t-cares of LUT
    ABC SAT-based don’t-care analysis
  Scan input vectors
    Voting mechanism
    Details on next slide
  Set values of don’t-cares and update netlist
    Majority vote decides don’t-care value
    Netlist updated to guarantee equivalent functionality

## Slide 17: Input Vector Scan
Sequence of local input vectors to LUT extracted from VCD file and examined in order
When don’t-care input vector is reached
  Find value of closest care state before and after don’t-care input vector
  If these values are identical, vote for that value
  Otherwise, no vote is cast
Each don’t-care in LUT has separate tally of votes

## Slide 18: Algorithm Walkthrough
0
0

## Slide 19: Iterative Flow
To verify modified don’t-care values, algorithm iterates until convergence
Placement and routing are not run again
Runtime on order of minutes
No modifications to timing characteristics

## Slide 20: Experimental Study
Same experimental setup as motivational experiments
  20 MCNC benchmark circuits
  Altera Quartus 10.1
  65nm Stratix III family
  ModelSim 6.3e
Combinational equivalence checking used to ensure circuit functionality unchanged
Three passes of optimization loop
  Negligible change after three passes
Worst-case sets don’t-cares to the opposite value of that obtained by algorithm

## Slide 21: Experimental Results
Dynamic power reduction
  Average: 4.0%
  Peak : 12.5%
Glitch power reduction
  Average: 13.7%
  Peak: 49.0%
Optimized vs. worst-case dynamic power reduction
  Average: 9.8%
  Peak: 30.8%

## Slide 22: Power & Don’t-care Ratio vs. Fanout
Average signal power increases with fanout due to increase in capacitance
Average don’t-care ratio shows decreasing trend with respect to fanout
Signals consuming most power are poor targets for glitch reducing algorithm based on don’t-cares

## Slide 23: Average Vote Bias
Vote bias is percentage of votes that were cast for the more popular setting
For all circuits tested, highly preferable setting existed for all don’t-cares
Suggests don’t-care values can be picked with high degree of confidence

## Slide 24: Conclusion
Future Work
  Integrate algorithm into power-aware FPGA CAD flow
  Investigate whether other stages of CAD flow could improve algorithm effectiveness
  Reduce runtime by integrating algorithm with incremental timing simulation
Shortcomings
  Algorithm seems to only address satisfiability don’t-cares (SDC)

## Slide 25: GlitchLess: Dynamic Power Minimization in FPGAs through Edge Alignment and Glitch Filtering
Julien Lamoureux, Guy G. Lemieux, Steven J.E. Wilton
University of British Columbia
Department of Electrical and Computer Engineering
Published in TVLSI 2008

## Slide 26: GlitchLess Overview
Adds programmable delay elements
  To align arrival times
  Act as filter to eliminate off-chip glitches
Applied after routing
Can be combined with other power-saving methods
Original circuit with glitch
Glitch removed by delaying input c

## Slide 27: Trade-Offs
Save glitch power
Delay elements
  Area overhead (modest increase)
  Speed overhead (very minimal since only early-arriving signals are delayed)
  Power overhead for driving additional circuit elements

## Slide 28: How Long Can Delays Be?
Actual range varies between benchmarks, but they all have similar shape
Most pulse widths < 10ns

## Slide 29: How Small Can Delays Be?
Longer pulse widths (over 200ps) are the ones that need to be aligned

## Slide 30: Potential Power Savings

## Slide 31: Programmable Delay Elements
Minimum delay
  Small: Align edges more precisely
  Large: Less overhead
Maximum delay
  Small: Less overhead
  Large: Able to suppress glitch from longer pulse
Number of delay elements (on input vector)
  Small: Less adaptable
  Large: More overhead
2

## Slide 32: Programmable Delay Elements
Each delay stage has slow and fast mode
  Mode controlled by value in SRAM
Bypass stages for very small delay
Number of stages determined by delay element parameters
Stage
Notes: Configuration of each delay element determined after placement and routing (when accurate timing is available)

## Slide 33: Placement of Delay Elements
Original
Scheme 1: LUT Inputs
BLE – Lookup Table and Flip-flop pair

## Slide 34: Scheme 1: LUT Inputs
Each input delayed individually
  Independently determine delay
  Delay element optional for each input
  Same minimum and maximum delay for all elements
Overhead increases exponentially with Number of delay elements

## Slide 35: Placement of Delay Elements
Original
Scheme 2: Gradual LUT Inputs
BLE – Lookup Table and Flip-flop pair

## Slide 36: Scheme 2: Gradual LUT Inputs
Delay elements in same location as Scheme 1
Maximum delay decreases by 50% for each input of an input vector
  Works due to variation of input arrival times
Reduces area overhead for large Number of delay elements without loss of effectiveness

## Slide 37: Placement of Delay Elements
Original
Scheme 3: LUT Inputs + Outputs
BLE – Lookup Table and Flip-flop pair

## Slide 38: Scheme 3: LUT Inputs + Outputs
Scheme 1, add delay elements to BLE output
  Output delay elements ignore parameter for Number of delay elements
1 output delay element eliminates multiple input delay elements
  Reduces overhead

## Slide 39: Placement of Delay Elements
Original
Scheme 4: CLB and LUT Inputs
BLE – Lookup Table and Flip-flop pair

## Slide 40: Scheme 4: CLB and LUT Inputs
Same concept from Scheme 3
Delay elements closer to CLB input (than to output of LUT)
Every CLB input has a delay element

## Slide 41: Placement of Delay Elements
Original
Scheme 5: LUT Inputs + Bank
BLE – Lookup Table and Flip-flop pair

## Slide 42: Scheme 5: LUT Inputs + Bank
Scheme 1, add bank of delay elements
  Any signal can use bank
Reduce number, size of input delay elements
  Long delays use bank
  Short delays use small input delay elements
Minimum bank delay = maximum input delay

## Slide 43: Experimental Setup
Area, power, and delay estimations
VPR (Versatile Place and Route) simulations
  Models original FPGA circuit
  Inertial Delay Model
HSPICE simulations
  Models delay elements
10 largest benchmarks each from MCNC, ISCAS89 benchmark suites
Manually set delay element parameters
Notes: Inertial Delay Model
  Mimics filtering effect of FPGA elements
Manually determine suitable values for the delay element parameters for each scheme (5 combinations)
Scheme 1/2 mimumum delay time = .25 ns (lower pulse widths are filtered out by other circuitry)
Scheme 1/2 maximum delay time = 8 ns (90% of pulse widths are less than that)
Scheme 1/2 number of delay elements = K – 1 (obviously the slowest path doesn’t need a delay element)

## Slide 44: Delay Element Overhead

## Slide 45: Select Results
Table 10: Overall power savings. (Abbreviated)
Notes: LUT size = 4
Results for 5 and 6 were similar to 4 (so not shown/given in paper)

## Slide 46: Conclusions and Future Work
Scheme 1 saves 18.2% of power
Scheme 2 saves 16.8% with less area and power overhead
Investigate newer technology
  Tend to have higher leakage power
Circuit-level implementation
  Reduce area overhead, increased PVT tolerance
Notes: PVT variation = Process, voltage, temperature

## Slide 47: Shortcomings
No physical experiments (all simulation-based)
Misuse of data cited from another paper
  “dynamic power still accounts for 62% of total power”
Tuan, Tim, et al. "A 90nm low-power FPGA for battery-powered applications."Proceedings of the 2006 ACM/SIGDA 14th international symposium on Field programmable gate arrays. ACM, 2006.
Notes: Paper from Xilinx

## Slide 48: Questions?