## Slide 1: Partial Reconfiguration Not just a half baked job of reconfiguring
Rohit Kumar
Research Student
University of Florida
Dr. Ann Gordon-Ross
Associate Professor of ECE
University of Florida

## Slide 2: Partial Reconfiguration is All Around Us
Changing situations…
…require part of the system to reconfigure on the fly

## Slide 3: Partial Reconfiguration is All Around Us
But, FPGA reconfiguration is disruptive
  Resets the device
  Lose all data
  Causes downtime
Downtime is dangerous

## Slide 4: Full Reconfiguration:
This is your FPGA
Task 1
Task 2
This is your
FPGA on PR
Task 1
Task 2
Static

## Slide 5: Why Partial Reconfiguration?
So what??
I’ll just put both tasks on the same device!
Sure, why not?
But, devices have limited space!
Not impressed
FPGA
Task 1
Task 2
Task 3
Task 4
Task 5
Task 6
Reason #1
Sharing many tasks on a single region saves area!

## Slide 6: Why Partial Reconfiguration?
I got it! I’ll just use PR on a tiny cheap FPGA and time- multiplex everything!
Okay, we’ll give you that one
But, it’s a trade off
  The more parallelism, the better the performance
  Plus, some tasks must be run in parallel
Reason #2
Using less area on a smaller device is less costly!

## Slide 7: Why Partial Reconfiguration?
So that’s it??
I pay a bunch more just to use less area?
Well, you know you could save power?
  Imagine you have two versions of a task
    High-performance version
    Low power version
  When performance is critical
    Load the high-performance version
  When performance is less critical
    Load the low-power one
Man, what a buzz-kill
FPGA
Reason #3
Replace tasks with low-power versions when possible!

## Slide 8: Why Partial Reconfiguration?
So what??
I’ll just use clock gating (CG) and dynamic frequency scaling (DFS), both of which are available for Xilinx FPGAs
Right… well… you see… actually….
Hmm…
Shut up

## Slide 9: Why Partial Reconfiguration?
Okay, but I’m not sold unless there are 4 reasons.
Did you know PR keeps your device safe in space?
  In space, cosmic radiation corrupts SRAM!
  These are called single event upsets (SEU)s
With PR, you can patch FPGA configuration memory
  Without turning off the device
  This is called “scrubbing”
But FPGA configuration memory uses SRAM!
FPGA
10111011
FPGA
01101100
Reason #4
PR keeps circuits safe in harsh environments

## Slide 10: So you wanna make a PR design…
First, we make partitions
  Partitions are like black boxes
    They start out empty
    Then we load modules
  Modules run tasks
  To change tasks
    Load a new module
    Old one is overwritten
Partition 1
Partition 2
The FPGA (not to scale)
a
b
a
f
f

## Slide 11: So you wanna make a PR design…
Modules have to fit like puzzle pieces
  Black boxes have a defined interface
  All modules must fit that interface
Where the ports are matters as well
  Ports must be in the same place for every module
  “Partition pins” are port location definitions
  They ensure connections are not broken during PR
Partition 1
Partition 2
The FPGA (not to scale)
a
b
a
f
f

## Slide 12: So you wanna make a PR design…
Quit sugar-coating it, sirs, I am not a child you know.
Oh, fine. This is what you’re going to learn today:
  Logically partitioning your application into modules
  Preparing your partitioned design in ISE
  Floor-planning the layout of your device in PlanAhead
  Implementing your design in PlanAhead
  Finding your inner child through meditation (time permitting)

## Slide 13: Step 1: Logical partitioning
Easy there buddy
Two components are mutually exclusive if
  Only one is used at a time
  One’s inputs don’t directly depend on the other’s outputs
Only mutually exclusive components share a partition
  So, before you can make your design…
  You must find as many of these as you can
The first step to make a PR design is breaking the application into sets of mutually exclusive components

## Slide 14: Step 1: Logical partitioning
Okay, lets do an example
This is an up/down counter
The add and the subtract
  …are mutually exclusive
  Only one is used
  They do not depend on each other
The store and the add
  …are not mutually exclusive
  The store depends on the add’s output
The add and subtract can share a partition
  The add forms one reconfigurable module
  The subtract forms another reconfigurable module
He’s still not reassured
Direction?
Direction = up
Result = 0
Result ++
Result --
Store Result
Get Direction
up
down
Direction = up
Result = 0
Result ++
count
Store Result
Get Direction
Result ++
PR!

## Slide 15: Step 2: Preparing your PR design
We’ve partitioned our design.
  Now let’s partition our code
Create a new ISE project

## Slide 16: Step 2: Preparing your PR design
Add a new VHDL source file
  This is going to be our top file with all of the structural descriptions

## Slide 17: Step 2: Preparing your PR design
This is our top file
  We have components for
    The DCM to stabilize the clock
    The partition (“count”)
    The static logic (“register_8b”)

## Slide 18: Step 2: Preparing your PR design
This is the our file
  We have components for
    The DCM to stabilize the clock
    The partition (“count”)
    The static logic (“register_8b”)
We wire it up like so

## Slide 19: Step 2: Preparing your PR design
To avoid errors
  Set the partition as a black box
  This will let us synthesize the | top file without any reconfigurable modules
Our reconfigurable modules
  Will be synthesized separately

## Slide 20: Step 2: Preparing your PR design
Now we need to make sure that our black box is not cut out
  Click on the top file
  Right click on “Synthesize XST”
  Choose “Process Properties…”
  Set “-keep_hierarchy” to “Yes”

## Slide 21: Step 2: Preparing your PR design
This our static logic
  Is basically a register
    …tied to the button
  It exports the current count
  It takes in the next value
Add this to your design

## Slide 22: Step 2: Preparing your PR design
Synthesize the top file!
You will get a warning
  …about the black box
  Don’t worry about it

## Slide 23: Step 2: Preparing your PR design
Now create a project for our add
  Each reconfigurable module needs its own project
  We’ll call the add “count_up”
  Add a new source, the VHDL isn’t tough

## Slide 24: Step 2: Preparing your PR design
To avoid errors
  We need to turn off a feature
    … that adds IO buffers to all the ports
  Right click “Synthesize – XST”
  Choose “Process Properties”
  Click “Xilinx Specific Options”
    It’s on the left pane
  Uncheck “Add I/O buffers”

## Slide 25: Step 2: Preparing your PR design
Make a new project for the subtract
  Call it “count_down”
  Follow the same procedure as “count_up”
  You’ll find the VHDL is very similar

## Slide 26: Step 2: Preparing your PR design
Synthesize both “count_up” and “count_down”
Create a UCF file for your top file
  This connects ports to physical pins on the FPGA
And now your design is ready to floor plan!

## Slide 27: Step 3: Floor planning the layout
We have partitioned our code
  Now lets decide where do these partition go in FPGA i.e., floor plan our partition
Xilinx PlanAhead is used for floor planning
After creating a new project for you top design you’ll get this

## Slide 29: Step 3: Floor planning the layout
Set the partition as reconfigurable partition
Assign reconfigurable modules to partitions

## Slide 30: Step 3: Floor planning the layout
Set the partition as reconfigurable partition
Assign reconfigurable modules to partitions

## Slide 31: Step 3: Floor planning the layout
Assign the FPGA area to the partition

## Slide 32: Step 4: Implementing your design
Now its quite a bit of mechanical clicking
  At the end you get full and partial bit streams
Full bitstream can only be loaded from outside of FPGAs
  SelectMAP based programmers
Partial bitstreams can be flashed from outside as well as inside of FPGA
  Instantiate ICAP based VHDL controllers in your design
DONE

## Slide 33: Now some cool stuff that our group has been doing in CHREC

## Slide 34: VAPRES: A Virtual Architecture for Partially Reconfigurable Embedded Systems
Abelardo Jara
Rohit Kumar
Research Students
University of Florida
Prepared by: Joseph Antoon
Presented by: Rohit Kumar
Dr. Ann Gordon-Ross
Assistant Professor of ECE
University of Florida

## Slide 35: Adaptive Hardware Applications
Kalman filter used for target tracking
  Finds likely location from noisy measurements
  Optimized filter depends on target type
Slow Target
Low Power | Constant gain
Low Bandwidth | Kalman Filter
Fast Target
High Power | Constant gain
High Bandwidth | Kalman Filter
Airborne Target
High Power | Variable Gain
Low Bandwidth | Multi-scale Smoother
Noisy Target
High Power | Variable Gain
Low Bandwidth | Kalman Filter

## Slide 36: Using Partial Reconfiguration
2. Platform studio
3. Import into ISE
6. Code PR
region HDL
System Specifications
1. Define system
5. Set PRRs as black boxes
top
static
prr_a
prr_b
4. Divide project into mandated hierarchy
7. Synthesize!
9. Map on to PlanAhead
8. Guess Estimate
a good floorplan
12. Write software
11. Implement!
10. Create “configurations”
Could you make it just a bit different…

## Slide 37: Identifying Issues With PR
Support
  Only supported by Xilinx
  Altera support announced
Lack of abstraction
  Manual partitioning
  Manual floor-planning
App-specific architectures
  Increased time-to-market
  Reduced flexibility
Frustrating
Design Flow!
In this work, we propose VAPRES
  A Virtual Architecture for PR Embedded Systems
  Abstracts base system from application
  Automates design flow and floor-planning
  Scalable, flexible features

## Slide 38: VAPRES Architecture
MicroBlaze CPU
PR
Region 1
PR
Region 2
PLB Bus
DCR
Bridge
PR Socket
PR Socket
FSL
Fast
Simplex
Links
Switch 1
Switch 2
IF
IF
IF
IF
IO
Module
To IO
MicroBlaze CPU
PR
Region 1
PR
Region 2
PLB Bus
DCR
Bridge
PR Socket
PR Socket
FSL
Fast
Simplex
Links
Switch 1
Switch 2
IF
IF
IF
IF
IO
Module
To IO
  PR Regions (PRRs)
    Independent clocks
    FIFO-based I/O
    Online placement
    Created separately
  MACS
    Intermodule network
  Flexible, scalable
    PR Region Count
    PR Region Size
    MACS bandwidth
      Module channel width
      Left to right channel width
      Right to left channel width
    IO Module Count
MicroBlaze CPU
PR
Region 1
PR
Region 2
PLB Bus
DCR
Bridge
PR Socket
PR Socket
FSL
Fast
Simplex
Links
Switch 1
Switch 2
IF
IF
IF
IF
IO
Module
To IO

## Slide 39: Design Methodology
Two separate design flows
  Base System
  Application
Applications made independently
  Only base system specs needed
Base Flow
App Flow
App Flow
App Flow
Base system specifications

## Slide 40: Base System Design Flow
System
Specs
User feeds specs to VAPRES
Base design created from specs
  Parametric templates used
System files generated
  Floorplan and Constraints
  Embedded Dev. Kit (EDK) Files
  HDL
Synthesis
Implementation
Bitstream generated
System downloaded to the board
Base system flow
Generate Bitstream
Implementation
Synthesis
HDL
Floorplan
Base Design
Templates

## Slide 41: Application Design Flow
Application Flow
Executable
Link
Synthesis
Generate Bitstream
Implementation
System
Specs
Partition App
  Hardware
  Software
Software flow
  Compile
  Link
Hardware Flow
  Synthesize
  Implement
  Bitstream gen
Download App
API
Compile
Application Decomposition
HDL
Source Code

## Slide 42: Revisiting Target Tracking
MicroBlaze CPU
Blank
PR Region
PLB Bus
DCR
Bridge
PR Socket
Switch 2
IF
IF
IO
Module
Sensor
ICAP
Filter
Storage
Aerospace Kalman Filter
Looks like a
spaceship
Aerospace Kalman Filter

## Slide 43: Seamless Filter Swapping
MicroBlaze CPU
Blank
Module
SW2
IF
IF
IO
Module
SW2
IF
IF
Blank
Module
Filter tracks target
  Target slows down
  Filter swap needed
First load new filter
  Spare region used
  Old filter continues
Redirect traffic
  Downtime is now negligible
  Previously in seconds
High Power Kalman Filter
Low Power Kalman Filter
Low Power Kalman Filter
Low Power Kalman Filter
Low Power Kalman Filter
The target changed!

## Slide 44: Summary
We developed VAPRES
  Virtual Architecture for Partially Reconfigurable Systems
Contributions
  Modular design methodology
  PR regions with independent, selectable clocks
  Highly parametric design
  Seamless filter swapping
Future work
  Algorithms for runtime module placement
  Tools to assist system design formulation
  Context save and restore for modules

## Slide 45: Thank you for attending
Questions?