## Slide 1: Hardware-Software Partitioning

## Slide 2: Hardware Software Definition
Definition: Given an application, hw/sw partitioning maps each region of the application onto
  either a hardware (custom circuits)
  or a software (microprocessors),
  but not both
A partition is a mapping of each region to either HW or SW
Mapping is done to meet certain Design Goals with Constraints

## Slide 3: Design Constraints & Goals
Space  Area
Power
Performance
Yield
Schedule
Cost

## Slide 4: You cannot get away with Everything !

## Slide 5: Challenges
Exploration Space α
  E.g. Configurations possible for 30 software components in an application which may be implemented as hardware = 230 = 1Billion
Each component for different tradeoffs may have
  Multiple software implementation
  Multiple hardware implementation

## Slide 6
10s
15s
25s
10s
5s
12s
8s
5s
Sw Time: 50s
Sw Time: 30s
Sw Time: 20s
Acknowledgement: Modified from G. Stitt’s slides in EEL5721
FIR()
ACCUM()
SEARCH()
5s
25s
10s
10s
15s
Possible Solutions:
Use fastest implementations
Use smallest implementations
Consider all “middle” implementations
5+30+20=55s
25+15+10=50s
10+15+20=45s
Performance:
Best Partition
15s
Process
Hardware Implementation Options : Area and Execution Time
Area Budget
Application with the Multiple Hardware Software Options

## Slide 7: Mathematical Modeling to arrive at the Optimum H/W-S/W Partition
= Hardware execution time of ith component
= Software Execution Time of the ith component
= Hardware Power of the ith component
= Software Power of the ith component
Any component is either implemented in Hardware of Software but not in both

## Slide 8: Granularity

## Slide 9: Dynamic Hardware-Software Partitioning: A First Approach
Greg Stitt, Roman Lysecky, Frank Vahid,
University of California, Riverside
DAC 2003, June 2-6,2003, Anaheim, California, USA

## Slide 10: Dynamic Hardware-Software Partitioning
Dynamically
  identify and re-implement
    critical software kernels, loops etc. to configurable fabric
      in order to achieve better performance, lower energy or meet other design goals

## Slide 11: Multiple Applications an Illustration

## Slide 12: Application Usage Profile: An Illustration
EEL5935
Mr. Jazz
Mr. Luigi
Mr. MTB
Music
Games
GPS
User
Data Access
SMS
Calls
Different users have different usage profiles
While designing a product usage profile needs to be assumed to give best user experience. However
  Usage Profile (Application usage) may be User/code dependent
    E.g. MP3, Camera, Video Playback, Call etc.
  Usage profile may change over-time
  Generic product assuming a certain profile
    is optimum for the “assumed” profile but sub-optimal in terms of area or performance for other usage profiles
Profiling in real time is key
  usage profile may identify critical kernels
    Critical components may be pushed to configurable area
      To boost the performance and reduce energy

## Slide 13: Dynamic HW/SW Partitioner Requirements
Detect critical code regions
Decompile and synthesize them to hardware
Place and Route the Hardware onto on-chip configurable logic
Update binary to communicate with the logic
Wait ! Did you say on-chip PnR ? You got to be kidding ! Right ?
All of the above with on-chip implementable, very lean algorithms

## Slide 14: Binary Level Partitioning and Advantage
Partitioning at the binary level
  offline or online
  Steps
    identify critical code sections, high loop sections
    Consider assembly code and object code as HW candidates
    Push these to configurable hardware
Advantage
  Works with any
    software compiler
    High level language
The Paper uses Binary Level partitioning approach.
Critical Loops identified and implemented in the Configurable logic

## Slide 15: Why Binary Level Partitioning instead of higher level optimizations ?
Dynamic Partitioning
  Needs to run on a small on-chip partitioning system
  Needs to be lean to be able to perform Place and Route etc. on-chip
  Higher Level Partitioning Methodologies may be good for offline analysis, but very difficult to implement due to the compute constrain.

## Slide 16: HW/SW Partitioning of Software Binary
Acknowledgement: Figure taken from G. Stitt, F. Vahid HW/SW Partitioning of Software Binaries ICCAD Nov 2002

## Slide 17: System Architecture (Top)
Microprocessor and Memory for normal Software application
On chip configurable module
1. Detects Most Frequently Executed Software region 2. Re-implements (1) in the configurable logic
Architecture Based on Triscend A7 (60MHz)

## Slide 18: System Architecture (Sub Blocks)
Direct Memory Access
Controller to access memory
Input
Output
Decompiles and synthesized selected binary regions for HW implementation
Detects Most Frequently executed application-software loops
32-bit i/p – o/p register
Partitioning Co-Processor Overhead:
Not much : Very Lean compared to Main Processor
Platform with multiple Main Processors may share single Partitioning co-processor, reducing the overhead further

## Slide 19: Simplified Configurable Logic Fabric
Simplified Fabric to just support inner loop implementation designed
Mapping, placing and routing a design to a general configurable logic fabric is time consuming

## Slide 20: Architecture Limitations
No sequential Logic support in the Configurable logic (in the platform chosen)
  Constraint:
    Loops to be implemented must have single cycle implementable body
Number of loop iterations must be determined before the loop executes, in order to specify the DMA block size request.
  Number of iterations may be determined :
    Statically in case of constant bounds
    Dynamically  requires extra instructions to configure the size of the DMA block request before HW execution starts
United States Patent 5,440,245 : Galbraith , et al. August 8, 1995 Logic module with configurable combinational and sequential blocks

## Slide 21: CLF Architecture
Either side connect-ability
(only at bottom)
4 channel:
Given Channel to Given Channel

## Slide 22: Tool Flow : Loop Profiler
Detects critical SW regions that should be implemented in HW
Is Non intrusive
Monitors instruction addresses on the memory bus
Increments branch frequency in the cache for a given backward branch
Small cache with a dozen entries
  Need to save area and power
Reference: Ann Gordon-Ross et. al Frequent Loop Detection Using Efficient Nonintrusive On-Chip Hardware
IEEE TRANSACTIONS ON COMPUTERS, VOL. 54, NO. 10, OCTOBER 2005

## Slide 23: Decompilation
Converts Software loops into higher level abstraction more suitable for synthesis
  Step 1 : Converts each assembly instruction to register transfer
  Step 2: Using Register Transfers Builds:
      CFG (Control Flow Graph) for software region
      DFG(Data Flow Graph) by parsing the Register transfers
  Step 3: Applies compiler optimizations to remove overhead due to assembly code and instruction set

## Slide 24: DMA Configuration Tool
Function: Maps the memory access of the decompiled loop onto the DMA Architecture
  Involves detection of
    Reads/ writes
    Increment and decrement address updates
    Single and block request modes
Remove following from Decompiled loop
  Loop counters and exit conditions
  Address calculations: As only sequential locations accessed
DMA functioning:
  DMA transfers data needed before the loop starts
  After HW initialization, HW starts a block request that fetches 1 memory location per cycle in case of a read or write

## Slide 25: Register Transfer Synthesis
Converts each o/p bit into Boolean expression
  By traversing the dataflow graphs of the software region
Limitation:
  Single cycle executable loop-bodies only
  Multi cycle would need behavioral synthesis to schedule loop operations

## Slide 26: Logic Synthesis  Tech Mapping  P&R
Converts Boolean equations into a netlist
Boolean equations transformed into DAG (directed acyclic Graph) of the Boolean Logic network
  Internal Nodes of DAG correspond to simple logic gates (AND/OR/INV, XOR)
Logic minimization
  Light weight suited for on-chip execution
    Applied at each node starting with the input nodes, while traversing through the network
    Uses single expand phase to achieve good optimization
Tech Mapping
  Traverses DAG starting from output nodes
    Combines nodes that may create 3 i/p 1 o/p LUT
    Further combine nodes (where possible ) to form 3 i/p 2 o/p LUTs

## Slide 27: LUT Placement Steps
Step 1: Determine relative placement of LUTs to one another
  by determining the critical path, and placing it on a horizontal row
Step 2 : For remaining non-placed nodes place as per dependency (i/p or o/p) w.r.t. placed
  Place above for inputs to Placed nodes
  Place below for outputs from Placed nodes
Step 3: Place in the Configurable Logic

## Slide 28: Routing
Simple Greedy algorithm
  Routes wires in most direct fashion
    Route the wires between input nodes and LUTs
    Route wires from LUTs to outputs
    Route wires connecting LUTs together
Routing decisions at Switch Matrices for within conifugrable logic fabric

## Slide 29: Bitfile Creation
Combines
  the Placed and routed hardware description with the DMA configuration information into a single bit file
Bitfile can be used to initialize the configurable logic

## Slide 30: Bitfile modification
Update software binaries to utilize HW for loops
Replace original software instruction for loop to a jump to HW initializing code
  Initializing code sends HW enable signal through Memory mapped register
  Code followed up with microprocessor power down trigger
  Upon finishing HW asserts completion signal causing a software interrupt
    Software interrupt wakes the microprocessor
  Jump instruction at the end of the hardware initialization code to the end of the original software loop
Notes: Draw cartoon for Second

## Slide 31: Tool : Performance and Area overhead
Typical tools for De-compilation, synthesis, and Place and Route need huge LSF machines
Designed tool very light weight and geared towards partitioning co-processor
Data Size: Memory required for the tool execution
Time : Execution time of each tool considering 60MHz clock and 1.5 cycle/Instruction

## Slide 32: Results
Definitions:
Loop Time Perc: Percentage of total software time, spent in the implemented loops
Loop Size Perc: Percentage of the total instructions that the loop required
Ideal Speedup: Speedup assuming HW implemented loops are executing in Zero time.
Sw Loop Time: Time required by the loop if completely in software
HW Loop Time: Time when loop implemented in HW
Notes: Where is the partitioning time ?
Partitioning is a one time even and would not be done often. Thus the partitioning time may not be considered

## Slide 33: Conclusion
Dynamic HW/SW Partitioning offers advantages over traditional approach:
  Transparent i.e. Benefits of partitioning even with regular software flows
  Can adapt as per actual usage profile
  Upto 2.6 average speedup

## Slide 34: Areas of Improvement of Future Work
Power required by the partitioning module and the HW running specified as 10-20% of total power
  Power data for individual modules not presented
Realistic loops have sequential logic and may not be always single cycle
  Extend implementation on sequential logic compatible CLF
  Extend to include mutli cycle loops
Applications seem too biased especially “url”, with 80% loop time with just 0.1% loop area overhead
Place and Route, synthesis would have been difficult to do on single partitioning chip:
  Today as on 2013 it should be possible to interface the modules with the cloud computing. I would rather have a complex algorithm run to get best suited partition profile, on a cloud network than to try small tricks with the lean co-processors
    This would be application dependent

## Slide 35: A Study of the Speedups and Competitiveness of FPGA Soft Processor Cores using Dynamic Hardware/Software Partitioning
Roman Lysecky, Frank Vahid,
University of California, Riverside
Design, Automation and Test in Europe Conference and Exhibition (DATE’05)

## Slide 36: Motivation (1/2)
Hard-Processor
  Pros: Performance
  Cons: Flexibility
Soft-processors
  Pros: Flexibility
  Cons: Degraded Performance and Energy Consumption
Can we leverage benefits of both using Warp Processing ?

## Slide 37: Motivation (2/2)
Warp Processing : Technique for
  optimizing a software application
    by dynamically and transparently re-implementing “critical software kernels” as custom circuits in on-chip configurable logic
Study MicroBlaze based Warp processing System to
  Eliminate the performance and energy overhead of a soft-processor compared to a hard-processor

## Slide 38: FPGA single-chip Systems: Hard-core Vs Soft-core
Hard-core
  Excellent Packaging and communication with the FPGA
  Lower Power and Higher Performance than Soft-core
  E.g. : Triscend, Atmel, Altera’s Excalibur, Virtex* with PowerPCs
Soft-core
  Lower Part cost
  Extreme Flexibility during design process
    Adding custom instructions or including/ excluding particular data-path coprocessors
    Quickly integrate the processor within a FPGA
    Varying number of processors as per need
  E.g. NIOS, NIOS II …, Picoblaze, Microblaze
Use Hardware / Software Partitioning Techniques to alleviate Power and Performance overhead of Soft Processors

## Slide 39: MicroBlaze Soft Processor Core
MicroBlaze – 32bit softcore by Xilinx
LMB – Local Memory Bus
BRAM – Block RAM : User Defined Size
OPB – On-Chip Peripheral Bus
Xilinx Platform Studio Tools
Synthesizes
design
Bitstream
Software Libraries
Application
Compile
Final
System
Bitstream
Specify system Architecture and configure MicroBlaze

## Slide 40: Key features of MicroBlaze
User Configurable options
  Tailor processor’s functionality as per the design need
  Configurable Instructions and data caches
  Incorporate additional hardware:
    Hardware multiplier ( mul instructions)
    Hardware Divider ( div instructions )
    Barrel Shifter (bs and bsi instructions)
      Hardware bit manipulations and absolute plus

## Slide 41: Peripheral Hardware available @ Present
Xilinx LogiCORE IP Floating-Point Operator v5.0 (Mar ‘11)
Available for
  Kintex™-7, Virtex®-7, Virtex-6,Virtex-5, Virtex-4, Spartan®-6, Spartan-3/XA,Spartan-3E/XA, Spartan-3A/AN/3A DSP/XA FPGAs
Supported operators:
  multiply
  add/subtract
  divide
  square-root
  comparison
  conversion from floating-point to fixed-point
  conversion from fixed-point to floating-point
  conversion between floating-point types
  Parameterized fraction and exponent word lengths

## Slide 42: Applications analyzed
brev (Powerstone benchmark suite)
  Critical kernel performs bit reversal heavily relying on shift operations
    Software only Implementation (without mul or barrel shift)
      N-bit shift by using n-successive add operations
    Configurable Hardware implementation
      2.1X speed up
“matmul”
  Critical Region : Matrix multiplication
    Hardware Multiplier provides 1.3X speedup

## Slide 43: MicroBlaze-based Warp Processor
Identify Critical Kernels in execution time
Implement critical Kernels in WCLA as cutom HW
WCLA – Warp Configurable Logic Architecture

## Slide 44: Warp Configerable Logic Architecture for Dynamic HW/ SW Partitioning
DADG: Data Address Generator
Used for any memory accesses to/for Configurable logic
LCH: Loop Control Hardware
Handles loops and controls executions
Reg 0, Reg 1 Reg 2:
i/p to CLF /or MAC (as per mapping)
Outputs from the configurable logic stored in Registers

## Slide 45: MicroBlaze Multi-processor warp processing system
Mutliple Soft-cores may be incorporated within a single FPGA
  Limited only by the FPGA Size
Multi-processor Warp Processing system may share a common DPM and WLCA and HW/SW partitioning may be done in round robin manner
  No Overhead due to additional DPMs
Partitioning tools may be implemented as software tasks running in one of the cores

## Slide 46: Experimental Setup
Execution Time and Power studied
Embedded systems applications chosen from Powerstone and EEMBC benchmark suites studies
MicroBlaze processor core implemented on Spartan3 FPGA
  Barrel Shifter and Multiplier configured in Hardware
  Note: MicroBlaze max frequency 85MHz; However FPGA circuits may run upto 250MHz

## Slide 47: Profiling Simulation
Xilinx Microprocessor Debug Engine
MicroBlaze
Soft App 1
Soft App 2
Soft App n
Inst Trace 1
Inst Trace 2
Inst Trace n
Simulate On-chip Profiler Behavior
Critical Region

## Slide 48: Energy Equations
Total Energy Consumed =
Energy Consumed by HW in Configurable Logic =
Energy Consumed by Microblaze =

## Slide 49: Performance / Power Simulation
Critical Regions
VHDL
Synopsys Design Compiler
UMC 0.18um
Library
Synthesis
Execution Traces of critical regions
Execute HW Circuits (VHDL model for WCLA) for each partitioned Critical Region
Determine final application performance
Xilinx XPower
MicroBlaze and system Component
(excluding WCLA)
Dynamic Power
Static Power
Configurable HW Power
MicroBlaze Power

## Slide 50: Results
ARM execution determined using Simple Scalar

## Slide 51: Conclusion
Warp processors (with soft-core), by pushing critical software kernels to the CFG can provide
  Flexibility of the Soft-core
    Due to soft-core implementation
  Competitiveness of a Hard-core processors (as ARM)
    Performance of the order of the Hard-core
      By leveraging special Configured HW
      5.8X (average) improvement (with MicroBlaze)
    Eliminates Energy Overhead
      By faster execution due to dedicated hardware and trimming down the soft-processor to perfectly fit design needs
      Average Energy reduction ~ 57%
  Opened Avenues for Soft-core processors which would not have been feasible previously due to energy/performance

## Slide 52: Areas of Improvement & Future Work
Real processing systems do not just do a execute just a single application at a time
  For realistic data, multiple applications should be run simultaneously
  Explore Parallel Processing architecture further
Power Estimation Data
  Estimation is good
    It would be good to see real data as well
Online Profiler has a dozen entries
  Number of entries should be configurable to avoid local maxima
Instead of simplified configurable logic fabric, how about using underlying FPGA physical fabric
Algorithm to come up with re-partitioning time interval should be worked up

## Slide 53: Questions

## Slide 54: Design Goals