## Slide 1: Course-Grained Reconfigurable Architectures
Patrick Cooke and Elizabeth Graham

## Slide 2: Introduction
FPGA Benefits
  Better performance than software
  Rapid prototyping
  Lower NRE costs
  Field-upgradable
FPGA Disadvantages
  Learning curve
  Lengthy compilation times
  Lack of portability

## Slide 3: Solution: CGRA
Learning curve
  High-level synthesis
  Simpler basic building blocks
Lengthy compilation times
  Separate virtual hardware and application compilation
  Shorter application compilation time
Lack of portability
  Hardware abstraction
  New FPGA, same application

## Slide 4: Intermediate Fabrics: Virtual Architectures for Circuit Portability and Fast Placement and Routing
James Coole, Dr. Greg Stitt
University of Florida
Department of Electrical & Computer Engineering
Published in CODES + ISSS 2010

## Slide 5: Intermediate Fabrics (IFs)
Specialized virtual reconfigurable architectures
  Configure FPGA with a specialized, higher-level FPGA

## Slide 6: IF Architecture
Data plane
  Functional units
  Tracks and switches
  Connections
Control plane
  State register
  State machine LUT
Stream plane
  Inputs and outputs

## Slide 7: Data Plane
Performs application calculations
Island-Style Topology
  Grid of CUs
    E.g., ALUs, multipliers, adders
  Routing resources in between CUs
    Tracks connect CUs
    Switch boxes connect tracks
    Connection boxes connect I/O from CUs to tracks

## Slide 8: Control Plane
Provides primitives for state machines and control logic
  State register
  Next state logic
  State-dependent output logic
  State-independent output logic
Limitation: Scalability
  Not scalable to many inputs or large state machines
  Data-parallel circuits require < 1% resources for control

## Slide 9: Stream Plane
Transfers data to and from external memories
  Saves data plane resources for computations
Components
  Counter
  Basic control
  Memory controller
  Optional specialized buffers
    E.g., smart buffers
    Improve memory bandwidth

## Slide 10: IF Overhead
High usage of MUXs for routing
Reduction techniques
  Decrease track density
  Long tracks
  Jump tracks
  Wide channels
  Connection box flexibility

## Slide 11: Experiments
Metrics
  Routability – % of random netlists routed successfully
  PAR time – Time to complete PAR on the IF
  Clock overhead – % clock frequency lowered to accommodate additional circuit complexity
Sample case studies (12 cases; 21 variations)
  Matrix Multiply – Inner product of two vectors
  Accum – Monitors an input stream, increments when value below threshold
  Max Filter – Image filter, selects max of 3x3 window

## Slide 12: Select Results
 | PAR Time Speedup | IF Area Overhead | IF Area Overhead Savings* | IF Clock Overhead
Matrix Multiply FXD | 112× | 16% | 63% | 16%
Matrix Multiply FLT | 602× | 31% | 58% | -11%
Accum FXD | 280× | 4% | 50% | 41%
Accum FLT | 323× | 14% | 29% | 25%
Max Filter | 444× | 9% | 56% | 23%
Average FXD | 275× | 16% | 48% | 18%
Average FLT | 1112× | 23% | 39% | 19%
Average | 554× | 18% | 45% | 18%
* Savings of IF area overhead versus using IF area overhead reduction techniques

## Slide 13: Routability vs Overhead
 | Routability | Overhead
2 Tracks per Channel | 89% | 15%
3 Tracks per Channel | 99% | 23%
4 Tracks per Channel | 100% | 28%
5 Tracks per Channel | 100% | 37%
Values averaged over different fabric sizes
  3×3, 4×4, 5×5, 6×6, 7×7, 8×8, 9×9, 12×8
  CUs are DSP48

## Slide 14: Conclusions
Average 554× PAR speedup
IF area overhead can be substantial, but routability remains relatively high
Overhead reduction techniques on average reduce overhead by 45%
IF clock overhead negligible to other system bottlenecks

## Slide 15: Future Work
Directly map IF routing resources to reduce overhead
Evaluate performance of multiple smaller IFs with respect to one large IF
Create library of IFs
Develop algorithms for automatically selecting most appropriate IF
IF synthesis (done manually in this paper)

## Slide 16: Shortcomings
IFs do not scale well
IF synthesis done by hand, so examples were overly simple
Besides random netlist generator, no tools developed for experiment or paper

## Slide 17: An FPGA-based Heterogeneous Coarse-Grained Dynamically Reconfigurable Architecture
Ricardo Ferreira, Julio Goldner Vendramini, Lucas Mucida Departamento de Informatica
Universidade Federal de Vicosa
Monica Magalhaes Pereira, Luigi Carro
Instituto de Informatica-PPGC
Universidade Federal do Rio
Grande do Sul
Published in CASES 2011.

## Slide 18: FPGA-based Coarse-Grained Reconfigurable Architecture (CGRA)
Virtual device implemented on any commercial off-the-shelf FPGA
Simple configuration algorithm enables fast prototyping
  Algorithm maps dataflow graphs (DFGs) onto word level reconfigurable architecture
Proposed CGRA is 10-100x faster compared to previous CGRA work

## Slide 19: CGRA Architecture
Three components
  Registers
    Normal and bypass
  Functional units (FUs)
    Heterogeneous or Homogeneous FUs
      Heterogeneous reduces cost, power, and complexity
      Homogeneous simplify scheduling, placement and routing
  Global interconnection network
    Single cycle latency between FUs
    Structured & Unstructured Communication Patterns

## Slide 20: Dynamic Interconnection Network
Multistage Interconnection Network (MIN)
  Given n inputs, n outputs and switch radix r, logr n stages with n/r switches each
Two parallel Omega networks
  Blocking networks
  Switch radix 4
    Works well on 6 input LUTs
    Half the cost of radix 2 network
  Each extra stage doubles number of paths connecting each input/output pair

## Slide 21: MIN Routing
Upper network routes first operand of each FU, lower network routes second operand
Commutative operators allow network to avoid conflicts by switching order of operands
Switches support multicast connections

## Slide 22: Scheduling, Placement and Routing (SPR)
SPR all performed at same time
Modulo scheduling
  Repeat schedule of configurations in loop
  Greedy heuristic
  Polynomial complexity
Placement and Routing
  Greedy heuristic

## Slide 23: SPR Algorithm
As Soon As Possible (ASAP) & As Late As Posssible (ALAP) scheduling to find slack
Initiation Interval (II)
  Number of network configurations
  Initialized based on DFG and architecture configuration
Starting from output, attempt place and route for each node from current level in current configuration
  If success, proceed to next level and next configuration until end of DFG
  If fail, increment II and restart

## Slide 24: Placement Algorithm
Request FU for node placement
If no available FU, request bypass register
  If no available register, placement fails
  Otherwise, reschedule node one level up
Placed nodes are immediately routed

## Slide 25: Routing Algorithm
Attempt to route placed node’s FU to destination FU
If routing fails, request bypass register
  If no available register, routing fails
  Otherwise, reschedule node one level up and attempt to route to register
Algorithm returns success or fail of routing attempt

## Slide 26: SPR Walkthrough
5 node DFG
2 FUs
1 bypass register
Initiation Interval starts at ceiling(5/2) = 3
Algorithm begins at node E
Assume node A is chosen for rescheduling

## Slide 27: Experiments
Setup
12 DFGs of digital signal processing benchmarks
6 architecture configurations
  3 medium configurations (64 I/O MINs)
  3 large configurations (256 I/O MINs)
  Each configuration had unique combination of heterogeneous FUs
Results
Medium configurations
  Instructions per cycle (IPC) range = 19-26
  20% overhead on minimum Initiation Interval
  Average CPU time = 40 ms
Large configurations
  Instructions per cycle (IPC) range = 37-104
  40% overhead on minimum Initiation Interval
  Average CPU time = 130 ms

## Slide 28: Resource Utilization
Xilinx Virtex6 configured using ISE 12.4
Medium architectures (64 I/O MINs)
  1% of FPGA register resources
  15% of LUT resources
  4% of DSP resources
Large architectures (256 I/O MINs)
  6% of FPGA register resources
  82% of LUT resources
  16-25% of DSP resources

## Slide 29: Conclusions/Future Work
Dynamic CGRA and SPR algorithm achieve on average 50% resource utilization per cycle and CPU time between 10-300 ms
Add local register file to FUs to reduce number of configurations in SPR algorithm
Integrate SPR tool into compiler tools for softcore FPGA processors
  Significantly increase performance of data intensive applications

## Slide 30: Shortcomings
No in-depth comparison of results with previous work
No comparison of CGRA circuits with equivalent FPGA circuits to evaluate quality of circuits mapped to CGRA