## Slide 1
Feb 2013
Jerry Redington
Principal System Architect
Xtensa – A Configurable Embedded Microprocessor

## Slide 2: Market Accepted, Market Proven Over 2 Billion Cores Worldwide
Games
Digital
Cameras
Auto
InfoTainment
Printers
Network Infrastructure
Network
Access
Storage
PC
Graphics
Home Entertainment
DTV
STB
Blu-ray
Receiver
Mobile Wireless
SmartPhone
Wireless
BaseStation
Samsung Galaxy-S
iPhone 4
Blackberry Bold 9780
Fujitsu LTE F-01D Android Tablet
UltraBooks

## Slide 3: Congratulations University of Florida
You are part of our University access program
  You have the ability to download our Xtensa Xplorer IDE
  Create an unlimited number of processor cores for software (ISS), hardware (FPGA) or System C simulations
    Create processors with almost all of our configuration options
    Access to our prebuilt Diamond and ConnX DSP processors
  Create custom interfaces and custom instructions with our TIE language (Verilog like)
    Create interfaces to augment data transport between the external world and Xtensa
    Create a range of instructions that will affect computational capacity
  Produce RTL suitable for FPGA exploration
    Target supported FPGA platforms with a complete microprocessor
    Create a Xilinx NGO netlist for inclusion in your FPGA SOC target

## Slide 4: RISC Microprocessors Have similar features, however implemented very differently
Modern RISC/DSP architectures
  All have instruction sets, however the instruction format varies
    Width of instruction, 16,24,32,40…,128 (VLIW)
    Fixed versus variable length, intermixing of instruction formats, multiple format encodings
    Single / Multiple issue
    SIMD
  Compiler support
    Minimum features; load/store, move, arithmetic, logical, shift, jump/branch, Processor control
    Floating point (single/double)
    Dividers, Multipliers, MAC (different format widths and sign)
    Saturation, min/max, DSP, zero over head loop… So many more
  Load / Store Architecture
    Memory widths vary 16, 32, 64, 128, 256, 512 bits per transaction
    Single, dual, or more load-store units
    Register file(s)
      single or multiple register files, width, depth (Compiler support)
      # of read/write ports per instruction, # of read/write ports per VLIW instruction word
      Windowed / shadowed RF

## Slide 5: RISC Microprocessors Have similar features, however implemented very differently
Modern RISC/DSP architectures
  Memory sub-system
    Unified, Private address range
    TCM, Tightly coupled (single cycle) memory interfaces
    Instruction / Data cache
      cache depth, line length, line locking, write through / write back, critical word first, line fill policies, replacement algorithms and of course exception handling
    FIFO interfaces (handshake interface)
    GPIO
  Exception / Interrupt Architecture
    Exception causes
    Interrupt sources, priority levels, NMI, vector entry points

## Slide 6: Why So Many Choices? All machines have a bias
Simply, embedded processors are biased toward and application
What drives microprocessor features
  Different markets value features differently
    Cell phones (battery and cost sensitive)
      Value power, die area, performance
    Desktop computers
      Value performance, power and die area
    USB Flash memory sticks
      Die area, power, performance
Applications drive microprocessor features
  Audio codecs (math fixed precision bias)
  Video codecs (fixed/floating point, SIMD)
  Image processing
  Baseband processors slanted towards wide SIMD
  Crypto engines (bit manipulation)

## Slide 7: Xtensa: Integrates Multiple Strengths Into A Single Microprocessor
10-100x better performance
than DSP/CPUs
Strengths
Control-oriented,
Software Development
Strengths
SIMD, VLIW,
Stream processing
Strengths
Task-specific, Differentiating, Direct point-to-point interfaces.
CPU Strengths
DSP Strengths
CPU
DSP
Custom
Strengths
Custom Logic
DPU
Dataplane Processor Unit
10-100x better performance than DSP/CPUs
Better control and tools than DSPs
More flexible than custom logic

## Slide 8: Degrees of Freedom with Xtensa
Configuration Options
  Pre-built features presented in a menu style
  Memory interfaces ($$, TCM)
  Pre-defined instructions (floating point, DSP, audio, baseband DSP)
  Interrupt and memory map
TIE: User Defined Interfaces
  GPIO
  FIFO
  Look-up-table (light weight memory interfaces)
TIE: User Defined Instructions
  Single cycle
  Multi-cycle
  Limited by your imaginations and of course physical rendering limitations
Xilinx FPA support for commercial development boards (Xilinx ML605)
  GUI support for target boards
  Download configurations directly into FPGA for software development
  JTAG probes for command and control of debug sessions
  Trace logic for non-intrusive debug sessions

## Slide 9: Xtensa – Configurability Click-box Options Include Pre-defined Extensions
Simple menus of options
From fine tuning of performance, power and area
  Size, type, width and access latency of memories. Optional prefetch unit.
  Load/Store unit characteristics
  Number of general purpose registers
  Number and priority levels of interrupts
To high-level, market-specific building blocks
  Common functional units:
    Floating point, multiplier, divider, NSA
  Complex application engines:
    HiFi Audio DSP family
    ConnX BBE16/32/64 Baseband DSP family
    ConnX Vectra LX quad-MAC DSP
    ConnX D2 dual-MAC DSP

## Slide 10: Xtensa – Extensibility Customize a DPU to Your Task
Using a simple Verilog-like language
Add:
Inputs and outputs
Scratchpad memories
Simple single-cycle instructions
Multi-cycle instructions
SIMD for vectorization
FLIX for parallel operations
I/O Queues
3 256 bit queues and “add” operation:
queue inA 256 in queue inB 256 in queue outC 256 out
operation ADD_XFER {} {in inA, in inB, out outC} {
assign outC = inA + inB;
}
Single Cycle Instruction:
Byteswap:
  operation BYTESWAP {out AR outReg, in AR inpReg}{}
  {
  assign outReg =
  {
  inpReg[7:0],
  inpReg[15:8],
  inpReg[23:16],
  inpReg[31:24]
  };
  }
+
inA
inB
outC
byte0
byte1
byte2
byte3
byte3
byte2
byte1
byte0
outReg
inReg

## Slide 11: Complete Development Tool Chain Mature and integrated for efficient development
Automatically adapts to options and any custom extensions
  Use for all Xtensa DPUs
  In single and multi-processor developments
Comprehensive development environment
  Xplorer IDE – Eclipse-based GUI
    Multiple processor system creation
  Includes industry-leading vectorizing compiler
    Advanced optimizations with automatic speed/area optimization
  Debugging, profiling, linking, assembling, power estimation tools
    GNU tools supported too
TRAX - Program trace module with compression
  Simulated or real target hardware trace

## Slide 12: Best in Class Simulation Models Options at Every Level of Abstraction
Cycle-accurate, pipeline-modeled ISS – most accurate in industry
  Included as part of the SDK
TurboXim: Fast functional simulator for software development
  Offers mixed mode simulation with ISS to generate statistical profiling information
  Performance in 10-50 Million simulation cycles per second
    On typical low cost PCs (3GHz Intel Xeon 5160 running Linux)
System modeling support
  XTMP and XTSC
    C and SystemC transaction based models
  Pin-Level modeling
    SystemC modeling at the pin-level for RTL co-simulation
  Supported by all major ESL vendors

## Slide 13: Xtensa - Full Development Automation Making DPUs Usable by All Engineers
Xtensa
Processor
Generator*
* US Patent: 6,477,697
Use standard ASIC/COT design techniques and libraries for any IC fabrication process
Complete Hardware Design
    Pre-verified RTL
    EDA scripts
    test suite
Customized Software Tools
  C/C++ compiler
  Debuggers
  Simulators
  RTOSes
1. Select from menu
2. Explicit instruction description (TIE)
Processor Configuration
Processor
Extensions
Iterate in Minutes!

## Slide 14: Xtensa Processor Generator Fully Automated Hardware and Software Tools Generation
System Modeling / Design
Instruction Set Simulator (ISS)
Fast Function Simulator (TurboXim)
XTSC SystemC System Modeling
XTMP C-based System Modeling
Pin Level cosimulation
Xenergy
Energy Estimator
Software Tools
GNU Software Toolkit
(Assembler, Linker, Debugger, Profiler)
Xtensa C/C++ (XCC) Compiler
C Software Libraries
Xplorer IDE
Graphical User Interface to all tools
Operating Systems
Hardware
EDA scripts
RTL
Synthesis
Block Place & Route
Verification
Chip Integration /
Co-verification
Designer-Defined Instructions
(optional)
Xtensa Processor Generator
Processor Generator Outputs
Application Source
C/C++
Compile
Executable
Profile using ISS
Software Development
To Fab / FPGA
Set/Choose Configuration options
System Development
Choose different configuration
- or -
Develop new instructions

## Slide 15: Complete Development Tool Chain Xplorer: Single IDE for All Development Stages
DPU Target
Edit
C, C++, ASM
Partition/LSP
Hardware
Compile
+ Link
C Libraries
Debug
+ Trace
Profile
ISS
Co-sim
System Models
FPGA
Si
FPGA
Si
Simulate
The whole development flow in one integrated tool

## Slide 16: Inside Xtensa

## Slide 17: Xtensa LX4 Block Diagram - System
VLIW (FLIX) Parallel Execution pipelines
Inst. Memory Management, Protection & Error Recovery
Data Memory Management, Protection & Error Recovery
Instruction
RAM x2
Instruction
ROM
Data
RAM x2
Data
ROM
External Interface
Processor Interface Control
Write Buffer
PIF Bridge
XLMI
Local Memory
Interface
Base ISA Feature
Designer-Defined Features (TIE)
External RTL & Peripherals
Configurable Function
Optional Function
Optional & Configurable Function
QIF32
RTL, FIFO, Memory, Xtensa
GPIO32
Designer-Defined Queues, Ports & Lookups
KEY
Trace Port
JTAG Tap Control
Data Address
Watch Registers
Instruction Address
Watch Registers
Timers
Interrupt Control
On-Chip Debug
Processor Controls
Exception Support
Exception Registers
Base Register File
Data Load/Store Unit
Instruction Fetch / Decode
Base ISA Execution Pipeline
Base ALU
Optional Functional Units
Register Files
Processor State
Device
Device
Bus Bridge
AHB-Lite/AXI
RAM
DMA
Device
System
Bus
Designer-Defined
Dual Load/Store Unit
Designer-Defined Functional Units
Register Files
Processor State
Register Files
Processor State
Instruction
Cache
Data
Cache
Prefetch

## Slide 18: Xtensa LX4 Block Diagram – Optional Functional Units
System
Bus
Device
Device
Processor Controls
Trace Port
JTAG Tap Control
Exception Support
Exception Registers
Data Address
Watch Registers
Instruction Address
Watch Registers
Timers
Interrupt Control
On-Chip Debug
Instruction Fetch / Decode
Base ISA Execution Pipeline
VLIW (FLIX) Parallel Execution pipelines
Base Register File
Base ALU
Designer-Defined Functional Units
Register Files
Processor State
Designer-Defined
Dual Load/Store Unit
Data Load/Store Unit
Inst. Memory Management, Protection & Error Recovery
Data Memory Management, Protection & Error Recovery
External Interface
Processor Interface Control
Write Buffer
PIF Bridge
Instruction
RAM
Instruction
ROM
Instruction
Cache
Data
RAM
Data
ROM
Data
Cache
Bus Bridge
AHB-Lite/AXI
RAM
DMA
Device
RTL, FIFO, Memory, Xtensa
XLMI
Local Memory
Interface
Base ISA Feature
Designer-Defined Features (TIE)
External RTL & Peripherals
Configurable Function
Optional Function
Optional & Configurable Function
QIF32
GPIO32
Designer-Defined Queues, Ports & Lookups
KEY
Prefetch
Optional Functional Units
Register Files
Processor State
MAC 16 DSP
Register Files
Processor State
MUL 16/32
Integer Divide
Single Precision Floating Point (FP)
Double Precision FP Acceleration
32-bit GPIO pair
(GPIO32)
32-bit Queue Interface pair (QIF32)
HiFi 2, -EP or HiFi3 Audio Engine
ConnX D2 DSP Engine
ConnX Vectra LX DSP Engine
(1,2 Load/Stores)
VectraVMB
(DSP Communications Acceleration Instructions)
FLIX3
(3-issue FLIX configuration)
Optional Functional Units
Choose pre-verified functionality.
Click-box options and side-by-side profiling allow easy “what-if” assessments.
ConnX BBE16 / BBE32uE / BBE64
(Baseband DSP)

## Slide 19: Xtensa LX4 Block Diagram – Customization
System
Bus
Device
Device
Processor Controls
Trace Port
JTAG Tap Control
Exception Support
Exception Registers
Data Address
Watch Registers
Instruction Address
Watch Registers
Timers
Interrupt Control
On-Chip Debug
Instruction Fetch / Decode
Base ISA Execution Pipeline
VLIW (FLIX) Parallel Execution pipelines
Base Register File
Base ALU
Register Files
Processor State
Designer-Defined
Dual Load/Store Unit
Data Load/Store Unit
Inst. Memory Management, Protection & Error Recovery
Data Memory Management, Protection & Error Recovery
External Interface
Processor Interface Control
Write Buffer
PIF Bridge
Instruction
RAM
Instruction
ROM
Instruction
Cache
Data
RAM
Data
ROM
Data
Cache
Bus Bridge
AHB-Lite/AXI
RAM
DMA
Device
RTL, FIFO, Memory, Xtensa
XLMI
Local Memory
Interface
Base ISA Feature
Designer-Defined Features (TIE)
External RTL & Peripherals
Configurable Function
Optional Function
Optional & Configurable Function
QIF32
GPIO32
Designer-Defined Queues, Ports & Lookups
KEY
Optional Functional Units
Register Files
Processor State
Prefetch
Designer-Defined Functional Units
Customization
Multi-issue FLIX (automatically used by the C compiler)
SIMD Instructions
Compound and Fusion instructions
Multi-cycle execution units
Registers / register files with automatic C data type support
GPIO and Queue interfaces
Wide (128-bit) load/store instructions

## Slide 20: Data Transport

## Slide 21
More flexible memory system
A total of 6 “ways” are now supported (previously 4)
  4-way cache AND local memories now supported
More combinations of different memories, a total of 6 from:
  Instruction Interface:
  (0-4 cache ways)
  +(0-2 RAMs)
  +(0-1 ROMs)
  Data Interface:
  (0-4 cache ways)
  +(0-2 RAMs)
  +(0-1 ROMs)
  +(0-1 XLMI)
Benefits
  4 cache ways with locking AND Prefetch extend this simple programming model approach into many more designs
  Add local memories and have other bus masters write directly to it via InboundPIF in more complex and predictable systems
$
$
$
$
RAM
RAM
ROM
Xtensa
0-4
0-2
$
$
$
$
RAM
RAM
ROM
XLMI
0-4
0-2
0-1
Instruction
Data
0-1

## Slide 22: Conventional Processors
Bus-based connectivity
FSM
Buffer
FSM
Processor
With Local Mem
System Bus
RTL
Data
RTL
Data

## Slide 23: Xtensa Processors
Connect via the System Bus in the same way, or…
With multiple higher bandwidth, point-to-point interfaces
FSM
Buffer
FSM
Xtensa Processor
With local Mem
System Bus
RTL
Data
RTL
Data
Scratch Mem
Scratch/Table lookup Mem
>1000 Special Memory interfaces
Slave Interface to/from local mem
>1Kb
>1Kb
>1Kb
>1Kb
>1000 Write Ports (GPIO)
>1000 Read Ports (GPIO)
FIFO
FIFO
FIFO
FIFO
>1Kb
>1Kb
>1Kb
>1Kb
>1000 Read Queues
>1000 Write Queues

## Slide 24: Multiple ports (GPIO) Eg. System Status and RTL control/setup
TIE Ports are GPIO interfaces
  Over 1000 ports can be specified
  Each port can be up to 1024 bits wide
Dedicated instructions
  Operating in parallel with processor’s Load/Store
System Bus
Xtensa
Over 1000 interfaces
Up to 1024 bits wide
RTL
RTL
RTL
RTL
RTL

## Slide 25: Queue Interfaces Expand the functionality of an existing RTL design
System Bus
Conventional processors/DSPs pass data over the system bus
FSM
Buffer
FSM
System Bus
Data
Data
DSP
Data processing
Up to 1024 bits wide,
>1000 interfaces
Xtensa can pass data directly, freeing up the system bus
FSM
Buffer
FSM
System Bus
Data
Data
570T Diamond Processor has one 32bit input Queue and one 32bit output Queue
Xtensa
Data processing
RTL is often written instead - to avoid system and bus limitations

## Slide 26: Dedicated Special Memory Interfaces Use special memory interface for tables, coefficients
Simple memory interface, not part of memory map
  Index up to 4G items
  Each item up to ~1000 bits wide
Dedicated instructions
  Operating in parallel to the processor’s Load/Store unit
  User-defined number of access cycles
  Read/Write multiple interfaces at once with VLIW
Wide read/write.
4G locations ~1000 data bits
Scratch memory
Coefficient, Mapping table
Filter coefficient storage.
Mapping tables.
Scratch memory.
Custom operations.
∆t
RTL
Dynamic Response
System Bus
Xtensa
RTL

## Slide 27: Instruction Designer

## Slide 28: Instruction Format
B-28
Base instruction set is 24-bit instructions
ADD ar, as, at
AR[r]  AR[s] + AR[t]
10000000
r
s
t
0000
23
0
8
4
4
4
4
ADD.N ar, as, at
AR[r]  AR[s] + AR[t]
r
s
t
1010
15
0
4
4
4
4
In assembler, density instructions are signified by the “.N” suffix.
The C/C++ Compiler infers 16-bit instructions automatically.
“Density” option adds 16 bit instructions

## Slide 29: FLIX – Flexible Length Xtensions
Create multi-issue VLIW-style processor to boost processor performance
  FLIX instructions can be 32, 64 or 128 bits wide (choose one)
  Modeless intermixing of 16-bit, 24-bit, and wide instructions
    Eliminates VLIW-style code-bloat
Designer-defined formats, # of slots in each format, operations in each slot
  Any combination of most base ISA and TIE operations in each slot
Compiler automatically generates instruction bundles from standard C Code to improve performance
Designer-Defined FLIX Instruction Formats with Designer-Defined Number of Operations
Example 5 – Operation, 64b Instruction Format
63
0
1
1
1
0
Operation 5
Op 4
Operation 1
Op 3
Operation 2
Example 3 – Operation, 64b Instruction Format
Operation 1
1
1
1
0
Operation 3
Operation 2
63
0
0
1

## Slide 30: Xtensa Instruction Pipeline
Instructions are executed in a RISC pipeline
  This is the minimal, 5-stage pipeline
  Instructions generally spend 1 clock cycle in each stage
  Pipeline stages of multiple instructions are overlapped in the pipeline
Instruction Fetch: instruction memory read
Register Read: instruction decode, and register operand read
Execute: ALU operation, or effective address calculation for load/store
Memory Access: read of local memory or cache
Writeback: register or memory write (instruction committed)
Execute
Register Read
Memory Access
Instruction Fetch
Writeback
1
2
3
4
5

## Slide 31: Notation: Pipeline Diagrams
B-31
(Prefetch)
  This example is for a 5-Stage pipeline
  This is a sequence diagram, not a block diagram!
    “RegFile Access” (read) in R-Stage and “RegFile Update” (write) in W-stage refer to different operations on the same (AR) register file
  Prior to I-Stage, the program counter stage (P-Stage) is sometimes shown
    P-Stage is almost always overlapped with other stages, so it is not generally illustrated.
Inst Decode
RegFile
Access
ALU
RegFile
Update
as
at
Inst
Memory
PC
Decode instruction
and
RegFile access
Read Instruction Memory
and align
instructions
Computation, or load/store address calculation
Data Memory/Cache Loads
Stage ALU result
Write result to AR RegFile
Send address to Inst Mems
(Commit)
ar
Local Memory / Cache
Execute
Register Read
Memory Access
Instruction Fetch
Writeback

## Slide 32: Xtensa 5-Stage Pipeline (Instruction Execution)
6000117f: ...
60001181: add.n a3, a5, a2
60001183: ...
Inst Decode
Regfile
Access
ALU
a3
Regfile
Update
a5
a2
result
Inst
Memory
PC
Decode instruction
and
access RegFile
Read Inst Memory
and align
instructions
Computation:
a2 + a5
Stage result
Cycle reserved for
Data Mem Access
for Loads
Write result to a3
in the RegFile
Send address to Inst Mems
(P)
E
R
M
I
W

## Slide 33: Example 32-bit Load Instruction
Inst Decode
Regfile
Access
AddrGen
a3
Regfile
Update
a5
0
Inst
Memory
PC
Decode instruction
and
access RegFile
Read Inst Memory
and align
instructions
Address Generation:
a5 + 0
Local memory read or Cache access
Write result to a3
in the RegFile
Send address to Inst Mems
(P)
E
R
M
I
W
6000117f: ...
60001181: l32i.n a3, a5, 0
60001183: ...
Data Memory
address
immediate

## Slide 34: Example 32-bit Store Instruction
Inst Decode
Regfile
Access
AddrGen
a5
0
Inst
Memory
PC
Decode instruction
and
access RegFile
Address Generation:
a5 + 0;
Read a3
(stage address and data)
Local memory write
Send address to Inst Mems
(P)
E
R
M
I
W
Data Memory
immediate
6000117f: ...
60001181: s32i.n a3, a5, 0
60001183: ...
Address
a3
a3
address
data

## Slide 35: Instruction Design Decisions
Compile time operands
  The instruction word limits the number and width of operands passed to an instruction
  Fixed at compile time
  Visible to the programmer
Dynamic
  Operands in the form of index(es) into a register file (compiler schedules these resources)
  Single/Multiple register file
  Ctypes
  Visible to the programmer
Intrinsic operands
  Are usually in the form of special purpose register like an Accumulator
  Instruction decoder understands how to enable the use of these registers
  Invisible to the programmer.
Single cycle instructions
  Integer ADD, AND,
Multi-cycle instructions (resource schedule parameters)
  Load/store
  MAC

## Slide 36: High Performance Techniques
Application specific instructions
  SAD, CRC, AES, DES
Fusion
  Merging serial operations into fused operation
  Load/Store merge with pointer math
SIMD
  Single Instruction Multiple Data
  Perform same operation across multiple elements of a vector word
VLIW
  Long Instruction Word
  Multiple operations in a single instruction word
  All operations execute in the same clock cycle

## Slide 37: Performance Techniques: Fusion
Fusion – Merging sequential operations to a single operation
Compiled Assembly
with a Fusion operation
(merging mul and slli)
…
mulshift a12,a10,a8;
…
X, <<
x
<<
2
Compiled Assembly
…
mul a13,a10,a8;
slli a12,a13,2;
…
cycle 1
cycle 2
for(i=0;i<SIZE;i++){
sum +=(A[i]*B[i])<< 2;
}
Original C Code

## Slide 38: Performance Techniques: SIMD
  for(i=0;i<SIZE;i++)
  sum[i] = A[i] + B[i];
Original C Code
iteration 1
A[]
B[]
sum
…
…
…
+
Typical Processor
=
Xtensa Processor with a
SIMD operation
(add operation on 4 data)
+
=
A[]
B[]
…
…
…
SIMD – Single operation on multiple data
iteration 0
+
sum
+

## Slide 39: Performance Techniques: VLIW
  for (i=0; i<n; i++)
  c[i]= (a[i]+b[i])>>2;
Original C Code
loop:
…
addi a9, a9, 4;
addi a11, a11, 4;
l32i a8, a9, 0;
l32i a10, a11, 0;
add a12, a10, a8;
srai a12, a12, 2 ;
addi a13, a13, 4;
s32i a12, a13, 0;
…
Compiled
Assembly
cycle 8
loop:
{ addi ; add ; l32i }
{ addi ; srai ; l32i }
{ addi ; nop ; s32i }
Compiled Assembly with a 64-bit FLIX
(bundling 3 operations in 64-bit FLIX inst.)
cycle 3
FLIX – Bundling multiple operations in a single instruction word

## Slide 40: A Simple Example
mytiefile.tie
operation ADD_BYTES {out AR sum, in AR fourbytes } {} {
assign sum = fourbytes[7:0] + fourbytes[15:8] + fourbytes[23:16] + fourbytes[31:24];
}
Behavioral Description
The combinational logic between operands
  In this example, the logic is between two registers of the AR register file
  By default, operation executes in a single cycle
Syntax is similar to Verilog
The logic is described in expressions: Begin with assign or wire
  assign: Assignment to any “out” or “inout” operand
  wire: Instantiates a local variable that can only be assigned once (More about wires later).

## Slide 41: Using TIE State in an Instruction
A TIE state operand is listed in the second set of “{ }” in the operation definition
A TIE state is an implicit operand in the sense that it does not appear in the assembly syntax or C intrinsic of the instruction
operation MAC24 {in AR m0, in AR m1}
{inout ACCUM} {
assign ACCUM = ACCUM + m0[23:0] * m1[23:0];
}
unsigned x, y;
MAC24(x, y); // ACCUM += x*y (24-bit multiply)
mac.c
mac.tie

## Slide 42: SIMD Example: 4-Way Add Operation
regfile simd64 64 16 v // 16 x 64bit wide registers
operation vec4_add16 {out simd64 sum, in simd64 A, in simd64 B} {} {
  wire [15:0] result0 = (A[15: 0] + B[15: 0]);
  wire [15:0] result1 = (A[31:16] + B[31:16]);
  wire [15:0] result2 = (A[47:32] + B[47:32]);
  wire [15:0] result3 = (A[63:48] + B[63:48]);
  assign sum = {result3, result2, result1, result0};
}
The new register file operands are explicit operands of the operation
Similar to using the AR register file as inputs/output in previous examples
vec4_add16.tie

## Slide 43: SIMD Example: 4-Way Add Example (2)
Now let’s use our register files from C code:
The register file’s name(simd64) is used as a new data type in C/C++. Variables of this type will be mapped by the C compiler to registers from the simd64 register file
simd64 A[VECLEN];
simd64 B[VECLEN];
simd64 sum[VECLEN];
for (i=0; i<VECLEN; i++){
sum[i] = vec4_add16(A[i],B[i]);
}
Note: You may define one or more data types for a given register file using the “ctype” construct.

## Slide 44: Operator Overloading
Enables use of standard C language operators such as “+” with user-defined data types.
Simpler, more portable “native C” programming model as opposed to using intrinsics.
The C compiler can infer an operation based on data types of the operator arguments.
simd64 a, b, c;
c = vec4_add16(a, b); // using intrinsics
c = a + b; // using operator overloading

## Slide 45: Scheduling TIE Operations
TIE compiler assumes a single-cycle schedule
  Input registers used at the beginning of the (E)xecute stage
  Output registers defined at the end of the (E)xecute stage
Use schedule to define multi-cycle operations
  Read inputs in use stages
  Write outputs, states and wires in def stages
  Use symbolic pipeline stage names
operation MACC {inout MRF acc, in MRF mul1, in MRF mul2} {} {
assign acc = TIEmac(mul1[23:0], mul2[23:0], acc, 1’b1, 1’b0); }
schedule macc_sched {MACC} {
// Read operands at start of Estage (stage 1)
use mul1 Estage; use mul2 Estage; use acc Estage;
// Write results at end of Estage+1 (stage 2)
def acc Estage+1;
}

## Slide 46: Back-to-Back MACC Pipeline Diagram with Data Dependency
MACC
Estage
my1
my2
my5
MACC
Estage+1
Cycle 0
Cycle 1
Cycle 2
…
macc my5, my1, my2
macc my5, my3, my4
…
my5
MACC
Estage
my3
my4
MACC
Estage+1
my5
bubble
If a data dependency exists in the source code, the processor inserts execution bubbles (delay cycles) until input operands are available.

## Slide 47: Two Cycle Operations using schedule
Two-cycle MACC
  Inputs registers are used at the beginning of the E stage
  Output registers are defined at the end of the E+1 stage
The data path for this 2-cycle operation is spread across the E and E+1 stages
This simple schedule does not explicitly partition the hardware between the two pipelined stages. (We need to use “retiming” in the synthesis flow)
Source routing
Result routing
Decoder
Control
MACC
MRF
ALU
R
E
M
See the TIE Reference Manual for more details

## Slide 48: Improved MACC Operation Schedule
operation MACC {inout MRF acc, in MRF mul1, in MRF mul2} {} {
assign acc = TIEmac(mul1, mul2, acc, 1’d0, 1’d0);
}
schedule macc_sched {MACC} {
use mul1 Estage; // read at start of Estage (stage 1)
use mul2 Estage;
use acc Estage + 1; // read at start of Estage+1 (stage 2)
def acc Estage + 1; // write at end of Estage+1 (stage 2)
}
Do not need to use acc until Estage+1
MACC
Partial logic
mul1
mul2
acc
MACC
Partial Logic
E
E+1
Pipe Stage
acc

## Slide 49: Back-to-Back MACC Pipeline Diagram – Improved Scheduling
MACC
Estage
my1
my2
my5
MACC
Estage+1
Cycle 0
my5
MACC
Estage
my3
my4
my5
MACC
Estage+1
Cycle 1
Cycle 2
“use acc Estage+1”
allows bypass
for data dependent
MACCs.
…
macc my5, my1, my2
macc my5, my3, my4
…

## Slide 50: Methods of Reducing TIE Area
regfile SR 64 4 s
operation VECMUL16 {out SR srr, in SR srs, in SR srt} {} {
wire [31:0] mtmp1 = srs[15:0] * srt[15:0];
wire [31:0] mtmp2 = srs[47:32] * srt[47:32];
assign srr = {mtmp2, mtmp1};
}
operation VECMAC16 {inout SR srr, in SR srs, in SR srt} {} {
wire [31:0] mtmp1 = srs[15:0] * srt[15:0];
wire [31:0] mtmp2 = srs[47:32] * srt[47:32];
assign srr = { srr[63:32] + mtmp2,
srr[31:0] + mtmp1 };
}
x
+
x
+
x
+
x
+
Two multiply operations
  How do we share the multipliers?
Design with shared functions and semantics.

## Slide 51: Nested Function Example
operation ADD8x4 {out AR sum, in AR in0, in AR in1}{}{
assign sum = as8x4(in0, in1, 1’b1);
}
operation SUB8x4 {out AR diff, in AR in 0, in AR in1}{}{
assign diff = as8x4(in0, in1, 1’b0);
}
function [31:0] as8x4 {[31:0] a, [31:0] b, add) {
wire [7:0] t0 = addsub(a[ 7: 0], b[ 7: 0], add);
wire [7:0] t1 = addsub(a[15: 8], b[15: 8], add);
wire [7:0] t2 = addsub(a[23:16], b[23:16], add);
wire [7:0] t3 = addsub(a[31:24], b[31:24], add);
assign as8x4 = {t3,t2,t1,t0};
}
function [7:0] addsub {[7:0] a, [7:0] b, add) {..}
Myfunction1.tie
8 addsub modules are instanced in HW
Hardware:
Each as8x4 function has 4 copies of addsub
as8x4 function calls addsub function
Two separate copies of as8x4

## Slide 52: Shared Function
Definition
  A single copy of hardware shared for all TIE operations
  Add the “shared” keyword to function description
Benefits
  Reduces area
  Enables iterative operations (discussed later)
Limitations
    A shared function should be kept simple, as it cannot be scheduled across more than one clock cycle
    A shared function cannot be nested
operation ADD8x4 {out AR sum, in AR in0, in AR in1}{}{
assign sum = as8x4(in0, in1, 1’b1);
}
operation SUB8x4 {out AR diff, in AR in 0, in AR in1}{}{
assign diff = as8x4(in0, in1, 1’b0);
}
function [31:0] as8x4 {[31:0] a, [31:0] b, add) shared { .. }
as8x4 function calls addsub function
Hardware:
Operations share one hardware instance of as8x4

## Slide 53: Sharing Hardware among Operations: semantic
regfile SR 64 4 s
operation VECMUL16 {out SR srr, in SR srs, in SR srt} {} {
wire [31:0] mtmp1 = srs[15:0] * srt[15:0];
wire [31:0] mtmp2 = srs[47:32] * srt[47:32];
assign srr = {mtmp2, mtmp1};
}
operation VECMAC16 {inout SR srr, in SR srs, in SR srt} {} {
wire [31:0] mtmp1 = srs[15:0] * srt[15:0];
wire [31:0] mtmp2 = srs[47:32] * srt[47:32];
assign srr = { srr[63:32] + mtmp2,
srr[31:0] + mtmp1 };
}
semantic arith {VECMUL16, VECMAC16} {
wire [31:0] atmp1 = VECMAC16 ? srr[31:0] : 0;
wire [31:0] atmp2 = VECMAC16 ? srr[63:32] : 0;
wire [31:0] mtmp1 = TIEmac(srs[15: 0], srt[15: 0], atmp1, 1'b0, 1'b0);
wire [31:0] mtmp2 = TIEmac(srs[47:32], srt[47:32], atmp2, 1'b0, 1'b0);
assign srr = {mtmp2, mtmp1};
}
Operation name used as qualifier

## Slide 54: FLIX – Flexible Length Xtensions
Create multi-issue VLIW-style processor to boost processor performance
  FLIX instructions can be 32, 64 or 128 bits wide (choose one)
  Modeless intermixing of 16-bit, 24-bit, and wide instructions
    Eliminates VLIW-style code-bloat
Designer-defined formats, # of slots in each format, operations in each slot
  Any combination of most base ISA and TIE operations in each slot
Compiler automatically generates instruction bundles from standard C Code to improve performance
Designer-Defined FLIX Instruction Formats with Designer-Defined Number of Operations
Example 5 – Operation, 64b Instruction Format
63
0
1
1
1
0
Operation 5
Op 4
Operation 1
Op 3
Operation 2
Example 3 – Operation, 64b Instruction Format
Operation 1
1
1
1
0
Operation 3
Operation 2
63
0
0
1

## Slide 55: TIE Language Reference: format
Format:
  format name width {slot_name0, slot_name1, …}
  Name: Name of the format
  Width: Wide instruction word width (32 or 64 or 128 bits)
  slot_name list: List of slots and their names (at most 15 slots)
TIE compiler computes width of each slot
Example:
  format myflix2 64 {slot_a, slot_b, slot_c}
slot _a
slot_b
slot_c
64-bit long

## Slide 56: FLIX Example
myflix.tie
loop:
{ l32i a8,a9,0 ; addi a9,a9,4 ; add a12,a10,a8}
{ l32i a10,a11,0 ; addi a11,a11,4 ; srai a12,a12,2}
{ s32i a12,a13,0 ; addi a13,a13,4 ; nop}
format myflix1 64 {slot_a, slot_b, slot_c}
slot_opcodes slot_a {L32I, S32I}
slot_opcodes slot_b {ADDI}
slot_opcodes slot_c {ADD, SRAI}
slot_a
slot_b
slot_c
The TIE compiler will create FLIX instructions (bundles of operations) for all possible combinations of slot opcodes (including NOP).
The C compiler will automatically infer FLIX instructions from C code to improve performance. No assembly programming required!

## Slide 57: Multiple FLIX Formats
loop:
{ l32i a8,a9,0 ; addi a9,a9,4 ; add a12,a10,a8 }
{ l32i a10,a11,0 ; bigtie a3, a3, m9, m12, 64 }
format myflix1 64 {slot_a, slot_b, slot_c}
format myflix2 64 {slot_a, slot_d}
slot_opcodes slot_a {L32I, S32I}
slot_opcodes slot_b {ADDI}
slot_opcodes slot_c {ADD, SRAI}
slot_opcodes slot_d {bigtie}
myflix.tie
Multiple Formats can be used to optimize utilization of instruction bits. A format with fewer slots can support operations that require many operands.

## Slide 58: END