## Slide 1: Improving Compression Ratios for High Bit-Depth Grayscale Video Formats
Dr. Alan D. George
Professor of ECE
University of Florida
Dr. Ann Gordon-Ross
Assoc. Professor of ECE
University of Florida
An Ho
Research Students
University of Florida

## Slide 2: Outline
Motivations
Evaluation Metrics
Current Solutions
Proposed Solutions
  Results Analysis
Conclusions

## Slide 3: Acknowledgements
Research project at CHREC
  NSF Center for High-Performance Reconfigurable Computing (CHREC)
    Founded in 2007
    Comprised of 4 university sites and over 30 industry and government partners
    3 main research domains
I/UCRC Program at NSF
  Industry/University Cooperative Research Center
    CHREC is both National Research Center and Consortium
    Basic and applied R&D in advanced computing in three major domains
See www.chrec.org for more info
Universities
Industry & Government
Basic Research
Applied R&D
CHREC

## Slide 4: Motivations
High bit-depth video format
  Use more than 8-bit per pixel
  Double the memory requirement per pixel
Overhead Persistent Infrared (OPIR)
  14-bit grayscale video
  High frame rate, at 300 Hz
Evaluated Video Test Set provided by Air Force Research Laboratory Space Vehicles Directorate
Cloud001
Cloud002
NoCloud001
Video
Compression Algorithm
Compressed Video
16-bit supported encoder
8-bit supported encoder
Lossless and Lossy

## Slide 5: Evaluation Metrics
Compression Ratio (CR)
  Quantifies the reduction in data size
  Higher CR values indicate smaller compressed file size
Root Mean Squared Error (RMSE)
  Measure the quality of a video
    Difference in pixel values in compressed file vs. raw, uncompressed file
Goal: 10 CR or more, 15 RMSE or less

## Slide 6: Current Solutions
Using video encoders to compress raw data
  Lossless mode: retain all original data
  Lossy mode: some data is lost but can achieve higher CR
Typical video encoders only support 8-bit video formats
Few existing encoders support high bit-depth video
Video
Compression Algorithm
Compressed Video
16-bit supported encoder
8-bit supported encoder
Lossless and Lossy

## Slide 7: Current Solutions
Using video encoders to compress raw data
  Lossless mode: retain all original data
  Lossy mode: some data is lost but can achieve higher CR
Typical video encoders only support 8-bit video formats
Few existing encoders support high bit-depth video
FFV1 used as baseline number for comparisons due to highest lossless CR (average of 1.62 CR)
Chart: CR
| FFV1 | FFVhuff | JPEGLS | JPEG2000
Cloud001 | 1.8495 | 1.1891 | 1.701 | 1.67
Cloud002 | 1.4759 | 0.967 | 1.401 | 1.36
NoCloud001 | 1.5156 | 1.0012 | 1.433 | 1.45
Baseline CR for each video using existing 16-bit encoders for lossless compressions

## Slide 8: Proposed Solutions
Add a preprocessing step before applying compression
  Modify input data to be more amenable to existing encoders
Methods evaluated:
  Filtering
  Region of Interest
  Factoring
  SuperFrame
  Bit-Stream Splitting
Video
Compression Algorithm
Compressed Video
Preprocessing Methods
Filtering
Region of Interest
Factoring
SuperFrame
Bit-Stream Splitting
16-bit supported encoder
8-bit supported encoder
Lossless and Lossy
OPIR Video Source
New
New

## Slide 9: Filtering
Filtering: reducing noise in a video using image processing
  Reducing noise would in turn reduce entropy of video
Evaluated using Gaussian, Median, Average, and Wiener
Results unimpressive:
  FFV1 as the encoder
  Gaussian shows lowest RMSE
  1.04x CR with RMSE over 100
Chart: Kernel Size
| 3.0 | 5.0 | 9.0 | 15.0 | 25.0 | 35.0
Average | 1.916 | 2.09 | 2.371 | 2.751 | 3.166 | 3.602
Median | 1.805 | 1.919 | 2.107 | 2.326 | 2.577 | 2.756
Wiener | 1.895 | 2.036 | 2.245 | 2.463 | 2.629 | 2.74
Gaussian | 1.78 | 1.781 | 1.781 | 1.781 | 1.781 | 1.781
Chart: Kernel Size
| 3.0 | 5.0 | 9.0 | 15.0 | 25.0 | 35.0
Average | 333.2867 | 468.7643 | 672.6812 | 895.7734 | 1145.6003 | 1318.1047
Median | 175.3026 | 270.15 | 438.8166 | 639.75 | 860.9646 | 1022.1546
Wiener | 128.7711 | 217.9564 | 365.8688 | 523.7079 | 694.1614 | 808.7274
Gaussian | 112.6632 | 112.9336 | 112.9336 | 112.9336 | 112.9336 | 112.9336
CR and RMSE for Filtering using different algorithm and kernel size

## Slide 10: Region of Interest (ROI)
ROI: split video into multiple regions (e.g. quadrants)
  Compress critical region using lossless compression
  Compress non-critical region using lossy compression
Critical region
Non-critical region

## Slide 11: Region of Interest (ROI)
ROI: split video into multiple regions (e.g. quadrants)
  Compress critical region using lossless compression
  Compress non-critical region using lossy compression
FFV1 as the encoder
  2.06x CR at RMSE of 50
Need automation in selecting ROI to be effective
CR and RMSE for ROI, averaged over the video test set using JPEG-LS, for varying quality factors

## Slide 12: Factoring
Factoring: reduce the number of bits by dividing pixel value by a factor number 2n
  n represents number of bits reduced or removed
Achieved average CR of 3.40 on average at factor 64
  2.10x increase
Factor number
FFV1 as encoder
Factoring results with the video test set for varying factor numbers in terms of CR

## Slide 13: Factoring
Factoring: reduce the number of bits by dividing pixel value by a factor number 2n
  n represents number of bits reduced or removed
Achieved average CR of 3.40 on average at factor 64
  2.10x increase
RMSE is similar across video
  RMSE of 18.5 at factor 64
Factor number
FFV1 as encoder
Factoring results with the video test set for varying factor numbers in terms of RMSE

## Slide 14: SuperFrame
SuperFrame: add redundancy by combining multiple frames into a single combined frame
  256x256 video with 4224 frames
  SuperFrame: 65536x4224 image
JPEG2000 is used as the SuperFrame encoder
  Popular image-compression algorithm for space applications
  Lossy or lossless mode
SuperFrame concept: Sequential video frames (a) are reorganized into a single SuperFrame (b) for frame-based compression
New

## Slide 15: SuperFrame Results
SuperFrame method improved CR significantly
Lossless compression mode:
  Average of 1.63x improvement
Lossy compression mode:
  At CR of 20, RMSE less than 20 for all videos
  Target CR and RMSE achievable
Chart: CR
| 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 10.0 | 20.0
Cloud001 | 0.64 | 3.67 | 8.7 | 14.88 | 21.69 | 27.27 | 44.76 | 77.67
Cloud002 | 2.936 | 15.98 | 39.95 | 69.3 | 95.33 | 111.58 | 133.62 | 149.42
NoCloud001 | 2.7 | 15.32 | 37.19 | 63.56 | 90.09 | 105.78 | 130.64 | 146.59
Chart: CR
| 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 70.0 | 100.0
Cloud001 | 0.09 | 0.25 | 0.59 | 0.96 | 1.37 | 1.68 | 2.36 | 4.81 | 7.79 | 10.5 | 13.8 | 20.71 | 28.72
Cloud002 | 0.09 | 0.54 | 1.25 | 1.99 | 2.79 | 3.59 | 6.28 | 18.12 | 32.45 | 46.56 | 60.66 | 82.33 | 100.02
NoCloud001 | 0.09 | 0.51 | 1.15 | 1.85 | 2.53 | 3.29 | 5.67 | 16.63 | 29.92 | 41.68 | 56.11 | 76.73 | 100.05
RMSE versus CR using the normal JPEG2000 image compression method
RMSE versus CR using a SuperFrame with JPEG2000

## Slide 16: Bit-Stream Splitting
Bit-Stream Splitting (BSS): split high bit-depth video into two 8-bit videos
  Allows use of 8-bit video encoders
  Access to more commercially developed encoder (e.g. H.264)
  Lossless compression on upper byte keeps overall RMSE low
BSS conceptual flow
New

## Slide 17: Bit-Stream Splitting Results
Evaluated multiple 8-bit lossless encoders using BSS
x264 provided the best CR
  3.40 for Cloud001
  2.45 for Cloud002
  2.60 for NoCloud001
Improve CR by 1.74x on average
Outperformed SuperFrame in lossless compression
Chart: CR
| FFV1 | FLASHSV | HUFFYUV | JPEGLS | PNG | QTRLE | X264 | JPEG2000
Cloud001 | 1.5725 | 1.1649 | 0.69077 | 1.554 | 1.7093 | 1.6681 | 3.3952 | 1.5
Cloud002 | 1.3502 | 0.99779 | 0.6413 | 1.3372 | 1.4883 | 1.5027 | 2.4464 | 1.29
NoCloud001 | 1.3607 | 1.0055 | 0.64627 | 1.3476 | 1.4999 | 1.5144 | 2.5901 | 1.31
CR from lossless compression with BSS

## Slide 18: Combination: BSS and Factoring
Evaluate combination of best performing methods
BSS and factoring:
  BSS using lossless x264
  Same low RMSE as factoring alone
On average:
  Increased CR by 22.4x at RMSE of 18.5
Better than using BSS or factoring alone
RMSE of 18.5
CR results when combining factoring and lossless BSS using x264 on the video test set with varying factor values

## Slide 19: Combination: BSS and SuperFrame
Apply BSS and then SuperFrame
JPEG2000 as encoder
BSS & SuperFrame has higher RMSE
BSS & SuperFrame has lower RMSE
BSS & SuperFrame has lower RMSE

## Slide 20: Combination: BSS and SuperFrame
Apply BSS and then SuperFrame
JPEG2000 as encoder
Closer look
BSS & SuperFrame has higher RMSE
BSS & SuperFrame has higher RMSE

## Slide 21: Summary and Conclusions
Extra preprocessing step enhanced CR for both lossy and lossless
  SuperFrame, BSS, factoring, and combinations of these methods
Tradeoff between large CR increase and loss of data quality
  Enable system designers to select appropriate preprocessing method
Expand on range of available encoders using new BSS method
  Use of 8-bit encoders on high bit-depth video format
Future works:
  Research space processor architectures for best fit to implement preprocessing methods
  Evaluate resource and overhead cost to run preprocessing methods

## Slide 22: Questions