## Slide 1: Comparative Analysis of Parallel OPIR Compression on Space Processors
  Eric Shea
  M.S. Student
  University of Pittsburgh
  An Ho
  M.S. Graduate, University of Florida
  (now at Harris)
2017 IEEE Aerospace Conference
  Dr. Alan D. George
  Mickle Chair Professor of ECE
  University of Pittsburgh
  Dr. Ann Gordon-Ross
  Assoc. Professor of ECE
  University of Florida

## Slide 2: Outline
Introduction
Video Preprocessing Methods
Compression Methods
Experimental Setup
Platforms Analyzed
16-Bit Encoder Analysis
8-Bit Encoder Analysis
16-Bit vs 8-Bit Encoder Analysis
Conclusions and Future Research

## Slide 3: Introduction
Video compression on space processors
  Increasing high bit-depth on next-generation image sensors presents unique challenges
    Limited resources, such as memory and download bandwidth, requires more efficient preprocessing and compression methods
    Existing methods use limited/incompatible proprietary data encoders lacking preprocessing for limited resource environments
    Balance between video quality and data throughput
We present novel real-time processing on high bit-depth video for different processor architectures
  Perform preprocessing and compression faster than transmitting raw data based on available bandwidth
  Achieve better compression ratios with minimal effect on video quality and latency

## Slide 4: Video Preprocessing Methods
  1) Bit-Stream Splitting (BSS) [1]
    Splits high bit-depth video into separate upper and lower byte video files
    Enables use of 8-bit encoders and parallelization
  2) SuperFrame [1]
    Consecutive frames placed in one massive SuperFrame to leverage image encoders
Bit-Stream Splitting
SuperFrame
[1] A. Ho, A. George, A. Gordon-Ross “Improving Compression Ratios for High Bit-Depth Grayscale Video Formats,” Proc. Of IEEE Aerospace Conference 2016

## Slide 5: Compression Methods
  1) Baseline method
    Serially compresses each split file using a single thread
  2) Parallelized method
    Uses FFmpeg’s built-in multithreading capabilities to operate on both split files in parallel
  3) Enhanced Parallelized method
    Executes multiple encoder threads in parallel
    Dynamically re-allocates threads to cores after thread completes execution
    Performed with BSS and 8-bit encoders

## Slide 6: Experimental Setup
Using video data taken from 14-bit Overhead-Persistent InfraRed (OPIR) image sensor
  Video files contain ~4000 frames of various cloud cover
  Files provided by AFRL Space
Using open source FFmpeg compression library [5]
  Encoders tested: PNG, FFV1, FFVhuff, JPEG-LS, FFV1 V3, x264
    Performed lossless compression with 16-bit encoders, and lossless and lossy compression with 8-bit x264
[5] FFMPEG [Online]. Available: http//:www.ffmpeg.org

## Slide 7: Platforms Analyzed
  ODROID-C2
    Amlogic S905 with quad-core ARM Cortex-A53 (akin to HPSC)
    1.50 GHz clock frequency
  Avnet Zedboard (akin to CSP)
    Xilinx Zynq-7020 with dual-core ARM Cortex-A9
    0.766 GHz clock frequency
  NXP P5040 Evaluation Board
    FreeScale P5040 with quad-core e5500
    2.20 GHz clock frequency
  BAE Systems RAD5545
    Extrapolated results [8] using device metrics which revealed that RAD5545 achieves, on average, 21.8% of P5040 performance
    0.466 GHz clock frequency
[8] T. Lovelly, D. Bryan, K. Cheng, R. Kreynin, A. George, A. Gordon-Ross, and G. Mounce, “A Framework to Analyze Processor Architecture for Next-Generation On-Board Space Computing,” Proc. of IEEE Aerospace Conference 2014.
COTs equivalent and space-grade processors

## Slide 8: 16-Bit Encoder Analysis
  PNG and FFV1 version 3 offered significant improvement with increasing number of cores
    Negligible improvement for FFV1 and FFVhuff
  FFVhuff offered fastest execution time due to inefficient compression of OPIR video
  P5040 and Amlogic S905 offered best 16-bit performance due to faster clock speeds
FFVhuff performed extremely well offering 11.6x speedup over PNG
No BSS required
RAD5545 achieves 21.8% performance of P5040
1.0x
2.0x
1.0x
1.7x
1.0x
1.0x
1.0x
1.0x
2.9x
2.4x
1.0x
3.9x
2.6x
1.0x
3.9x
2.6x
Offers 4.7x average speedup over next fastest platform, S905
No improvement
No improvement
FFVhuff performed extremely well offering 4.2x speedup over PNG

## Slide 9: 8-Bit Encoder Analysis
  x264 supports multithreading using pthreads
  Execution time decreased by nearly 2x using two threads compared to single thread
    Increases overall with increasing quality factor due to addition of quantization step
    Augmented compression method performed extremely well with 3.4x average speedup over baseline method
    Relative speedup between compression methods increases with increasing quality factor
4.2x
1.0x
1.0x
3.6x
1.0x
1.0x
3.2x
3.5x
BSS required
1.0x
3.2x
1.0x
3.5x
1.0x
3.2x
1.0x
2.9x
Offers 2.8x average speedup over next fastest platform, P5040
Fastest due to efficient handling of threads
RAD5545 achieves 21.8% performance of P5040
S905 outperforms P5040 but was opposite for 16-bit encoders
Best speedup between compression methods with increasing quality factor
1.3x
1.2x
1.1x
1.0x
3.6x
1.0x
2.3x
1.0x
1.9x
1.0x
1.9x
1.0x

## Slide 10: 16-Bit vs 8-Bit Encoder Analysis
  BSS with x264 compression results in fastest total run-time for bandwidths less than 3 Mbps
    Provided highest compression ratio [1]
  FFVhuff provided fastest 16-bit execution time but performed worst in total run-time
    Does not compress OPIR video efficiently
  Mix between RAW and JPEGLS being fastest at much higher bandwidths
Raw data fastest at all bandwidths
[1] A. Ho, A. George, A. Gordon-Ross “Improving Compression Ratios for High Bit-Depth Grayscale Video Formats,” Proc. Of IEEE Aerospace Conference 2016
JPEGLS fastest at high bandwidths
Total Run Time = Execution Time + Transfer Time
1.0x
2.7x
1.0x
2.2x
RAW fastest
RAW Fastest
1.0x
2.7x
1.0x
2.7x
JPEGLS fastest at high bandwidths
FFVhuff averaged 2.6x slower than x264

## Slide 11: Conclusions and Future Research
Analysis of performance of 16-bit and 8-bit encoders on multiple space processors
  Analyzed execution time using three different compression methods
    PNG and FFV1 version 3 offered much improvement with increasing number of cores
    16-bit encoders executed faster since BSS not needed
    P5040 had 4.7x speedup over Amlogic S905
  Analyzed total run-time
    BSS and x264 combination was fastest at lower bandwidths while JPEGLS and RAW were fastest at higher bandwidths
    Amlogic S905 and P5040 had best performance due to highest clock speeds
Expand analysis to new devices and SuperFrame method
  Use SuperFrame method to leverage image encoders
  Integrate encoder IP cores on FPGAs and analyze total run-time