## Slide 1
Research highlighted in this presentation was supported by CHREC members and by the I/UCRC Centers Program
of the National Science Foundation under Grant Nos. EEC-0642422 and IIP-1161022.
2017 IEEE Aerospace Conference, 10MAR17
Investigators and Students
Christopher Wilson, Sebastian Sabogal, Alan D. George, Ann Gordon-Ross
Research Partners
University of Pittsburgh, University of Florida
Hybrid, Adaptive, and Reconfigurable Fault Tolerance

## Slide 2: Outline
Acknowledgements
Background
  Space Environment & Design Challenges
  CSP Concept & CSPv1 on ISS
  FPGAs & Partial Reconfiguration
  Asymmetric Multiprocessing
Approach
Conclusions & Future Work

## Slide 3: Acknowledgements
Research Project at CHREC
  NSF Center for High-Performance Reconfigurable Computing (CHREC)
    Founded in 2007
    Comprised of 4 university sites and 30+ industry and government partners
    3 main research domains
I/UCRC Program at NSF
  Industry/University Cooperative Research Center
    CHREC is both National Research Center and Consortium
    Basic and applied R&D in advanced computing in three major domains
See www.chrec.org for more info
Universities
Industry & Government
Basic Research
Applied R&D
CHREC

## Slide 4: Background

## Slide 5: Harsh Space Environment
Challenging Environment
  Designers must consider hazards of radiation effects
Radiation Particles and Sources
  Solar flares & coronal mass ejections
  Galactic cosmic rays
  Trapped protons & high-energy ions
Radiation Effects
  Temporal effects
    Single Event Effects (SEE): Upset (SEU), Transient (SET), Latch-up (SEL), Burnout (SEB), Gate Rupture (SEGR),Functional Interrupt (SEFI)
  Cumulative effects
    Total Ionizing Dose Levels (TID)
    Enhanced low-dose-rate sensitivity (ELDRS)

## Slide 6: Design Challenges
Challenges
  Limited downlink bandwidth
  Escalating demands for high-performance on-board sensor-data and autonomous processing
Requirements
  Space environments have strict requirements and restrictions
  Performance (throughput and real-time)
  Size, Weight, Power, Cost (SWaP-C) & Reliability
Radiation Effects
  Radiation from space is harmful to electronic devices
  Radiation commonly manifests as SEEs
    Occurs when particle strikes device causing deposit or removal of energy which inverts transistor state
    Usually observed as bit-flip in memory cell and can result in several upset modes (i.e. reset of device, silent data error, system crash, system hang etc…) on general-purpose processor
Low Power
Low Cost
Speed
Depend-ability
Lifetime
0011
1000

## Slide 7: CHREC Space Processor (CSP)
Overview
Concept
Create high-performance and reliable space computing platform to fulfill variety of demands in mission requirements
Hybrid system (COTS + RadHard technology)
Hybrid processor (Xilinx Zynq-7020) (Fixed + Reconfigurable logic subsystems)
Motivation
Multifaceted hybrid space computer

## Slide 8: CSPv1 Onboard ISS on STP-H5
Successfully Installed on ISS with Space Test Program – Houston 5 (STP-H5) as part of ISS SpaceCube Experiment Mini (ISEM)
Features 2 CSPv1 Computing Cards
Launched in Feb 19 on SpaceX CRS-10
Preliminary Functional Checkout Successful
SpaceX CRS-10 Launch
STP-H5 Installation
CSPv1 Flight Unit

## Slide 9: Zynq SoC Architecture
Fixed logic: dual-core ARM® Cortex™-A9
Reconfigurable logic: Artix®-7 FPGA

## Slide 10: Effects of SEE on FPGAs
Field-Programmable Gate arrays (FPGAs) Provide Large Amounts of Logic Resources Connected with Complex, Configurable Routing Network
  Logic resources: LUTs & FFs
  Routing resources: switchboxes
  Specialized resources: BRAMs, DSPs, etc.
Configuration Memory Stores FPGA Design
  Modification of configuration memories affects functionality of device
  SEE can cause bit-flips and other errors
Mitigation on FPGAs
  Accepted practice to run Triple Module Redundancy (TMR) on circuits and scrubbing
    TMR – triplicated circuit with voter for error masking
    Scrubbing – background config. memory checking for FPGAs

## Slide 11: Intro. to Partial Reconfiguration
Partial Reconfiguration (PR): Process of Reconfiguring Sections of FPGA at Runtime
  Program PR module (PRM) without reconfiguring entire FPGA and without interrupting remainder of system
  Rotation of PRMs for large suite of available applications
Reduce Vulnerable Configuration Area & Power Consumption
Extend Post-Mission Operation and Capabilities
Dynamically Switch between Multiple Fault-Tolerance Techniques
Zynq-7020 FPGA floor plan w/ purple-outlined PR regions

## Slide 12: Introduction to AMP
What is AMP?
  Asymmetric multiprocessing (AMP) is mechanism that allows multi-core devices to have cores that run their own operating systems or bare-metal applications
Advantages of AMP
  Security
    Secure software zoning of secure applications
  Fault-tolerance
    Separate application and critical flight software
    Redundant processing
  Interactive and real-time processing
SMP
AMP

## Slide 13: Approach

## Slide 14: Introduction to Hybrid Adaptive Reconfigurable Fault Tolerance
PROBLEM
Hybrid SoCs present numerous architectural advantages, however, there are FT architectural disadvantages
Systems need to respond to changing environment
MOTIVATION
Find synergy of hybrid SoC subsystems for FT
Use adaptive systems to optimize system configuration for current radiation environment
CHALLENGE
Realize flight-system proof-of-concept testbed
Involves understanding of integration of CPU and FPGA subsystems

## Slide 15: Fault-Tolerant Computing Facet
Fault-Tolerant Computing (FTC)
Research Focused on Improving Reliability of CSPv1 with FTC
Hybrid Capability
  Build FT strategy for hybrid SoC architecture by combining fixed and reconfigurable FT strategies
Reconfigurable Capability
  Environmentally aware configuration manager monitors FPGA configuration upsets while scrubbing to approximate current upset rate
  Adapt to changing upset rate by optimizing usage of resources in performance-reliability trade space
  FT modes in fixed-logic processor and reconfigurable-logic FPGA

## Slide 16: HARFT Modes of Operation
3
MODES Fault Tolerance
HARFT
01
MODE
02
MODE
03
MODE
Asymmetric Multiprocessing (AMP)
Cores run pseudo-independently for greater reliability in hard environments
Additional functionality possible with real-time operation on second core
FPGA-Enhanced Fault Tolerance (FEFT)
    PRRs in SPS operate MicroBlaze in simplex, duplex, or triplex configurations for reliability
Hardware accelerators can take place of soft cores for additional app acceleration
Symmetric Multiprocessing (SMP)
Dual-core HPS operates using both cores together for maximum performance
Accelerated modes including OpenMP and distributed processes available

## Slide 17: HARFT Architecture Overview
Programmable
Logic
Hard
Processing
System
ICAP
Storage
I/O
Interconnect
SPS
Static
Configuration
Manager
· · ·
Partial
Reconfiguration
Region N-1
Partial
Reconfiguration
Region 0
M
M
M
M
M
Memory
FRAME
ECC
High-Performance Hard Processing System (HPS) [ARM Cores]
Redundant Soft Processing System (SPS) [FPGA]
  Lockstepped MicroBlazes aggregated as one
Static Triplicated Configuration Manager (ConfigMan)
  Configuration memory scrubbing
  Manages system configuration
Partial Reconfiguration Modules
  MicroBlaze soft-core processors
  Auxiliary peripherals or accelerators

## Slide 18: ConfigMan Features
Environmentally Aware
  Performs readback scrubbing to detect faults in configuration memory
  Aging-window algorithm for approximating SEU rate (i.e., number of faults for given period of time)
System Adaptation with Dynamic- Mode Switching
  Repurpose system resources for performance or for reliability based on current SEU rate
  Aggregate or decouple HPS cores
  Reconfigure PRMs
  Manual mode switching: User-implemented policy for reconfiguring system behavior in advance

## Slide 19: Concept of Operation
Reliability Mode 2
HPS in AMP mode
SPS in triplex operation
Reliability Mode 1
HPS in AMP mode
SPS in duplex operation
Programmable
Logic
ICAP
Storage
I/O
Interconnect
SPS
Static
Configuration
Manager
M
M
M
M
M
Memory
FRAME
ECC
Soft Core
Soft Core
Soft Core
Auxiliary
Auxiliary
Auxiliary
Reliability Mode 0
HPS in AMP mode
SPS in simplex operation
High-Performance Mode
HPS in SMP mode
SPS is not present

## Slide 20: Prototype Description
Proof-of-Concept Prototype for HARFT was Developed using Digilent ZedBoard containing Zynq-7020 (same Device as CSPv1)
HARFT Concept Encompasses several Degrees of Freedom in System Configurations and User-Defined Policies for Configuration Management
HARFT Prototype
  HPS configuration:
    SMP: CPU0 + CPU1 run Xilinx Linux
    AMP: CPU0 runs Xilinx Linux, CPU1 runs baremetal or RTOS application
  SPS configuration: 3 PRRs, mix of MicroBlazes and AXI4 peripherals
  ConfigMan configuration: Mode switching based on user-configurable upset thresholds
  Miscellaneous details: Prototype contains logic or software for development and debugging that would not be present in actual flight

## Slide 21: Resource Utilization
Prototype Total Resource Utilization
Resource | Used | Available | Util%
Slice-LUTS | 13931 | 53200 | 26.19
Slice-Registers | 11303 | 106400 | 10.62
BRAM Tile | 1 | 140 | 0.71
RAMB36 | 0 | 140 | 0.00
RAMB18 | 2 | 280 | 0.71
DSP48E1 | 18 | 220 | 8.18
PRR Resource Utilization
Resource | PRR0 | PRR1 | PRR2 | Total
Slice-LUTS | 2428 | 2433 | 2440 | 13931
Slice-Registers | 1884 | 1884 | 1884 | 11303
BRAM Tile | 0 | 0 | 0 | 1
RAMB36 | 0 | 0 | 0 | 0
RAMB18 | 0 | 0 | 0 | 2
DSP48E1 | 6 | 6 | 6 | 18
HARFT on Zynq SoC Floorplan
Color | Component
Cyan | ConfigMan
Purple | SPS-SL
Light Blue | Miscellaneous resources
Yellow, Red, Blue | MicroBlaze PRMs

## Slide 22: Performance Modeling
Processor | Computational Density (GOPS) |  | 
 | INT8 | INT16 | INT32
ARM Cortex-A9 Dual-Core | 32.02 | 16.01 | 8.00
ARM Cortex-A9 Single-Core | 16.01 | 8.00 | 4.00
MicroBlaze Processor | 0.125 | 0.125 | 0.125
Operation | Duration (sec)
Readback (Entire FPGA) | 14.5246
Readback (Frame) | 0.001888
Writeback (Entire FPGA) | 19.9478
Writeback (Frame) | 0.002593
Configuration | Iterations/sec
HPS (ARM) with Caches Single-Core | 1993.6778
HPS (ARM) w/o L2 Cache Single-Core | 1971.2254
SPS (MicroBlaze) | 9.5975
Computational Density Device Metrics
FPGA Scrubbing Duration
CoreMark Benchmarking
Processor Performance
  Dual-core ARM > single-core ARM
  Single-core ARM > MicroBlaze core
  Benchmark may not be large enough to fully leverage L2 cache memory
Configuration Memory Scrubbing is Relatively Faster than Upset Rates in LEO

## Slide 23: Reliability Modeling
Challenges
  Need for modeling from system, not component, perspective
  Clear and practical methodology for assessing design with COTS
Overview
  4-stage methodology for estimating reliability of computers for small satellites from system-level perspective due to radiation
  Reviewed with NASA GSFC radiation effects branch
Key Usage Features
  Gauge general board reliability to provide first-order estimates
  Help compare reliability of different boards designs
  See how each component effects affects overall design reliability
  Evaluate FTC mechanisms of within given design
  Relies on state-of-the-art tools (CRÈME, RHA, SECCA etc…)
C. Wilson, A. George, and B. Klamm “A Methodology
for Estimating Reliability of SmallSat Computers in
Radiation Environments,” 2016 IEEE Aerospace Conf.,
Big Sky, MT, Mar 5 - 12, 2016.
Component Analysis
Radiation Data Collection
Mission Parameters, RTRP
Fault-Tree Construction
Component Radiation
List Concerns
Radiation Literature Database Survey
Established Tools
Dynamic Fault Tree
ESTIMATE

## Slide 24: Reliability Over Time
HARFT Reliability with L2 Cache Disabled
HARFT Reliability with L2 Cache Enabled
“FPGA” – If every bit on FPGA was essential for reference
Upset Rates Calculated for LEO
L2 Cache is Responsible for Majority of Upsets in Processing System
FEFT-TMR reliability near 1 because scrubber correction rate is higher than LEO upset rate
AMP next best
PS modes become worse with L2 cache enabled

## Slide 25: Performance vs Upsets Per Day
Upset Rates Calculated for LEO
Calculations for SMP Estimated by Doubling Single-Core Results
Only useful to switch between AMP, SMP,
and FEFT-Triplex when L2 cache is disabled
Upsets Per Day vs. Performance with L2 Cache Disabled
Upsets Per Day vs. Performance with L2 Cache Enabled
HPS shows drastically higher performance but much more prone to upsets
FEFT-Duplex and FEFT-Simplex are viable options

## Slide 26: Conclusions
Major Challenges Lie Ahead…
  Small missions are becoming more prevalent
    SoC and hybrid devices will become more common on spacecraft
  Radiation will have different effects on architectures and hybrid fault-tolerance techniques will be needed
Hybrid Adaptive Reconfigurable Fault Tolerance
  Novel, hybrid fault-tolerant framework (HARFT) designed to adapt to dual architecture needs of SoC device
  Prototype demonstrated 3 configurable modes
    (1) Symmetric Multiprocessing (SMP) + Accelerators
    (2) Asymmetric Multiprocessing (AMP) + Accelerators
    (3) FPGA Enhanced FT + Sub-configurations (TMR, duplex, etc…)

## Slide 27: Future Plans
Evolving HARFT
  Mature HARFT prototype into user- defined framework
  Extend experimentation and analysis with fault injection and radiation beam testing
  Map HARFT on Zynq UltraScale+ MPSoC
    FT modes for quad-core ARM Cortex-A53 (HPS)
    FT modes for UltraScale Architecture PL (SPS clusters + high-performance HW acceleration)
    Lockstepped ARM Cortex-R5 (ConfigMan)
HARFT in Flight
  Derivative of HARFT framework is planned for Space Supercomputing for Image and Video Processing (SSIVP) on STP-H6 mission (2018)
Performance
Power
Dependability
Redundant
Soft Core
Redundant
Soft Core
Redundant
Soft Core
Accelerator1
Accelerator0
Accelerator2
Voter
Arbiter

## Slide 28: Questions?