## Slide 1: SCIPS: An Emulation Methodology for Fault Injection in Processor Caches
Nicholas Wulf
Grzegorz Cieslewski
Ann Gordon-Ross
Alan D. George
3/7/2011

## Slide 2: Fault Injector Background
Automated fault-injection tools
  Validation of system design characteristics
  Demonstration of system robustness in presence of certain faults
Fault injectors typically fall into 1 of 3 categories
  Hardware-Based: Physical radiation of device
    Complete test of all device components
    Expensive and requires special testing platform
  Simulation-Based: Modeling of faults and their effects in simulated environment
    Full control over fault placement and observation
    Requires simulation; May not consider all fault types
  Software-Based: Modify software to simulate faults during runtime
    Cheaper that hardware-based, more accurate/realistic than simulation-based
    Restricts testing from certain important components such as processor cache

## Slide 3: SPFI-TILE: SW-Based Injector
The Simple Portable Fault Injector (SPFI)
  Represents group of fault-injectors, each targeting different systems
    PowerPC, FPGA, Embedded PowerPC on FPGA
  Software runs as normal, pauses at random point, corrupts single bit, and resumes execution
  SPFI analyses output of test program
    If output is incorrect, then error has occurred
SPFI-TILE: Injector for TILE64
  Able to inject faults into several areas
    Register file, main memory, instruction stream
  Tests a single-bit upset during runtime
  Able to target specific tile when test program parallelized on multiple tiles
  Easily portable to MAESTRO device

## Slide 4: Adding Cache Injection
Testing cache for susceptibility to faults is critical to total system verification
  Cache typically largest component on die
    Larger physical size causes increased upset rate
  Unfortunately, SW-based fault injectors can’t access cache directly
SPFI-TILE can leverage abilities to emulate cache injection
  Lack of cache injection is major downside to SW-based fault injectors
  Cache injection makes SW-based much more attractive approach
Faulty cache data must be loaded in order to cause errors
  As usual, SPFI-TILE randomly pauses execution during test program
  Steps through instructions until reaching the first load instruction (FLI)
  Data being loaded from is corrupted before the load
  Execution resumes with corrupted load data, emulating cache fault
IBM PowerPC 970MP

## Slide 5: Drawback to FLI Method (FLIM)
No direct access to cache, no knowledge of its true behavior
  Must assume all load instructions (LI) are equally likely to load faults
First Load Instruction Method (FLIM) favors certain LIs
  Example code on right illustrates this unbalanced injection problem
  Ex. Code loops continuously from 1st to 5th address due to jump instruction
  SPFI-TILE stops randomly on any 1 of the 5 instructions, then looks for FLI
    FLI for 2nd address is Load_2
    FLI for all other address is Load_1
  Load_1 receives 80% of injections
This unbalanced injection results in biased measurements
  Unrelated to unequal fault-inducing prob. from hidden cache behavior
  Simply an artifact of the instruction execution flow
Address | Instruction
1st | Load_1
2nd | Load_2
3rd | Non-Load
4th | Non-Load
5th | Jump to 1st Address
Example of simple loop in a programs instruction stream

## Slide 6: Injection Balancing with SCIPS
SCIPS provides method to balance injection rates
  Stands for Smooth Cache Injection Per Skipping
  Modifies FLIM by randomly skipping LIs instead of always using FLI
Consider same sample code with 5-address loop
  With SCIPS, there is a 50% chance that the FLI is skipped and the next LI is used for injection instead
  What is chance of injecting into Load_2?
    20% chance to stop on 2nd Address and 50% chance to use the FLI
    80% chance to not stop on 2nd Address and 50% chance to skip to the next LI
    (0.2)(0.5) + (0.8)(0.5) = 50%
Simply adding a single skip 50% of the time removes the unbalanced injection problem caused by FLIM
Address | Instruction
1st | Load_1
2nd | Load_2
3rd | Non-Load
4th | Non-Load
5th | Jump to 1st Address
Example of simple loop in a programs instruction stream

## Slide 7: SCIPS and Convolution
How does previous example work with more complex code?
  Assume that example loop executes 20 times (100 instructions total)
    Probability of stopping on nth LI is
  The probability of SCIPS skipping n LIs is given by its PMF Pskip[n]
    For previous 50-50 example,
  Let PSCIPS[n] equal the fault-injection probability of injecting into the nth LI using SCIPS with a skipping PMF equal to Pskip[n]
    Calculating PSCIPS[n] for given n involves summing the following values
      Probability of skipping 0 times when the nth LI is the FLI
      Probability of skipping 1 time when the (n-1)th LI is the FLI
      Probability of skipping 2 times when the (n-2)th LI is the FLI
      Continue this pattern until Pskip[n] reduces to zeros
    This pattern is equivalent to
The problem of finding the right PMF for Pskip[n] is identical to finding an FIR filter to remove AC signals from the code!

## Slide 8: Simulation Results
Theoretical prediction (top) and simulation (bottom) of fault-injection probabilities across all load instructions for synthetic code using FLIM (highly peaked line) and SCIPS (smoother line)
Theoretical (top) and simulated (bottom) injection count PFM for a given load instruction using FLIM (dispersed groups) and SCIPS (tight grouping)
MATLAB analysis used to test theory
  Synthetic code generated to simulate injections
    Created set of 200 instructions that loops 25 times
    LIs randomly distributed throughout set (20% LIs)
  Provides theoretical and simulated results
    Theoretical results based on convolution analysis
    Simulated results based on 100,000 test runs
      Each consisted of randomly stopping within the code and randomly choosing a LI based on PMF
Results confirm SPIPS convolution theory
  Results on right show injection prob. for each LI
    About 1000 LIs, so an average of 0.1% is expected
    SCIPS smoothes out unbalanced injection probabilities
  Left results show inj. count PMF for a given LI
    Based on 100,000 injections across 1000 LIs, the average number of injections for a given LI is 100

## Slide 9: Testing on SPFI-TILE
Integrated SCIPS into SPFI-TILE to confirm effectiveness
  Parallel (5 tiles) integer matrix multiply code used as test program
    Calculates C matrix as product of A (550x600) and B (600x650) matrices
    Innermost loop (in red on right) accounts for 99% of total calculation time
      Recieves 99% of injections
Innermost loop of matrix multiply code is focus of the test
  Bottom right shows the address range of innermost loop’s execution
  Each box represents single instruction
    40 total instructions (0x11DA8 – 0x11EE0)
    Gray boxes not included in loop
    Red boxes represent LIs
      Predicted FLI probabilities shown
    White boxes show non-load instructions
  Addresses 0x11DB0 and 0x11EC0 receive 1/3 of injections with FLIM
for (int i=0; i<rowCount; i++) {
for (int j=0; j<dimWC; j++) {
int sum = 0;
for (int k=0; k<dimInner; k++) sum += matA[i][k] * matBtp[j][k];
matC[i][j] = sum;
}
}
Main loop for parallel matrix multiply test program (innermost loop highlighted in red)
Addresses for innermost loop (LIs highlighted in red with predicted FLI probabilities)

## Slide 10: SPFI-TILE Results
Different skipping PMFs were applied to SCIPS during tests
  Each column in figure represents injection distribution for unique PMF
  PMFs are uniform from 0 to some max number of skips
    Equivalent to using a moving average filter on FLIM distribution (1st column)
Results show SCIPS removes imbalance caused by FLIM
  FLIM equivalent to skipping 0 times
    0x11DB0 and 0x11EC0 most likely for injection
  As skipping range increases, injection peak is stretched across subsequent LIs
    Near uniform results when skipping range reaches 13 or more

## Slide 11: Conclusions
SW-based fault injectors can emulate cache injection by monitoring instruction stream and modifying memory
  This emulation strategy inherently leads to unbalanced injection rates that are uncharacteristic of the hidden cache behavior
SCIPS provides method to balance biased injection rates
  MATLAB simulation shows 97% reduction in variance of inj. prob.
  SPFI-TILE experiment showed near complete smoothing of injection rates with as low as 13 skips
SCIPS behavior is well defined and analogous to convolution
Acknowledgements
  Special thanks to Marti Bancroft and the National Reconnaissance Office for their support in providing equipment and tools